## Slide 1: PBIC Automated Vehicle Module Series
Last Updated: July 7, 2019
Notes: Slides were developed in 2019 Michael Clamann and Laura Sandt, UNC Highway Safety Research Center. Funding was provided by the Pedestrian and Bicycle Information Center (PBIC).
Suggested Citation: Clamann, M. and Sandt, L. PBIC Automated Vehicle Module Series. Pedestrian and Bicycle Information Center, Chapel Hill, NC: 2019.
Disclaimers:
The focus of this module series is on automated vehicles, not connected and automated vehicles (CAV). In the context of these materials, vehicle connectivity is a possible component of vehicle automation, but it is not assumed to be part of the technology.
Use of links, companies and products in these materials are for instructive purposes only and do not imply endorsement or support of any of the linked information, services, products, or providers.

## Slide 2: Acknowledgement
This material is based upon work supported by the Federal Highway Administration under Cooperative Agreement No. DTFH61-16-H-00029. Any opinions, findings, and conclusions or recommendations expressed in this publication are those of the Author(s) and do not necessarily reflect the view of the Federal Highway Administration and the National Highway Traffic Safety Administration.
Notes: Disclaimer: This material is based upon work supported by the Federal Highway Administration under Cooperative Agreement No. DTFH61-16-H-00029. Any opinions, findings, and conclusions or recommendations expressed in this publication are those of the Author(s) and do not necessarily reflect the view of the Federal Highway Administration and the National Highway Traffic Safety Administration.

## Slide 3: Learning Objectives
After completing these modules, students will be able to:
Understand basic automated vehicle (AV):
  Terminology
  Technology components
  Development history, demonstrations, and future projections
  Testing procedures
  Rulemaking
Articulate the challenges with detection and processing of pedestrians and bicyclist (ped/bike) info, and human-machine communication
Explain the factors involved in crashes and agency/public reactions during early deployment
Define key priorities and opportunities to enhance ped/bike safety and mobility as more AV technologies emerge
Describe the regulatory environment and government agencies involved in AV deployment

## Slide 4: Available Modules
Key Definitions
AV Development: Past, Present, and Future
AV Technology: How it Works (or Doesn’t)
AV Testing Basics
Pedestrian and Bicyclist Interaction
Rulemaking Basics for AVs
Considerations for Ped/Bike Planners, Engineers, and Stakeholders
Notes: Notes to Instructor:
Select a link to jump to a specific module

## Slide 5: Key Definitions
Notes: Notes to Instructor: This module summarizes key automated vehicle terminology used in these modules and explains the six SAE automation levels.

## Slide 6: Automation Terminology
Automation – An electronic or mechanical device that operates one or more vehicle functions without direct human control
Automated vehicle – A vehicle equipped with driving automation technologies. Refers to a vehicle with any form of driving automation (SAE Level 1-5).
Advanced driver assistance system (ADAS) - Hardware and software designed to help drivers with specific tasks with the goal of improving safety and/or reducing driver workload. Refers to SAE Level 0-2 features.
Automated driving system (ADS) – Hardware and software capable of performing all aspects of the driving task on a sustained basis. Refers to an SAE Level 3-5 vehicle.
Conventional Vehicle - A vehicle designed to be operated by a human driver during part or all of every trip.
Other terms such as self-driving, autonomous, driverless, highly automated, and unmanned have also been used to describe vehicles with automated driving systems
Notes: Speaker notes:
There is a lot of confusion over the vocabulary used to describe automated vehicles. Multiple terms can be used to describe similar or identical technology and terms are often used inconsistently or incorrectly. To reduce confusion, these modules will employ terms defined in NHTSA and SAE reports. The definitions are introduced here to provide a common understanding of what constitutes an “automated vehicle.”
Further reading:
Descriptions of currently available advanced driver assistance systems (ADAS) are summarized at the National Safety council’s MyCarDoesWhat.org.
Automated Vehicles 3.0: Preparing for the future of Transportation (https://www.transportation.gov/av/3/preparing-future-transportation-automated-vehicles-3)
Reference:
Surface Vehicle Recommended Practice J3016: Taxonomy and Definitions for Terms Related to Driving Automation Systems for On-Road Motor Vehicles (June 2018)

## Slide 7: Automation Terminology
Dynamic Driving Task (DDT) - All the tactical functions required to operate a vehicle in traffic, including:
  Lateral control (steering)
  Longitudinal control (acceleration and deceleration)
  Monitoring the driving environment
  Responding to objects and events
  Planning maneuvers
  Signaling and maintaining visibility
  (DDT does not include strategic functions such as selecting destinations and scheduling trips)
Notes: Speaker notes:
These terms are frequently used to explain the capabilities and limitations of automated vehicles, particularly in current engineering standards (e.g., SAE) and government policy documents. DDT summarizes all the tasks that can be performed by a human driver or automation and lays the foundation for introducing the six automation levels.
Point out that monitoring, responding, and signaling to pedestrians and bicyclists are all tasks that drivers do that will need to be performed by driving automation, if automated vehicles are going to be deployed.
Reference:
Surface Vehicle Recommended Practice J3016: Taxonomy and Definitions for Terms Related to Driving Automation Systems for On-Road Motor Vehicles (June 2018)

## Slide 8: Automation Terminology
Operational Design Domain (ODD) - Operating conditions under which a system is designed to function, including:
  Environmental (e.g., weather, temperature)
  Geographical (e.g., parking lot, highway, national park, closed course)
  Time-of-day (e.g., day, night, dusk)
  Roadway characteristics (e.g., lane markings, construction zone)
Notes: Speaker notes:
ODD can be summarized a “where and when” the vehicle can operate without human input.

## Slide 9: Automation Terminology
Fallback – Following a system failure or exit from the vehicle’s ODD:
  Response by a human driver to take over the DDT or move the vehicle to safety, or
  Response by an ADS to move the vehicle to safety

## Slide 10: Automation Terminology
Artificial Intelligence - Sophisticated software algorithms required to perform the steps used to perceive objects and make decisions
Example techniques:
  Machine learning
  Deep learning (DL)
  Deep reinforcement learning
  Deep neural networks (DNN)
  Convolutional neural networks (CNN)
  Recurrent neural networks (RNN)
Notes: Speaker notes:
The inner workings of these artificial intelligence algorithms are generally the topic of advanced computer science lectures. In general, machine learning allows a computer to make an informed prediction about incoming sensor data based on rules programmed into an algorithm. This process allows the machine to “learn” from experiences and self-improve, but it is only capable of processing data that it recognizes. So any new data encountered will lead to unexpected outcomes.
Deep Neural Networks are constructed to mimic the interconnected web of neurons in the human brain. A DNN is comprised of many layers of interconnected neuron nodes. Starting with an input layer, data is fed through hierarchal layers of neural nodes to an output layer. Each layer receives data as input, classifies the data, and passes the data on as an output to the next layer. Neural nodes within layers assign a weight to the data that either strengthens or diminishes the input based on classification criteria. Once data has fully passed through the network, the machine classifies the data based on its weights at neural nodes in each layer of the algorithm. Deep neural networks need to be trained on large datasets that include all possible conditions.

## Slide 11: Connectivity Terminology
Vehicle to everything (V2X) communication
  Transfer of information between vehicles and other entities. This would be facilitated by new network communication technology
Vehicle to infrastructure (V2I)
  Communication between vehicle and the highway and traffic system, such as traffic lights, signs, and roads.
Vehicle to pedestrian (V2P)
  Communication between vehicle and pedestrians to indicate vehicle intent and produce warnings.
Vehicle to vehicle (V2V)
  Communication between vehicles to share basic information about lateral and longitudinal control and provide early warnings about upcoming hazards. V2V would be required for vehicle platooning.
Vehicle to device (V2D)
  Communication between vehicles and electronic devices, such as smartphones and other wearable technologies
Notes: Speaker notes:
A connected transportation system where vehicles can communicate information with each other and their environment could enhance road safety by improving the ability of the driving system to accurately coordinate decisions based on environmental conditions. Connected vehicle technology can be deployed independently of automated vehicles but could be used to augment automation in the future.
In platooning, vehicles travel close together in an automated convoy to increase traffic capacity and fuel economy. A lead vehicle transmits control data (i.e., acceleration, braking, steering) so the following vehicles can react accordingly.
Notes to Instructor:
These modules are limited in their attention to connected vehicle topics. For additional information, see OST-R information on connected vehicles available at https://www.its.dot.gov/research_areas/connected_vehicle.htm

## Slide 12: Network Communication Terminology
Network communication technology supporting V2X includes:
  Fifth generation networking (5G)
    Uses existing wireless networking architectures
    Signals transferred between devices over long range through cellular towers
  Dedicated short range communications (DSRC)
    Radio-based communication network
    Designed for short- or medium-range (1000 feet) communication between vehicles and with infrastructure.
    Radio signals transmitted through on- board units (OBUs) on vehicles or roadside units (RSUs)
Notes: Speaker notes:
V2X requires some kind of wireless communication technology to move signals between vehicles and other connected nodes.
5G uses existing infrastructure, but it will be shared with other network users (e.g., smartphones)
DSRC requires Installing new infrastructure, but it will be dedicated only to transportation systems
Image Source: https://www.its.dot.gov/cv_basics/cv_basics_what.htm

## Slide 13: Levels of Automation
Automated vehicles are generally described using six SAE Levels of Automation.
An automated vehicle refers to vehicles capable of SAE Levels 1-5.
An automated driving system (ADS) refers to SAE Levels 3-5.
Full automation refers only to SAE Level 5.
Notes: Reference:
Surface Vehicle Recommended Practice J3016: Taxonomy and Definitions for Terms Related to Driving Automation Systems for On-Road Motor Vehicles (June 2018)

## Slide 14: SAE Levels of Automation
Notes: Speaker notes:
SAE developed a taxonomy including six automation levels to describe how responsibilities are divided between a driver and a system for different types of automated vehicles. The levels range from ranging from no driving automation (level 0) to full driving automation (level 5). The levels of driving automation are associated with roles played by the driver and the system when in performing the dynamic driving task (DDT) and/or DDT fallback. The SAE Levels of Automation are broadly used when describing automated vehicle functions and capabilities.

## Slide 15: Student discussion
What is the difference between self-driving and driverless?
Notes: Notes to Instructor:
Potential student activity 1: find an article in the news that talks about “autonomous” vehicles. What level of autonomy are they referencing?
Potential student activity 2: have a class discussion around the question, “what are the advantages and disadvantages of self-driving cars?” Make a list of each. Consider revisiting at the end of the course to see if the students’ opinions have changed.

## Slide 16: AV Development: Past, Present, and Future
Notes: Notes to Instructor:
This module provides a recent history of AV technology development (since the 1980s) and highlights of current applications and future projections.

## Slide 17: The Past (Early History of Automated Vehicles)
CMU Navlab
Mercedes VaMoRs
Modern improvements in AV technology due to:
  Exponential advances in computer processing power to run AI
  Availability of big data for training and testing AI algorithms
Navlab vehicles from 1986-1996. Photo by Mary Jo Dowling of Carnegie Mellon University.
Notes: Speaker Notes:
Modern AV research dates back to the mid 1980s.
The Navlab in the Carnegie Mellon school of Computer Science has been developing a series of computer-controlled vehicles since 1984. they also conducted early pedestrian detection research.
Mercedes VaMoRs (Versuchfahrzeug für autonome Mobilitaet und RechnerSehen, translation: “research vehicle for automated mobility and computer vision”). Used different sensors to interpret lines on the road similarly to how automated vehicles work today. It was first demonstrated in 1986 and was capable of speeds up to 60mph,
VaMoRs led to the Eureka PROMETHEUS Project, a 750 million Euro driverless vehicle project that ran from 1987 to 1995. The final product of PROMETHEUS was a car that drove without human intervention for 98 miles
The computer science concepts in AI required for AVs were developed in the 1950s and applied to vehicles in the 1980s, but the performance of these AI systems was limited. The sudden surge in innovation in the 200s and beyond was due to the availability of more powerful computers and the data to inform the advanced AI.
Image source: https://frc.ri.cmu.edu/~hpm/book98/fig.ch2/p042.html

## Slide 18: DARPA Grand Challenges
In 2001 Congress demands 1/3 of military ground combat vehicles uncrewed by 2015
DARPA announces the first race for self-driving cars in 2003 to motivate innovation
Three DARPA challenges between 2004 and 2007
Notes: Speaker notes:
DARPA is the Defense Advanced Research Projects Agency. Their mission is to “make pivotal investments in breakthrough technologies for national security.”
The 2003 DARPA challenge was open to anyone and offered a $1M prize to the first to finish a difficult 142 mile course in under 10 hours.
2004 Grand Challenge had 15 teams and no winner (best distance was 7.5 miles). In 2005, 195 teams tried to complete a 132-mile off-road course for $2 million. Stanford’s “Stanley” won in under 7 hours. Other finishers included CMU, Gray Insurance, and OshKosh Truck Corp (pictured). In 2007, the third challenge featured a 60-mile urban course to be completed in under 6 hours for $2 million. Tartan Racing’s “Boss” won in 4:10 and the Stanford team came in second.
  Several competitors went on to form driverless car companies. Stanford’s AI lab (SAIL) had closed in 1980, and reopened under Sebastian Thrun in 2004. Thrun’s team won DGC in 2005 and placed second in 2007. Thrun went on to develop the Google Driverless Car. The Program Manager for the Challenge was Gil Pratt, who now runs Toyota Research. Chris Urmson of the CMU team was hired by Thrun and went on run Waymo and later Aurora.
  Image source: DARPA: https://archive.darpa.mil/grandchallenge04/Web_Photos/sat/Full/DARPAGCSa_30.jpg

## Slide 19: The Present: (Current applications: Ridesharing)
Notes: Speaker notes:
Autonomous vehicles could change multiple transportation concepts. The examples on these next slides show 3 different applications.
Waymo started the Waymo One early rider program at the end of 2018 in the Phoenix metro area. Waymo One lets participants use an app to call an autonomous Waymo vehicle to bring them to a destination within a service area. It was originally open to 400 participants called the “Early Riders” who could travel in a 100 square mile service area. Each car included a backup driver during deployment. Participants were required to sign non-disclosure agreements.
Reference:
Morgan Stanley (2017). The EDGE: Autonomous Vehicles. Available at https://www.morganstanley.com/im/publication/insights/investment-insights/ii_edge_autonomousvehicles_us.pdf?1544764367308
Image Source: Waymo Team: https://medium.com/waymo/waymo-one-the-next-step-on-our-self-driving-journey-6d0c075b0e9b

## Slide 20: Current applications: Trucking
Notes: Speaker notes:
Interstate highways provide a welcome environment for automated vehicles because of:
  Clear markings, consistent speeds and gradual turns
  No traffic lights, less chaotic scenery to confuse sensors, and
  Reduced numbers of vulnerable road users
Trucking companies could reduce costs by decreasing the number of drivers and taking advantage of platooning
  In truck platooning, a lead truck sends wireless commands to one or more following trucks to regulate speed, steering, braking and distance between the trucks
  Air drag is reduced, reducing fuel consumption by up to 15%
  Safety distance between trucks can be reduced from 50 to 15 meters, reducing highway congestion
  Platooning could reduce the driver’s workload, or remove the driver entirely
This application is controversial because reducing the number of drivers will also affect many people’s livelihoods, as there are currently 3.5 million truck drivers in the US alone.
Image source: Volpe https://www.volpe.dot.gov/news/researchers-reveal-safety-impact-following-distances-between-heavy-trucks-automated-platoons

## Slide 21: Current applications: Urban Shuttles
Notes: Speaker Notes:
Short shuttle routes are a convenient entry point for automated vehicles. There are several advantages:
Fixed routes are easy to maintain
Low speeds present fewer safety challenges
Help solve first- and last-mile challenges, expanding the reach of mass transit
  Early deployments at residential communities, office parks, large events, resorts, parks, and school campuses
Urban shuttles are a possible gateway technology to on-demand routes
Image source (clockwise from left):
Vital Vegas: https://vitalvegas.com/downtown-las-vegas-self-driving-shuttle/
University of Michigan Mcity: https://mcity.umich.edu/mcity-driverless-shuttle-testing-begins/
ecoPRT: http://ecoprt.com/

## Slide 22: The Future: (The billion dollar questions)
When will “fully autonomous” vehicles become available to the general public?
How long will we have a mixed fleet where AVs and human-driven vehicles coexist?
Notes: Speaker Notes:
Hypothetical projections of the total U.S. vehicle fleet composition with respect to level of automation, indicating that lower levels of automated vehicles will represent a large portion of the vehicle fleet for a long period of time. Data are hypothetical as there is currently no industry consensus or reliable estimate for specific levels of automation over time.
Image Source: Sandt, L. & Owens, J.M. (August 2017). Discussion Guide for Automated and Connected Vehicles, Pedestrians, and Bicyclists. Pedestrian and Bicycle Information Center. Chapel Hill, NC.

## Slide 23: Pace of tech development: Moore’s Law example
Notes: Speaker Notes:
Moore’s law is an observation of a historical trend in computing technology that shows an exponential increase in computing capacity (doubling every 2 months). Many have acknowledged that this growth trend cannot continue in perpetuity. Yet it is one indicator that the computing power and cost of AV-related technologies will continue to improve over time, making more tech breakthroughs possible.
Notes to Instructor:
Moore’s Law is named for Gordon Moore, one of the inventors of integrated circuits, and Chairman of Intel. Moore observed in the 1970s that they could squeeze twice as many transistors on an integrated circuit every 24 months. Given that the electrons have less distance to travel, the circuits also run twice as fast, providing an overall quadrupling of computational power. Source: https://www.kurzweilai.net/the-law-of-accelerating-returns
Image source: Singularity.com http://www.singularity.com/images/charts/MooresLaw.jpg
Potential student reading assignment: https://medium.com/s/ai-and-the-future-of-computing/when-moores-law-met-ai-f572585da1b7.

## Slide 24: Context within other innovations
Notes: Speaker Notes:
Consumers may opt for ridesharing over individual ownership due to reduced costs and convenience
  The driver is the most expensive element in a rideshare, and removing the driver would reduce long-term costs
  Removing the driver could dramatically increase vehicle utilization rates, further reducing individual cost
Without the need to drive, passengers can reallocate their time
  The average American spends almost an hour a day commuting.
  Time in an automated vehicle could to work or for entertainment, opening new markets for in-vehicle services
High utilization may also lead to changes in cities
  A single car requires multiple parking spaces (i.e., home, work, entertainment, etc.)
  Higher vehicle utilization rates and options for remote parking will reduce the space needed for parking in urban centers

## Slide 25: Student discussion
What is “driving” the pace of AV development?
  Speculation over profits?
  Desire for safety or environmental reform?
  Elon Musk?
  Advancements in data storage and computing?
  Other?
Who is “driving” the change? Who has a seat at the table? Who doesn’t?
Notes: Notes to Instructor:
Potential student activity 1: Student discussion: Which of the three applications described in this module is the most feasible? Which is the most attractive to you and why?
Potential student activity 2: Find a news article about automated vehicles that includes a target date for deploying an AV. Do you think they will meet that goal? Why, or why not?
Further Reading: https://sci.uoregon.edu/urbanism-next-0

## Slide 26: AV Technology: How it Works (or Doesn’t)
Notes: Notes to Instructor: This module provides an overview of the key components used to sense, understand and take action on the road.

## Slide 27: AV Technology Building Blocks
The collection of hardware and software required to perceive, localize, decide/path plan and control the driving task.
Photo: Udacity
Notes: Speaker notes:
The collection of hardware and software elements required for automated driving is sometimes called the “AV Stack.” It includes elements that perceive, localize, decide/path plan and control
Perceive
  Vision sensors locate and identify objects and structures relevant to the dynamic driving task
  Navigation sensors, such as GPS and inertial measurement units (IMU) track the vehicle’s location
Localize
  Algorithms estimate the vehicle’s location relative to objects and structures using sensor data
Decide/Plan Path
  Behavior modules determine trajectory and driving strategy
Control
  automation operates acceleration, braking and steering.

## Slide 28: Current AV “Vision” Technology
Camera
  Cost-effective detection of texture and color
  (e.g., signs, lane markings, lights)
  Con: very data intensive
Lidar
  Detects distances and shapes in 3 dimensions
  (e.g., cars, pedestrians, curbs, small obstacles)
  Con: Not effective in many adverse weather conditions
Radar
  Detects distances, position and speed
  (e.g., cars, large obstacles)
  Con: Low resolution
Ultrasound
  High resolution, inexpensive
  (e.g., objects at low speed)
  Con: Very short range
Bosch Mobility Solutions Radar
Velodyne Lidar
Notes: Speaker notes:
These sensors are the “eyes” of an automated vehicle.
Cameras are much like the high-resolution video cameras in many consumer products. They require a light source, but they are the only sensor that can identify colors.
A lidar emits laser signals that travel from the sensor and bounce back from obstacles. Images are derived from the amount of time it takes for each signal to bounce back. With this data, lidar can calculate the distance between itself and the obstacle along with the exact size of the object. Lidar signals can be blocked by rain and snow.
Radar emits radio waves from that bounce back from obstacles. This is the same technology used in aviation. Radar can travel relatively long distances and are less likely to be absorbed by weather.
Ultrasound sensors produce sound waves that reflect of objects. They are high resolution but are only used at close range for applications such as automated parking.
AV manufacturers are experimenting with different combinations of these sensors. Using multiple sensors simultaneously to leverage the strengths and offset the limitations of the different sensor types is called sensor fusion. Sensor fusion can also Waymo uses all 4; Tesla uses radar, cameras and ultrasound; Cadillac uses radar and cameras only.
Image source: Bosch long range radar (Bosch Mobility Solutions), Velodyne Lidar products (Velodyne LiDAR)
Further Reading:
Combs, T., Sandt, L., Clamann, M. and McDonald, N. (2019). Automated Vehicles and Pedestrian Safety: Exploring the Promise and Limits of Pedestrian Detection. American journal of Preventative Medicine. ;56(1):1-7.

## Slide 29: How AV “vision” of pedestrians and bicyclists differs from humans
Computer processors convert vision sensor data to useful information
  Image acquisition by sensors
  Preprocessing/enhancement
  Segmentation
  Feature extraction
  Recognition
Photo: The Next Platform
Notes: Speaker notes:
Sensors by themselves only return visual data. Complex algorithms are required to convert that data into information used for driving, much like our brains are used to interpret sensory information we take in through our eyes, ears and skin. Perception of objects requires several steps, summarized by common characteristics of computer vision technology.
Image acquisition: an image must be captured by a camera and converted to a manageable entity
Preprocessing methods are applied to enhance the data of the image prior to computational processing. The image is processed and converted into a suitable format for further analysis.
Segmentation is the process of partitioning a digital image into multiple segments (sets of pixels, AKA “superpixels”). The goal is to simplify and to change the representation of an image into something that is more meaningful to the computer and easier to analyze.
Feature extraction (also “image representation and description”) is performed to extract and highlight features with some quantitative information which is essential to distinguish one class of objects from another
Recognition is the process to assign a label to an object, based on the information provided by its features. Moreover, it involves assigning meaning to a set of recognized objects
Note: To assign a label to an object, the label must have been created in advance. Detection algorithms are fallible and can miss some objects; so it is important that the algorithms have a backup or fallback condition.

## Slide 30: Humans are hardwired to detect other humans
Notes: Speaker Notes:
Even with very little information, humans are able to determine that motion is coming from another human.
Image Credit: CG Society

## Slide 31: Computers have to be trained to recognize humans
Notes: Speaker Notes:
These images show an example of perceptual invariance. Most humans, after some review, recognize the shapes in quadrant A as the same 3-dimensional shape. Similarly, we recognize the shapes in B are different, and also different from the shapes in A. Even when the images are warped, as they are in quadrant C, we recognize them as the same. Quadrant D shows the same shapes distorted through filters, but still recognizable. If we think of the images in quadrant D as being viewed through fog, rain, snow or a dirty windshield, we see how this may be relevant to spotting pedestrians and cyclists from the vehicle. Computer vision needs to be programmed to address each scenario, while humans don’t require extra training.
Image Credit: Lehar S. (2003) The World In Your Head, Lawrence Erlbaum, Mahwah, NJ. p. 53, Fig. 3.5, uploaded by the author to https://en.wikipedia.org/wiki/Gestalt_psychology#/media/File:Invariance.jpg.

## Slide 32: How effective is autonomous emergency braking at protecting pedestrians?
Insurance Institute for Highway Safety tested 11 small SUVs in 2019
  9 earned “superior” or “advanced” ratings
  … based on ability to avoid or mitigate crashes in 3 common pedestrian crash scenarios
  Only 2 out of 11 vehicles avoided collisions in all pedestrian dart-out scenarios
  “No crash avoidance technology is designed to address every possible crash scenario.” (IIHS, 2018)
One vehicle with “superior” IIHS rating received a 69% fulfillment score in the European NCAP crash test
Notes: Speaker Notes:
A “superior” rating does not mean that the AEB is 100% effective. 2 out of 4 vehicles with “superior” (the highest) ratings struck pedestrians during tests.
These tests are important to ranking different vehicles, but we have to remember that they do not represent real-world conditions.
IIHS estimates that pedestrian detection systems could potentially mitigate or prevent up to 65 percent of single-vehicle crashes with pedestrians in the three most common crash configurations and 58 percent of pedestrian deaths in these crashes if all vehicles were equipped with AEB systems
IIHS tests are performed under ideal conditions:
Dry asphalt in clear weather (no rain, snow, hail, fog, smoke, etc.)
Road is straight and flat
No other vehicles, obstructions or objects are present
Road has clear, consistent markings
Ambient illumination is consistent, and there is no glare from the sun (no nighttime tests)
Pedestrian test equipment has no rips, tears or inconsistent markings
All test vehicles have less than 5,000 miles and tires are new
Fuel tanks are filled to 75-90%
Cargo is no more than 200 lbs over vehicle curb weight
Brakes are warmed up and AEB is calibrated prior to testing
These technologies are not being tested on bikes in the US. NCAP tests on bicycle detection introduced in 2018.
References:
Insurance Institute for Highway Safety (2018). Pedestrian Autonomous Emergency Braking Test Protocol (Version 1). https://www.iihs.org/.../test_protocol_pedestrian_aeb_v1.pdf
Notbremsassistenten: So gut schneiden sie ab. https://www.adac.de/rund-ums-fahrzeug/tests/assistenzsysteme/notbremsassistenten-vergleich/
Further Reading:
IIHS Status Report (February 2019). Safe Passage: New ratings address pedestrian crashes. 54(2). https://www.iihs.org/externaldata/srdata/docs/sr5402.pdf

## Slide 33: Bicycle detection has different requirements
Not all autonomous emergency braking systems react to bicycles
Additional challenges from higher speeds:
  Sensors need wider fields of view
  Less time to make a decision to brake
Not formally tested in US
2 scenarios introduced in Europe in 2018 (Euro NCAP)
  Crossing vehicle path
  Riding same direction as the vehicle
Notes: Speaker Notes:
Cyclist detection and braking requires more data and less time to make a decision, which is a technical challenge.
Reference:
https://www.euroncap.com/en/vehicle-safety/the-ratings-explained/vulnerable-road-user-vru-protection/aeb-cyclist/
Image Source: Euro NCAP: https://www.euroncap.com/en/vehicle-safety/the-ratings-explained/vulnerable-road-user-vru-protection/aeb-cyclist/

## Slide 34: Detection Challenges
Automated vehicles rely on computer vision to detect and categorize vulnerable road users
Variations in height, posture, speed, carried loads, etc. create a challenge to automated vehicle vision systems
Different transport modes, like wheelchairs, scooters, knee walkers, hoverboards, tricycles, etc. challenge computer vision systems
Computer vision can be confused by “adversarial images”
  In one study, a Google image classifier interpreted a 3D-printed turtle as a “rifle”
Notes: Speaker Notes:
In 2015, a cyclist yielded right of way to a Google test vehicle by performing a track stand (i.e., the rider was standing on the pedals and balancing the bike, but not moving forward). The Google car stopped because it did not know how to proceed. The detection issue is also one of several errors that let to the Uber crash in Arizona.
Note that “different transport modes” applies to people with disabilities
Notes to Instructor:
Video of a close call involving a Nissan test vehicle in 2017: https://twitter.com/Korben/status/837990377097428992/video/1
Image Credit: New Scientist: https://www.newscientist.com/article/2152331-visual-trick-fools-ai-into-thinking-a-turtle-is-really-a-rifle/

## Slide 35: Steps beyond “detection” are equally important

## Slide 36: Example: First Pedestrian Fatality from an Automated Vehicle
Notes: Speaker notes:
An Uber Technologies, Inc. test vehicle struck and killed a pedestrian crossing the street on Sunday, March 18 at 9:58pm
  Nighttime conditions
Vehicle was a modified 2017 Volvo XC90
  One vehicle operator
  Self-driving system engaged (sensors included cameras, radar and Lidar)
  The Volvo collision avoidance function with automatic emergency braking was disabled
  Vehicle was travelling at 43 mph in a 45 mph speed zone

## Slide 37: Example: First Pedestrian Fatality from an Automated Vehicle
Data recorded by the self-driving system showed:
  Radar and Lidar observed the pedestrian 6 seconds before impact
  The system classified the pedestrian as a series of objects:
    an unknown object
    a vehicle
    a bicycle
  System determined emergency braking was needed at 1.3 seconds before impact
    Emergency braking maneuvers were not enabled (to reduce the potential for erratic vehicle behavior)
    The vehicle operator is relied on to intervene, but was watching her phone when the pedestrian stepped into the road
Notes: Speaker notes:

## Slide 38: Student discussion
The League of American Bicyclists proposes that AVs should be required to pass a “vision test” that proves
  ”their ability to recognize and respond to people bicycling and walking”
  (Review at: https://bikeleague.org/content/take-action-require-autonomous-vehicles-see-bicyclists-and-pedestrians)
How should regulators go about creating a “vision test” for AVs?
Notes: Notes to Instructor:
This discussion could also be presented after the testing/regulation modules.

## Slide 39: AV Testing Basics
Notes: Notes to Instructor: Methods automated vehicle developers use to evaluate automated vehicle safety

## Slide 40: Test Methods
Rigorous testing is required to ensure the safety of automated vehicles
Testing can be performed in several ways:
  Naturalistic
    Testing performed on public roads around other road users
    Examples:
      Customer testing
      Structured testing on public roads
      Public roads with professional drivers
  Supervised
    Testing is separated from real-world without contact with the public
    Examples:
      Closed tracks
      Simulation

## Slide 41: Naturalistic Test Methods
Customer testing
  Consumer vehicles are capable of recording data during everyday use
  Data are recorded and uploaded to the manufacturer for analysis.
  Test locations are unlimited
  e.g., Tesla
Structured testing on public roads
  Consumers drive test vehicles for everyday use under manufacturer supervision
  Test locations are often limited
  Data are recorded by engineers
  e.g., Volvo DriveMe
Public roads with professional drivers
  Test vehicles operated by professional engineers on public roads
  Data are maintained and recorded by engineers
  Test locations are limited
  e.g., Waymo, Uber
Notes: Notes to Instructor:
Structured testing on public roads with consumers driving test vehicles was widely announced by Volvo in 2017, but was not implemented.
References: Volvo DriveMe
Original plan: https://www.theguardian.com/business/2017/feb/02/volvo-seeks-volunteers-for-self-driving-car-trial-in-west-london-public-roads
Revision: https://www.theverge.com/2017/12/14/16776466/volvo-drive-me-self-driving-car-sweden-delay

## Slide 42: Supervised Test Methods
Closed tracks
  Test vehicles operated by professional engineers on closed test tracks that can replicate known real-world situations and events, but other road users are part of the research team.
  Data are maintained and recorded by engineers
  e.g., Waymo, Nissan, Toyota
Simulation
  Test vehicles and driving conditions are represented by software models.
  No real vehicles are used.
  Simulations can rapidly replicate known combinations of driving scenarios

## Slide 43: Realism/Control Tradeoff
Test methods that are easiest for experimenters to control lack real-world variety and uncertainty
Test methods with the most realism are more challenging for data collection and less safe
Test miles are far less than the 3 trillion miles driven annually in the US
Realism
Control
Simulation
Closed Track
Public Road, Safety Driver
Public Road, Customer
Notes: Speaker notes:
There are 212 million licensed drivers in the US (BTS), and the average US driver drives approximately 13,500 miles per year (FHWA). Each time an AV is tested for 1,000,000 miles, that is equivalent to 100 people driving for 8 or 9 months. Therefore, miles driven for AV tests is far less than the 3 trillion miles driven annually in the US, and there are innumerable driving scenarios that engineers will not be able to experience through testing alone. This leads to an ongoing conversation about “how safe is safe enough?” that adds to the challenge of deployment.
A combination of test methods is essential; one test method is not enough.

## Slide 44: HFES Policy Statement
Automated vehicles require careful testing before deployment on public roads
Automated vehicles should support the needs of human drivers and other users
Automated vehicles should be safe and understandable
Automated vehicles should be accompanied by detailed training for drivers
Notes: Speaker notes:
The Human Factors and Ergonomics Society is the largest human factors professional society in the US. They have over 5,000 active members. This is their policy statement on AV technology.
Notes to Instructor:
Compare with other policy statements:
HFES: http://cms.hfes.org/Cms/media/CmsImages/HFES_Policy_Statement_Autonomous_Vehicle_Safety.pdf
NACTO Policy Statement: https://nacto.org/wp-content/uploads/2016/06/NACTO-Policy-Automated-Vehicles-201606.pdf
ITE Policy Statement: https://www.ite.org/pub/?id=6059BDBD-AAEF-45E4-58F6-F14962022873
APBP: https://www.apbp.org/news/402457/APBP-Adopts-AV-Policy-Statement.htm

## Slide 45: Student Discussion
Should AVs be tested in real-world locations where pedestrians and bicyclists are present?
How does the current testing process relate to pedestrian and bicycle safety?
What amount of testing or evidence is needed for people to feel that AVs are “safe” enough to share roads with pedestrians and bicyclists?
What role does the city or state have in shaping testing requirements?
Notes: Notes to Instructor:
Differences in state regulations are available through the National Conference of State Legislators: http://www.ncsl.org/research/transportation/autonomous-vehicles-self-driving-vehicles-enacted-legislation.aspx
As of this writing (2019), 15 states regulate AV testing and 23 bills have been introduced.
Student Assignment: Look up testing requirements in different states and compare current policies.

## Slide 46: Important Takeaway
Test locations and conditions define
where vehicles will be operational in the future
what our safety metrics will be

## Slide 47: Patient Zero: The First AV-involved Crashes and Responses

## Slide 48: First Automated Vehicle Fatality
A 2015 a driver was killed when his Tesla Model S struck a semi trailer
Saturday, May 7, 2016 at 4:40 p.m.
  Daylight with clear weather conditions
Tesla Model S, traveling eastbound on US Highway 27A (US-27A)
  “Autopilot” was engaged and set to 74 mph
  Had automated emergency braking system
Following the crash
  Telsa battery disengaged but the car continued coasting at a shallow angle off the right side of the roadway
  Came to rest perpendicular to the highway in the front yard of a private residence.
Notes: Speaker notes:
The driver, Josh Brown, was a 40-year-old man on his way back from a family vacation in Orlando. He had spent 11 years in the Navy and was a successful technology business owner. His driver’s license was current. He had received 8 speeding tickets between 2010 to 2015, but had not been involved in any crashes. He was in good health and was not taking any no medications. No drugs or alcohol were found in his system. The cause of the crash was a combination of the truck driver not yielding and Brown’s overreliance on the vehicle’s automation that caused him to stop attending to the road ahead.
Tesla drivers are expected to maintain control of the vehicle and attend to driving at all times. However, Tesla’s safety feature for this is to make sure the driver periodically grasps the steering wheel.
Reference:
https://www.ntsb.gov/investigations/AccidentReports/Pages/HWY16FH018-preliminary.aspx

## Slide 49: Crash Location
Notes: Image source: New York Times - https://www.nytimes.com/interactive/2016/07/01/business/inside-tesla-accident.html

## Slide 50: Perspectives
NHTSA
  “A safety-related defect trend has not been identified at this time and further examination of this issue does not appear to be warranted.”
Tesla
  “Final report on Autopilot issued by NHTSA is very positive.”
Driver’s Family
  “Change always comes with risks, and zero tolerance for deaths would totally stop innovation and improvements.”
NTSB
  “System safeguards, that should have prevented the Tesla’s driver from using the car’s automation system on certain roadways, were lacking and the combined effects of human error and the lack of sufficient system safeguards resulted in a fatal collision that should not have happened.”
Notes: Speaker notes:
Perspectives on the tragedy varied.
References:
NHTSA investigation (page 12): https://static.nhtsa.gov/odi/inv/2016/INCLA-PE16007-7876.PDF
Elon Musk: https://twitter.com/elonmusk/status/822128741228756992?lang=en
Family statement from Landskroner Grieco Merriman: https://www.globenewswire.com/news-release/2017/09/11/1117570/0/en/Landskroner-Grieco-Merriman-Issues-Statement-on-Behalf-of-the-Family-of-Joshua-Brown.html
Chairman Robert L. Sumwalt: https://www.ntsb.gov/news/press-releases/Pages/PR20170912.aspx

## Slide 51: First Pedestrian Fatality from an Automated Vehicle
An Uber Technologies, Inc. test vehicle struck and killed a pedestrian crossing the street.
Sunday, March 18 at 9:58pm
  Nighttime conditions
Vehicle was a modified 2017 Volvo XC90
  One vehicle operator
  Self-driving system engaged (cameras, radar and Lidar)
  The Volvo collision avoidance function with automatic emergency braking was disabled
  Vehicle was travelling at 43 mph in a 45 mph speed zone
Pedestrian was dressed in dark clothing and pushing a bicycle
  Did not look in the direction of the vehicle before crossing
  Crossed the road 360 feet from the nearest crosswalk in a section not directly illuminated by lighting.
  Entered the roadway from a brick median (see next slide)
Notes: Speaker Notes:
The bicycle did not have side reflectors and the front and rear reflectors, along with a forward headlamp, were perpendicular to the path of the oncoming vehicle.
A full report of the fatality is pending.
Reference:
https://www.ntsb.gov/investigations/Pages/HWY18FH010.aspx

## Slide 52: Crash Location
Notes: Possible Class discussion:
Who was at fault in the Uber crash?
How would someone safely cross this road at night?
References:
Google maps: https://www.google.com/maps/place/N+Mill+Ave,+Tempe,+AZ+85281/@33.4364913,-111.9432021,143m/data=!3m1!1e3!4m5!3m4!1s0x872b09338c84a6a3:0x4eb48ca97885c3f7!8m2!3d33.4399425!4d-111.9446799

## Slide 53: Moving beyond the crash “blame game”
Consideration of broader patterns
  How did the environmental, policy and human roles interact to create the situation?
  This requires good data!
Proactive changes to underlying systems to prevent crashes:
  Roadway designs, policies, laws, etc.
Respectful dialogue about the values, beliefs, and assumptions that shape our systems
Notes: Speaker Notes:
The “blame game” refers to the tendency to identify one entity who is at fault following a crash. If we want to move past the blame game, we will need to acknowledge that each of us in this room has a role to play in improving safety and finding solutions through technologies or the other systems we design.
We need to dive deeper and look for patterns. This requires data. We need to work on this, as a profession, and we need to advocate for access to AV-related data. In the absence of this data, we allow a whole lot of assumptions about what is happening or speculation about what will happen fill the void.
And to be truly transformative, we need to go further under the water line and talk about the things that we don’t often talk about – what are our assumptions, beliefs, and values about these technologies?

## Slide 54: Example: San Francisco pro-active approach to crash data collection
Updated police crash report and trauma registry questions to support “tagging” of incidents involving automated vehicles
Notes: Speaker Notes:
The recent proliferation of new mobility technologies presents a challenge to the local and state governments who regulate them, and the hospitals and trauma centers charged with treating injuries associated with these emerging vehicle types. This methodology in San Francisco is a response to the need for timely and high-quality data to empirically track and better understand injuries arising from use of these formerly uncommon vehicles. It provides an opportunity to study emerging innovations and to inform data-driven injury prevention efforts (Vision Zero SF, 2019).
Reference: Vision Zero SF Injury Prevention Research Collaborative. 2019. A Methodology for Emerging Mobility Injury Monitoring in San Francisco, California Utilizing Hospital Trauma Records: Version 1.0. San Francisco, CA. Available at: https://www.sfdph.org/dph/EH/PHES/PHES/TransportationandHealth.asp
Image Source: https://www.sfdph.org/dph/files/EHSdocs/PHES/VisionZero/Emerging_Mobility_Injury_Monitoring_Methodology.pdf

## Slide 55: Student Discussion
Who was at fault in the Tesla and Uber crashes?
Who was involved other than the drivers and the pedestrian?

## Slide 56: Pedestrian and Bicyclist Interaction with AVs
Notes: Notes to Instructor: This module includes a summary of issues specific to pedestrians and cyclists navigating near automated vehicles

## Slide 57: Pedestrian Crossing Process
Interactions between a pedestrian and a driver include six processes (performed by both):
  Select a path
  Look for an approaching driver/crossing pedestrian
  Detect the other person and assess the relative location
  Evaluate the others’ intention
  Decide on a response
  Execute the response
A collision can occur when driver and pedestrian both fail to perform any one of these processes
Notes: Reference:
Snyder, M. G. and R. L. Knoblauch (1971). Pedestrian safety: The identification of precipitating factors and possible countermeasures. National Highway Traffic Safety Administration. Report DOT FH-11-7312. U.S. Department of Transportation, Washington, DC.

## Slide 58: Challenges in Driver/Pedestrian Interactions
When pedestrians cross a street:
  Communication is poor, so drivers & pedestrians assume common norms about right-of-way
    At a crosswalk
    Midblock
  Pedestrians are often harder for drivers to see than other objects on the road
    More complexity when entering and leaving parking spots
  Pedestrians need to adjust their situation to the road environment (i.e., from the sidewalk) when crossing
To prevent collisions, drivers and pedestrians need to:
  Detect each other
  Communicate
AVs and VRUs will need to interact in new ways
Notes: Reference:
Shinar, D. (2017). Pedestrians. In Traffic Safety and Human Behavior (2nd ed.). Emerald Publishing.

## Slide 59: Communication Challenges
People want to know whether they have been seen by the automated vehicle
  With no driver, there is no one to “wave on” a VRU or acknowledge detection with eye contact
  New communication strategies will be needed for automated vehicles
    Especially if the automation is imperfect!
  Conventions vary according to local culture
Two types of messages to communicate:
  Right of way communication (to regulate traffic)
  Warnings (to prevent imminent crashes)
Notes: Speaker notes:
From a young age we are taught to make eye contact with the driver. When there is no driver, generations will need to replace these old habits with new ones (or learn how to understand mixed fleets). This will take time.

## Slide 60: Approaches to pedestrian communication
Notes: Speaker notes:
The next three slides will show some early approaches to V2P communication. This is an excerpt from an early Google patent for presenting text on the hood of the car to provide crossing advice to pedestrians. Their sample message for the patent was, “SAFE TO CROSS” and an image of a pedestrian running in front of a car. They presented other signaling combinations as well, including audio.
Reference:
Urmson, C, I. Mahon, D. Dolgov, and J. Zhu. Pedestrian Notifications. Google, Inc., assignee. 16 Patent US 9196164 B1. 24, 2015

## Slide 61
Image: TechCrunch
Notes: Speaker notes:
Daimler-owned “Smart” shows messages on the front of the car, below waist level. In addition to providing advice, smart proposes using this space to identify the next rider for ride sharing applications.

## Slide 62
Image: Drive.ai
Notes: Speaker notes:
This prototype design from Drive.ai appears on the side of the vehicle and includes text and a reinforcing image advising the pedestrian to cross.
The three designs on the preceding slides represent early industry prototypes, which are all different. Inconsistency is a bad idea because it sends mixed and confusing messages to VRUs. We have national standards for road signs… will we require car to car standards?
To be visible at 100 feet, stationary legible text requires letters that are at least 6-inches tall (MUTCD requires 9-inches). A visible “safe to cross” message would be 47 inches wide. Moving displays should be even larger. Is 100 feet enough? At 25 mph, a car moves 100 feet before the avg pedestrian can cross a lane (37 fps).
Combine this with differences in language abilities for adults and children, and text is not a good solution for pedestrian communication.

## Slide 63: Communication Challenges
What does “safe to cross” mean…
  On a 2-lane road or a 4-lane road with traffic possibly coming from both directions?
  When a pedestrian is on the same side of the road or on the far side of the road?
  When there is one pedestrian or groups of pedestrians waiting on different corners of an intersection?
Vehicle messages need to work in different road conditions, traffic volumes and a changing audience
  Mixed fleets of automated and legacy vehicles mean pedestrians may see different messages from different vehicle types

## Slide 64: Additional challenges for bicyclists
Bicyclists are expected to ride on road with other vehicles
Have the same low visibility problems as pedestrians
Vary in ability, flexible in behavior
    May not have formal training on traffic rules
    … which makes them less predictable than other vehicles
Vulnerable in crashes
  5.7 times more likely to be fatally injured than vehicle occupants, when involved in a crash
Unstable, conscious of effort, often perceived as an intruder (Wegman et al., 2012).
Notes: Reference:
Wegman, F., Zhang, F. and Dijkstra, A. (2012). How to make more cycling good for road safety? Accid. Anal. Prev., 44(1), 19-29.

## Slide 65: V2X Solutions
Challenges of V2P communication could be solved by V2D or V2I
Vehicle to device (V2D)
  Vehicles push messages and warnings to mobile devices
  Allows a message to be sent to a VRU directly, in the proper context
  Fails when the VRU is not carrying a mobile device (e.g., children)
Vehicle to Infrastructure (V2I)
  Messages sent to objects in the built environment, like crosswalks
  VRUs can communicate to vehicles through infrastructure (e.g., a button at a crosswalk), and vehicles can send messages to compatible objects (e.g., walk/don’t walk)
  Messages limited to locations where the technology is installed

## Slide 66: Benefits to Pedestrians and Cyclists
Consistent vehicle speeds
  Automated vehicles can be programmed to reliably follow lower speed limits, which reduce the severity of crashes
Data collection
  Detailed data recorded automatically by GPS and vision systems will facilitate rapid system improvements
  In the event of a crash, detailed data will be available for reporting and reconstruction
  Will present privacy concerns for people detected and recorded by vision systems

## Slide 67: Student Discussion
How should an AV communicate with pedestrians and bicyclists?
Are there solutions that would also work for human-driven vehicles?

## Slide 68: Rulemaking for AVs
Notes: Notes to Instructor:
This module summarizes federal and state responsibilities and proposed regulation for automated vehicles, along with a summary of deployment issues recognized by NHTSA

## Slide 69
Notes: Speaker Notes:
In the Executive branch of the US Government, the Cabinet serves as an advisory body to the President. The two cabinet members most directly related to automated vehicles are the Secretary of Defense and the Secretary of transportation. While research on automated vehicles existed prior to 2001, Department of Defense funding was a catalyst to AV research through the DARPA Grand Challenges. The Department of Transportation (DOT) plays a more direct role in transportation oversight.

## Slide 70: US Department of Transportation
Mission:
  “Serve the United States by ensuring a fast, safe, efficient, accessible and convenient transportation system that meets our vital national interests and enhances the quality of life of the American people, today and into the future.”
Administrations:
  Federal Aviation Administration (FAA)
  *Federal Highway Administration (FHWA)
  *Federal Railroad Administration (FRA)
  *Federal Transit Administration (FTA)
  Maritime Administration (MARAD)
  Office of Inspector General (OIG)
  *Federal Motor Carrier Safety Administration (FMCSA)
  *National Highway Traffic Safety Administration (NHTSA)
  *Office of the Secretary of Transportation (OST)
  Pipeline and Hazardous Materials Safety Administration (PHMSA)
  Saint Lawrence Seaway Development Corporation (SLSDC)
Notes: Speaker Notes:
Entities marked with an asterisk are directly related to surface transportation. However, the AV guidance released in 2018 (version 3.0) encourages all administrations to collaborate on issues related to AVs.

## Slide 71: State and Federal Responsibilities
Federal responsibilities:
  Setting Federal Motor Vehicle Safety Standards (FMVSS) for new motor vehicles and motor vehicle equipment (manufacturers must certify compliance before they sell the vehicles)
  Enforcing FMVSS compliance
  Investigating and managing recalls for safety-related defects and non-compliances
  Communicating with and educating the public about motor vehicle safety issues
  Issuing guidance for vehicle and equipment manufacturers
State responsibilities
  Licensing drivers and registering motor vehicles
  Enacting and enforcing traffic laws and regulations
  Conducting safety inspections
  Regulating insurance and liability
Notes: Speaker Notes:
States and the federal government have different responsibilities related to regulating transportation.
In an AV, the “driver” may be replaced by software, which is part of the vehicle. This blurs many of the lines previously drawn between state and federal responsibilities. For example, who will “license” an AV to drive?
References:
https://www.transportation.gov/sites/dot.gov/files/docs/AV%20policy%20guidance%20PDF.pdf
https://www.nhtsa.gov/laws-regulations/fmvss

## Slide 72: NHTSA Guidance for Automated Vehicle Development
Since 2016, there have been three versions of the voluntary guidance for automated vehicle development
Supports industry innovation by limiting regulations
Provides guidance to state regulators
Provides a list of safety elements to be considered during design
Recommends self-documentation for assessment, testing, and validation
Does not apply to commercial motor vehicles
Notes: References:
https://www.transportation.gov/AV/federal-automated-vehicles-policy-september-2016
https://www.nhtsa.gov/sites/nhtsa.dot.gov/files/documents/13069a-ads2.0_090617_v9a_tag.pdf
https://www.transportation.gov/av/3

## Slide 73: Voluntary Guidance and Best Practices
A Vision for Safety (2.0) includes 2 main sections:
ADS Safety Elements
  Full Title: Voluntary Guidance for Automated Driving Systems (ADS)
  Summarizes 12 safety elements to help automotive industry stakeholders (i.e., entities engaged in in ADS testing and deployment) identify and resolve safety issues prior to deployment
Technical Assistance to States
  Full Title: Technical Assistance to States, Best Practices for Legislatures Regarding Automated Driving Systems
  Differentiates federal and state roles in ADS regulation
Notes: Speaker Notes:
A vision for Safety emphasizes that the guidance is voluntary
Reference:
https://www.nhtsa.gov/sites/nhtsa.dot.gov/files/documents/13069a-ads2.0_090617_v9a_tag.pdf

## Slide 74: Section 1: ADS Safety Elements
Intended to help entities engaged in in ADS testing and deployment identify and resolve safety issues prior to deployment
System Safety
Operational Design Domain
Object and Event Detection and Response
Fallback (Minimal Risk Condition)
Validation Methods
Human Machine Interface
Vehicle Cybersecurity
Crashworthiness
Post-Crash ADS Behavior
Data Recording
Consumer Education and Training
Federal, State, and Local Laws
Notes: Notes to Instructor:
While Vision for Safety (2.0) is not the most current version of the guidance, it maintains the list of “safety elements.” These represent the 12 elements AV manufacturers are expected to describe when reporting to regulators prior to deployment.
Brief descriptions of each element are as follows:
System safety, or vehicles free of “unreasonable” safety risks
Operational design domain, or the conditions or geographic areas where the vehicles can operate (can they drive in rain, or on gravel roads?)
Object and event detection: Testing entities should have a documented process for assessing and testing their vehicles’ ability to avoid pedestrians, bicyclists, animals and other potential road hazards
Fallback to “minimal risk condition,” or, if a vehicle malfunctions, how quickly can it be brought to a state where it can’t do any harm?
Validation methods: Testers should develop validation methods to mitigate the safety risks of their systems
Human-machine interface: How do the vehicles communicate to their passengers, especially the ones that don’t have traditional controls?
Cybersecurity: Companies testing systems should incorporate best practices and design principles from NHTSA, the National Institute of Standards and Technology, SAE International and others to keep their vehicles from being hacked
Crashworthiness: What happens when non-automated vehicles run into automated vehicles, and how will the AV occupants be protected?
Post-crash behavior: How can AVs be made safer after a crash, such as by shutting down a fuel pump or moving the vehicle out of the roadway?
Data recording: Learning from crash data will be critical to the development of safe vehicles. NHTSA is working with SAE International to establish uniform data elements for crash reconstruction
Consumer education and training: Vehicle testers and dealers need to be able to accurately describe how their vehicles work.
Compliance with federal, state and local laws

## Slide 75: Element 1: System Safety
Encourages developers and designers to implement a systems engineering approach to ensure ADSs are devoid of unreasonable safety risks.
Recommendations include:
  Following standards developed accredited standards-developing organizations (e.g., SAE, ISO) and standards and processes available from other industries (e.g., aviation, space, military)
  Including a hazard analysis and safety risk assessment
  Implementing strategies for handling ADS malfunctions

## Slide 76: Element 2: Operational Design Domain (ODD)
Specific conditions under which a given ADS or feature is intended to function
Includes system operating conditions and limitations for
  Roadway types (interstate, local, gravel, etc.)
  Geographic area (city, mountain, desert, etc.);
  Speed range;
  Environmental conditions (weather, day/night, etc.)
Notes: Speaker Notes:
An example would be trucks operating on highways, or slow urban transport shuttles described in the Usage Models module

## Slide 77: ODD Example: Waymo One
Planners should have the ability to define AV service areas within their transportation plans
  Routes
  Speed
  Occupancy limits
  Fees
Notes: Speaker Notes:
Waymo One ODD:
Passengers cannot select a destination outside an approved geography, and software will not create a route that travels outside of a “geo-fenced” area, which has been mapped in detail
Vehicles are designed to automatically detect sudden changes (such as a snowstorm) that would affect safe driving within their operational design domain and come to a safe stop until conditions improve
Vehicles are capable of complying with federal, state, and local laws within their geographic area of operations, including relevant speed limits, traffic signs, and signals.
Reference:
https://storage.googleapis.com/sdc-prod/v1/safety-report/Safety%20Report%202018.pdf

## Slide 78: Element 3: Object and Event Detection and Response
Detection by the driver or ADS of any circumstance relevant to the immediate driving task and response to those circumstances
Applies to system and driver responses under normal and crash avoidance conditions
Notes: Speaker Notes:
This element address a wide variety of foreseeable encounters, including emergency vehicles, temporary work zones, and other unusual conditions (e.g., police manually directing traffic or other first responders or construction workers controlling traffic). Language in the guidance states, “Testing entities should have a documented process for assessing and testing their vehicles’ ability to avoid pedestrians, bicyclists, animals and other potential road hazards”

## Slide 79: Element 4: Fallback (Minimal Risk Condition)
The vehicle should respond in the safest manner possible in the event of…
  HAV system failure
  Human driver’s response failure when transitioning from automated to manual control
Requires detecting:
  Malfunctions
  Operation in a degraded state
  Operation outside of the ODD
Notes: Speaker Notes:
In situations where the ADS is outside of its defined ODD or in which conditions dynamically change to fall outside of the ADS’s ODD, the vehicle should transition to a minimal risk condition. This is where a “handoff problem” for Level 3 automation can occur if this requires a sudden switch to human control. The handoff problem occurs when the person in the driver’s seat suddenly has to take control in an emergency and needs time to assess the situation properly… Which may not be acceptable in emergency situations.
Fallback to “minimal risk condition,” or, if a vehicle malfunctions, how quickly it can be brought to a state where it can’t do any harm may vary according to the operational domain (e.g., bridge vs. empty rural road vs. congested highway)

## Slide 80: Element 5: Validation Methods
Demonstrate the ADS would be able to perform during
  Normal operation
  Crash avoidance situations
  Fallback strategies
Evaluation domains include:
  Public roads
  Closed tracks
  Simulation
    With or without humans
IEEE Spectrum
Notes: Speaker Notes:
This is covered in detail in the AV Testing Basics module

## Slide 81: Element 6: Human Machine Interface (HMI)
Manner in which the ADS exchanges information with the driver
Inform the human operator through various indicators that the ADS is:
  Functioning properly
  Currently engaged in ADS mode;
  Currently “unavailable” for use;
  Experiencing a malfunction; and/or
  Requesting control transition from the ADS to the operator.
Divide responsibilities between the operator and the automation
  Design for teamwork/cooperation
Enable safe transitions between automated and manual modes
  Regain attention, diagnose, act, and confirm the transition occurred safely
  (Possibly with little or no warning)
Manage interactions between AVs, their operators and other road users
  Keep stakeholders informed
Notes: Speaker Notes:
An HMI should also consider people with disabilities, seniors, children, etc.

## Slide 82: Element 7: Vehicle Cybersecurity
Minimize risks to safety due to cybersecurity threats and vulnerabilities through protection, detection and recovery
Applies to:
  Each ADS
  Overall vehicle design into which it is being integrated
  Broader transportation ecosystem
Report to the Auto-ISAC all discovered incidents, exploits, threats and vulnerabilities from internal testing, consumer reporting, or external security research
Intel
Notes: Speaker Notes:
Auto-ISAC is the automotive information sharing and analysis center: https://www.automotiveisac.com/

## Slide 83: Element 8: Crashworthiness
Evaluate and consider countermeasures that will protect all occupants in any alternative planned seating or interior configurations during use
May include new occupant protection systems that provide enhanced protection to occupants of all ages and sizes
Includes unoccupied vehicles.
Notes: Speaker Notes:
Developers can consider lessons learned in the aviation industry, where in the event of a crash, unsecured objects can become becomes dangerous projectiles.
Image Source:
H. Miller (1957) Advertisement for “America’s Independent Electric Light and Power Companies”

## Slide 84: Element 9: Post-Crash ADS Behavior
Account for methods of returning ADSs to a safe state after being involved in a crash
Immediately after a crash
  Shutting off the fuel pump
  Removing motive power
  Moving the vehicle to the safest place available
  Disengaging electrical power
  Communicating with an operations center
Longer-term
  Equipment and processes necessary to ensure safe operation of the ADSs after repairs
Notes: Speaker Notes:
Sensors are very sensitive and easily damaged. Decisions will need to be made after a crash to determine whether the vehicle is still roadworthy or if it can be repaired at all. This may require a sophisticated self-diagnosis by the vehicle itself.

## Slide 85: Element 10: Data Recording
Data related to the occurrence of malfunctions, degradations, or failures that can be used to establish the cause of a crash
The analysis of any ADS crash could lead to safety developments and prevention of that crash scenario in other ADSs
Vehicles should record, at a minimum, all available information relevant to reconstructing the crash.

## Slide 86: Element 11: Consumer Education and Training
Entities are encouraged to develop education and training programs to address the operation of ADSs for
  Employees
  Dealers
  Distributors
  Consumers
Relevant content includes:
  ADSs’ functional intent
  Operational parameters
  System capabilities and limitations
  Engagement/disengagement methods
  HMI
  Fallback scenarios,
  Operational design domain parameters
  Mechanisms that could alter ADS behavior while in service

## Slide 87: Element 12: Federal, State and Local Laws
Development of ADSs should account for all governing traffic laws when operating in automated mode for the region of operation
ADSs may temporarily violate certain state motor vehicle driving laws in some situations (e.g., to travel safely past a broken-down vehicle on the road).
ADSs may need to address new or revised legal requirements

## Slide 88: Honorable Mention: Privacy and Ethical Considerations
Manufacturers’ privacy policies and practices should ensure:
  Transparency
    Provide consumers with accessible, clear, meaningful data privacy notices
  Choice
    Regarding the collection, use, sharing, retention, and deconstruction of personal data
  Respect for Context
    Data should be used only in the manner originally intended
  Minimization, De-Identification and Retention
    Collect and retain a minimum of personal data for the shortest possible time
  Data Security
    Develop data protection measures commensurate with harm resulting from a data breach
  Integrity and Access
    Maintain accurate data that can be reviewed by the owners
  Accountability
    Ensure entities collecting consumer data comply with applicable data privacy notices
Ethical Considerations
  Ensure manufacturers, regulators and road users work together to address the ethical dimensions of decisions made by AVs
MIT Moral Machine
Notes: Speaker Notes:
Privacy and ethics appeared in in the original version of the guidance, but were removed in the second version, A Vision for Safety.
Version 1.0 content on privacy referred to the Alliance of Automobile Manufacturers’ Privacy Principles for Vehicle Technologies and Services, which is summarized on this slide.

## Slide 89: Section 2: Technical Assistance to States
Best Practices for Legislatures
  Encourage competition & innovation
  Provide licensing & registration procedures
  Provide reporting & communication with public safety
  Remove legal barriers to AVs
Best Practices for State Highway Safety Officials
  New administrative roles
  Test applications
  Test permissions
  Test drivers
  Registration and title
  Coordination with public safety
  Liability and insurance
Notes: Speaker Notes:
This is a list of the subject headings that appear in the guidance. This section clarifies federal and state roles, provides a framework for states to write laws & regulations, and encourages states to evaluate existing laws so as not to create barriers to AVs.
States can act independently if NHTSA has not adopted a safety standard.
AVs disrupt the current balance between state and federal roles because vehicle hardware and software can be programmed in advance to perform driver tasks. AVs thus blur the distinction between “drivers” and “vehicles.”

## Slide 90: Additional US DOT Authority
Federal Motor Carrier Safety Administration (FMCSA)
  “Regulates the safety of commercial motor carriers operating in interstate commerce, the qualifications and safety of commercial motor vehicle drivers, and the safe operation of commercial trucks and motor coaches.”
  Holds public demonstrations of commercial vehicle technology (e.g., platooning)
  Maintains authority to ensure safe commercial operations
Federal Highway Administration (FHWA)
  “Supports State and local governments in the design, construction, and maintenance of the U.S. highway system”
  Conducts research to understand the needs of automated vehicles with respect to traffic control devices
Federal Transit Administration (FTA)
  “Provides financial and technical assistance to local public transit systems, including buses, subways, light rail, commuter rail, trolleys and ferries”
  Assists transit agencies to ensure safe testing and deployment of automated transit bus systems
Notes: References:
FMCSA: https://www.fmcsa.dot.gov/mission
FHWA: https://www.fhwa.dot.gov/about/
FTA: https://www.transit.dot.gov/about-fta

## Slide 91: Proposed Legislation (House)
SELF DRIVE Act (HR 3388)
  Safely Ensuring Lives Future Deployment and Research in Vehicle Evolution Act
Clarifies federal and state roles
  Preempts of state laws relating to vehicle design, construction, and systems
  Preserves state laws relating registration, licensing, insurance, inspections, and traffic
  States regulate of motor vehicle dealers
  States may impose higher performance requirements
Creates a framework for NHTSA to exempt autonomous vehicles from current Federal Motor Vehicle Safety Standards
  (as long as there is no reduction in safety)
  Gradual increase in annual exemptions from 25K to 100K by year 3
Institutes a review and eventual update to Federal Motor Vehicle Safety Standards
Notes: Speaker notes:
Passed House September, 2017

## Slide 92: SELF DRIVE Act (cont.)
Manufacturers submit safety assessment letters to NHTSA
  Requires NHTSA to publish a rulemaking and safety priority plan
  After a rulemaking, submit safety assessment certifications
Bars DOT from requiring preapproval or precertification before implementation
Requires vehicle manufacturers to develop a cybersecurity plan
Consumers to receive notice of practices for gathering and using owner/occupant information
Allows certain parts manufacturers to perform testing
  current law allows testing only by vehicle manufacturers;
Establishes an advisory council within NHTSA, with subcommittees to address:
  Cybersecurity
  Sharing of situational testing information
  Access for individuals with disabilities and senior citizens
  Consumer privacy and security
Notes: Speaker Notes:
“Safety assessment letters” content are derived from the NHTSA safety elements.

## Slide 93: AV START Act (S 1885)
American Vision for Safer Transportation through Advancement of Revolutionary Technologies Act
Topics covered:
  Preemption
    States may not issue licenses
  VOLPE report
  Testing
  Exemptions increased
  Mandatory safety evaluation report
  HAV Technical Safety Committee
  Consumer education
  Cybersecurity
Notes: Speaker Notes:
Introduced September 2017, not yet submitted for vote (i.e., not passed)

## Slide 94: Student discussion
When vehicles are fully autonomous:
  Who will need a driver’s license, the operator or the vehicle?
  Will driver’s licenses be issued at the state or federal level? How will the test be administered?
  Who will be insured? The operator? The owner? The vehicle? The individual technology components?
The current regulatory environment encourages innovation through voluntary guidance. What are the advantages and disadvantages of this approach?
The Senate bill regulating automated vehicles (AV START) stalled after it was submitted to the Committee on Commerce, Science, and Transportation. What are the competing interests that slowed its passage?

## Slide 95: Considerations for Ped/Bike Planners, Engineers, and Stakeholders

## Slide 96: Opportunities Ahead
Research to understand impacts and improve technology
Investment in complementary solutions and critical transportation services
  Walkable, bikeable environments with supportive land uses and universal design
  Focus on place-making and social inclusion
  Machines will never be able to replace human-human interactions and support systems that some vulnerable populations need
Define and test the appropriate role for AVs and new technologies in these spaces and systems (e.g., define the ODD)
Mitigate unintentional consequences
  Safety
  Equity
  Sustainable revenue sources/financing

## Slide 97: Examples of Policy Principles
AV Principles for Healthy and Sustainable Communities
  Shared-use
  Pooled
  Low-emissions
  Right-sized
  Part of an efficient multimodal system
  Efficient land use
  Complete and livable streets
  Transportation Equity
(California Governor’s Office of Planning and Research)
Notes: Reference:
http://opr.ca.gov/docs/20181115-California_Automated_Vehicle_Principles_for_Healthy_and_Sustainable_Communities.pdf

## Slide 98: ODD: AVs in parking lots
In some locations, 1/3 of pedestrian crashes occur in parking lots.
What if we could redesign these zones to
  minimize pedestrian-vehicle interactions?
  maximize the use of equitable transportation technology?

## Slide 99: Automation Strengths and Weaknesses
Humans appear to surpass present-day machines in respect to the following:
Ability to detect a small amount of visual or acoustic energy
Ability to perceive patterns of light or sound
Ability to improvise and use flexible procedures
Ability to store very large amounts of information for long periods and to recall relevant facts at the appropriate time
Ability to reason inductively
Ability to exercise judgment
Present-day machines appear to surpass humans in respect to the following:
Ability to respond quickly to control signals and to apply great force smoothly and precisely
Ability to perform repetitive, routine tasks
Ability to store information briefly and then to erase it completely
Ability to reason deductively, including computational ability
Ability to handle highly complex operations, i.e. to do many different things at once.
Notes: Speaker notes:
Research in the aviation industry dating back to the 1950s provided guidelines for human/automation teaming that remain helpful today. As the three outlined examples describe, people are good in new situations where the solution requires improvisation. Machines are good when tasks are repetitive and routine, situations that would be tedious or boring for a person. Machines are also good at paying attention to and responding to many things at once, which people are also bad at (like texting and driving).
An ideal balance of responsibilities for automated vehicles puts the vehicle in charge of the routine aspects of driving, and an “operator” in charge of setting goals (like where to go) and responding to new situations. But this opens the problem of transitioning between human and automated control modes…
This list is the “Fitts List,” also known as the “MABA-MABA” list (for “men are better at, machines are better at”) conceived in 1951 for dividing tasks between air traffic controllers and automation. Much of it is still relevant today
Reference:
Fitts, P. M. (1951). Human engineering for an effective air navigation and trafficcontrol system. Washington, DC: National Research Council

## Slide 100
Safety: Present pedestrian and bike crash types
Source: UNC Highway Safety Research Center, NC Crash Data, 2007-2014
Notes: Speaker notes:
The current factors that contribute to pedestrian and bicycle crashes can be attributed to a driver failing to see or react quickly enough to a pedestrian or bicyclist, sometimes due to driver distraction or impairment. Many other crashes occur when drivers fail to yield or pass a bicyclist safely.
So new technologies that can detect pedestrians and bicyclists better and provide more predictable reactions could be very, very important for improving the safety and comfort of pedestrians and bicyclists.

## Slide 101: What will be the crash types of the future?
Hypothetical Data
Notes: Speaker notes:
So as the revolution in automation continues, it is important to be mindful and to think about how walking and bicycling may be affected.
For example, how will the nature of roadway crashes involving pedestrians and bicyclists change?
Perhaps we might see fewer human driver errors, but more problems with failed systems or vehicle programming, or drivers may poorly understand when and how to use automated features.
Or we may see people adapting to automated vehicles and changing the ways that they walk and bike and look for and communicate with traffic, and that might cause new problems as well.

## Slide 102: How will public health change?
Notes: Speaker notes:
Another important question is how automated vehicles will impact public health. Perhaps we see fewer crashes, but if people end up spending more sedentary time in vehicles, will other public health problems emerge?

## Slide 103: AVs could change the system for the better… Or worse
Increased mobility for those unwilling or unable to drive
  Improved independence, reduction in social isolation, and access to essential services
Reduced cost of congestion
  Vehicle occupants free to do other activities
  Lead to an increase in overall vehicle miles traveled?
  Which, in turn, could return the increases in negative externalities of driving, like congestion
  Does this erode the comparative advantage of public transit?
Commuters more willing to travel longer distances to work
  People relocate further from the urban core
Decrease need for proximate parking as AVs drive themselves to satellite parking
  Resulting in increased urban density?
  And undermining urban parking revenues
Notes: Reference:
Anderson, J., Kalra, N., Stanley, K., Sorenson, P., Samaras, C. and Oluwatola, O. (2014). Autonomous Vehicle Technology: A Guide for Policymakers. Rand Corporation. https://www.rand.org/pubs/research_reports/RR443-2.html

## Slide 104: Student discussion
What land use and roadway design elements support current travel modes and ALSO automated vehicles?
  e.g., lighting, delineated spaces, protected bike lanes, etc.

## Slide 105: Student discussion
What roadway design elements will need to be reconsidered?
  E.g., Lane widths, intersections, signals, pavement markings/signs, curbside management
What planning and land use issues will need to be reconsidered?
  Parking requirements
  Role of transit, etc.