## Slide 1: Intersections
Instructor course information
Notes: Report No. FHWA-SA-19-034

## Slide 2: Module Outline
General considerations
Geometric design and markings
Signal strategies
Other intersections
International examples

## Slide 3: Safety and Comfort at Intersections

## Slide 4: Major Considerations
Mitigate risk at conflict points
Balance visibility and path placement with convenience
pedbikeimages.org – Gary Thomas
Notes: Notes: This image shows an atypical intersection (two, three-leg intersections close to each other). It also shows clearly marked paths for pedestrians (continental-style high-visibility crosswalk markings) and bicyclists (the dashed lines in the lower left show how the bicycle lane extends across the intersection).

## Slide 5: Design Principles for Pedestrians
Slow vehicular traffic
Make people walking visible to traffic
Make vehicular traffic visible to people walking
Encourage predictable actions (drivers and pedestrians)
Minimize crossing distance for people walking

## Slide 6: Bicycles can traverse intersections…
Mixed in with autos
Adjacent to autos in painted bike lanes
Adjacent to pedestrians in separated bike lanes (street-level or raised)
At dedicated and controlled bicycle crossings
Over or under
Notes: Source: Slide adapted from Tab Combs (2019)
Image available: http://www.pedbikeimages.org/details.php?picid=1383

## Slide 7: Bicyclist Safety & Comfort at Intersections
Conventional bike lanes and shared lanes
Separated bike lanes with mixing zones
Separated bike lanes through roundabouts
Protected intersections
MassDOT Separated Bike Lane Planning and Design Guide
Notes: Key Message: This graphic illustrates the conflict points for bicyclists at the four common intersection configurations.
Source: FHWA. (2019). Bikeway Selection Guide. Available: https://safety.fhwa.dot.gov/ped_bike/tools_solve/docs/fhwasa18077.pdf
(Image from MassDOT appears in the FHWA Bikeway Selection Guide cited above)

## Slide 8: Common Safety Problems
Right hook for bikes
  When a driver and bicyclist are traveling in the same direction and the driver turns right, crashing into the bicyclist
Left-turn crossing pedestrian traffic
  When a left turning vehicle hits a pedestrian who is crossing the street
  Animated scenarios available: http://www.pedbikeinfo.org/resources/resources_details.cfm?id=5151
Notes: Notes: [click the link to show some of the scenarios to help students visualize the safety problems from different perspectives]

## Slide 9
pedbikeimages.org – Dan Burden
Notes: Student Question: What are some challenges that people walking and bicycling might face when trying to access the land uses on either side of this corridor?
Image: http://www.pedbikeimages.org/mediumimages/va.charlottesville.wideroad-large.jpg

## Slide 10: Geometric design and Markings

## Slide 11: Pedestrian-Friendly Intersections
Tight
Simple
Slow speed
Avoid free-flow movements
Easy to understand
  If complex, broken into smaller steps
Pedbikeimages.org - Pennsylvania Department of Transportation
Notes: Notes: This slide lists several important factors for pedestrian-friendly intersection design.
Source: adapted from Pedestrian and Bicycle Information Center. (2015). Bicycle and Pedestrian Transportation Short Series, Class 2.

## Slide 12: Curb Radii
Size of the corner relates directly to the length of the crosswalk
Accommodate large vehicles, don’t design for them
Smaller turning radii
  Position vulnerable users in a more visible locations
  Provide space for properly aligned curb ramps
  Reduces vehicle turning speed
NACTO
Notes: Key Message: Curb radii should be designed to maximize pedestrian space and shorten pedestrian crossing distance to the greatest extent feasible. The designer should distinguish between “designing for” and “accommodating” the needs of large vehicles. Accommodating means allowing for a vehicle to complete a turn with latitude to use adjacent or opposing lanes on the origin or destination street.
Notes: Generally, for local urban streets, curb radii should be between 10–15 feet unless special circumstances require a larger radius. Where on-street parking or bike lanes are present, designers should use the “effective” curb radii, rather than the actual, to create a more compact intersection that encourage slower speeds.
Connection to other Module: Designing for Walking and Bicycling
Source:
FHWA (2016). Achieving Multimodal Networks: Applying Design Flexibility & Reducing Conflicts. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_networks/
NACTO. (2013). Urban Streets Design Guide, “Corner Radii.” Available: https://nacto.org/publication/urban-street-design-guide/intersection-design-elements/corner-radii/
San Francisco Better Streets Plan, “Curb Radius Changes.” Available: https://www.sfbetterstreets.org/find-project-types/pedestrian-safety-and-traffic-calming/traffic-calming-overview/curb-radius-changes/
Image: https://nacto.org/wp-content/themes/sink_nacto/views/design-guides/retrofit/urban-street-design-guide/images/corner-radii/effective-turning-radius.png

## Slide 13: Ramp Design
2 ramps at each corner are best
Level landings should be provided
Max 1:12 ramp slope
VTRANS
Notes: Key Message: Curb ramp design is especially important for wheelchair users. Two curb ramps (one for each street to be crossed) are preferred to one diagonal ramp, which directs pedestrians with wheelchairs, walkers, or strollers into the middle of the intersection. Ramps should also allow enough space for a level sidewalk surface to be maintained.
Connection to other Module: Accessibility and ADA
Source:
Image: Vermont Agency of Transportation. Vermont Pedestrian and Bicycle Facility Planning and Design Manual. (2002). Figure 3-23

## Slide 14: Crosswalk Design
Marked crosswalks indicate optimal or preferred locations for pedestrians to cross and help designate right-of-way for motorists to yield to pedestrians
FHWA
Notes: Notes: [Remind students that not all legal crosswalks are marked].
Source: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 15: Crosswalk Visibility
What a pedestrian sees
Notes: Key Message: Marked crosswalks must be visible to the DRIVER. These crosswalk markings are in very poor condition but are still visible to a pedestrian waiting to cross.
Connection to other Module: This slide is also shown in the module on Designing for Walking and Bicycling.
Source: adapted from FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 16: Crosswalk Visibility
What a driver sees
Notes: Key Message: The same crosswalk is virtually invisible to the driver; yet it’s the driver who is expected to react to this traffic control device.
Connection to other Module: This slide is also shown in the module on Designing for Walking and Bicycling.
Source: adapted from FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 17: Crosswalks – Additional Measures
Improve visibility
Reduce crossing distance
Improve driver yielding
Reduce driver speed
Alexandria T&ES
Pedbikeimages.org – Dan Burden
Pedbikeimages.org – Dan Burden
Pedbikeimages.org – Peter Speer
Notes: Key Message: The presence of a crosswalk alone may not improve the safety of a street.
Notes: Designers should consider additional features such as those shown on the slide – in-street yield/stop sign, pedestrian refuge island, curb extension, and advance stop/yield lines.
Connection to other Module: the modules on Strategies for Safer Speeds and Safety Analysis cover many of these countermeasures.
Source: Adapted from FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 18: Raised Intersection
Reduce vehicle speeds
Improve pedestrian crossing environment
Reduce need for curb ramps (still detectable warnings)
Pedbikeimages.org - Pennsylvania Department of Transportation
Notes: Source: FHWA. (2013). PEDSAFE: Pedestrian Safety Guide and Countermeasure Selection System, “Raised Pedestrian Crossings” Available: http://www.pedbikesafe.org/PEDSAFE/countermeasures_detail.cfm?CM_NUM=7

## Slide 19: Channelization
Prioritizes vehicle speeds and flows
Island can reduce crossing distance and provide pedestrian refuge, but…
  Crosswalk placement and visibility are critical
FHWA, Designing for Pedestrian Safety
Notes: Key Message: Channelized right turns allow drivers to turn without decelerating as much as they would at a non-channelized intersection. Although the channelization islands can break up a long crossing distance and provide a refuge for pedestrians to wait, higher vehicle speeds and potential for poorly-placed crosswalks can make crossing the channelized lane dangerous for pedestrians.
Notes: This type of channelization is not recommended by NACTO: “Channelized turning ‘porkchop’ islands are not recommended and should be avoided. Turning traffic often fails to yield to pedestrians crossing at these locations.” (NACTO, 2013).
Source:
FHWA and PBIC. “Designing for Pedestrian Safety – Interchanges.” Webinar, presented October 5, 2010.
NACTO. (2013). Urban Street Design Guide.

## Slide 20: Considerations for Channelized Right Turns
Channelization island design
Enhanced crosswalk visibility
  High-vis markings
  Flashing beacons
  Signage
  Raised crosswalks
Slip lane angle
FHWA, PEDSAFE
Pedbikeimages.org – Dan Burden
Notes: Key Message: If channelization must be used, there are several design elements that can make the intersection more accommodating to pedestrians. The design of the channelization island or “pork-chop” should be large enough to accommodate pedestrians and should include ramps if it is raised (preferred). To enhance visibility of the crosswalk, designs may include high-visibility crosswalk striping, flashing beacons, signage, and/or raised crosswalks. The geometric design of the lane also affects how easily drivers can see pedestrians and other drivers. The angle and longer length of the slip lane on the right causes drivers to slow down, give them room to safely stop for pedestrians, and improve driver and pedestrian visibility.
Source: FHWA. (2013). PEDSAFE: Pedestrian Safety Guide and Countermeasure Selection System, “Improved Right-Turn Slip-Lane Design.” Available: http://www.pedbikesafe.org/PEDSAFE/countermeasures_detail.cfm?CM_NUM=24

## Slide 21: Bicycling through Intersections
Intersection elements that can help with merging maneuvers and manage queuing:
  Pavement markings (including color)
  Signage
  Medians
  Signal detection
Pedbikeimages.org – Greg Griffin, AICP
Notes: Key Message: Designs should reduce conflict between bicyclists (and other vulnerable road users) and vehicles by heightening the level of visibility, denoting a clear right-of-way, and facilitating eye contact and awareness with competing modes.
Notes: The configuration of a safe intersection for bicyclists may include elements such as color, signage, medians, signal detection, and pavement markings. Intersection design should take into consideration existing and anticipated bicyclist, pedestrian, and motorist movements. In all cases, the degree of mixing or separation between bicyclists and other modes is intended to reduce the risk of crashes and increase bicyclist comfort.
Source: NACTO (2014). Urban Bikeway Design Guide, Second Edition, “Bicycle Signal Heads.” Available: https://nacto.org/publication/urban-bikeway-design-guide/bicycle-signals/bicycle-signal-heads/
Image: http://www.pedbikeimages.org/mediumimages/7107880369_301ad27aa9_k.jpg

## Slide 22: Right-turn Lanes and Bicycles
Dedicated right-turn lanes present a challenge for bicyclists
Solutions:
  Through/right instead of dedicated right-turn lane
  Shared right-turn lane
  Maintain bicycle lane to the left of right-turn lane
FHWA MUTCD (2009) Figure 9C-4
Notes: Key Message: Where a bike lane is dropped at an intersection approach, bicyclists continuing straight through the intersection can face conflicts and discomfort if they must move to the left into the through traffic lane (to get out of a dedicated right-turn lane).
Notes: Dedicated right-turn lanes often allow vehicles to make right turns on red, which can be dangerous for pedestrians (discussed later in this module), but many agencies use them where there are high volumes of right-turning motor vehicles. In these instances the correct placement of the bike lane is to the left of the right-turn lane (as shown in the image). Drivers are required to yield to bicyclists before entering the right turn lane. This merging area is marked with dashed lines. Another option for dealing with right turns is replacing dedicated right-turn lanes with shared through/right lanes. Dual right-turn lanes should not be used on streets with bike lanes.
Source: AASHTO. (2012). Guide to Bicycle Facilities, 4th Edition.

## Slide 23: Right-turn Lanes and Bicycles
NACTO
Notes: Notes: The use of shared-lane markings in a right-turn only lane are permitted by the MUTCD, but this may not be the most comfortable option for bicyclists.
Source: https://mutcd.fhwa.dot.gov/knowledge/faqs/faq_part9.htm#mkgsq11

## Slide 24: Intersection Treatments
Two-Stage Turn Queue Box
Bike Box
pedbikeimages.org – Toole Design Group
pedbikeimages.org – Zachary Kaufman
Notes: Key Message: Both are examples of treatments that can reduce turning conflicts between motorists and bicyclists.
Notes: Both markings have interim approval from FHWA.
Two-stage turn queue boxes can help bicyclists make left turns at multilane signalized intersections from a right-side separated bike lane or bike lane (or right turns from a left side separated bike lane or bike lane). Keep in mind that this configuration usually increases delay for bicyclists because they need two separate green indications to complete their movement.
A bike box is a designated area at the head of a traffic lane at a signalized intersection that provides bicyclists with a safe and visible way to get ahead of queuing traffic during the red signal phase. Right-turn-on-red should be restricted to prevent vehicles from encroaching on the bike box.
Source: NACTO. (2014). Urban Bikeway Design Guide. Available: https://nacto.org/publication/urban-bikeway-design-guide/intersection-treatments/

## Slide 25: Intersection Treatments
Pedbikeimages.org – Katy Lang
Guides bicyclists and makes their movements more predictable
Call attention to potential conflict areas
Shows that bicyclists have priority before turning vehicles
Notes: Key Message: There are a variety of options for marking the intended path of bicyclists through intersections, including at driveways and ramps. The MUTCD specifies dashed lines that may contain arrows or the bicycle symbol, if needed. The use of green paint is also permitted to mark conflict points, like at this intersection with a one-way street that has a separated bike lane behind a parking lane.

## Slide 26
Pedbikeimages.org – Dan Gelinne
Notes: Notes: MUTCD Section 3B.08 shows dotted line extensions through intersections. At the intersection shown on the slide, Seattle chose to use green paint through the intersection.
Source: FHWA. (2009). Manual on Uniform Traffic Control Devices. Available: https://mutcd.fhwa.dot.gov/

## Slide 27
Alta Planning + Design
Notes: Notes: Marked conflict points at driveways on a separated bicycle lane in a small town.
Image: http://ruraldesignguide.com/files/2016-12/russelville-by-mike-repsch-alta-.jpg

## Slide 28
Pedbikeimages.org – Andrew Miller
Notes: Notes: This image shows the use of “elephant’s feet” dashed lines with green paint and the bicycle symbol to alert drivers who will be crossing the path of bicyclists at an unusual angle at this T-intersection in Chicago.

## Slide 29: Signal Strategies
Notes: Key Message: Signal timing influences delay, compliance, safety, and mode choice.

## Slide 30: Traffic Signal Strategies
Use a short signal cycle length
  Reduces delay and increases compliance for all users
At high-use crosswalks, pedestrians should get a signal at every cycle
Adjustments to minimum green intervals, red clearance time, and extension time may be needed to ensure that bicyclists can safely cross
Notes: Notes: Short signal cycle lengths minimize delay in a complex network environment, reducing wait times in all directions and creating crossing opportunities at closer intervals. If pedestrians wait too long, there may not be enough room for them to stack safely on the sidewalk; many will start crossing against the light when there are gaps in traffic. In typical downtown environments and other areas of high pedestrian activity, pedestrian push buttons are not needed; pedestrians expect and should get a pedestrian cycle at every signal phase, this creates a more predictable urban environment for everyone.
Source:
adapted from Pedestrian and Bicycle Information Center. (2015). Bicycle and Pedestrian Transportation Short Series, Class 2.
NACTO. (2014). Urban Bikeway Design Guide. Available: https://nacto.org/publication/urban-bikeway-design-guide/

## Slide 31: Traffic Signal Strategies
Keep the number of signal phases to a minimum
Adjust timing for peak/off-peak volumes
Time signals for the speed you intend traffic to go
  Synchronize signals at or below the target speed
Notes: Key Message: Signalization may not be an obvious as geometric design, but it has an important role to play in the quality of a transportation system.
Notes: “The operation of a traffic control system should closely mirror a city’s policy goals and objectives. Managing traffic signals is important because signals directly impact the quality of the transportation system. While geometric enhancements to a corridor may demarcate space for bikes and buses and create a more multi-modal cross-section, signal timing influences delay, compliance, safety, and mode choice.” (NACTO 2014)
Source: NACTO. (2014). Urban Bikeway Design Guide, Second Edition. Available: https://nacto.org/publication/urban-street-design-guide/intersection-design-elements/traffic-signals/signalization-principles/

## Slide 32: Right Turn on Red Restrictions
Can reduce conflicts between turning vehicles and pedestrians
Consider in areas with high pedestrian volumes or exclusive pedestrian phases
Minimal impact on vehicle traffic
Can be used in conjunction with LPI
Pedbikeimages.org – Dan Burden
Notes: Key Message: Where right turns on red (RTOR) are permitted and pedestrians are present, issues often arise when drivers 1) do not come to a complete stop before turning, 2) pull forward into the intersection and block the crosswalk, or 3) are intently looking left for gaps in approaching vehicles and not looking for pedestrians to the right (PEDSAFE, n.d.). Prohibiting RTOR during certain times or always can reduce conflicts between turning vehicles and pedestrians. Restrictions can be applied citywide or in specific districts or zones where conflicts are most likely to arise (NACTO, 2013). New York City has prohibited RTOR citywide except where permitted by posted signs. NYCDOT conducted safety studies to determine where RTOR would be allowed (NYCDOT, 2009).
One potential concern with prohibiting RTOR is a possible increase in conflicts between right-turning vehicles and pedestrians during the green phase. Implementing LPI can address this issue.
Source:
NACTO. (2013). Urban Streets Design Guide, “Corner Radii.” Available: https://nacto.org/publication/urban-street-design-guide
NYCDOT. (2009). “Right Turn on Red” in Sustainable Streets Initiative. NYCDOT. Available: https://www1.nyc.gov/html/dot/html/about/stratplan.shtml
FHWA. (2013). PEDSAFE: Pedestrian Safety Guide and Countermeasure Selection System, “Right Turn on Red Restrictions.” Available: http://www.pedbikesafe.org/PEDSAFE/countermeasures_detail.cfm?CM_NUM=49

## Slide 33: Accessible Pedestrian Signals (APS)
Communicate information about pedestrian timing in nonvisual format such as audible tones, verbal messages, and/or vibrating surfaces (MUTCD, Section 4A.02)
MUTCD 4E.08 provides guidance on locating pushbuttons and APS devices
Required features of APS (MUTCD 4E.09-4E.13)
  Pushbutton locator tone
  Audible and vibrotactile indications of the WALK
  Tactile arrow aligned with the direction of travel on the crosswalk
  Automatic volume adjustment
Notes: Notes: Proposed PROWAG requires APS where pedestrian signals are installed.
Connection to other Module: Accessibility and ADA
Source: National Academies of Sciences, Engineering, and Medicine. (2011). Accessible Pedestrian Signals: A Guide to Best Practices (Workshop Edition 2010). Washington, DC: The National Academies Press. https://doi.org/10.17226/22902.
More information from: http://www.apsguide.org/index.cfm

## Slide 34
FHWA
Notes: Key Message: This simple signal timing tweak enables pedestrians to get a head start and avoid the conflicts that occur when pedestrians and turning vehicles start their movements simultaneously. LPIs have been shown to reduce pedestrian-vehicle collisions as much as 60% at treated intersections.
Notes: LPI gives pedestrians a bit of a head start (minimum 3-7 seconds) to let them start crossing before motor vehicles do. This means pedestrians are already 10-15 feet into the crosswalk when vehicles start their turns. This enables drivers to see the pedestrians; when pedestrians are present, drivers wait their turn. This strategy should be paired with right-turn-on-red restrictions. If an intersection has particularly high pedestrian traffic, an exclusive pedestrian phase might be more appropriate.
Important: Make sure that an LPI is accompanied by an audible noise that lets visually impaired pedestrians know that it’s safe to cross.
Source:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.
FHWA. (2013). PEDSAFE: Pedestrian Safety Guide and Countermeasure Selection System. Available: http://www.pedbikesafe.org/PEDSAFE/countermeasures_detail.cfm?CM_NUM=12

## Slide 35: Leading Pedestrian Interval
NACTO
Notes: Key Message: Rendering on the left shows the pedestrian-only phase, and the right shows the approximate position of pedestrians once through and turning vehicle traffic are given the green light.
Notes: Where a bikeway on the through movement conflicts with turning traffic, use a leading bicycle interval along with the leading pedestrian interval. A leading bicycle interval clears the intersection of all cyclists quickly and can help prevent right hook collisions (link to a video illustrating this problem is saved with the slide “Common Safety Problems”).
Source: Image from NACTO. (2013). Urban Street Design Guide, “Leading Pedestrian Interval.” Available: https://nacto.org/publication/urban-street-design-guide/intersection-design-elements/traffic-signals/leading-pedestrian-interval/

## Slide 36: Signal Detection
Loop detectors should be provided for bicyclists at intersections
pedbikeimages.org – Carl Sundstrom
Notes: Key Message: The needs of bicyclists must be considered when setting signal timing.
Notes: AASHTO states that at signalized intersections where bicycle traffic exists or is anticipated, the timing of the traffic signal, as well as the method of detecting the presence of bicyclists, should be considered. The MUTCD also requires that where visibility-limited signal faces are used, they must be adjusted so bicyclists can see the signal indication, or if they cannot, then separate signal faces must be provided for bicyclists. Loop detectors should be designed to respond to the presence of bicyclists at intersections either through separate detectors in bike lanes (shown above) or by marking the “sweet spot” with a pavement marking to show the location that a bicyclist must stand in order to be detected.
Source: National Highway Institute. (2002). Bicycle Facility Design, Course Number 142046. McLean, VA: Federal Highway Administration.

## Slide 37: Bicycle Signal Heads
At intersections:
  With bicycle-specific movements
  Where bicycle movements need to be separated in time from conflicting vehicular movement
  With high bicycle volumes
pedbikeimages.org – Adam Coppola Photography
Notes: Key Message: In 2013, FHWA issued the Interim Approval for Optional Use of Bicycle Signal Face (IA-16). Bicycle signals are widely used in Europe and China, and they are currently being used by at least a dozen U.S. local governments or State DOTs. The interim approval details technical conditions including the signal indications and the design of the bicycle signal faces.
Notes: Bicycle-specific signals are recommended “at intersections with contra-flow bicycle movements that otherwise would have no signal indication and where a normal traffic signal head may encourage wrong-way driving by motorists.” (NACTO, 2014)
Source:
NACTO Urban Bikeway Design Guide 2nd Edition (2014). Available https://nacto.org/publication/urban-bikeway-design-guide/bicycle-signals/bicycle-signal-heads/
FHWA. (2014). BIKESAFE: Bicycle Safety Guide and Countermeasure Selection System, “Bicycle Signal Heads.” Available: http://www.pedbikesafe.org/BIKESAFE/countermeasures_detail.cfm?CM_NUM=55
Additional Info: PBIC webinar: http://www.pedbikeinfo.org/training/webinars_PBIC_LC_042518.cfm

## Slide 38: Other Intersections

## Slide 39: Interchanges
Pedestrian travel often not considered in interchange design
  High vehicle speeds at on- and off-ramps
  Lack of crossing or walking infrastructure
Pedbikeimages.org – Barbara Gossett
Notes: Key Message: Walking through and around interchanges can be extremely difficult for pedestrians, as their needs are often not considered in interchange design.
Source:
FHWA. (2013). PEDSAFE: Pedestrian Safety Guide and Countermeasure Selection System, “Pedestrian Accommodations at Complex Interchanges” Available: http://www.pedbikesafe.org/PEDSAFE/countermeasures_detail.cfm?CM_NUM=30
Hughes, Warren; Jagannathan, Ram; Sengupta, Dibu; and Hummer, Joe. (2010). Alternative Intersections/Interchanges: Informational Report. Washington, DC: Federal Highway Administration, Office of Safety.

## Slide 40: Interchanges
Incorporate pedestrian facilities into interchange planning and design phases
Design interchange crossings like other urban intersections:
  Slow vehicle approach speeds
  Short crossing distance
  Appropriate signs, signals, and markings
Jug-handle design can be beneficial for pedestrians and bicyclists
Notes: Source: FHWA. (2013). PEDSAFE: Pedestrian Safety Guide and Countermeasure Selection System, “Pedestrian Accommodations at Complex Interchanges” Available: http://www.pedbikesafe.org/PEDSAFE/countermeasures_detail.cfm?CM_NUM=30

## Slide 41: Roundabouts
Bicyclists may merge with vehicle traffic or travel as pedestrian on sidewalk (or shared-use path)
Bicycle ramp should include detectable warning
FHWA
Notes: Notes: Bicycle lanes should not be marked in the circular roadway of a modern roundabout. Instead, according to the 2012 AASHTO Guide for the Development of Bicycle Facilities, the bicycle lane line should become a dotted line prior to the crosswalk at the roundabout entrance and a transition ramp to a widened sidewalk should be provided. This transition ramp should include detectable warnings. Bicyclists then have the option of riding through the roundabout (where motor vehicle speeds are reduced to a comfortable speed) or dismounting and continuing around the roundabout as a pedestrian.
Source: FHWA (2010). Technical Summary: Roundabouts (FHWA-SA-10-006).
Image: https://safety.fhwa.dot.gov/intersection/innovative/roundabouts/fhwasa10006/images/f19.jpg

## Slide 42: Roundabouts
Principles for designing roundabouts for those using non-visual cues:
  Use features to guide pedestrians away from where they should not cross
  Orient curb ramps in the direction of the crosswalk
  Ramps, channelization and splitter islands should all align
NCHRP
Notes: Notes: The image shows landscaping that discourages crossing to the central island and provides an edge that blind pedestrians can follow (i.e., trail) with the long cane to locate a curb ramp. Three principles for designing crosswalks for people who rely on nonvisual information are:
Landscaping, fences, or other features should restrict the ability of pedestrians to cross at locations other than crosswalks, or at least make it very clear where crossing is not intended and provide guidance to the crosswalk location.
Curb ramps should be oriented so that the running slope is in the same direction as the crosswalk and/or the edges of landscaping or ramps should be aligned in the direction of travel on the crosswalk.
The far side of the crosswalk and any channelization and splitter islands should be aligned with the nearside ramp and should be designed to compensate for the expected error in the crossing angle.
Connection to Other Module: Accessibility and ADA
Source:
National Academies of Sciences, Engineering, and Medicine (2017). Crossing Solutions at Roundabouts and Channelized Turn Lanes for Pedestrians with Vision Disabilities: A Guidebook. Washington, DC: The National Academies Press. https://doi.org/10.17226/24678.
U.S. Access Board, “Modern Roundabouts,” Available: https://www.access-board.gov/enforcement/221-research/research-on-public-rights-of-way/modern-roundabouts. [Accessed June 2019].

## Slide 43: Options at Minor Intersections
Neighborhood traffic circles and mini roundabouts
  Can fit within existing ROW
  Traffic calming effect
  May have traversable or non-traversable islands
  May include splitter islands
  Should have pedestrian crossings
NACTO
Notes: Key Message: Mini roundabouts and neighborhood traffic circles are an option for traffic calming at lower-speed roadways (typically 30mph or less) and residential areas. For roadways with speeds greater than 35mph, additional traffic calming measures may be needed. Bicycles can typically navigate these intersections comfortably as vehicles or use the provided pedestrian crossings. (FHWA 2010)
Notes: “Mini-roundabouts are distinguished from neighborhood traffic circles primarily by their traversable islands and yield control on all approaches, which allows them to function as other roundabouts do. Neighborhood traffic circles are typically built at the intersections of local streets for reasons of traffic calming and/or aesthetics. They typically are operated as two-way or all-way stop-controlled intersections and frequently do not include raised channelization to guide approaching traffic into the circulatory roadway. At some neighborhood traffic circles, left-turning vehicles must turn in front of the central island, potentially conflicting with other circulating traffic.” (FHWA, 2010)
Source:
NACTO. (2013). Urban Street Design Guide. Available: https://nacto.org/publication/urban-street-design-guide/intersections/minor-intersections/mini-roundabout/#footnotes
FHWA. (2010). Mini Roundabouts Technical Summary. Available: https://nacto.org/docs/usdg/fhwa-mini-roundabouts-technical-report.pdf

## Slide 44: Protected Intersections
Massachusetts Department of Transportation
Notes: Key Message: Also called setback or offset intersections. Used where separated bike facilities lead up to an intersection, this design keeps bikes physically separated and improves sightlines. Small curb radii reduce vehicle turning speeds. And as shown in this rendering, larger vehicles can be accommodated where necessary using mountable truck aprons on corner islands.
Notes: [The Master Video List includes a link to a video that walks the viewer through this concept in six minutes]
Source:
NACTO. (2019). Don’t Give Up at the Intersection. Available: https://nacto.org/wp-content/uploads/2019/05/NACTO_Dont-Give-Up-at-the-Intersection.pdf
Massachusetts Department of Transportation. (2015). Separated Bike Lane Planning and Design Guide. MassDOT

## Slide 45: Protected Intersections
Corner islands extend bike lane separation as far into the intersection as possible
  Creates a bike queue area after the crosswalk
  Should discourage cars from turning faster than 10 mph
Bicycle and pedestrian crossings set back from travel lane
Setback creates waiting zone for turning cars
Shorter, potentially simpler crossings for pedestrians
Bicycle-friendly signal phasing
Notes: Key Message: Features and benefits listed on the slide. MUTCD Chapter 4E, PROWAG, and local standards for signal timing and location guidance still apply for making this facility design accessible.
Source:
NACTO. (2019). Don’t Give Up at the Intersection. Available: https://nacto.org/wp-content/uploads/2019/05/NACTO_Dont-Give-Up-at-the-Intersection.pdf
Massachusetts Department of Transportation. (2015). Separated Bike Lane Planning and Design Guide. MassDOT.

## Slide 46: Protected Intersections
pedbikeimages.org – Nathan Roseberry
Notes: Notes: Image shows a protected intersection in Chicago. Other U.S. cities using protected intersections include New York, NY; San Francisco, CA; Portland, OR; Davis, CA; San Jose, CA; and Salt Lake City, UT.

## Slide 47: Protected Intersections
Setback between vehicles and bike lane improves visibility
Corner islands extend the bike lane protection into the intersection
NACTO
Notes: This slide is animated
Key Message: Setback places the waiting bicyclist in the sightline of turning drivers, compared to a conventional intersection where bicycles are not in the turning driver’s sightline.
Source: NACTO. (2019). Don’t Give Up at the Intersection. Available: https://nacto.org/publication/urban-bikeway-design-guide/dont-give-up-at-the-intersection/

## Slide 48: International Examples
pedbikeimages.org – Dan Burden
Delft, the Netherlands
Notes: Key Message: The protected intersection is inspired by Dutch intersection design. The next two slides present other examples of intersection designs from abroad that would be innovative if introduced in the United States.

## Slide 49: International Examples
Large, grade-separated intersections
  Vehicle traffic elevated, pedestrians and bicycles continue at-grade underneath (Haderslev Municipality, Denmark)
  Circular bicycle and pedestrian bridge over vehicle-only intersection (Eindhoven, The Netherlands)
Bicycle-friendly design for multilane roundabouts
  Slower vehicle speeds achieved through narrower lanes (Auckland, New Zealand)
Notes: Source:
FHWA. (2015). Delivering Safe, Comfortable, and Connected Pedestrian and Bicycle Networks: A Review of International Practices. Washington, DC: FHWA.
FHWA. (2016). Bicycle Network Planning & Facility Design Approaches in the Netherlands and the United States. Washington, DC: FHWA.

## Slide 50: International Examples
Signal timing and feedback
  “Green wave” corridors with signals timed for bicyclists (Netherlands and Denmark)
  Multiple green phases for bicyclists per cycle (Denmark)
  Responsive signal timing increases green phases for bicycles when rain or snow are detected (Groningen, Netherlands)
  Pedestrian signals that provide wait time estimates (Netherlands)
Notes: Source: FHWA. (2015). Delivering Safe, Comfortable, and Connected Pedestrian and Bicycle Networks: A Review of International Practices.

## Slide 51: Summary
Pedestrians
  Visibility (for drivers and pedestrians) is important
  Simplify crossings and shorten distances
Bicycles
  Separate from vehicle traffic
  Position waiting bicyclists in visible and expected locations
Both
  Establish clear right of way and priority for these modes