## Slide 1: Safety Analysis
Instructor Course Information
Notes: Report No. FHWA-SA-19-034

## Slide 2: Module Outline
Defining and measuring safety
Safety analysis fundamentals
Roadway safety management process
Safety effectiveness evaluation
Notes: Notes: This lecture is designed to introduce current methods of safety analysis for pedestrian and bicyclists. After this lecture students should feel comfortable with some of the language and methods used to study pedestrian and bicycle safety. This lecture will also address some of the current limitations inherent in bicycle and pedestrian safety analysis.

## Slide 3: Big Picture
Why does safety matter to planners?
How much safety is enough?
Has safety received enough attention?
Who is responsible for safety?
Can ped/bike safety be made more compatible with other interests?
pedbikeimages.org – Dan Burden
Notes: Key Message: This slide is to get you thinking about the big picture safety issues. Who’s responsible for safety? Why isn’t there a greater incentive to build safer roadways?
Could there be greater compatibility between safety, mobility, and access than in present systems?
Notes: Balancing ped/bike safety with other interests is important but difficult. Air quality, congestion, global climate change, and energy use issues should also be considered. An important element of pedestrian and bicycle planning is creating a culture of traffic safety, which means institutionalizing and creating public demand for safety.
Source:
Slide adapted from: PBIC. (2011). Graduate Level Bicycle and Pedestrian Planning Course.
Hauer, E. (2007). “A case for evidence-based road safety delivery” in Improving traffic safety culture in the United States: The journey forward. Ed. Kisinger, P. Washington, D.C.: AAA Foundation for Traffic Safety.
Image: http://www.pedbikeimages.org/mediumimages/crossing.3.boulder.broadway(8).jpg

## Slide 4: Defining and Measuring Safety
Notes: Key Message: In the simplest terms, safety can be defined as the absence of risk or danger. Focusing this term to address transportation, road safety can be characterized by the ability of a person to travel freely without injury or death. A perfectly safe transportation system would not experience crashes between various road users. Though absence of all crashes is an optimal condition, and many transportation agencies have a goal of zero deaths on the road, the reality is that people continue to get injured or killed on streets and highways across the nation. The responsibility of all transportation professionals and road users, not only those in the road safety field, is to minimize the frequency of crashes and the resulting deaths and injuries using all currently available tools, knowledge, and technology. This challenge is made more complex due to the many factors influencing safety, from infrastructure to vehicle design to human behavior.
Source: FHWA. (2017). Road Safety Fundamentals; Concepts, Strategies, and Practices that Reduce Fatalities and Injuries on the Road. Ed. Daniel Carter. U.S. Department of Transportation. Available: https://rspcb.safety.fhwa.dot.gov/rsf/

## Slide 5: Safety Analysis Questions
Benchmarking
How many fatalities and serious injuries are occurring in my area?
How does this compare to other areas?
Crash Trends and Contributing Factors
When/where are crashes occurring?
Countermeasures
What are the countermeasures to address these characteristics?
What are the major contributing factors?
What locations (intersections or segments) show the most potential for safety improvement?
Sites for Safety Improvement
Notes: Notes: High-quality safety analysis demands high-quality data. Unfortunately, poor data availability and low-quality data limit the types of analyses that can be conducted. The data requirements depend on the type of analysis and what safety questions are being asked. Data needs may include total crashes, total fatalities and serious injuries, roadway data, contributing factors (age, impairment, speed, etc.), traffic volume data, etc.
Connection to other Module: Bicycle and Pedestrian Data for Planning
Source: FHWA. (2017). Road Safety Fundamentals; Concepts, Strategies, and Practices that Reduce Fatalities and Injuries on the Road. Ed. Daniel Carter. U.S. Department of Transportation. Available: https://rspcb.safety.fhwa.dot.gov/rsf/

## Slide 6: Measuring Safety - Crashes
Common elements of police reported crashes:
  Date/time
  Crash location
  Weather conditions
  Light conditions
  Injury severity
  Types of vehicles
  Characteristics of persons involved
  Crash narrative and diagram
Notes: Key Message: We analyze crash data to both identify problems and to evaluate how well treatments are working. However, crashes are relatively rare events, especially those involving bicyclists and pedestrians, so surrogate measures are often needed to evaluate treatment effectiveness (shown on forthcoming slide).
Notes: Local analyses typically include all ped/bike crashes, rather than just fatalities, because numbers of fatalities are small and fluctuate so widely. Several years (at least) are required to observe trends in crashes involving bicyclists and pedestrians, especially trends in fatalities. Crashes are currently viewed as the most objective and reliable measurements of road safety. However, there are challenges with crash data, such as human error in reporting, unreported crashes, and the length of time it often takes for crashes to be entered into a database.
Only traffic-related crashes involving motor vehicles are reported to authorities and most States have a minimum threshold of injury or property damage for the police department to file a crash report.
Source: FHWA. (2017). Road Safety Fundamentals; Concepts, Strategies, and Practices that Reduce Fatalities and Injuries on the Road. Ed. Daniel Carter. U.S. Department of Transportation. Available: https://rspcb.safety.fhwa.dot.gov/rsf/

## Slide 7: Analyzing and Interpreting Crash Data
  Who, where, when
    These factors are not “causal” but may be surrogates for risk
    May help identify location types or populations for intervention
NHTSA (2018)
Chicago’s Vision Zero Action Plan
Notes: Key Message: In conducting studies, be careful not to assume correlation is the cause of an “effect.” Nevertheless, some correlates (for example, age group involvement) may suggest target populations for countermeasures. Databases are subject to errors in reporting, errors of omission, and errors in data entry. Demographic analyses can help you understand if certain populations are overrepresented in crashes and fatalities.
Connection to other Module: The full graphic from Chicago’s Vision Zero Action Plan is included in the Equity module.
Source:
Slide adapted from: PBIC. (2011). Graduate Level Bicycle and Pedestrian Planning Course.
National Center for Statistics and Analysis. (2019, March). Pedestrians: 2017 data. (Traffic Safety Facts. Report No. DOT HS 812 681). Washington, DC: National Highway Traffic Safety Administration.
City of Chicago. Vision Zero Action Plan. Available: http://visionzerochicago.org/wp-content/uploads/2016/05/17_0612-VZ-Action-Plan_FOR-WEB.pdf

## Slide 8: Analyzing and Interpreting Crash Data
What – crash type
  Relies on the diagrams and narratives in crash reports
  Crash types are defined by a sequence of events
    E.g., bicyclist position and direction, crash location, etc.
Notes: Key Message: The selection of effective countermeasures to prevent bicyclist and pedestrian crashes is hindered by computerized State crash files that contain insufficient details about the crashes. Analysis of these files often provides data that includes where pedestrian and bicyclist crashes occur, such as the city, street, type of street, or intersection; when crashes occur, such as the time of day or day of the week; and the characteristics of the victims, such as their age, gender, and severity of injuries. These data, however, do not provide adequate detail to determine the sequence of events that lead up to and cause crashes. That is where crash typing can fill a gap. To determine the crash type, analysts typically need to review the crash report narrative, diagram, and geographic details.
Notes: These analyses can be conducted at the local, regional or State level. The slide shows a report for the State of North Carolina and an excerpt showing how the crash type “Motorist Overtaking Bicyclist” can be broken out by the speed limit on the road where the crash occurred. In this case, researchers call out that two-thirds of motorist overtaking crashes take place on roadways with a speed limit of over 40 mph and suggest that this is a likely contributing factor in the over-representation of fatal and disabling injuries among these collisions.
Source:
Pedestrian and Bicycle Information Center, “About PBCAT” Available: http://www.pedbikeinfo.org/pbcat_us/about.cfm
Vann, M., Thomas, L., and Levitt, D. (2018). North Carolina Bicycle Crash Types 2012-2016. North Carolina Department of Transportation. Available: http://www.pedbikeinfo.org/pbcat_nc/pdf/summary_bike_types12-16.pdf

## Slide 9: Measuring Safety - Crashes
Crash frequency
Crash rate
The number of crashes normalized by a population or metric of exposure (e.g., traffic volume or population)
Crash outcome
Measured by the types of injuries sustained to the people involved in the crash
The number of crashes occurring per year or other unit of time
Notes: Key Message: Crash rate calculation (crashes per amount of traffic) is a simplistic measure that may be useful when comparing sites with similar characteristics and traffic volumes. Crash rates implicitly assume that crashes and exposure are linearly related. However, the relationship between crashes and volume is often not linear and can therefore lead to wrong conclusions if that assumption is made when considering volume increases on a road or comparing roads of different types. The use of safety performance functions (SPFs) can help avoid this error (SPFs are discussed later in this module).
Source: FHWA. (2017). Road Safety Fundamentals; Concepts, Strategies, and Practices that Reduce Fatalities and Injuries on the Road. Ed. Daniel Carter. U.S. Department of Transportation. Available: https://rspcb.safety.fhwa.dot.gov/rsf/

## Slide 10: Measuring Safety – Injury Surveillance
Captures motor vehicle- involved injuries that may not show up in crash data
Captures other injuries that may be infrastructure-related
Challenges
  Linkage to crash data
  Obtaining access and interpreting
Safe States Alliance
Notes: Key Message: Hospital records are also often the only source of information on bicycle and pedestrian crashes that are not recorded by the police, such as those that occur in non-roadway locations like parking lots and driveways.
Notes: Injury surveillance systems (ISS) typically provide data on emergency medical services (EMS), hospital emergency departments, hospital admissions/discharges, trauma registry, and long-term rehabilitation. This information is used to track injury causes, severity, costs, and outcomes. Although an injury associated with a traffic crash is only one type of injury in these medical systems, traffic crash injuries can be a useful source of data in bridging the gap between traditional traffic safety and public health issues. Hospital data can also be used to identify the full magnitude of crashes for a specific user group or demographic that is not recorded or reported by law enforcement. For example, hospital data can help safety professionals better understand the number of bicyclist crashes, since many bicycle-related crashes are not reported to law enforcement.
Source: FHWA. (2017). Road Safety Fundamentals; Concepts, Strategies, and Practices that Reduce Fatalities and Injuries on the Road. Ed. Daniel Carter. U.S. Department of Transportation. Available: https://rspcb.safety.fhwa.dot.gov/rsf/
Image: Injury Surveillance Workgroup 8 (ISW8). Consensus Recommendations for Pedestrian Injury Surveillance. Atlanta (GA): Safe States Alliance, 2017.

## Slide 11: Measuring Safety - Surrogates
Conflicts/near miss
  Sudden change in speed or trajectory/path
Observed behaviors
  E.g., driver yielding, vehicle speed, pedestrian use of crosswalks
User perceptions
  A measurement of how safe a user feels under various network scenarios
Notes: Notes:
Conflicts may be defined as a sudden change in speed or trajectory/path, use of audible warnings (yelling, horn-blowing), etc. to avoid a collision. These data may be collected via in-person observation or by coding of video data.
Near misses occur when a cyclist almost crashes (with a car or other object) but escapes physically unscathed. These data would be collected by crowdsourcing, surveys, or interviews.
Behaviors (these must be observable) that are sometimes used as surrogates:
In pedestrian studies, motorist behaviors such as yielding to pedestrians at a crosswalk; slowing; speed.
For pedestrians: looking behaviors (before crossing), use of crosswalks (versus undesignated areas), complying with signals, etc.
In bicyclist studies, yielding at merge/conflict areas (depending on who has right-of-way); lateral space allowed when passing (often for bike lane, other roadway facilities studies); possibly signaling intentions, others, depending on what is being studied.
User perceptions or rankings by users or expert groups (how comfortable; how safe) are also used in setting performance measures and or safety ratings for roadways (LOS and others will be discussed in a later lecture). The methods of collection are like those used for near miss data.
Student Question: Ask students to consider what these data might tell us that crash data can’t. How might these data be used in different stages of planning and evaluation?
Source: Slide adapted from: PBIC. (2011). Graduate Level Bicycle and Pedestrian Planning Course.

## Slide 12: Potential for Crashes and Injury
Number of pedestrians or bicyclists
Traffic volume
Traffic speeds
Lanes (number, width, configuration)
Sight distance and visibility
Number of intersections/ conflict areas
Pedbikeimages.org – Nina Walfoort
Notes: Notes: The intent of this slide is to introduce some examples of factors that may affect exposure to crashes in addition to numbers of pedestrians or bicyclists. Many others could be listed in addition to the ones here. Also, these factors likely interact, so factors that may reduce risk in some situations may increase it in others.
Source: Slide adapted from: PBIC. (2011). Graduate Level Bicycle and Pedestrian Planning Course.

## Slide 13: Measuring Safety - Challenges
Single sources of data do not tell the entire story
Changes over time
  E.g., reporting thresholds
Data availability
Ability to link/combine data sources
Shortcomings of crash reporting forms and databases
Biases, inconsistent reporting
  E.g., inaccurate locations, wrongly assigned fault or crash type
Notes: Notes: Changes in how officers code crashes, changes in reporting thresholds, and others may result in changes in apparent numbers of crashes that are due to differences in measurement. Shortcomings in crash reporting forms can include the failure to collect an item; lack of suitable “levels” of the item; too many/too few codes; and contradictory information between variables. The last bullet questions how well officers understand right-of-way with respect to bicyclists and pedestrians. They may be trained in some areas and not in others. For instance, do officers assume if cyclist had a head injury (and were removed before they arrived) that they weren’t wearing a helmet? If pedestrian was killed, and motorist claims “They appeared out of nowhere”…”I wasn’t on the phone” – can they be trusted? These problems are subtle & difficult to detect. There may also be problems with spatial data as officers and witnesses may not be able to accurately describe the location of the crash.
Source:
Slide adapted from: PBIC. (2011). Graduate Level Bicycle and Pedestrian Planning Course
FHWA. (2017). Road Safety Fundamentals; Concepts, Strategies, and Practices that Reduce Fatalities and Injuries on the Road. Ed. Daniel Carter. U.S. Department of Transportation. Available: https://rspcb.safety.fhwa.dot.gov/rsf/

## Slide 14: Measuring Safety
Many safety problems go unreported….
https://www.youtube.com/watch?v=5XKcHvSCK4Y
Ling, Cherry, Dhakal (2017)
Notes: Key Message: Single sources of safety data do not give a complete picture of the safety risks on our roads.
Notes: For example, using crash data by itself leaves safety practitioners with purely reactive approaches – identifying locations where crashes have already happened. Many crashes go unreported and there can be causes of injury to bicyclists and pedestrians that do not involve cars, but that can be mitigated through design and maintenance.
Source:
YouTube video from University of Tennessee Civil and Environmental Engineering Department, Bicycle Accidents at Railroad Crossings.
Ling, Z., Cherry, C. R., & Dhakal, N. (2017). Factors influencing single-bicycle crashes at skewed railroad grade crossings. Journal of Transport & Health, 7, 54-63. Open access at: https://www.sciencedirect.com/science/article/pii/S2214140516303450?via%3Dihub#!
FHWA. (2017). Road Safety Fundamentals; Concepts, Strategies, and Practices that Reduce Fatalities and Injuries on the Road. Ed. Daniel Carter. U.S. Department of Transportation. Available: https://rspcb.safety.fhwa.dot.gov/rsf/
Image: https://ars.els-cdn.com/content/image/1-s2.0-S2214140516303450-gr3.jpg

## Slide 15: Safety Analysis Fundamentals
Notes: Notes: This section is about conducting safety analysis. Some concepts and terminology are introduced first, followed by different approaches for conducting safety analysis.

## Slide 16: Quantifying Safety Performance
Performance Measure | Accounts for Regression-to-the-Mean | Performance Threshold
Average Crash Frequency | No | No
Crash Rate | No | No
Equivalent Property Damage Only (EPDO) Average Crash Frequency | No | No
Relative Severity Index | No | Yes
Critical Rate | No | Yes
Excess Predicted Average Crash Frequency Using Method of Moments | No | Yes
Level of Service of Safety | No | Yes
Excess Expected Average Crash Frequency Using SPFs | No | Yes
Probability of Specific Crash Types Exceeding Threshold Proportion | Not Affected | Yes
Excess Proportions of Specific Crash Types | Not Affected | Yes
Expected Average Crash Frequency with Empirical Bayes (EB) Adjustments | Yes | Yes
EPDO Average Crash Frequency with EB Adjustment | Yes | Yes
Excess Expected Average Crash Frequency with EB Adjustments | Yes | Yes
Notes: Notes: This slide introduces the various safety performance measures as listed in the Highway Safety Manual. There are various measures of safety performance and different measures can produce different results when prioritizing sites for safety improvement. This table indicates the reliability of the different performance measures for ranking sites with potential for improvement. More reliable methods (shown at the bottom of the table) account for regression-to-the-mean and set a performance threshold.
Source: AASHTO. (2010). Highway Safety Manual.

## Slide 17: Which site would you select based on crash frequency?
A
B
Measure of Safety | Int. A | Int. B
Crash Frequency (crashes/year) | 10.1 | 6.8
Notes: Notes: This slide introduces the concept of using crash frequency as the safety performance measure. In this case, the analyst would select Intersection A as the top priority with respect to crash frequency.

## Slide 18: Which site would you select based on crash rate?
Measure of Safety | Int. A | Int. B
Crash Frequency (crashes/year) | 10.1 | 6.8
Total Entering Volume (vehicles/day) | 10,000 | 2,500
Crash Rate (crashes/million-vehicles) | 2.8 | 7.5
Notes: Notes: This slide introduces the concept of using crash rate as the safety performance measure. In this case, the analyst would select Intersection B as the top priority with respect to crash rate.

## Slide 19: Quantifying Safety Performance
Crash rates (crashes per unit exposure)
  Assumes crashes and exposure are linearly related
Relationship is often non-linear
“Empirical evidence shows that the relationship between expected accident frequency and traffic flow is usually not a linear one.”
-- Hauer (1997)
Notes: Notes: This slide hints that there is a more reliable way to quantify safety performance. As discussed earlier, crash rates (crashes per unit exposure) implicitly assume that crashes and exposure are linearly related; often, the relationship is non-linear.
Source: Hauer, E. (1997). Observational Before–After Studies in Road Safety: Estimating the Effect of Highway and Traffic Engineering Measures on Road Safety. Elsevier Science, Ltd, Oxford, United Kingdom.

## Slide 20: Quantifying Safety Performance
Safety performance functions (SPFs)
  Mathematical equations that relate crashes to exposure
  Account for non-linear relationship
Example SPF:
Total Crashes = exp-3.63 * Length * AADT0.53
Notes: Notes: Safety performance functions (SPFs) are mathematical equations that relate crashes to exposure. SPFs account for the non-linear relationship between crashes and exposure. These equations are typically estimated using a statistical procedure that involves curve-fitting. The specific function or shape of the SPF may depend on the type of facility and crash type being investigated.
Source: AASHTOWare Safety Analyst™ documentation.

## Slide 21: Relationship Between Crashes and Exposure (Example 1 of SPF)
Crashes per Unit Time
FHWA
Notes: Notes: This is a hypothetical example of an SPF illustrated in a graph. The horizontal axis shows exposure and the vertical axis shows the number of crashes. If the relationship between crashes and exposure is linear, the line will be a straight line instead of a curve.
Source: FHWA. (2017). Road Safety Fundamentals; Concepts, Strategies, and Practices that Reduce Fatalities and Injuries on the Road. Ed. Daniel Carter. U.S. Department of Transportation. Available: https://rspcb.safety.fhwa.dot.gov/rsf/

## Slide 22: Relationship Between Crashes and Exposure (Example 2 of SPF)
FHWA
Notes: Notes: This is another example of an SPF. The shape of the SPF depends on the type of facility, crash type, and severity.
Source: FHWA. (2017). Road Safety Fundamentals; Concepts, Strategies, and Practices that Reduce Fatalities and Injuries on the Road. Ed. Daniel Carter. U.S. Department of Transportation. Available: https://rspcb.safety.fhwa.dot.gov/rsf/

## Slide 23: Example SPF from Highway Safety Manual
SPF for predicting number of pedestrian-vehicle crashes in a year at a 4-leg signalized intersection in an urban-suburban arterial
Variables: total intersection AADT, minor road AADT, major road AADT, pedestrian volume, and maximum number of lanes to be crossed by a pedestrian
Developed using data from Toronto and Charlotte
  Need to calibrate if using in other jurisdictions or time periods
Notes: Notes: This slide is an example SPF that is documented in the Highway Safety Manual. This SPF was estimated using data from Toronto and Charlotte and can be used to predict the number of pedestrian-vehicle crashes in one year at a 4-leg signalized intersection.
The SPF includes total intersection AADT (AADTTotal), minor road AADT (AADTmin), major road AADT (AADTmaj), sum of daily pedestrian volumes crossing all intersection legs (Pedvol), and the maximum number of legs crossed by a pedestrian in any crossing maneuver at the intersection considering the presence of refuge islands (nlanesx).
If this SPF is used in other jurisdictions, it needs to be calibrated. The procedures for calibration can be found in the Highway Safety Manual.
Source: AASHTO. Highway Safety Manual, 1st Edition, Volume 2, Chapter 12. p 12-36, 12-37.

## Slide 24: Hypothetical Numerical Example to Illustrate Application of SPF
Total AADT = 36,000; Minor road AADT = 14,000; Major road AADT = 22,000; Pedestrian volume = 5,000 per day; Maximum number of lanes to cross after considering the presence of refuge islands = 2
  = 0.21 pedestrian-vehicle crashes per year (i.e., about 1 pedestrian-vehicle crash every 5 years)
Notes: Notes: Here is a numerical example to illustrate the application of the SPF that was shown in the previous slide. Using the inputs, the calculation can be made using a calculator or an excel spreadsheet.

## Slide 25: Regression to the Mean
Poll: have you heard of the term regression to the mean?
  Yes
  No
If yes, can you explain what it means?
Notes: Notes: Regression to the mean is an important concept in the context of analyzing and interpreting crash data.
Source: Slide adapted from the UNC Highway Safety Research Center’s Road Safety Academy, (2018).

## Slide 26: Regression to the Mean
Crashes are random events that naturally fluctuate over time
Regression to the mean (RTM) refers to the phenomenon of ‘averaging out’ in statistics
May lead us to confuse random change with real change
Notes: Notes: Crashes are random events that naturally fluctuate over time at any given site. This crash fluctuation makes it difficult to determine whether changes in observed crash frequency are due to changes in site conditions or random natural fluctuations.
So, regression to the mean refers to the phenomenon of ‘averaging out’ in statistics. So, if the crash count at a site is unusually high in a particular year, it is very likely that it is going to approach its average in the next year.
If we are not careful, this phenomenon may lead us to confuse random change with real change.
Source: Slide adapted from the UNC Highway Safety Research Center’s Road Safety Academy, (2018).

## Slide 27: Regression to the Mean
Notes: Key Message: What you see here is a graph to illustrate what was mentioned in the previous slide. This graph shows the observed crash frequency per year. It is apparent that the crash frequency randomly goes up and down every year.
Notes: What you also see is the expected average crash frequency (also called the long-term average) and short-term average crash frequency. So, the message is that the short-term frequency is not necessarily a good indicator of the long term expected average crash frequency.
This is hypothetical data, but the phenomenon is real.
Source: Slide adapted from the UNC Highway Safety Research Center’s Road Safety Academy, (2018).

## Slide 28: Estimating the Expected Average Crash Frequency
Empirical Bayes (EB) method
  One approach for estimating expected average crash frequency (i.e., long-term average value)
Weighted average of two parameters:
  Observed crash count at a site
  Predicted crash count based on the SPF
Notes: Notes: One approach for estimating the expected average crash frequency (i.e., long-term average value) is the use of the empirical Bayes (EB) method. If the EB method is used, the expected average crash frequency is called the EB estimate.
The EB estimate is the weighted average of two parameters: (1) observed crash count at a site, (2) predicted crash count based on the SPF. This concept is illustrated using a schematic in the next slide.

## Slide 29: Illustration of EB Method
FHWA
Notes: Notes: This schematic shows the difference between the observed number of crashes, predicted number of crashes, and the expected number using EB.
Source: FHWA. (2017). Road Safety Fundamentals; Concepts, Strategies, and Practices that Reduce Fatalities and Injuries on the Road. Ed. Daniel Carter. U.S. Department of Transportation. Available: https://rspcb.safety.fhwa.dot.gov/rsf/

## Slide 30: Road Safety Management Process

## Slide 31: Road Safety Management Process
Planning
Implementation
Evaluation
Identify safety issues, develop projects to mitigate safety issues, and prioritize projects
Schedule and implement projects
Determine the effectiveness of projects
Notes: Key Message: The safety management process can be viewed in three general components. These components are carried out by the agency (or agencies) responsible for managing the safety of the road system.
Notes:
Planning - The agency uses crash data and other safety data to identify safety issues or problem locations, diagnose crash contributing factors, and develop potential strategies to address or mitigate the contributing factors. These strategies might also be referred to as countermeasures or treatments. The agency must also weigh the potential strategies and decide which ones to implement within the given budget.
Implementation - The agency programs, designs, and constructs the selected projects.
Evaluation – The agency compares the safety performance before and after (or uses some other method) to evaluate the effectiveness of implemented projects.
Source: FHWA. (2010). Highway Safety Improvement Program Manual.

## Slide 32: Site, Systemic, and System-Wide Approaches
Site
Systemic
System-wide
Targeting locations that show potential for safety improvement based on crash-based performance measure(s)
Targeting focus crash and facility types based on presence of risk factors
Treating a safety problem across the entire transportation network based on policy
Notes: Notes: Similar processes can be used to identify, treat and evaluate specific sites and the system. It’s important to not just choose one method or the other. System-wide is a general term that refers to treating safety issues across an entire transportation system using policies or campaigns. Systemic is a more specific term that refers to identifying a subset of a transportation system based on risk factors and implementing safety efforts that address the characteristics of that subset.
The systemic and system-wide approaches are covered later in this lesson.
Source: FHWA. (2017). Road Safety Fundamentals; Concepts, Strategies, and Practices that Reduce Fatalities and Injuries on the Road. Ed. Daniel Carter. U.S. Department of Transportation. Available: https://rspcb.safety.fhwa.dot.gov/rsf/

## Slide 33: Site-Level Safety Management
Network Screening
Diagnosis
Countermeasure Selection
Economic Appraisal
Project Prioritization
Safety Effectiveness Evaluation
Notes: Notes: Site-level safety management is the process of identifying and addressing safety issues at high-priority sites. Site-level safety management can be further divided into six distinct steps. This step is presented in Part B of the first edition of the Highway Safety Manual. Many of these steps are included in this set of slides, except economic appraisal and project prioritization.
Source: FHWA. (2017). Road Safety Fundamentals; Concepts, Strategies, and Practices that Reduce Fatalities and Injuries on the Road. Ed. Daniel Carter. U.S. Department of Transportation. Available: https://rspcb.safety.fhwa.dot.gov/rsf/

## Slide 34: Network Screening
Select sites with high potential for safety improvement
  Typically through analysis of crash data
Key to effective network screening is to select an appropriate performance measure
  Account for differences in traffic volume
    Can be addressed using SPFs
  Account for possible bias due to regression to the mean
    Can be addressed using the EB method
  Account for crash severity
    Can be addressed by focusing on fatal and serious injury (or all injury) crashes
Notes: Notes: Network screening is the process of selecting high priority sites through an analysis of crash data.
The key to effective network screening is selecting an appropriate performance measure. Network screening methods should appropriately account for three major factors that can affect the screening outcome:
Differences in traffic volumes (can be addressed using SPFs that were discussed earlier)
Possible bias due to RTM (can be addressed using the EB method discussed earlier)
Crash severity

## Slide 35: Exercise: Network Screening
Roadway characteristics and crash data from city in United States
Enclosed Excel file shows the following measures for each segment representing the 8-year study period:
  Observed (reported) number of pedestrian crashes
  Predicted number of pedestrian crashes based on SPF
  Expected number of pedestrian crashes based on EB method
  Expected-excess number of pedestrian crashes
    = (Expected number of crashes) – (Predicted number of crashes)
Notes: [Skip this slide and the next slide if you are not using the assignment “Network Screening Exercise”]
Notes: This slide will include a network screening exercise using data on pedestrian crashes in roadway segments (midblock) from a city in the United States.
SPFs have been estimated using data on roadway characteristics and pedestrian crashes. The enclosed Excel file shows the following measures for each midblock segment:
Number of pedestrian crashes in 8 years. If this is used for network screening, then this approach does not account for differences in exposure and site characteristics among sites and does not account for possible bias due to regression to the mean.
Predicted pedestrian crashes based on an SPF that was estimated. This accounts for exposure and site characteristics but does not account for possible due to regression to the mean.
The last two measures are the expected number of crashes and the expected-excess number of crashes. Both these measures make use of the SPF and are based on the EB method, and hence, account for the exposure, site characteristics, and possible bias due to regression to the mean.
Source: W. Kumfer, L. Thomas, L. Sandt, and B. Lan. (2019). Midblock pedestrian crash predictions in a systemic, risk-based pedestrian safety process. Journal of the Transportation Research Board, Transportation Research Board. https://doi.org/10.1177/0361198119847976

## Slide 36: Exercise, cont.: Network Screening
23,000+ midblock segments
Use different measures to conduct network screening
Select top 100 segments based on each measure by sorting the excel file on each measure in decreasing order
Questions:
  Do all measures give same set of top 100 segments?
  Do certain segments consistently rank in top 100?
  What are the characteristics of top ranked segments?
Being a top 100 segment does not necessarily imply that a treatment is warranted
  These segments are prime candidates for further investigation
Notes: Notes:
Data are available for more than 23,000 midblock segments.
The exercise involves using different measures to conduct network screening. Select top 100 segments based on each measure:
Questions to ask:
  Do all the methods give you the same set of top 100 segments?
  Do certain segments consistently rank in the top 100 regardless of the measure?
Being a top 100 segment does not necessarily imply that a treatment is warranted, but these segments are probably prime candidates for further investigation.
Source: W. Kumfer, L. Thomas, L. Sandt, and B. Lan. (2019). Midblock pedestrian crash predictions in a systemic, risk-based pedestrian safety process. Journal of the Transportation Research Board, Transportation Research Board. https://doi.org/10.1177/0361198119847976

## Slide 37: Diagnosis - Purpose
Investigate sites identified in network screening
  Understand crash patterns
  Diagnose underlying factors
Notes: Notes: The purpose of diagnosis is to further investigate the sites identified in network screening to better understand the crash patterns and to identify crash contributing factors.

## Slide 38: Diagnosis - Process
Review safety data (e.g., crash history)
Assess supporting documentation
Assess site conditions and traffic operations
Observe road user behaviors
FHWA (aerial imagery via NH GRANIT)
Notes: Notes: The diagnosis process involves a review of all relevant data. This can include the crash history, supporting documentation, and past studies (e.g., behavioral studies, speed studies, traffic counts). The diagnosis process also benefits from a field visit to assess the conditions of the site and observe traffic operations, road user behavior, and road user interactions.
Relevant questions include:
1. Are road users obeying the rules of the road?
2. Are there design or operational characteristics that are leading to poor behavior?
3. Are there potential changes that could be made to the design or operational characteristics that would improve behavior?
Source: Aerial imagery is from New Hampshire Geographically Referenced Analysis and Information Transfer System(NH GRANIT). Available for download at: http://www.granit.unh.edu/data/downloadfreedata/category/databycategory.html

## Slide 39: Road Safety Audits
Formal examination of a planned or existing facility by an experienced, independent team
  Focused solely on safety issues
Why perform an audit?
  Complement crash data or crash data are incomplete
  Help identify causes of problems and solutions
  Engage decision makers and the public
Notes: Key Message: The Road Safety Audit (RSA) is a formal diagnosis process that also covers countermeasure selection. This can be used as a reactive approach or a proactive approach for improving safety.
Source: Slide adapted from: PBIC. (2011). Graduate Level Bicycle and Pedestrian Planning Course

## Slide 40: Road Safety Audits - Process
Identify/prioritize sites
Gather team
  Independent
  Multidisciplinary
Review background data
Perform audits in various conditions
Prepare/present report
Discuss and incorporate recommendations with “client”
Notes: Source: Slide adapted from: PBIC. (2011). Graduate Level Bicycle and Pedestrian Planning Course

## Slide 41
FHWA
Notes: Key Message: Road Safety Audits may consider all modes, but there are mode-specific RSA tools available from FHWA.
Images: FHWA. (2007). Pedestrian Road Safety Audit Guidelines and Prompt Lists.
FHWA. (2012). Bicycle Road Safety Audit Guidelines and Prompt Lists.

## Slide 42: Road Safety Audits - Decision Points
What to do with audit info?
  Balance against and compare to other data sources (crash data, survey or complaint data)
  May need to perform audits at different times
  Prioritize: Develop weighting factors/scores or other systems
  Use to identify potential treatments
Notes: Source: Slide adapted from: PBIC. (2011). Graduate Level Bicycle and Pedestrian Planning Course

## Slide 43: Countermeasure Selection
Preceding steps:
  Collect data
  Engage the public
  Inventory conditions
  Prioritize locations
  Analyze safety issues
FHWA
Notes: Notes: Engage the public is in bold because we haven’t talked about this yet in this module, but qualitative data are important. Consider recently completed on ongoing public engagement efforts before embarking on a new effort to collect public input.
Connection to other Module: Inclusive Public Engagement
Source: Blackburn, L., Zegeer, C., and Brookshire, K. (2018, July update). Guide for Improving Pedestrian Safety at Uncontrolled Crossing Locations. Federal Highway Administration. [FHWA-SA-17-072]. Available: https://safety.fhwa.dot.gov/ped_bike/step/docs/STEP_Guide_for_Improving_Ped_Safety_at_Unsig_Loc_3-2018_07_17-508compliant.pdf

## Slide 44: Identify Effective Treatments
Information about design, implementation, effectiveness:
  Pedsafe/Bikesafe
  FHWA Proven Safety Countermeasures
  NCHRP Report 500 Series
  NHTSA Countermeasures that Work
Notes: Notes: These are shown on subsequent slides.

## Slide 45: Pedsafe/Bikesafe
http://www.pedbikesafe.org/PEDSAFE/
http://www.pedbikesafe.org/BIKESAFE/
Notes: Sources:
http://www.pedbikesafe.org/PEDSAFE/
http://www.pedbikesafe.org/BIKESAFE/

## Slide 46: FHWA Proven Safety Countermeasures
http://safety.fhwa.dot.gov/provencountermeasures
http://safety.fhwa.dot.gov/provencountermeasures
Notes: Source: http://safety.fhwa.dot.gov/provencountermeasures

## Slide 47: NCHRP Report 500 Series
Collecting and Analyzing Safety Highway Safety Data
Run-Off-Road Collisions
Head-On Crashes
Stop-Controlled Intersection
Signalized Intersections
Horizontal Curves
Trees / Utility Poles
Older Drivers
Pedestrians
Rural Emergency Medical Services
Work Zone Collisions
Heavy Trucks
Notes: Notes: In 1998, the American Association of State Highway and Transportation Officials (AASHTO) approved its Strategic Highway Safety Plan, which was developed by the AASHTO Standing Committee for Highway Traffic Safety with the assistance of the Federal Highway Administration, the National Highway Traffic Safety Administration, and the Transportation Research Board Committee on Transportation Safety Management. The plan includes strategies in 22 key emphasis areas that affect highway safety. The plan's goal is to reduce the annual number of highway deaths by 5,000 to 7,000. Each of the 22 emphasis areas includes strategies and an outline of what is needed to implement each strategy. The National Cooperative Highway Research Program (NCHRP) has developed a series of guides to assist State and local agencies in reducing injuries and fatalities in targeted areas. The guides correspond to the emphasis areas outlined in the AASHTO Strategic Highway Safety Plan. Each guide includes a brief introduction, a general description of the problem, the strategies/countermeasures to address the problem, and a model implementation process.
Source: http://www.trb.org/main/blurbs/152868.aspx

## Slide 48: NHTSA Countermeasures That Work
Seat Belts and Child Restraints
Distracted and Drowsy Driving
Alcohol-Impaired Driving
Drugged Driving
Aggressive Driving and Speeding
Motorcycle Safety
Older and Younger Drivers
Pedestrians and Bicycles
Notes: Key Message: “Countermeasures That Work” is a source of potential behavioral measures to address the safety issues listed on the slide. It is the main reference for State Highway Safety Offices (SHSOs).
Notes:
Describes major strategies and countermeasures that are relevant to State Highway Safety Offices.
Summarizes strategy/countermeasure use, effectiveness, costs, and implementation time.
Provides references to the most important research summaries and individual studies.
Source: Richard, C. M., Magee, K., Bacon-Abdelmoteleb, P., & Brown, J. L. (2018, April). Countermeasures that work: A highway safety countermeasure guide for State Highway Safety Offices, Ninth edition (Report No. DOT HS 812 478). Washington, DC: National Highway Traffic Safety Administration.

## Slide 49: Compare Countermeasures
When faced with many potential countermeasures, how does one choose which one(s) to implement?
  SUBJECTIVE COMPARISONS
  OBJECTIVE COMPARISONS
  Which will garner the most public support?
  Which is most appropriate for the area?
  Expected effectiveness -> decreases in crashes (CMFs)
  Expected costs -> installation and maintenance
Notes: Source: Slide adapted from the UNC Highway Safety Research Center’s Road Safety Academy, Lesson 3, (2018).

## Slide 50
Notes: Notes: This table provides initial countermeasure options for uncontrolled crossings on various roadway conditions. Each matrix cell indicates possibilities that may be appropriate for designated pedestrian crossings. Not all countermeasures listed in the matrix cell should necessarily be installed at a crossing.
A marked crosswalk is useful to show pedestrians and drivers preferred crossing locations. However, for multi-lane roadway crossings where vehicle AADTs are in excess of 10,000, a marked crosswalk alone is typically not enough (Zegeer, 2005). Under such conditions, more substantial crossing improvements are also needed to prevent an increase in pedestrian crash potential. Examples of more substantial treatments include the refuge island, PHB, and RRFB.
Source: Blackburn, L., Zegeer, C., and Brookshire, K. (2018, July update). Guide for Improving Pedestrian Safety at Uncontrolled Crossing Locations. Federal Highway Administration. [FHWA-SA-17-072]. Available: https://safety.fhwa.dot.gov/ped_bike/step/docs/STEP_Guide_for_Improving_Ped_Safety_at_Unsig_Loc_3-2018_07_17-508compliant.pdf

## Slide 51
Notes: Notes: In addition to roadway characteristics, practitioners should also consider safety issues (like those listed in the table on the slide) and the surrounding land development context, pedestrian travel patterns, countermeasure effectiveness, and costs when considering what countermeasure(s) are best suited for the crossing.
Source: Blackburn, L., Zegeer, C., and Brookshire, K. (2018, July update). Guide for Improving Pedestrian Safety at Uncontrolled Crossing Locations. Federal Highway Administration. [FHWA-SA-17-072]. Available: https://safety.fhwa.dot.gov/ped_bike/step/docs/STEP_Guide_for_Improving_Ped_Safety_at_Unsig_Loc_3-2018_07_17-508compliant.pdf.

## Slide 52: Design Flexibility
Flexibility to approaching bicycle and pedestrian facility design, using:
  AASHTO guides
  NACTO guides
  FHWA guides
  ITE guides
  ADAAG guidelines
  State DOT guides
Notes: Key Message: There area a variety of resources to use as guidelines for design. FHWA encourages agencies to appropriately use these guides and other resources to help fulfill the aims of the 2010 USDOT Policy Statement on Bicycle and Pedestrian Accommodation Regulations and Recommendations - "...DOT encourages transportation agencies to go beyond the minimum requirements, and proactively provide convenient, safe, and context-sensitive facilities that foster increased use by bicyclists and pedestrians of all ages and abilities, and utilize universal design characteristics when appropriate."
Notes: FHWA supports a flexible approach to bicycle and pedestrian facility design, particularly in urban areas. The American Association of State Highway and Transportation Officials (AASHTO) bicycle and pedestrian design guides are the primary national resources for planning, designing, and operating bicycle and pedestrian facilities. The National Association of City Transportation Officials (NACTO) Urban Bikeway Design Guide and the Institute of Transportation Engineers (ITE) Designing Walkable Urban Thoroughfares guide builds upon the flexibilities provided in the AASHTO guides, which can help communities plan and design safe and convenient facilities for pedestrian and bicyclists. Additional guidance for rural areas can be found in the FHWA guide, Small Town and Rural Multimodal Networks (2016).
Connection to Other Module: This slide is also shown in the module Designing for Walking and Bicycling.
Source: FHWA. (August 20, 2013). Memorandum: Bicycle and Pedestrian Facility Design Flexibility. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/guidance/design_flexibility.cfm [Accessed May 2019]

## Slide 53: Crash Modification Factor (CMF)
Useful for comparing countermeasures
Indicates proportion of crashes expected after implementing a safety countermeasure
  CMF = 1.0 (crashes not expected to change)
  CMF = 0.8 (crashes expected to decrease by 20%)
  CMF = 1.3 (crashes expected to increase by 30%)
Notes: Key Message: Many agencies consider the CMF of potential countermeasures when deciding which treatments to implement.
Source: adapted from slides developed by Daniel Carter for the Crash Modification Factor Clearinghouse

## Slide 54: How is a CMF used?
Compare safety performance of various alternatives
Capture greatest gain with limited funds
Compare results of new analyses with existing CMFs to check reasonableness
Check validity of assumptions in cost-benefit analyses
Notes: Source: adapted from slides developed by Daniel Carter for the Crash Modification Factor Clearinghouse

## Slide 55: CMF - Limitations
To develop high-quality CMFs:
  Sound evaluation method
  Large sample size
Bicycle and pedestrian crashes are relative rare
  Very few high-quality CMFs to guide selection of bicycle (especially) and pedestrian countermeasures
Notes: Source: adapted from slides developed by Daniel Carter for the Crash Modification Factor Clearinghouse

## Slide 56: Systemic Safety Approach
Basic tenets of a systemic safety approach
  Identifies safety concern based on data at system level
  Establishes common characteristics (risk factors) of locations where severe crashes frequently occur
  Emphasizes deploying one or more countermeasures to address underlying circumstances at many locations where risk factors are present
  Utilizes lower-cost countermeasures to address common contributing factors at many locations
Notes: Key Message: Many traditional network screening techniques for identifying sites for potential safety improvement base investment decisions on the site analysis approach. Such techniques focus primarily on specific locations with a history of severe crashes (often referred to as hot spots or black spots). However, compelling evidence indicates that severe crashes are widely distributed across State and local highway systems, and very few individual locations in rural areas and on local systems experience a high number or sustained occurrence of severe crashes. As a result, States will have trouble meeting their safety performance goals by only investing in high-crash locations; some systemic deployment will be needed. Thus, some agencies added a systemic approach to their safety management efforts.
Notes: As part of the Highway Safety Improvement Program (HSIP), the requirement to address the potential for crashes to occur suggests the need to include a systemic approach to safety in the safety management process. The systemic approach to safety involves widely implemented improvements based on high-risk roadway features correlated with specific severe crash types. The approach provides a more comprehensive method for safety planning and implementation that supplements and complements traditional site analysis. The approach also helps agencies broaden their traffic safety efforts and consider risk as well as crash history when identifying where to make improvements
Source: Preston, H., Storm, R., Dowds, J., B. Bennett. (2013). Systemic Safety Project Selection Tool. Federal Highway Administration [FHWA-SA-13-019]. Available: https://safety.fhwa.dot.gov/systemic/fhwasa13019/sspst.pdf

## Slide 57: Systemic Safety Approach
“A systemic approach addresses sites with similar risk factors, regardless of crash history. The approach falls along a spectrum of other approaches to safety that are more or less proactive in treating sites based on risk or prior crash history.” – NCHRP 893
NCHRP
Notes: Notes: Although few have focused on pedestrian issues, lessons from places that are implementing systemic safety approaches are consistent. The benefits of a systemic approach include:
Stronger basis for decisions: Accounts for important factors, such as activity/exposure and randomness, that are often excluded from a traditional crash “hot spot” approach when identifying locations for improvement.
Effective use of resources: Helps focus resources on crash risks that are most prevalent across the network and guides selection of appropriate treatments and locations to reduce the most serious crashes.
Data-driven approach: Provides a data-driven/analytical method and screening tools that can be used to justify funding decisions, even if there is not a specific crash history at a given location. A data-driven process also creates new opportunities to provide an equitable risk-based assessment across a jurisdiction.
More proactive approach: Takes a forward-looking approach to address safety issues without waiting for a crash history to develop at any given location.
Consistency: Helps avoid dealing with broad safety issues one project at a time and instead treats risks more widely and consistently. Ultimately, a systemic approach is intended to lead to more informed decision making and optimized investment, which will result in accelerated safety improvements.
Source: National Academies of Sciences, Engineering, and Medicine 2018. Systemic Pedestrian Safety Analysis. Washington, DC: The National Academies Press. https://doi.org/10.17226/25255.

## Slide 58: System-Wide Approach
Policy-based improvements
Address all necessary sites
Notes: Notes: The system-wide (or systematic) approach is based on improving all eligible locations with a given treatment or bringing all eligible locations up to standard. For example, an agency may update the policy on the types of pavement markings used for crosswalks. The system-wide approach would upgrade the crosswalk markings at all locations. This could be done with a pavement marking contract or in conjunction with future projects (whenever a project touches an eligible site).

## Slide 59
LPIs have proven safety benefit for people walking
Low-cost; slight addition in vehicle delay
All intersections are evaluated against prioritization guidelines for citywide signal deployment as part of DC’s Vision Zero program
FHWA
System-Wide Example: Leading Pedestrian Intervals (LPIs) in Washington D.C.
Notes: Key Message: The District Department of Transportation (DDOT) began its first phases of LPI implementation throughout Washington, DC in 2006. Employing LPIs continued incrementally following the introduction of the Pedestrian Master Plan 2009. DDOT introduced LPIs to more than 90 intersections throughout Washington, DC in 2018. Washington, DC now has LPIs installed in 312 out of the city's approximately 1,650 signalized intersections as of February 2019. Deployment of LPIs at more intersections throughout the city is set to continue as the District pushes for zero traffic fatalities by 2024.
Notes: LPIs allow pedestrians to establish a presence and increase their visibility in the crosswalk before the signal change, leading to fewer pedestrian-vehicle conflicts and increased motorist yielding. These treatments have resulted in reductions in vehicle collisions with people walking of up to 60 percent. Additionally, LPIs have a relatively low cost and cause only a slight addition in vehicle delay.
Connection to other Module: Intersections
Source: Source: FHWA Safety Compass Newsletter. (Spring 2019). “Systematically Implementing Leading Pedestrian Intervals.” Available: https://safety.fhwa.dot.gov/newsletter/safetycompass/2019/spring/#s5
Image: https://safety.fhwa.dot.gov/newsletter/safetycompass/2019/spring/images/p11.png

## Slide 60: System-Wide Example: Leading Pedestrian Intervals (LPIs) in Washington D.C. cont.
Criteria for LPI installation
LPI is recommended if at least 7 criteria are met (4-6 merits further analysis)
Traffic signal changes can be made in 30-60 minutes
Effectiveness evaluation through annual pedestrian crash analysis
Protected pedestrian movements.
School zones.
Pedestrian crash history.
Cross-product of vehicle and pedestrian volumes.
Major pedestrian generators.
Crosswalks parallel to T-intersection or one-way streets.
Distances between parallel curb lines and crosswalks.
Sight line obstructions.
Existing intersection level of service.
Minor street splits governed by pedestrian minimums.
Other considerations.
Notes: Notes: DDOT developed detailed criteria for evaluating LPIs at signalized intersections based on guidelines used in other jurisdictions, including the cities of Toronto, San Francisco, Portland, and Los Angeles, as well as the State of Florida. DDOT uses the criteria to prioritize LPI implementation and capture the magnitude and severity of pedestrian-vehicle interactions at signalized intersections. The criteria also help the agency to identify locations where physical characteristics of the intersection could make those interactions more dangerous.
Connection to other Module: Intersections
Source: FHWA Safety Compass Newsletter. (Spring 2019). “Systematically Implementing Leading Pedestrian Intervals.” Available: https://safety.fhwa.dot.gov/newsletter/safetycompass/2019/spring/#s5

## Slide 61: Safety Effectiveness Evaluation

## Slide 62: Safety Effectiveness Evaluation
Determine how projects have affected safety performance
Use results to make future decisions, allocate funds, and change policies
Chart: Pedestrian-Vehicle Crashes vs. LPI Installation
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Number of Signals with LPI | 0 | 2 | 2 | 10 | 15 | 18 | 25 | 31 | 36 | 40
Pedestrian-Vehicle Crashes | 15 | 17 | 18 | 14 | 12 | 10 | 9 | 7 | 5 | 5

## Slide 63: Effectiveness Evaluations
Choice of method is affected by:
Before/After Studies
1
Cross-Sectional Studies
2
Nature of Treatment
Available Data
Site Type
Notes: Key Message: The purpose of the effectiveness evaluation process is to evaluate the change in crashes that occurred as a result of the project. In other words, a quantitative estimate of the effect of a treatment, project, or a group of projects.
Notes: Observational studies refer to evaluations of changes implemented to improve the transportation system. In other words, we are not implementing treatments for the purpose of the evaluation.
By contrast, in experimental studies we select sites for improvement and similar sites for control sites (no improvement) through a random selection process. With the experimental study, we’re therefore able to directly attribute differences between the control and treatment sites to the treatment. Observational studies are much more common among agencies, because agencies function with limited budgets and typically need to prioritize projects based on the benefits returned. In this sense, the random selection process will not optimize investment selection.
Observational studies can be before/after or cross-sectional. Depending on the nature of the treatment, site type, and available data, an agency may choose to use before/after or cross-sectional studies.
Source: Slide adapted from the UNC Highway Safety Research Center’s Road Safety Academy, Lesson 3, (2018).

## Slide 64: Before/After Studies
Examines crash data before and after the treatment is installed
Types of before/after studies:
Simple Before/After
Before/After with Reference or Comparison Groups
Does not account
for many biases
Represents a group of methods
Account for changes in volumes and other factors
Notes: Key Message: There are several different types of observational before/after studies. These include:
The simple (naïve) observational before/after study;
The observational before/after study with reference and/or comparison groups
Notes: The naïve observational before/after does not account for many of the biases including change in traffic volume, regression to the mean, and other trends in the system. By including a reference and comparison group, you start to account for many of these biases. Before/after with reference/comparison group is not just one method, but a family of methods. Depending on the context, you may choose one method over the other.
Source: Slide adapted from the UNC Highway Safety Research Center’s Road Safety Academy, Lesson 3, (2018).

## Slide 65: RTM Bias in Before/After Studies
Notes: Notes: Bias due regression to the mean (RTM) can occur when sites are selected for treatment due to a short-term spike in crashes. In this case, the perceived effectiveness of the treatment could be very different from the actual reduction to the treatment. Naïve before/after methods cannot account for this bias. The EB method discussed earlier can account for this bias.
Source: Slide adapted from the UNC Highway Safety Research Center’s Road Safety Academy, Unit 4, (2018).

## Slide 66: Cross-Sectional Studies
Compare crash data for sites with and without treatment over same time period
Why do a cross-sectional study?
  Treatment installation dates unknown
  Volumes and crash counts in before period unknown
Cross-sectional methods have limitations
  How to develop reliable CMFs with cross-sectional methods is an ongoing area of research
    Propensity score matching methods
    Case control methods
Notes: Key Message: The observational cross-sectional study is used to evaluate a treatment where a set of sites are treated, and other sites are not.
Notes: When we do not have installation dates or the crash and volume data before the treatment, it is useful to apply the observational cross-sectional study.
We use this when, for example, we want to know how intersections with channelized right-turn lanes compare to intersections without the turn lanes, and no data are available to allow evaluation of the difference in crash counts before and after installation. The observational cross-sectional study has some limitations. One limitation is the question of cause and effect.

## Slide 67: Summary
Quality of safety data varies; and a single source of data can not tell the whole safety story
Many safety problems go unreported
The relationship between crashes and volume is not linear
A systemic safety approach helps agencies broaden their traffic safety efforts and consider risk as well as crash history