## Slide 1: Systems Perspectives in Ped/Bike Planning and Design
Instructor course information
Notes: Report No. FHWA-SA-19-034
Acknowledgement: Some of the content in this module was presented at the Transportation Research Board 2019 Annual Meeting and has been adapted with permission from Michael Kenneth Lemke, Texas A&M University; Becky Nauman, University of North Carolina; Kristen Hassmiller Lich, University of North Carolina; and Jill Kuhlberg, University of North Carolina. We are grateful for their contribution of slide material and time in reviewing these slides.

## Slide 2: Outline
Describe a “system” and its characteristics
Learn basic systems thinking terminology and theory
Identify systems thinking applications for stakeholder engagement (causal loop diagramming) and policy analysis
Notes: Key Message: The goals of this module are to:
Describe a “system” and its characteristics.
Learn basic systems thinking terminology and theory.
Identify systems thinking applications for stakeholder engagement (causal loop diagramming) and policy analysis.

## Slide 3: What is a System?
Wikimedia Commons
Pixabay.com
Pixabay.com
Wikimedia Commons
Notes: Student Question: Can you give me an example of a system?
[instructor to write the responses down on the whiteboard or a piece of paper for future reflection/discussion].
Some potential answers:
Human body
Family
Beehive or other “ecosystem”
Software systems
Healthcare system
Manufacturing system
Cities (which include land uses and roadway systems)
Source:
All images labeled for noncommercial reuse. Images from:
https://cdn.pixabay.com/photo/2017/08/08/17/51/animal-2612075_960_720.jpg
https://upload.wikimedia.org/wikipedia/commons/6/6b/Man_shadow_with_organs.png
https://pixabay.com/photos/family-eating-at-the-table-dining-619142/
https://upload.wikimedia.org/wikipedia/commons/c/c4/I-90_and_I-5_cloverleaf_seattle_washington.jpg

## Slide 4: Systems…
Have parts + order
Can be nested within larger systems
Dynamically adjust
Are more than the sum of their parts
Pixabay.com
Notes: [When the instructor goes through the above, ask the class for help in describing these properties within the systems that they identified in the last slide.]
Key Message:
Systems have parts. These parts have inter-connections with each other and may need to be laid out in a specific order or sequence for the system to function or serve its purpose. A good test of a systems is whether you can take away a part and see if the system will function properly. A bicycle is a simple system for transportation. If you take away the front wheel or the chain, will the system function?
Systems can be nested within greater systems. Think about the human body: you can have an organ, such as the brain, that acts as a system of neuron exchange across different parts of the brain, functioning within the larger system of the body. Similarly, a transit system can operate within the larger dynamics of an entire city.
Systems dynamically maintain stability or equilibrium through feedback; systems are designed to achieve a purpose and have structures that will adjust to system inputs and outputs to meet that purpose. For example, the human body needs to maintain a certain PH level, so the brain, kidneys, and lungs work together to monitor levels and excrete acids or bases into the blood stream or release Carbon Dioxide through the lungs to maintain the right level.
Systems have emergent properties and behaviors that individual parts do not have. Systems, in other words, are more than the sum of their parts but reflect greater attributes and relationships between components of the system. For example: we think of transportation system performance, reliability, safety, comfort, as an emergent property of the system, not of a single part.
Source:
Image from: https://pixabay.com/photos/camera-inside-mechanics-technician-943244/

## Slide 5: Systems Thinking is About…
Recognizing inter-connectedness
Understanding (and ultimately managing) dynamic complexity
Moving beyond “A to B” or linear thinking and problem-solving
Notes: Key Message:
Systems thinking is a scientific field that has been around for decades. It has been applied in areas such as systems engineering, ecology, business, education, psychology (there are family systems counselors), and public health. Increasingly, it is being introduced to the transportation community.
Planners are often natural systems thinkers, because they are trained to recognize the inter-relationships between transportation, land use, economic development, the environment, and to see cities as dynamic systems.
At the core of systems thinking, is a recognition of the inter-connectedness of the work that we do within the transportation system, and a greater appreciation for that complexity. As complexity is better understood, it becomes more manageable. Transportation planners and policy makers can become trained in systems thinking methods, to actually help them identify better leverage points for system-level changes that will advance their active travel goals.
And as problem solvers, systems thinking can help unlock new insights about the nature of a problem, unintended consequences, and partnerships to help find new solutions.

## Slide 6: Systems Thinking in Action
UNC Highway Safety Research Center (Data source: NHTSA FARS)
Notes: Key Message:
Imagine that your boss hands you a trend line, showing a rise in pedestrian and bicycle fatalities, and says: “Your job is to solve this problem! What should we do to decrease pedestrian fatalities?”
Looking at trend lines, sometimes called behavior over time graphs, is often a starting place for systems thinking. Seeing trends over time helps you to see inflection points and to generate hypotheses about what was going on at different points in time.
Student Question: Looking at this graph, what do you think was happening from 2007 to 2010, when pedestrian fatalities started to reverse trends?
Possible answers:
Economic recession and recovery
Increase in smart phones market penetration/saturation and use
Introduction of ride-hailing services like Uber and Lyft
The rise of the opioid epidemic
Source:
Image from UNC Highway Safety Research Center (Laura Sandt). Graph depicts data from the National Highway Traffic Safety Administration’s Fatality Analysis Reporting System (FARS).

## Slide 7: Interconnectedness
Sandt et al. 2018
Notes: Key Message: Behavior over time graphs may prompt you to think about any number of things that may be causing a rise in pedestrian fatalities. One study ran a systems thinking workshop with a group of stakeholders and identified more than 40 variables they believed were contributing to the trend, all highly interconnected to each other.
This is a different approach than many engineers are commonly taught to use. In most cases, we’re taught that if we want to understand a phenomenon, we must analyze the crash data. We tend to look at one variable at a time in relation to the outcome, and let our models “control” for the inter-relationships. We aim to limit the messiness as much as possible, rather than recognize that complexity. And we often ignore that the crash data sets we have are quite limited, and rarely measure the more important elements of the system that we think are affecting our outcomes.
So as we try out systems thinking, we might immediately expand our universe about the nature of the problem, and who we might need to engage to work with.
Source: Image from: Sandt L, Naumann R, Lich KH, Kuhlberg J, Heiny S. (2018). Explaining the rise in pedestrian fatalities: a systems approach. Collaborative Sciences Center for Road Safety Project under U.S. DOT grant #69A3551747113.

## Slide 8: Dynamic Complexity
Sandt et al. 2018
Notes: Key Message: We talked earlier about properties of a system, in that it has certain structures and dynamics that regulate its functions. Feedback loops are an important element of a system. There are two types of feedback loops: positive, or reinforcing, feedback loops that tend to amplify a change and negative, or balancing, feedback loops that tend to bring a system back closer to equilibrium.
Here’s an example of a reinforcing feedback loop that you may be familiar with when called by another name: the Safety in Numbers effect. The “O” and “S” on the diagram indicates that as one variable increases, the variable next in line will change in the “Opposite” or “Same” direction. Sometimes you will see these on systems diagrams shown as “+” or “-.”
It goes like this [instructor starts at the top left of the graphic and circles around clockwise]: As more pedestrians walk, drivers see more people and perceive that they need to be more attentive in going through the area. This has the effect of possibly reducing speeds and leading to fewer crashes, which leads to fewer pedestrian deaths, which may lead to more people perceiving that it is safe and comfortable to walk, thus completing a “virtuous cycle” whereby more pedestrians traveling actually result in fewer crashes (per population or per exposure unit) over time.
It’s a nice example as well in that it makes connections between some of the variables identified in the earlier slide: exposure and distraction/attentiveness.
These loops can go in either direction, such that a virtuous cycle can become vicious. As we have more crashes, and more pedestrian deaths, we may see fewer people walking, and when drivers aren’t used to seeing pedestrians on a regular basis, they might perceive that they don’t need to be as attentive, and then we might continue to see attention go down, distraction go up, and crashes and fatalities increase.
Source: Image from: Sandt L, Naumann R, Lich KH, Kuhlberg J, Heiny S. (2018). Explaining the rise in pedestrian fatalities: a systems approach. Collaborative Sciences Center for Road Safety Project under U.S. DOT grant #69A3551747113.

## Slide 9: Dynamic Complexity
???
Notes: Key Message: Feedback loops can be nested within other feedback loops, and they can operate on different time scales, such that some operate in short cycles, and others have quite a bit of time delay before the effects can be measured in another part of a system. This can sometimes help explain results that may not necessarily be intuitive, or results that are non-linear.
For example, people’s cognitive interaction with the road—or the feedback they get from their environment while traveling—and the level of attentiveness they perceive to be required, happen almost instantaneously and subconsciously. The feedback loop of building and making safer roads can take years and years to plan, program, design, and construct new facilities.
Source: Image on the left from: Sandt L, Naumann R, Lich KH, Kuhlberg J, Heiny S. (2018). Explaining the rise in pedestrian fatalities: a systems approach. Collaborative Sciences Center for Road Safety Project under U.S. DOT grant #69A3551747113.

## Slide 10: A Spectrum of Systems Tools
Notes: Key Message: So in the last few slides, we have started to very recognize that there are broader systems around us. These systems have components that are related through feedback. And we’ve started to question how these systems function to produce the outcomes we care about, such as pedestrian or bicycle fatalities, and where we might intervene as pedestrian and bicycle professionals. We have been working on the informal side of the spectrum, but it’s helpful to know that there are entire curricula and courses of study devoted to more formal methods and approaches to study systems. Systems programs are often housed in Engineering Colleges and many industrial engineering programs teach systems theory and modeling courses. There are also systems courses offered in Business Schools, focusing more heavily on organizational operations.
In the last half of this class, we’re going to cover two formal systems methods, one qualitative and one quantitative, that can be used in the context of pedestrian and bicycle planning, design, and policy making.
Image: Hovmand, Peter, S. (2014). Community Based System Dynamics. Springer, NY. https://doi.org/10.1007/978-1-4614-8763-0

## Slide 11: Systems Methods Toolbox
Qualitative
  Causal loop diagramming
  Network mapping
  Process flow diagramming
Quantitative
  System dynamics simulation
  Microsimulation
  Cost-effectiveness analysis
Mixed methods
  Preference elicitation
  System dynamics
Philip McMaster- Flickr Creative Commons
Notes: Key Message: Again, while we can’t cover the range of systems methods to problem-solving, we are going to cover an example of community-based systems thinking through causal loop diagramming and using systems dynamics simulation for policy scenario analysis.
These are examples of systems tools and not all the systems tools and methods that exist.
Source: Hovmand, Peter, S. (2014). Community Based System Dynamics. Springer, NY. https://doi.org/10.1007/978-1-4614-8763-0

## Slide 12: Community-Based Systems Thinking
Notes: Key Message: Community-based systems thinking is a participatory method for involving communities in the process of understanding and changing systems from the endogenous or feedback perspective. Endogenous perspective, means recognizing the dynamics that are internal to the system, rather than exogenous or external system forces. In other words, it’s learning to identify the feedback loops we were discussing before and leverage or adjust them.
Source: Hovmand, Peter, S. (2014). Community Based System Dynamics. Springer, NY. https://doi.org/10.1007/978-1-4614-8763-0

## Slide 13
Steele, R. (2015). Implementing an integrated and transformative agenda at the regional and national levels. United Nations ESCAP Conference.
Notes: Key Message: Imagine five people with limited vision being asked to describe an elephant.

## Slide 14
Steele, R. (2015). Implementing an integrated and transformative agenda at the regional and national levels. United Nations ESCAP Conference.
Notes: Key Message: The elephant is so big, that each person can only get hold of a certain part. So each sees or feels something different and no one can agree on what the elephant is. Community-based systems thinking is needed because in our transportation system, we often create plans, make decisions, and act based on incomplete information. Bringing in stakeholders helps us to see the full scope of the system.
Connection to other Module: see Inclusive Public Engagement for more community engagement techniques.

## Slide 15: Let’s Conceptualize a System Together!
Causal loop diagram/map:
A visual aid showing how components of a system are inter-related
Group model building:
A participatory approach and guided activity
Community-based systems thinking
Notes: Key Message: One approach to community-based systems thinking is to go through a group model-building process to develop a causal loop diagram. The transportation field is chock-full of predictive models designed to forecast future growth scenarios or estimate relationships between individual variables and an outcome of interest, such as crashes. Most of these models are built by researchers or “experts” using historical data or literature to develop a conceptual sense of how to structure the model. Systems thinking can complement these approaches, by leveraging the knowledge and intuition and experiences from a larger group of people, who can collectively move beyond just the data on hand or the work of the past.

## Slide 16: Elements of a Causal Loop Diagram (CLD)
Variables
  Noun/noun phrase
  Makes sense to go up or down over time
Arrows
  A change in X causes a change in Y, all else equal
Polarity
  Variables change in same direction (+ or S)
  Variables change in opposite directions (- or O)
Feedback loops
  Reinforce change (R)
  Counteract change or seek balance (B)
Slide adapted with permission from Becky Naumann, University of North Carolina
Notes: [Go through items listed on the slide and point them out in the model example.]
Key Message: Before we get into the group learning process, let’s first break down the elements of a causal loop diagram. We touched on some of these earlier in the lecture.
Source: Image from: Sandt L, Naumann R, Lich KH, Kuhlberg J, Heiny S. (2018) Explaining the rise in pedestrian fatalities: a systems approach. Collaborative Sciences Center for Road Safety Project under U.S. DOT grant #69A3551747113.

## Slide 17: Drawing a CLD (causes  focal variable  consequences, with loops)
Slide adapted with permission from Kristen Hassmiller Lich, University of North Carolina
Notes: Key Message: Now let’s build a model together as a group. For this example, we’ll begin with something that probably everyone in the room can relate to: being a student and getting graded. This is the focal variable we’re interested in mapping, so we put it in the middle of the diagram.
Notes: The remaining steps will build out a “system,” following the steps below. The instructor may choose to draw these on a white board instead and get input from the class on what to put on the board.
Step 1: Define a focal variable of interest (student grades).
Step 2: On the left side of your page, write down some factors you believe impact the focal variable. For each, write whether a change in one will lead to an increase or decrease in the other (using s/o or +/- symbols).
Step 3: On the right side of the page, write down factors affected by a change in the focal variable.
Step 4: Draw lines from any right-side variables that feedback into left side variables.
Step 5: Draw hash marks on the lines that indicate a “delay” in the system.
Step 6: Discuss how the feedback loops might drive trends or behaviors over time, and any other insights.

## Slide 18: Drawing a CLD (causes  focal variable  consequences, with loops)
Slide adapted with permission from Kristen Hassmiller Lich, University of North Carolina
Notes: Notes:
Step 1: Define a focal variable of interest (student grades).
Step 2: On the left side of your page, write down some factors you believe impact the focal variable. For each, write whether a change in one will lead to an increase or decrease in the other (using s/o or +/- symbols).
Step 3: On the right side of the page, write down factors affected by a change in the focal variable.
Step 4: Draw lines from any right side variables that feedback into left side variables.
Step 5: Draw hash marks on the lines that indicate a “delay” in the system.
Step 6: Discuss how the feedback loops might drive trends or behaviors over time, and any other insights.

## Slide 19: Drawing a CLD (causes  focal variable  consequences, with loops)
Slide adapted with permission from Kristen Hassmiller Lich, University of North Carolina
Notes: Notes:
Step 1: Define a focal variable of interest (student grades).
Step 2: On the left side of your page, write down some factors you believe impact the focal variable. For each, write whether a change in one will lead to an increase or decrease in the other (using s/o or +/- symbols).
Step 3: On the right side of the page, write down factors affected by a change in the focal variable.
Step 4: Draw lines from any right-side variables that feedback into left side variables.
Step 5: Draw hash marks on the lines that indicate a “delay” in the system.
Step 6: Discuss how the feedback loops might drive trends or behaviors over time, and any other insights.

## Slide 20: Drawing a CLD (causes  focal variable  consequences, with loops)
Slide adapted with permission from Kristen Hassmiller Lich, University of North Carolina
Notes: Notes:
Step 1: Define a focal variable of interest (student grades).
Step 2: On the left side of your page, write down some factors you believe impact the focal variable. For each, write whether a change in one will lead to an increase or decrease in the other (using s/o or +/- symbols).
Step 3: On the right side of the page, write down factors affected by a change in the focal variable.
Step 4: Draw lines from any right-side variables that feedback into left side variables.
Step 5: Draw hash marks on the lines that indicate a “delay” in the system.
Step 6: Discuss how the feedback loops might drive trends or behaviors over time, and any other insights.

## Slide 21: Drawing a CLD (causes  focal variable  consequences, with loops)
Slide adapted with permission from Kristen Hassmiller Lich, University of North Carolina
Notes: Notes:
Step 1: Define a focal variable of interest (student grades).
Step 2: On the left side of your page, write down some factors you believe impact the focal variable. For each, write whether a change in one will lead to an increase or decrease in the other (using s/o or +/- symbols).
Step 3: On the right side of the page, write down factors affected by a change in the focal variable.
Step 4: Draw lines from any right-side variables that feedback into left side variables.
Step 5: Draw hash marks on the lines that indicate a “delay” in the system.
Step 6: Discuss how the feedback loops might drive trends or behaviors over time, and any other insights.

## Slide 22: Drawing a CLD (causes  focal variable  consequences, with loops)
What are the most important variables that, when they change, trigger change in the focal variable?
  In a good way
  In a bad way
Can you group these variables in a meaningful way? Think about 2-3 key variables and organize the rest (draw arrows, indicate polarity)
What is missing….
  Causes of causes?
  Missing variables needed to trigger a change? (XY, but only in the presence of Z)
What are the key consequences of change in the focal variable?
Are there any reinforcing feedback loops that will be triggered – virtuous cycles that will benefit you or vicious cycles that will undermine your efforts to improve things?
Are there any balancing loops that will be triggered, in which aspects of the system counteract change? Limit it?
Slide adapted with permission from Kristen Hassmiller Lich, University of North Carolina
Notes: Notes:
Step 1: Define a focal variable of interest (student grades).
Step 2: On the left side of your page, write down some factors you believe impact the focal variable. For each, write whether a change in one will lead to an increase or decrease in the other (using s/o or +/- symbols).
Step 3: On the right side of the page, write down factors affected by a change in the focal variable.
Step 4: Draw lines from any right-side variables that feedback into left side variables.
Step 5: Draw hash marks on the lines that indicate a “delay” in the system.
Step 6: Discuss how the feedback loops might drive trends or behaviors over time, and any other insights.

## Slide 23: In-Class Activity
Get into groups of 2-3
Select a focal variable of interest
  You could focus on any issue of interest: pedestrian crashes, roadway widening, mode shift, access to affordable housing
Take 15 minutes to “map” the system on your own
Compare with your partner and identify similarities and differences in the systems you drew
Report insights back to the group
Notes: Notes: This activity will require about 30 minutes, as well as pencils and blank sheets of paper (preferably legal paper). Give students about 15 minutes to put their thoughts on paper, 5-7 minutes to discuss as pairs, and 5-7 minutes to share their insights back with the class. The instructor can walk around and see if the students are correctly applying the components of CLDs.

## Slide 24: Systems Thinking to Dive Below the Surface
Ecochallenge.org
Notes: Key Message: By mapping a system together, you moved past individual events and started to think about what elements of the system that can’t be seen are contributing to a problem. This is what systems thinking is designed to help you do: to explore and question the underlying structures of the systems we work within. These systems exist, and we all have a mental picture in our minds of what this system is like, based on our interactions with the system. Think about the five men touching the elephant. Each had some strongly held beliefs and assumptions about that elephant, but we don’t often enough take the time to articulate what we see and believe alongside others and learn together.
Source: https://www.nwei.org/iceberg/

## Slide 25: Community-Based Systems Thinking Can…
Help in strategic planning to better understand complexity and how systems behave
Reframe the problem or issue and identify new sources of “data”
Allow stakeholders to view the larger system they are embedded within and support cross-sector collaboration
Support identification of high impact leverage points, policy dialogue and comparison

## Slide 26: Systems Methods Toolbox
Qualitative
  Causal loop diagramming
  Network mapping
  Process flow diagramming
Quantitative
  System dynamics simulation
  Microsimulation
  Cost-effectiveness analysis
Mixed methods
  Preference elicitation
  System dynamics
Philip McMaster- Flickr Creative Commons
Notes: Key Message: You now have a sense of how to draw a causal loop diagram, and how doing so within a group participatory approach can lead to new thinking about a system. Now let’s show a more quantitative approach, where we can convert our understanding of systems dynamics from CLDs to models that can simulate changes over time and help us identify high-impact leverage points in a system to support policy evaluation or scenario development.
Again, we’re still focusing on only a narrow set of systems tools and there are many other systems tools and methods that exist beyond what is shown here.

## Slide 27: Bicycling Safety Causal Loop Diagram
Macmillan et al. 2014
Notes: Key Message: The diagramming exercise alone can be seen as a stakeholder intervention and group learning process that can be useful in structuring a dialogue around pedestrian and bicycle issues. But it can also be a jumping off point for doing more sophisticated simulations of different policy scenarios.
The following example is drawn from a journal article published in Environmental Health Perspectives by Macmillan, Connor, Witten, Kearns, Rees, & Woodward (2014). It is based on a study done in Auckland, New Zealand.
The problem the community was seeing was that urban growth had led to an increase in car ownership/use and a decline in public transportation and bicycling. The project team used a community participatory systems dynamic modeling approach, involving community, academic, and policy stakeholders, to develop a causal loop diagram.
They developed a preliminary set of feedback loops, combined them with primary and secondary data from prior studies, and then refined the feedback loops through two workshops with about 30 different stakeholders as well as individual meetings and interviews where they used cognitive mapping techniques. Cognitive mapping is a technique designed to elicit the implicit causal theories of interviewees, linking perceptions and behaviors around the question of interest. This resulted in a causal loop diagram specific to commuter bicycling.
Source: Macmillan A, Connor J, Witten K, Kearns R, Rees D, Woodward A. (2014). The societal costs and benefits of commuter bicycling: simulating the effects of specific policies using system dynamics modeling. Environmental Health Perspectives;122(4):335-344.

## Slide 28: Bicycling Safety Simulation Model
Macmillan et al. 2014
Notes: Key Message: Here’s an example of the list of studies that were used to inform the simulation model, alongside expert opinion, stakeholder insights, and primary data sources such as national census and survey data.
Source: Macmillan A, Connor J, Witten K, Kearns R, Rees D, Woodward A. (2014). The societal costs and benefits of commuter bicycling: simulating the effects of specific policies using system dynamics modeling. Environmental Health Perspectives;122(4):335-344.

## Slide 29: Bicycling Safety Simulation Model
Testing and validation:
  Fidelity of participatory process
    Appropriate stakeholders
    Balanced comprehensiveness/comprehensibility
    Policy insights related back to feedback structure
  Formal validity tests
    Sensitivity analysis
Simulated from 1991-2051
  Historic simulations (1991-2012) were compared to actual data
  Prospective simulations (until 2051)
Macmillan et al. 2014
Notes: Key Message: To build confidence in their model, they worked to ensure that there was a high-fidelity participatory process, and they also performed sensitivity analyses to look at how uncertainty in the data would alter the shape of behavioral curves over time. They also looked back in time to see how well simulations on historical data compared to the actual data before undertaking prospective simulations.
Source: Macmillan A, Connor J, Witten K, Kearns R, Rees D, Woodward A. (2014). The societal costs and benefits of commuter bicycling: simulating the effects of specific policies using system dynamics modeling. Environmental Health Perspectives;122(4):335-344.

## Slide 30: Bicycling Safety Simulation Model
Compared policy scenarios that might be most likely to alter the shape of trends in cycling over time:
  Baseline (no policies implemented)
  Regional Cycle Network (RCN)
  Arterial segregated bicycle lanes (ASBL)
  Self-explaining roads (SER)
  Both ASBL + SER
Macmillan et al. 2014
Notes: Key Message: The Regional council had a 30-year transport strategy that includes development of an arterial network of mixed cycling infrastructure (a Regional Cycling Network). They were also contemplating two other options:
ASBL: One-way physically segregated lanes on each side of every arterial road in the region by 2051.
SER: Transformation of all local through roads into self-explaining roads (SER) by 2050, creating low-speed local streets using features such as street narrowing, trees, and art.
For the simulation, these three options were compared against a baseline of no policies implemented, as well as a combined approach of both ASBL and SER.
Source: Macmillan A, Connor J, Witten K, Kearns R, Rees D, Woodward A. (2014). The societal costs and benefits of commuter bicycling: simulating the effects of specific policies using system dynamics modeling. Environmental Health Perspectives;122(4):335-344.

## Slide 31: Bicycling Safety Simulation Model
Four key outcomes of interest:
  Bicycle mode share
  Cyclist serious injuries/deaths
  Cyclist serious injury/death rate
  Annual air pollution mortality
Macmillan et al. 2014
Notes: Key Message: They were interested in four separate outcomes of interest. We show the simulated outcomes of these over the next four slides.
Source: Macmillan A, Connor J, Witten K, Kearns R, Rees D, Woodward A. (2014). The societal costs and benefits of commuter bicycling: simulating the effects of specific policies using system dynamics modeling. Environmental Health Perspectives;122(4):335-344.

## Slide 32: Simulation Results: Bicycle Mode Share
Macmillan et al. 2014
Notes: Source: Macmillan A, Connor J, Witten K, Kearns R, Rees D, Woodward A. (2014). The societal costs and benefits of commuter bicycling: simulating the effects of specific policies using system dynamics modeling. Environmental Health Perspectives;122(4):335-344.

## Slide 33: Simulation Results: Cyclist Serious Injuries/Deaths
Macmillan et al. 2014
Notes: Source: Macmillan A, Connor J, Witten K, Kearns R, Rees D, Woodward A. (2014). The societal costs and benefits of commuter bicycling: simulating the effects of specific policies using system dynamics modeling. Environmental Health Perspectives;122(4):335-344.

## Slide 34: Simulation Results: Cyclist Serious Injuries/Death Rate
Macmillan et al. 2014
Notes: Source: Macmillan A, Connor J, Witten K, Kearns R, Rees D, Woodward A. (2014). The societal costs and benefits of commuter bicycling: simulating the effects of specific policies using system dynamics modeling. Environmental Health Perspectives;122(4):335-344.

## Slide 35: Simulation Results: Annual Air Pollution Mortality
Macmillan et al. 2014
Notes: Source: Macmillan A, Connor J, Witten K, Kearns R, Rees D, Woodward A. (2014). The societal costs and benefits of commuter bicycling: simulating the effects of specific policies using system dynamics modeling. Environmental Health Perspectives;122(4):335-344.

## Slide 36: Insights from SD Simulation Modeling?
Insights into the underlying structure of key problems of interest and how systems behave
Platform for learning and to facilitate policy discussions, decision making, and action
Can be used to integrate many sources of data and identify data needs for future studies
Slide adapted with permission from Michael Kenneth Lemke, Texas A&M University

## Slide 37: Recap: Terms and Concepts
Behavior over time graphs: a good starting place for systems thinking and hypothesis generation
Key system structures: balancing and reinforcing feedback loops
Key processes: causal loop diagramming and group model building
Notes: Notes: Have the students describe these and ask any questions about them.

## Slide 38: Additional Systems Reading and Examples
Roadway accidents (Kumar & Umadevi, 2011)
Traffic safety policy (Goh & Love, 2012)
Interactions between climate change, road safety, and economic factors (Alirezai et al., 2017)
Highway system sustainability (Egilmez & Tatari, 2012)

## Slide 39: Summary
Systems thinking can…
Help in strategic planning to better understand complexity and how systems behave
Reframe the problem or issue and identify new sources of “data”
Allow stakeholders to view the larger system they are embedded within and support cross-sector collaboration