## Slide 1: User and Mode Characteristics
Instructor course information
Notes: Report No. FHWA-SA-19-034

## Slide 2: Outline
What’s different about active travel?
Capabilities, needs, behaviors
  Pedestrians
  Bicyclists
Trip purposes
Bicycle as design vehicle
E-bike trips

## Slide 3: What’s Different About Active Travel?
Peak periods on a facility may occur outside the typical 6-9 am and 3-7 pm “commute” hours
Walk and bike trips tend to link with transit trips
Some trips are for exercise or leisure
Susceptible to severe injury in even minor incidents
Others?
pedbikeimages.org – Adam Coppola Photography
Notes: Student Question: What else makes planning and designing for active travel different than planning/designing for motorized transportation?

## Slide 4: Pedestrians

## Slide 5: Pedestrians’ Wide Range of Capabilities
Children
  Impulsive and unpredictable
  Short and hard for drivers to see
Seniors
  Experience a reduction in vision, hearing, agility, balance, speed, concentration, and strength
  Have reduced abilities under low light/night conditions
Persons with disabilities
  Visually- or hearing-impaired
  Permanent or temporary physical disability
  Mentally or emotionally impaired
Notes: Notes: Generally, children under the age of ten should not be unsupervised on or near roads. Research has shown that parents often overestimate the safe crossing ability of their children. Safe street-crossing behaviors are a motor skill that can be improved with practice and to cross a street safely, young children must engage in several cognitive processes all at once.
Connection to Other Module: Accessibility and ADA
Source: Percer, J. (2009). Child Pedestrian Safety Education: Applying Learning and Developmental Theories to Develop Safe Street-Crossing Behavior (DOT HS 811 190). Washington, DC: National Highway Traffic Safety Administration.

## Slide 6: Design Elements of a Comfortable Walking Environment
Along the Roadway
Level cross slopes and continuous sidewalks
Improved sight distances at driveways
Clear path of travel between buffer and streetscape elements (signs, benches, etc.)
Crossings
Speed reduction for motor vehicles
Time and distance needed to cross the roadway
Ease of movement from walkway to street level
Conspicuity of people walking
Notes: Notes: A note on the last bullet: Conspicuity is related to sight distances, street lighting, and warning signs or markings including marked crosswalks – anything that helps drivers expect to see people walking and then actually see them.
Student Question: If these are the “basics” for a comfortable walking environment, what else effects a pedestrian’s willingness to walk or their comfort while doing so? Keep in mind the range of capabilities that were mentioned on the previous slide. (Students might mention issues like land use, destinations, facility maintenance, weather, personal security, availability/cost of other modes, etc.).
Connection to other Module: Many of these elements are covered in more detail in the module, Accessibility and ADA.
Source: Adapted from FHWA (2006) University Course on Bicycle and Pedestrian Transportation, Lessons 9 and 11
Background image: pedbikeimages.org – Dan Burden

## Slide 7: Who are Vulnerable Populations?
Individuals (or members of sociodemographic groups) likely to experience unmet need for safe, comfortable, convenient, affordable mobility
Vulnerability can stem from perceived or objective…
  Lack of mobility or access
  Exposure to unsafe travel conditions
  Exposure to unsecure travel conditions
  Inequitable enforcement (more on next slide)
Why is this relevant to pedestrians?
  Walking is by far the most prevalent mode — especially among vulnerable populations
Notes: Source: Slide adapted from Tab Combs (2019)

## Slide 8: Vulnerable Populations – Inequitable Enforcement
ProPublica
Notes: Key Message: People walking may experience each trip or the surrounding environment very differently. For example, an analysis in Jacksonville, Florida, found that while the city’s population is 29% black, black pedestrians received 55 percent of the pedestrian tickets issued from 2012 to 2017.
Source: Kate Rabinowitz, ProPublica, 2017. Available: https://features.propublica.org/walking-while-black/jacksonville-pedestrian-violations-racial-profiling/

## Slide 9: Pedestrian Behavior
How far would you be willing to walk to use the crosswalks?
FHWA
Notes: Key Message: This image presents a hypothetical, but very common, scenario: in City X, observations reveal that many people are crossing midblock from the shopping center to the bus stop, resulting in frequent conflicts with vehicles. The city wants to improve safety in this area. Should the city pursue an education campaign or make changes to the environment?
Student Question: What are the other factors influencing this behavior?
Convenience - Crossing midblock provides a more direct route to the bus stop. People coming from the shopping center are likely carrying shopping bags, which could be difficult to carry long distances.
Previous experience - It is likely that people have successfully crossed similar streets (or even the same street) in this manner many other times, so their limited previous experience suggests this is a safe option.
Time pressure - Buses run on a schedule, and people may want to cross as quickly as possible to be sure they catch the next bus.
Source: Image and notes adapted from FHWA. Road Safety Fundamentals; Concepts, Strategies, and Practices that Reduce Fatalities and Injuries on the Road. (2017). U.S. Department of Transportation. Ed. Daniel Carter. Available: https://rspcb.safety.fhwa.dot.gov/rsf/

## Slide 10: Pedestrian Behavior
When designing solutions to safety problems, it’s important to keep in mind:
  Humans are not exclusively logical, rational beings
  People generally don’t simply do what they are told to do
  Changing behavior requires an understanding of all influencing factors
Notes: Source: FHWA. Road Safety Fundamentals; Concepts, Strategies, and Practices that Reduce Fatalities and Injuries on the Road. (2017). U.S. Department of Transportation. Ed. Daniel Carter. Available: https://rspcb.safety.fhwa.dot.gov/rsf/

## Slide 11: Bicyclists

## Slide 12: Bicyclists’ Wide Range of Capabilities
Bike handling & agility
Familiarity with laws, location, infrastructure, and behavior of other road users
Decision making ability
Physical attributes
Speed & distance
Confidence & comfort
  With bicycling itself
  With other auto traffic & other users
Notes: Source: Slide from Tab Combs (2019)

## Slide 13: Who Bikes?
pedbikeimages.org – Dan Burden
Notes: Student Question:
Opportunity for open discussion among the class:
Describe what you see in each of these images.
How are they same or different from the first thing that comes to mind when you think of a “bicyclist”
Source:
Image (bottom left): http://www.pedbikeimages.org/largeimages/delmar.004.jpg
Image (middle): http://www.pedbikeimages.org/largeimages/sthelena.m(20).jpg
Image (upper right): http://www.pedbikeimages.org/largeimages/bikelanes.embarcadaro2.sanfrancisco.jpg

## Slide 14: Whom Do We Want to Bike?
Children
  Less visible to motorists
  Slower speed
  Less well-developed decision making
  Unfamiliarity with motorists’ experience
  Greater harm from crashes, pollution
Seniors
  Slower reaction time
  Slower speed
  Reduced visual acuity
  Comfort & risk
  Greater risk of harm from crashes, falls, pollution
Women
  Personal security concerns
  [assumed] More likely to prioritize comfort & risk avoidance
  Additional travel demands
Notes: Key Message: The next few slides present special considerations and potential barriers for different user groups.
Source: Slide from Tab Combs (2019)

## Slide 15: Whom Do We Want to Bike?
People of Color
  Personal security concerns
  Poorer quality infrastructure
  Disproportionate harm from auto traffic (crashes, pollution)
Low-Income
  Poorer quality infrastructure
  Disproportionate exposure to auto traffic
  Disproportionate harm (crashes, pollution) due to exposure and inferior health care access
People with Disabilities
  May have slower speeds & reaction times
  Less visible to motorists
  Wider footprint
  Greater risk of harm
Notes: Source: Slide from Tab Combs (2019)

## Slide 16: Whom Do We Want to Bike?
Bikeshare Customers
  More likely tourists and/or casual riders
  Likely lower comfort & skill levels
Delivery/Livery Cyclists
  (not messengers)
  Slower speeds, bigger footprints
  Less nimble
Confident Cyclists
  Can be any of the above, but small % of cyclists
  More comfortable with cars than peds
  Fast & agile
  Sensitive to faulty detection equipment
  Vulnerable to on-street hazards
Notes: Source: Slide from Tab Combs (2019)

## Slide 17
Graphic by Toole Design Group
Notes: Notes: The previous slide summarized types of trips. But trip purpose is only one of the factors used to classify different types of bicycle riders – comfort level, bicycling skill and experience, and age all play a role. Keep in mind that people may not fit into a single profile and that their profile may change day-to-day or even trip-to-trip. Someone who is comfortable riding in bike lanes on a relatively high-volume road for a commute trip wouldn’t necessarily feel comfortable on that same route if they were traveling with kids or cargo.
Source: FHWA. Bicycle Facility Selection Guide. (2019). Office of Safety. Available: https://safety.fhwa.dot.gov/ped_bike/tools_solve/docs/fhwasa18077.pdf

## Slide 18: Trip purposes
Notes: Key Message: The purpose of the trip is one of the many factors that defines user types. The purpose of a trip may help define preferences for specific routes and facility types.

## Slide 19: Walking Trips
League of American Bicyclists using 2017 National Household Travel Survey data
Notes: Connection to other Module: The Introduction module contains slides with data about all walk and bike trips and commute trips.
Source: Bicycling and Walking in the United States: 2018 Benchmark Report by League of American Bicyclists, available https://bikeleague.org/benchmarking-report. This early analysis of FHWA NHTS data was conducted by Dr. Ralph Buehler for the League of American Bicyclists.
Image: Figure 1.1.7 in the Benchmark Report.

## Slide 20: What about walking and biking in small town or rural areas?
Walking and bicycling is common, but facilities are often lacking
Destinations in the community core are often walkable distances apart
Opportunities for bicycle tourism in and around public lands
pedbikeimages.org – Reuben E. Moore
Notes: Notes: Rural and small-town America is diverse and varied throughout the country. According to the FHWA’s “Planning for Transportation in Rural Areas,” 75% of America’s 3,000 counties qualify as rural and cover 81% of the land area. Approximately 19% of the population live in rural areas. Though residents in rural areas may live long distances from services, rural town centers are often compact hubs with a grid pattern that keeps most destinations within a few miles of each other.
Source: FHWA Small Town and Rural Multimodal Networks Guide (2016)
Image: http://www.pedbikeimages.org/mediumimages/100_0040.jpg

## Slide 21: Walking and Biking in Small Towns or Rural Areas -- Challenges
Auto-oriented
  Highway as “main street”
  Pedestrian crossings often not defined
  Lack of ped/bike facilities
Constrained terrain
  Physical constraints for cost-effective ped/bike facilities
Other
  Public lands access
  Agricultural uses
  Winter maintenance on active transportation facilities
Notes: Source: FHWA Small Town and Rural Multimodal Networks Guide (2016)
Image: pedbikeimages.org – Dan Burden

## Slide 22: Bicycle Trips
League of American Bicyclists using 2017 National Household Travel Survey data
Notes: Connection to other Module: The Introduction module contains slides with data about all walk and bike trips and commute trips.
Source: Bicycling and Walking in the United States: 2018 Benchmark Report by League of American Bicyclists, available https://bikeleague.org/benchmarking-report. This early analysis of NHTS data was conducted by Dr. Ralph Buehler for the League of American Bicyclists.
Image: Figure 1.1.6 in the report listed above.

## Slide 23: Bicycling Trips
Recreational
Start and end points are often the same
Directness of route less important
Wide range of trip distances
Groups or individual
Utilitarian
Frequent starts and stops
Greater need for secure bicycle parking
Desire for flat topography and “normal” clothing
Notes: Key Message: Trip purpose affects bicyclist route choice and behavior.
Notes: For example, a time-constrained trip like a commute trip might lead the bicyclist to choose a more direct route, even if it is less comfortable. For a trip on a more flexible timeline, a bicyclist might choose a more comfortable route. Utilitarian is often used interchangeably with “commute,” but a utilitarian trip includes any trip needed to take care of daily needs (i.e., shopping, appointments, social gatherings, etc.). Keep in mind that most true commute trips are occurring when motor vehicle volume is also at its highest. A recreational trip is for exercise or leisure, or both.
Source:
AASHTO (2012). Guide for the Development of Bicycle Facilities, 4th Edition, Chapter 2.
City Cycling (2012), eds. John Pucher and Ralph Buehler, Chapter 5.

## Slide 24: Bicycle as Design Vehicle
VTRANS
Notes: Key Message: Keep in the mind the length and width of different styles of bicycles.
Source:
Image: Vermont Agency of Transportation. Vermont Pedestrian and Bicycle Facility Planning and Design Manual. (2002). Figure 4-1.

## Slide 25
Pedbikeimages.org – Dan Burden
Notes: Key Message: Plan for bicycles of different length and widths and bicyclists of different heights.

## Slide 26: E-bike Users
Why do people choose electric-assist bicycles?
  Reduce physical exertion
  Conquer challenging topography
  Replace car trips
  Carry more cargo or kids
In the U.S., limited research has shown that e-bike users do not differ from conventional bicycle riders in terms of safety behaviors
Notes: Key Message: Electric bicycles or electric-assist bicycles, often called e-bikes, are becoming increasingly popular because they can make biking easier or more comfortable, which potentially allows for a greater diversity of bicycle trips and riders.
Notes: Most research to-date in the U.S. is based on surveys of owners of electric-assist bicycles.
Sources:
MacArthur, John, Christopher Cherry, Michael Harpool, and Daniel Scheppke. (2018). A North American Survey of Electric Bicycle Owners. [NITC-RR-1041]. Portland, OR: Transportation Research and Education Center (TREC).
Langford, B. C., Chen, J., & Cherry, C. R. (2015). Risky riding: Naturalistic methods comparing safety behavior from conventional bicycle riders and electric bike riders. Accident Analysis & Prevention, 82, 220-226.

## Slide 27: Summary
Pedestrians have a wide range of capabilities that should be considered in the planning and design of facilities
Trip purpose affects route choice and behavior
People may experience each trip through the surrounding environment differently