## Slide 1: Bicycle and Pedestrian Data for Planning
Instructor course information
Notes: Report No. FHWA-SA-19-034

## Slide 2: Module Outline
Types of data and data uses
Environment data
  Facility inventories
Behavior data
  Volume counts
  Trips/mode share
Estimating bicycling and walking trips
Emerging data sources
Notes: Connection to other Module: The topic of crash data is introduced in this module but covered in more detail in the module, Safety Analysis.

## Slide 3: Why Collect Data?
Planning and funding
  Determine when/where people walk and bicycle (or not)
  Identify presence and quality of facilities
Benchmarking
  Show whether goals are being met (or need to be reevaluated)
  Compare to other areas
Accountability
pedbikeimages.org – Adam Coppola Photography
Notes: Key Message: Collecting accurate bicycle and pedestrian data has many benefits that range from justifying funding, to understanding why and where people travel by bike or on foot, to creating a safer environment for all road users.
Notes: The availability of data about walking and bicycling lags the availability of data for other modes. Think about how many times you’ve been in a vehicle that has driven over pneumatic tubes taped to the roadway. Think about every time you’ve paid a fare and boarded a transit vehicle, entered and exited a rail system, bought a plane ticket, etc. There is a saying: if it doesn’t get counted, then it doesn’t count.
Source: Adapted from Bob Schneider. (2008). Data Collection and Performance Measures. Powerpoint presentation. UC Berkeley.
Image: http://www.pedbikeimages.org/details.php?picid=2253

## Slide 4: Why Collect Data?
“Data” in pedestrian and bicycle transportation means qualitative AND quantitative
  Spreadsheets and maps can’t tell you everything
  Remember to go out and talk to people
Unsplash – Timon Studler
Notes: Image: https://unsplash.com/photos/ABGaVhJxwDQ

## Slide 5: Data Types
Environment
Facility inventory & traits
Land uses
Population socio-demographics
Perceptions
Behavior
Volume and use
Pedestrians
Bicyclists
Motor vehicle ADT & mix
Transit
Crashes
Trip and mode share
Notes: Notes: Bold indicates the types of data that will be covered in more detail in this module. These data types are shown on a Venn diagram to remind us that there is some overlap in the collection and uses for these data. Each type of data only conveys part of the picture. For example, you will almost always need to relate behavior data back to the environment (e.g., facilities, population, conditions of use, etc.)
Source: This slide was adopted from a presentation by Carl Sundstrom and Libby Thomas for the Pedestrian and Bicycle Information Center (2011, updated 2015).

## Slide 6: Uses in Planning and Performance Measurement
Identifying and/or prioritizing projects
Comparing alternatives
Evaluating scenarios
Benchmarking
Establishing a baseline
Notes: Source: Semler, C.; Vest, A.; Kingsley, K.; Mah, S.; Kittleson, W.; Sundstrom, C.; and Brookshire, K. (2016). Guidebook for Developing Pedestrian and Bicycle Performance Measures. [FHWA-HEP-16-037]. Washington, DC: United Stated Department of Transportation, Federal Highway Administration.

## Slide 7: Environment data

## Slide 8: Environment: Existing Data Sources
Population sociodemographic (US Census Bureau)
  Decennial Census and American Community Survey
TIGER Line files (US Census Bureau)
  National road data
Aerial imagery
Pedbikedata.org (PBIC)
  Infrastructure data from various agencies

## Slide 9: Environment: Data Collection
Inventories (roads, sidewalks, paths)
  Data managed in GIS, CAD, or spreadsheets
  May need to prioritize by focusing on key destinations
    Schools
    Shopping/employments centers
    Transit facilities
  May need to inventory entire network for accessibility by persons with disabilities
Notes: Key Message: Primary data include inventories or audits. These involve walking or driving along streets, filling out pre-specified forms that include boxes to identify the presence and quality of sidewalks, lighting, transit stop landings, etc.
Notes: Both pedestrian or bicyclist supports AND hazards or barriers are collected. These data are then inventoried in spreadsheets and managed using programs such as GIS or CAD. Since this data collection activity is resource intensive, it makes sense to prioritize certain locations that attract pedestrian or bicycle activity such as libraries, schools, and shopping centers. This data collection can be conducted zone-by-zone or community-wide.
Many agencies end up with a complete inventory of their pedestrian facilities as part of their self-evaluation for compliance with the Americans with Disabilities Act. The purpose of this evaluation is to identify barriers in programs and activities that prevent persons with disabilities from access. For public rights-of-way this involves assessing sidewalks, curb ramps, slope, pedestrian push buttons (i.e., communication devices), bus stops, work zones, shared use paths, and parking lots. The inventory is used as the foundation for a Transition Plan.
Connection to other Module: Accessibility and ADA
Source: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 10: Environment: Data Collection
Qualitative infrastructure assessment
  Slopes
  Pavement quality
  Sight distances and visibility
  Crossing times
Quantitative assessment
  Gap studies: enough time to cross between cars?
pedbikeimages.org – Dan Burden
Notes: Notes: Other data that are often collected includes sidewalk slope, cross-slope, and surface variation. These data can help answer questions such as: Is width or number of lanes of the crossing a concern? Is there the possibility of multiple threat collisions? Is speed of traffic a concern? These assessments may also be used by maintenance departments.
Connection to other Module: ADA and Accessibility
Image: http://www.pedbikeimages.org/largeimages/audit1.parkinglot.edge.jpg

## Slide 11: Environment Data
What you can do once you have environment data…
Assess access to destinations by different populations
Plan and program for maintenance
  Especially for compliance with accessibility requirements
Measure route directness or network quality
Notes: Connection to other Module: Facility and Network Analysis covers methods for assessing network quality.

## Slide 12: Behavior Data

## Slide 13: Crashes
Existing data: Fatality Analysis Reporting System (FARS)
  Run queries about fatalities only
  Only includes traffic-related crashes
Local interest in:
  Crash frequency
    Broken down by number of pedestrian/bicycle crashes
  Crash types
  Crash locations
    Spatially-presented crash occurrence or rates
Notes: Key Message: National sources of pedestrian and bicycle collision data tend to focus almost exclusively on fatal collisions. At the local level, more detail is often needed to guide ped/bike safety efforts and facility development.
Notes: For example, it is important to understand which types of crashes are occurring, such as right-hook or left cross. While the frequency of crashes is useful, it is even more useful when paired with data about exposure. For example, the average number of bicyclists or pedestrians in a city or at a location as well as the number of vehicles. Finally, it is important to collect location data in order to map crash frequency, type (if applicable), and/or collision rate, although calculating rates is still a simplistic measure.
Connection to other Module: Safety Analysis and Countermeasure Selection covers crash data in more detail.
Source: This slide was adopted from a presentation by Carl Sundstrom and Libby Thomas for the Pedestrian and Bicycle Information Center (2011, updated 2015).

## Slide 14: Bicycle and pedestrian volumes
Notes: Notes: Several methods for collecting bicycle and pedestrian count data will be discussed.

## Slide 15: Existing Data
U.S. Census Bureau
  Commute trips only
    Decennial Census
    American Community Survey
Pedbikedata.org (PBIC)
  Count data from various agencies
Notes: Notes: The U.S. Census is the best source for information on the journey to work commute. All main travel modes are counted. The American Community Survey (ACS) replaced the Decennial Census’ “long form.” It relies on continuous data collection from a sample. For small units of analysis you may only be able to aggregate data over several years.
Pedbikedata.org includes data that are publicly available or made available upon request. Data may be stored in GIS, a spreadsheet, or a PDF.

## Slide 16
Robert Schneider (Data Source: ACS)
Notes: Notes: This map is an example of walk commute to work share in Milwaukee County, based on ACS data.
Student Question: Ask students to discuss what they may or may not be able to learn by examining mode share at this scale.
Source: This slide was adapted from a presentation by Robert Schneider.

## Slide 17: Bicycle and Pedestrian Volume Data
Why count people walking and bicycling?
  Set performance measures
  Prioritize programs, projects, funding
  Put crash data in context
  Pair with geospatial data inventories of facilities
  Evaluate long-term trends
  Others?
pedbikeimages.org – Krista Nordback
Notes: Notes: High quality data allow an agency to set performance measures, prioritize programs and infrastructure funds, manage transportation operations efficiently and effectively, and eventually evaluate the long-term trends of walking and bicycling. Count, or volume, data provide the foundation for measuring nonmotorized travel and monitoring trends of a facility or network. They put crash data in context to better understand the exposure to risk.
Image – shows pneumatic tube bicycle counter used as a permanent continuous counter on the Hawthorne bridge in Portland, Oregon. http://www.pedbikeimages.org/details.php?picid=2518
Student Question: Can you think of other reasons to count people walking and bicycling?
Example responses:
estimate social, economic, and health impacts of walking and bicycling
report program impact to elected officials
conduct before/after studies
calibrate a regional model
adjust signal timing at an intersection (if turning movement counts are conducted at an intersection)
Sources:
Pedestrian and Bicycle Information Center, “Counting and Estimating Volumes.” Available: http://www.pedbikeinfo.org/topics/countingestimating.cfm (Accessed June 2019).
Pedestrian and Bicycle Information Center, “Bicycle and Pedestrian count Programs: Summary of Practice and Key Resources,” Available: http://www.pedbikeinfo.org/resources/resources_details.cfm?id=5101

## Slide 18: Traffic Monitoring Programs
State DOTs and other agencies collect vehicular count data
Applying factors and calibration
Notes: Notes: In vehicular traffic monitoring, State DOTs and other transportation agencies typically collect both permanent count and short duration count data and utilize it to estimate AADT (average annual daily traffic) based on applying seasonal factors and other calibration factors.
Source: This slide was adopted from a presentation by Krista Nordback for the Pedestrian and Bicycle Information Center.

## Slide 19: Can these Methods be Applied to Biking and Walking?
Pedbikeimages.org – Laura Sandt
Pedbikeimages.org – Dan Burden
Notes: Notes: Yes! And ideally, nonmotorized count data are collected and managed by the same group that oversees vehicle counts at the local, regional, and/or State level.
Key differences from motorized counting:
Most nonmotorized data collection programs have a much smaller number of monitoring locations, and these limited location samples may not accurately represent the entire geographic area of interest.
Nonmotorized traffic will typically have higher use on lower functional class roads and streets as well as shared use paths and pedestrian facilities, simply because of the more pleasant environment of lower speeds and volumes of motorized traffic. Conversely, motorized traffic monitoring focuses on higher functional class roads that provide the quickest and most direct route for motorized traffic.
Technologies for counting pedestrians and bicyclists still are evolving. Error rates for technologies used to count motorized traffic generally are better understood, as are the procedures for managing or reducing these errors.
Student Question: Think back to our lesson on user needs and mode characteristics. What is unique about walking and bicycling that might make it more difficult to count these trips?
Potential responses: pedestrian and bicyclists are less confined to fixed paths of travel, they make unpredictable movements, easier for them to take short cuts, they sometimes travel in closely spaced groups.
Connection to Other Module: User and Mode Characteristics
Source: FHWA, Traffic Monitoring Guide. Available: https://www.fhwa.dot.gov/policyinformation/tmguide/ (accessed June 2019).
http://www.pedbikeimages.org/details.php?picid=339
http://www.pedbikeimages.org/details.php?picid=392

## Slide 20: Key Questions for Collecting Volume Data
What are you counting?
Where are you counting?
For how long?
Permanent? Temporary? Medium-term?
Notes: Notes:
First, it is important to define what you are counting – pedestrians only, pedestrians and bicyclists (separately or combined), or bicyclists only. What about cars?
Second, you define the locations where you will be counting, for example, sidewalks, intersections, shared-use paths, or on-street bicycling facilities. If you are counting along a segment, this is called a “screenline” count. If you are counting where two or more roadways and/or commercial driveways meet, this is called an “intersection turning movement count.”
Third, you define how often or for how long you will be conducting counts, for example: permanently, temporarily, or periodically.
Source: Adapted from the Pedestrian and Bicycle Information Center. (2015). Bicycle and Pedestrian Transportation Short Series, Class 3.

## Slide 21: Aspects of a Count Program
Site Selection
  Inventory existing data
  Continuous counter site selection
  Short duration count site selection
  System expansion
  Equipment
    Selection
    Installation
    Validation
    Maintenance
Data Management
  Quality checking
  Site grouping
  Temporal adjustment factor creation
  Applying temporal adjustment factors
  Data sharing
  Reporting
Notes: Key Message: This lesson will not go into detail on all of these aspects. This slide is intended to help students think about the level of effort, timeline, and funding that might be needed to properly design a count program.
Notes: “Inventory existing data” – don’t just go looking for bike/ped counts, investigate what your community is doing in terms of vehicle counts. Many agencies already conduct manual counts of vehicles at intersections. Do they count bicyclists and pedestrians as well? If not, this could be a good starting place for a community.
Source: Pedestrian and Bicycle Information Center (2017) “Bicycle and Pedestrian count Programs: Summary of Practice and Key Resources,” Available: http://www.pedbikeinfo.org/resources/resources_details.cfm?id=5101

## Slide 22: Collecting Bicycle and Pedestrian Volume Data
Types of counts:
  Continuous permanent
    Record travel patterns over time
  Short duration
    Record spatial distribution of travel
Key Resources:
  FHWA Traffic Monitoring Guide, Chapter 4
  NCHRP Report 797
  Coding Nonmotorized Station Location Information in the 2016 Traffic Monitoring Guide Format
Notes: Key Message: FHWA’s Traffic Monitoring Guide and NCHRP Report 797 Guidebook on Pedestrian and Bicycle Volume Data Collection contain information about the different technologies that can be used to collect continuous nonmotorized traffic data and the steps for setting up a data program. They also cover short duration counts and the steps for adjusting count data.
Notes: “Even though both of these modes preceded the automobile, the monitoring of nonmotorized traffic has not been systematic or widespread in the U.S. and, even today, is not nearly as comprehensive as motorized traffic monitoring.” (TMG, pg. 4-1).
Source: FHWA, Traffic Monitoring Guide and Coding Nonmotorized Station Location Information in the 2016 Traffic Monitoring Guide Format. Available: https://www.fhwa.dot.gov/policyinformation/tmguide/ [Accessed June 2019].

## Slide 23: Count Recommendations
Use permanent AND short duration counters
Selecting continuous counter sites
  Factor group: collection of count sites that represent different travel patterns facility types, or volume levels (e.g., commute, recreational)
  Minimum 3-5 counters per factor group
Short duration counts
  Collected manually or with a counting device
  7 continuous days a week
  Count in high volume months
  Validate equipment
  Share data!
Pedbikeimages.org – Krista Nordback
Notes: Notes: This slide is intended to help students start thinking about the time and equipment requirements for a count program.
Source: This slide was adopted from a presentation by Krista Nordback, PBIC.
Image – Inductive loop bicycle counter on road and sidewalk and passive infrared counter on sidewalk counts pedestrians and bicyclists on sidewalk plus bicycles on the road in Chapel Hill, North Carolina. http://www.pedbikeimages.org/details.php?picid=2517

## Slide 24: Counting Technology
Inductive Loop
Piezoelectric
pedbikeimages.org – Krista Nordback
Notes: Key Message: The NCHRP and FHWA references previously mentioned provide detailed information about different counting technologies. These images are included here so that you can become familiar with what continuous counting might look like out in the field. In both images, the use of the bicycle counter is combined with a passive infrared counter. Since the passive infrared counter counts people walking or bicycling, an agency can take the bicycle counts from the other technology and subtract those to get a count for pedestrians. Perhaps you’ve passed over or by one of these devices while you were walking or bicycling!
Images:
Left: http://www.pedbikeimages.org/details.php?picid=2516
Right: http://www.pedbikeimages.org/details.php?picid=2514

## Slide 25: Getting to AADPT and AADBT
Continuous count stations: permanent counting sites that provide data continuously (24 hours, 7 days a week)
Enough data to allow calculation of accurate adjustment factors
  Time of day
  Day of week
  Monthly
Temporal adjustment factors are applied to short duration counts
Pedbikeimages.org - PeopleForBikes
Notes: Notes: A few slides back we introduced AADT (annual average daily traffic). Even though it doesn’t specify the mode, the assumption has always been that this means motor vehicles. AADPT is the acronym for pedestrians and AADBT is the acronym for bicyclists. Some agencies may use AADNT (annual average daily nonmotorized traffic) to cover pedestrian and/or bicycle traffic.
Permanent counter installation sites generate data throughout the year which allows researchers and practitioners the ability to calculate adjustment factors for time of day, day of the week and month of the year.
This means that when short duration counts are collected in a greater variety of geographic locations, the factors previously calculated based on the permanent count sites in the area can be applied to extrapolate from short duration counts to AADPT and AADBT.
Source: This slide was adopted from a presentation by Sarah O’Brien.
Image: http://www.pedbikeimages.org/details.php?picid=2268

## Slide 26: Example Manual Counts: National Bicycle and Pedestrian Documentation Project
Short duration counts (project or cyclic)
2 hours
5 to 7 PM
Tues., Wed., or Thurs. in mid-September
bikepeddocumentation.org
Robert Schneider
Notes: Key Message: Many communities get their start in bike/ped volume data collection by participating in the National Bicycle and Pedestrian Documentation Project.
Notes: National Bicycle and Pedestrian Documentation Project lays out the systematic approach for a community to develop local factors to calibrate short duration and manual counts to develop AADPT and AADBT estimates.
Source: This slide was adopted from a presentation by Krista Nordback, PBIC.

## Slide 27: Example: Using Volume Data for Safety Analysis
Continuous counts at three locations on a university campus
Two-hour manual counts at all 22 intersections on campus
Extrapolated volume estimates and compared with reported crashes at intersections
Schneider, Grembek, Braughton (2013) via NCHRP 797
Notes: Key Message: The combination of continuous and short duration counts allowed researchers to create a measure of exposure for a pedestrian safety analysis of campus intersections. Results showed that pedestrian crash risk was generally higher at intersections along the boundary roadways with the lower pedestrian volumes. Pedestrian risk in the evening was estimated to be more than three times higher than in the daytime.
Notes: Nine more short case studies about the use of bike/ped volume data are available in the appendix of NCHRP Report 797.
Source: National Academies of Sciences, Engineering, and Medicine (2014). Guidebook on Pedestrian and Bicycle Volume Data Collection. Appendix A. Washington, DC: The National Academies Press. https://doi.org/10.17226/22223.

## Slide 28: What About Other Users?
Scooters, tandem bicycle, recumbent bicycles, cargo bicycle, strollers, Segways, bike taxis….
Consider how other users would be categorized for manual counts and captured (or not) by continuous counters
Most important: a consistent approach
Example: Metro (Los Angles) suggests counting push scooters with pedestrians
Notes: Source: Southern California Association of Governments and Metro, Available: http://media.metro.net/projects_studies/call_projects/images/metroscag_bikepedcounttrainingmanual.pdf (Accessed May 2019)

## Slide 29: Trip and mode share data
Notes: Notes: National sources of data and local options like Household Travel Surveys will be discussed.

## Slide 30: National Household Travel Survey (FHWA)
Conducted every 5-7 years since 1969
Latest round made available in 2017
Most useful for benchmarking, estimating general trends
No longer interviewer-assisted, short trips might be under-reported
States, cities, and MPOs can purchase additional sampling of their area
Notes: Key Message: National Household Travel Survey is one good example of mode share data available for the entire country for all types of trips (not just trips to work). Additional info about the latest NHTS Survey available at: nhts.ornl.gov/
Source:
This slide was adopted from a slides by Carl Sundstrom, Libby Thomas, and Robert Schneider for the Pedestrian and Bicycle Information Center.
FHWA. (2017). Summary of Travel Trends: 2017 National Household Travel Survey. https://nhts.ornl.gov/assets/2017_nhts_summary_travel_trends.pdf
Image: http://www.pedbikeimages.org/details.php?picid=2238

## Slide 31: U.S. Census American Community Survey
Travel data limited to commute trips by workers age 16 and over
Updated data released every year for larger urbanized areas
Rural/less densely-populated areas can get estimates from 5-year samples
Can be mapped by linking data tables to Census geography shapefiles in GIS
U.S. Census Bureau FactFinder query about trips by mode in Atlanta, GA
Notes: Key Message: The U.S. Census Bureau only collects information about commute trips (for workers 16+). But these data are collected more frequently than the NHTS and can be used at a finer geographic scale. As commute trips often are some of the longest trips that a person must make in their daily routine, active transportation is likely to be under-represented in commute-only trips. Additionally, the share of commute trips vs. overall household travel stands at less than 20% of total household VMT in the U.S. based on the latest National Household Travel Survey data.
Notes: The American Community Survey collects data on an ongoing basis, January through December. Rural and less densely-populated communities might have to rely on the 5-year data samples rather than having easy access to 1-year ACS data. Researchers and planners can download ACS datasets and link them to ArcGIS shapefiles of Census geography (Census tracts, block groups) to map the commute characteristics across a region.
Source:
Image: U.S. Census Bureau, ACS B080006 Table, City of Atlanta, 2013-2017, Sex of Workers by Means of Transportation to Work. Downloaded from: https://factfinder.census.gov/

## Slide 32: Regional Mode Share Data Sources
Larger MPOs sometimes undertake a regional Household Travel Survey
Usually once/10 years or less frequently
Target a statistically-significant sample of the households
Travel diaries to document trip purpose and mode
Can be GPS-assisted
Nashville Area MPO
Notes: Key Message: Larger MPOs will sometimes undertake their own regional Household Travel Survey to support the regional Travel Demand Model Update. This is a large undertaking and most MPOs would not do it more than once every 10 years. The results can be very helpful as they describe travel patterns specific to the local region, and account for a variety of trip purposes, rather than relying on a national-level dataset or only looking at commuting-to-work trips.
Notes: Example: Nashville Area MPO conducted a regional Household Travel Survey in 2012, which included a health and physical activity element. Participating households were asked to use a personal wearable GPS device. The Nashville Area MPO’s study goal was to collect demographic, household, basic health and travel information from a representative sample of 6,000 households located within all study-area counties using an address-based sample (ABS) design. The study consisted of a small pretest followed by two periods of data collection in the spring and fall of 2012. During this study effort, survey data were successfully collected from 6,397 households across the entire study region. This report contains the results for 6,256 of those households; the 5,164 households in the Nashville Area MPO and 1,092 in the outer counties.
Source: Image - Nashville Area MPO and Westat (2013). Middle Tennessee Transportation and Health Study Final Report. Table 136: All Trip Modes Regional Summary. Retrieved from http://www.nashvillempo.org/docs/research/Nashville_Final_Report_062513.pdf

## Slide 33: No Data are Perfect!
Reported trip length discrepancies from different sources:
StreetLight Data
Notes: Key Message: Survey data is reported based on a sample of households and trips and is subject to recall error and other errors.
Notes: The private company StreetLight Data is showing an average shorter trip distance for bicycle and pedestrian trips than what is based on the National Household Travel Survey. This might be due to survey responders being more prone to forgetting short trips, especially since for 2017 NHTS interviewer-assisted recall was no longer used. Other possible factors might be “trip-breaking”—StreetLight algorithms deciding to break a trip into two if the person walking or bicycling took a break in the middle for another activity (i.e., to make a phone call or to have lunch). In these tables, CHTS stands for California Household Travel Survey. More about the samples below.
Source: StreetLight Multimode Methodology, Data Sources, and Validation Version 2.0 Updated March 2019. Available: https://www.streetlightdata.com/wp-content/uploads/2019/04/StreetLight_Active-Mode_Methodolgy-and-Validation_190408.pdf (Accessed May 2019).
Samples for tables:
For comparison of bike trips, StreetLight Data analyzed roughly 81.6 million bicycle trips across the continental US that occurred in May-June 2017 and May-June 2018. NHTS surveyed 129,000 households across the country and analyzed 8,000 bike trips while California Household Travel Survey surveyed 42,431 households with fever than 5,900 bike trips.
For comparison of walk trips, StreetLight Data analyzed over a billion walk trips across the continental U.S. that occurred in May-June 2017 and May-June 2018. NHTS surveyed about 129,000 households across the country and analyzed 81,200 walk trips while California Household Travel Survey surveyed 42,431 households and looked at just under 65,000 walk trips.

## Slide 34: Other Sources of Trip & Mode Share Data
NHTSA’s National Survey of Bicyclist and Pedestrian Attitudes & Behaviors (2012)
  Trip purpose
  Availability of facilities
  Injuries
  Perceptions
  Knowledge of laws
NHTSA
Frequency of Bicycle Helmet Usage
Notes: Key Message: National Survey of Pedestrian and Bicyclist Attitudes and Behaviors can be a good additional source of typical behaviors, trip length, etc. for bicyclists and pedestrians. A total of 7,509 interviews were conducted among a national representative sample of individuals 16 or older.
Notes: 2012 NHTSA survey assessed the extent to which respondents engaged in bicycling and walking outdoors; demographic and typological descriptions of bicyclists and pedestrians; the extent and frequency of using electronic devices while biking or walking; attitudes and perceptions about bicycling and pedestrian activity; the availability and use of bike paths and lanes in the community; knowledge of various laws pertaining to bicyclists and pedestrians; and changes in bicycling and pedestrian behavior and attitudes since the previous survey in 2002.
Connection to other Module: User and Mode Characteristics
Source: NHTSA (2013). 2012 National Survey of Bicyclist and Pedestrians Attitudes and Behaviors. Volume 2: Findings Report. https://www.nhtsa.gov/sites/nhtsa.dot.gov/files/811841b.pdf

## Slide 35: Example: Washington State
State-level Student Travel Survey
  Partnership of State DOT & health department
  Representative sample of parents and schools (via phone interview) asked about:
    Mode of travel to/from school
    Reason for not walking, biking, or taking bus
    Perception of school’s support for active transport
Notes: Key Message: While acknowledging that school bus transportation is safe, but expensive, and that transportation by private vehicles add to roadway congestion, Washington State wanted to learn more about the opportunities and barriers for walking and bicycling to school. Baseline estimates were collected in 2014 and the survey was repeated in 2016. The state has a lot of data about student use of school bus service, so the survey is intended to fill the gap in knowledge about choice/attitudes related to other modes and inform their investment decisions about transportation services.
Findings: 17% of students walk to school, which is higher than the national average. But the State notes that there are a significant percentage who live within 1 mile of their school who do not walk or bike and many further away that could ride the school bus but don’t.
Notes: This data collection effort will help the State reach goals for their Safe Routes to School program and contained within their Target Zero Safety Plan.
Connection to other Module: School Travel
Source: Washington State 2016 Student Travel Survey State Report, 2017, Available: https://www.wsdot.wa.gov/sites/default/files/2009/01/09/ATP_WA-2016-Student-Travel-Survey-Report.pdf (Accessed June 2019).
Image: pedbikeimages.org – Chris Metka available: http://www.pedbikeimages.org/details.php?picid=301

## Slide 36: International Example: Copenhagen Bicycle Account
Two data sources for biennial assessment bicycling:
  Phone interviews and data from Danish National Travel Survey
  Field measurements of bicycle travel time on select facilities
Mode share, state of facilities, public satisfaction, etc.
Used for planning, political lobbying, and communicating efforts to the public
Other countries have used this as a model
Notes: Key Message: The Greater Copenhagen Region (population 1.7 million) publishes an annual bicycle account that tracks how cycling patterns change over time. Copenhagen is widely considered one of the most bike-friendly cities in the world. The region has a goal that one out of every two commuters chooses to bicycle, but the number peaked in 2014 at 45% and was down to 41% in 2016 and the number of privately-owned vehicles is rising.
Notes:
Performance measures include:
Average bicycle speed by bicycle superhighway route.
Millions of bicycle trips per year by geographic area (region-wide, Copenhagen and Frederiksberg, suburbs, and outlying areas).
Mode to work/school by geographic area.
Bicycling kilometers per day.
Per-capita bicycling kilometers per day.
Number of sick days reduced per year (assumes one day reduced per 1,200 km cycled by a person).
Reduction in car trips and car kilometers traveled during peak periods due to bicycling.
Average bicycle trip length.
Economic worth of faster road travel due to reduced auto travel demand as a result of bicycling.
Reduction in carbon dioxide emissions.
Source:
Federal Highway Administration. (2016). Delivering Safe, Comfortable, and Connected Pedestrian and Bicycle Networks: A Review of International Practice. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/global_benchmarking/page04.cfm#Performance
Copenhagen City of Cyclists: The Bicycle Account 2016, available: http://www.cycling-embassy.dk/wp-content/uploads/2018/02/CPH-Bicycle-Account-2016.pdf

## Slide 37: Estimating Bicycling and walking Trips
Notes: Key Message: Even though walking and bicycling are both nonmotorized modes of travel that are often considered concurrently, there are critical differences that need to be considered when attempting to explain or forecast travel demand: the distance range (0.7 mile average trip length for walk, 2.3 miles for bike), network needs, user characteristics, and trip purpose types are substantially different between the two modes.
Connection to Other Module: User and Mode Characteristics
Source: National Academies of Sciences, Engineering, and Medicine. (2014) Estimating Bicycling and Walking for Planning and Project Development: A Guidebook. Washington, DC: The National Academies Press. https://doi.org/10.17226/22330.

## Slide 38: Goals of Estimating Demand
Predict levels of activity, and help inform decisions on issues such as:
  Future facility use
  Project prioritization
  The impact of future development
pedbikeimages.org – PeopleForBikes
Notes: Key Message: Sound forecasting can support planning for bicycle and pedestrian infrastructure.
Notes: Bicycle and pedestrian forecasting allows planners and engineers to understand, quantify, and plan for the demand for bicycle and pedestrian infrastructure. Regions and cities spend significant time, effort, and resources on travel demand forecasting. Many legislative requirements, such as congestion management process monitoring, regional transportation plan development, and statewide project development, require auto or transit trip forecasting. However, no similar equivalents are in place for bicycle and pedestrian forecasting.
Source: Pedestrian and Bicycle Information Center, Bicycle and Pedestrian Forecasting Tools: State of the Practice. (2015). Available: http://www.pedbikeinfo.org/cms/downloads/PBIC_WhitePaper_Forecasting.pdf (Accessed June 2019).
Image: http://www.pedbikeimages.org/largeimages/alyson%20west%20-%20danishathleticcyclistsPFB.jpg

## Slide 39: Key Differences from Forecasting Vehicle Trips
The relationship to land use and the travel network
Acceptable trip distances vary by trip purpose
People living in compact, mixed-use setting make more one-stop journeys; bike/walk is more likely for these trips
The natural environment is of greater consequence
Concerns about personal safety
Age and gender differences observed between motorized and nonmotorized travelers and between bicyclists and pedestrians
Notes: Key Message: When it come to individuals choosing whether or not to walk or bicycle, there is a fairly complex set of decisions being made concurrently, involving multiple factors and tradeoffs, with most being highly location specific. If a car is available to someone, the choice to use that car is not as sensitive to many of the factors listed on the slide. Forecasting for nonmotorized trips is a challenging but necessary task that researchers and practitioners are continually refining.
Connection to other Module: User and Mode Characteristics
Source: National Academies of Sciences, Engineering, and Medicine. (2014). Estimating Bicycling and Walking for Planning and Project Development: A Guidebook. Washington, DC: The National Academies Press. https://doi.org/10.17226/22330.

## Slide 40: Methods by Geographic Scale
Local level
  Factor methods and sketch planning techniques
  Aggregate demand models
  Bike share forecasting
Corridor and sub-area level
  GIS and spatial tools
  Network simulation tools
Regional level
  Regional travel demand forecasting models
  Activity and tour-based models
Notes: Key Message: Subsequent slides will cover the methods in bold. It is not because these methods are recommended over others, its simply because the factor methods and sketch planning techniques are the most accessible and the regional level tools are the most pervasive, so it is important to be familiar with the opportunities and challenges for incorporating bicycle and pedestrian trips.
Notes: Each of these methods are summarized in the PBIC resource listed below.
Source: Pedestrian and Bicycle Information Center. (2015). Bicycle and Pedestrian Forecasting Tools: State of the Practice. Available: http://www.pedbikeinfo.org/cms/downloads/PBIC_WhitePaper_Forecasting.pdf (Accessed June 2019).

## Slide 41: Methods by Geographic Scale
There is also some overlap…
PBIC adapted from NCHRP 08-78
Notes: Source: Pedestrian and Bicycle Information Center. (2015). Bicycle and Pedestrian Forecasting Tools: State of the Practice. Available: http://www.pedbikeinfo.org/cms/downloads/PBIC_WhitePaper_Forecasting.pdf (Accessed June 2019).

## Slide 42: Factor Methods and Sketch Planning Techniques
Estimate demand using Census data or traffic volumes on adjacent streets
Advantages:
  Suitable for day-to-day needs
  Limited need for software
  Relies on existing or easily collected data
Notes: Key Message: These are the techniques most likely to be employed by a practitioner or agency that does not have knowledge of more sophisticated techniques or special software. These methods can be used to prioritize projects, predict the amount of walking/bicycling in one area using data collected from another area, and develop bicycle and pedestrian trip generation rate estimates. With these easier-to-use methods, it can be difficult to validate forecasts because these tools are generally based on broad data sets or may not account for enough contextual factors.
Notes: These techniques include using activity levels at one facility (such as a multi-use path or bike lane) to predict demand at a new facility, using Census data or surveys to model relationships between activity levels and contextual factors. Factor methods and sketch planning techniques can rely on spreadsheets and do not require sophisticated software. Data typically used for these methods have included Census and household travel survey data, land use data, and pedestrian/bicycle infrastructure data.
Source: Pedestrian and Bicycle Information Center. (2015). Bicycle and Pedestrian Forecasting Tools: State of the Practice. Available: http://www.pedbikeinfo.org/cms/downloads/PBIC_WhitePaper_Forecasting.pdf (Accessed June 2019).

## Slide 43: Travel Demand Modeling: Enhancing Trip-Based Models
NCHRP
NMT = nonmotorized travel
LU = land use
Notes: Key Message: Regional travel demand forecasting models are typically used to plan and forecast roadway and transit networks. Modifying these models to account for bicycle and pedestrian trips would likely include reducing the size of traffic analysis zones (TAZs) and obtaining and incorporating new data inputs. This method may not be ideal, but it can be an important first step since all major urban areas have regional travel demand models and they are used as the basis to justify funding requests for transportation investments and to demonstrate environmental compliance.
Notes: On the left you see the traditional “Four-Step Model” approach, which does not account for bicycling and walking modes. On the right, you see an enhanced approach that is proposed by the authors of NCHRP Report 770. Researchers worked with Puget Sound Regional Council in the Seattle area to create a template trip-based model that is more sensitive to land use and nonmotorized travel. It introduced a “pre-mode-split” step which first divides trips into intra- vs. interzonal groups and THEN performs a mode-split specific step to each of these groups.
Source:
National Academies of Sciences, Engineering, and Medicine 2014. Estimating Bicycling and Walking for Planning and Project Development: A Guidebook. Washington, DC: The National Academies Press. https://doi.org/10.17226/22330.
Pedestrian and Bicycle Information Center. (2015). Bicycle and Pedestrian Forecasting Tools: State of the Practice. Available: http://www.pedbikeinfo.org/cms/downloads/PBIC_WhitePaper_Forecasting.pdf (Accessed June 2019).
Image: Figure 4-7 in Estimating Bicycling and Walking for Planning and Project Development: A Guidebook.

## Slide 44: Travel Demand Modeling: Tour-Based Models
Travel diary data about individuals and travel activities are collected and extrapolated to the larger population
Reflect complexity of trip choice and opportunities for multi-stop trip chaining
Advantages:
  Better account for effects of built environment and travel behavior
  May be more appropriate for activity at a more refined geographic scale than regional travel demand models
Notes: Key Message: Tour-based models can account for bicycling and walking more easily than TAZ/Trip-based models (as summarized on the previous slide). They determine travel choice based on an individual’s daily activity pattern in the form of trip “tours.” However, the creation of these models is resource-intensive and requires specialized software packages and expertise.
Notes: These models use an individual’s daily activity, as recorded in a travel diary, to develop a relationship between the transportation system (including levels of congestion and network connectivity) and demand for travel. These individuals or households and their travel activities are then extrapolated to the larger population. These models can use parcel-level or point-level information rather than TAZs.
Source:
National Academies of Sciences, Engineering, and Medicine 2014. Estimating Bicycling and Walking for Planning and Project Development: A Guidebook. Washington, DC: The National Academies Press. https://doi.org/10.17226/22330.
Pedestrian and Bicycle Information Center. (2015). Bicycle and Pedestrian Forecasting Tools: State of the Practice. Available: http://www.pedbikeinfo.org/cms/downloads/PBIC_WhitePaper_Forecasting.pdf (Accessed June 2019).

## Slide 45: Example: Tour-Based Model
NCHRP
Notes: Key Message: This table shows the variables that researchers used in a set of tour-based models they developed for public use based on data from the Puget Sound Regional Commission in the Seattle area.
Source: National Academies of Sciences, Engineering, and Medicine. (2014). Estimating Bicycling and Walking for Planning and Project Development: A Guidebook. Washington, DC: The National Academies Press. https://doi.org/10.17226/22330.

## Slide 46: New Demand Assessment Need?: Micromobility
NACTO
Notes: Question for Students: This is an opportunity to talk about when, or if, emerging modes should be incorporated in forecasting methods.
Source: Adapted from slides by Robert Schneider (2019).
NACTO. (2019). Shared Micromobility in the U.S.: 2018. Available: https://nacto.org/shared-micromobility-2018/

## Slide 47: Emerging Data Sources

## Slide 48: Potential Additional Volume Data Sources
StreetLight Insight data
  Uses cell phone location-based services (LBS) data
  Sample of 23% of US and Canadian adults, 12% of commercial trucks
  STRAVA
  Self-reported bicycling and running from GPS/activity loggers
  Not a statistically representative sample
StreetLight Data
San Francisco Pedestrian Activity Heat Map
Notes: Key Message: StreetLight is one of the private providers that is using cell phone location-based services (LBS) data in combination with machine learning algorithms to detect trips and separate them by mode. In combination with origin and destination data, mode share information for those trips can be very valuable for transportation planning. Strava is another private data source that may be utilized to document that bicycle and pedestrian users are using a corridor. Based on voluntary GPS tracking of bicycling, running, walking, and some winter activities. However, these data are likely skewed towards recreation and higher-income populations who use sports activity loggers.
Source:
San Francisco pedestrian activity heat map (yellow-more activity), Source: StreetLight Multimode Methodology, Data Sources, and Validation Version 2.0 Updated March 2019. https://www.streetlightdata.com/wp-content/uploads/2019/04/StreetLight_Active-Mode_Methodolgy-and-Validation_190408.pdf

## Slide 49: Summary
The availability of data about walking and bicycling lags the availability of data for other modes
Accurate data can be used to establish a baseline, compare alternatives, benchmark, evaluate scenarios, and identify or prioritize projects
  Count data are important for a variety of analyses, including safety analyses
Forecasting supports planning decisions at the local, corridor, and regional levels
Crowdsourced data offers new opportunities