## Slide 1: Pedestrian Facility Signing and Pavement Markings
Lesson 10
Publication No. FHWA-HRT-05-104
Notes: Lesson No.: 10
Session Title: Pedestrian Facility Signing and Pavement Markings
Learning Objectives:
Upon completion of this lesson, students will be able to:
Describe the regulatory, directional, and warning signs related to pedestrians.
Describe the pavement word, symbol, and crosswalk markings that affect pedestrians.
Discuss some of the intelligent transportation systems (ITS) technologies used to improve and enhance signs and pavement markings.
Preinstruction:
Ask the class to report on the examples they found of poorly signed and marked pedestrian areas. Have them describe what problems they noted at the location. Elicit their ideas on how the situation could be remedied through improved signing and marking.
Student Participation:
Prepare a drawing of an unsigned, unmarked complex intersection or interchange. Ask the students to design a signing and marking plan that will accommodate both motorized and nonmotorized traffic.
Followup:
Assign reading for lesson 11.
Session Time: 45–60 minutes

## Slide 2: Lesson Outline
Regulatory signs.
Warning signs.
Directional signs.
Pavement word and symbol markings.
Crosswalk markings.
ITS technology.
Notes: Key Message: Provide the students with an overview of the lesson.
Est. Presentation Time: 1 minute
Suggested Comments:
This slide is optional.

## Slide 3: Regulatory Signs
Stop.
Yield.
Signs related to pedestrian signals.
Pedestrian prohibitions.
No “right turn on red.”
Pedestrian crossings.
Source: MUTCD, http://mutcd.fhwa.dot.gov
Notes: Key Message: Regulatory signs can have an impact on pedestrian movement.
Est. Presentation Time: 3 minutes
Suggested Comments:
These signs are used to inform motorists or pedestrians of a legal requirement and should only be used when the legal requirement is not otherwise apparent. They are generally rectangular in shape, usually consisting of a black legend on a white background, and shall be reflectorized or illuminated. Many motorist signs, including stop signs, yield signs, turn restrictions, and speed limits, have a direct or indirect impact on pedestrians.
The signs on this slide are examples of various regulatory signs.
(The instructor may decide whether to discuss the examples shown)

## Slide 4: Warning Signs
Advance pedestrian crossing.
Pedestrian crossing.
Playground.
School bus stop ahead.
Advance school crossing.
School crossing.
Source: MUTCD, http://mutcd.fhwa.dot.gov
Notes: Key Message: Warning signs alert motorists and pedestrians to potential conflicts.
Est. Presentation Time: 3 minutes
Suggested Comments:
Warning signs are used to inform unfamiliar motorists/pedestrians of unusual or unexpected conditions. Warning signs predominantly fall under the permissive category (“may” condition), and when used, should be placed to provide adequate response times. Warning signs are generally diamond-shaped with black letters or drawings on a yellow background and shall be reflectorized or illuminated. Overuse of warning signs is thought to lead to disrespect and should be avoided.
The signs in this slide (clockwise from top left) are predominantly used to warn motorists of possible pedestrian conflicts.
(The instructor may decide whether to discuss the examples shown.)

## Slide 5: Directional Signs
To aid tourists.
To help new residents.
To provide the most direct pedestrian routes.
Source: MUTCD, http://mutcd.fhwa.dot.gov
Notes: Key Message: Directional signs are a third type of sign meant to assist pedestrians.
Est. Presentation Time: 1 minute
Suggested Comments:
Directional signs for pedestrians are intended to assist people who are new to the area or to assist residents who may not know the most direct route to a destination by foot. Use distances meaningful to pedestrians, such as the number of blocks or average walking time. They generally have white text on a blue background, like the example in this slide.

## Slide 6: Pavement Word and Symbol Markings
Stop bars.
PED XING.
SCHOOL XING.
Notes: Key Message: Pavement word and symbol markings may be used as motorist control devices.
Est. Presentation Time: 1–3 minutes
Suggested Comments:
The Federal Highway Administration (FHWA) Manual on Uniform Traffic Control Devices (MUTCD) allows the use of pavement word and symbol markings such as Stop bars (to let cars know where to stop at an intersection), SCHOOL XING, or PED XING, as motorist warning devices. These may be helpful on high-volume or high-speed streets with unusual geometrics (such as vertical or horizontal curves) in advance of a pedestrian crossing area. Markings should be colored white and placed to provide an adequate motorist response. Their use should be kept to a minimum to retain effectiveness. Consideration should be given to snow conditions that may obliterate the markings during portions of the year in some regions of the United States and to the local agency’s ability to maintain these pavement markings. If used, word or symbol markings should generally be placed in each approach lane (except for the SCHOOL message). Some agencies have also attempted to communicate with pedestrians by using pavement word markings such as LOOK BOTH WAYS or other symbols that encourage pedestrians to look for vehicles and to enter the road cautiously.

## Slide 7: Crosswalk Markings
Source: Safety Effects of Marked versus
Unmarked Crosswalks at Uncontrolled Locations
Notes: Key Message: Crosswalks provide guidance for pedestrians and alert road users to pedestrian crossing points across a roadway.
Est. Presentation Time: 1–3 minutes
Suggested Comments:
According to MUTCD, “Crosswalk markings provide guidance for pedestrians who are crossing roadways by defining and delineating paths on approaches to and within signalized intersections, and on approaches to other intersections where traffic stops. Crosswalk markings also serve to alert road users of a pedestrian crossing point across roadways not controlled by highway traffic signals or STOP signs. At nonintersection locations, crosswalk markings legally establish the crosswalk.” This slide presents several different pavement marking patterns used to delineate a crosswalk.
Marked Versus Unmarked Crosswalks
In the United States, there has been considerable controversy concerning marked crosswalks and whether they increase or decrease pedestrian safety at uncontrolled crossing locations (i.e., intersections or midblock locations with no traffic signals or stop signs on the main road approach). Some believe that marked crosswalks enhance the visibility, safety, and mobility of pedestrians, while others think that such markings generate overly confident feelings of safety that may cause pedestrians to be more vulnerable to collisions with motor vehicles. Consult the Federal Highway Administration University Course on Bicycle and Pedestrian Transportation Student Workbook (Student Workbook) for the findings of the Zegeer, et al., study and the recommendations for when a marked crosswalk should be installed; as always, good engineering judgment should be used in individual cases when deciding where to install crosswalks.

## Slide 8: ITS Technology
In-roadway warning lights.
Countdown signals.
Animated eyes displays.
Detection devices.
Illuminated pushbuttons.
Notes: Key Message: Intelligent transportation systems technology is being developed to improve and enhance the safety of pedestrians at intersections and midblock crossing locations.
Est. Presentation Time: 1 minute
Suggested Comments:
The following five devices will be discussed in the upcoming slides.

## Slide 9: In-Roadway Warning Lights
Notes: Key Message: In-roadway warning lights are being used at crosswalks to alert motorists to the presence of a pedestrian crossing or preparing to cross the street.
Est. Presentation Time: 1–3 minutes
Suggested Comments:
The amber light-emitting diode (LED) lights are embedded in the pavement on both sides of the crosswalk and oriented to face oncoming traffic. When the pedestrian activates the system, either by using a pushbutton or through detection from an automated device, the lights begin to flash at a constant rate, warning the motorist that a pedestrian is in the vicinity of the crosswalk ahead.
The amber LEDs flash in unison at a rate designed for maximum motorist recognition and are visible during the daylight as well as at night. The flashing lights are only activated when a pedestrian wants to cross and are automatically shut off after a set period of time, i.e., the time required for a pedestrian to safely cross the street. If installed in conjunction with the means to detect the presence of pedestrians while in the crosswalk, the crossing interval can be extended, in which case the lights would continue to flash and allow slower pedestrians to safely cross.
The slide shows two examples of crosswalks with in-roadway warning lights. The lights in the left picture are off and are more difficult to see; in the one on the right, you can note the presence of lights that are activated.

## Slide 10: Pedestrian Countdown Signals
Notes: Key Message: Pedestrian countdown signals are used in conjunction with conventional pedestrian signals to provide information to the pedestrian about the amount of time remaining to safely cross the street.
Est. Presentation Time: 1–3 minutes
Suggested Comments:
It is hypothesized that pedestrians will use this information to make better decisions about when to enter the crosswalk. Depending on user preference, the countdown timer starts either when the WALK/walking person indication appears or when the flashing DON’T WALK or flashing hand indication appears. The timer continues counting down through the flashing DON’T WALK (flashing hand) clearance interval. When the steady DON’T WALK or steady hand indication appears, the countdown signal will be at zero.

## Slide 11: Animated Eyes Display
Notes: Key Message: Animated eyes are intended for use at pedestrian crosswalks as an alternative to conventional pedestrian signals.
Est. Presentation Time: 1–3 minutes
Suggested Comments:
By including a prompt as part of the pedestrian signal, animated eyes displays are expected to encourage pedestrians to look for turning vehicles. The prompt is a pair of animated eyes that scan from side to side at the start of the WALK indication. Depending on user preference, the animated eyes can be illuminated separately from the standard pedestrian symbol (walking person) for the beginning of the WALK phase or illuminated concurrently with the standard symbol. The animated eyes can also be illuminated repeatedly at regular intervals throughout the WALK phase to prompt pedestrians who did not begin to cross at the start of the WALK phase.

## Slide 12: Detection Devices
Source: PBIC, www.pedbikeimages.org
Notes: Key Message: Microwave and infrared devices detect the presence of pedestrians near the intersection and assist them in crossing the roadway.
Est. Presentation Time: 1–3 minutes
Suggested Comments:
Microwave Detector
The microwave pedestrian detector provides the means to automatically detect the presence of pedestrians in the targeted curbside area and/or while moving in a designated crosswalk area. When used at the curbside area, it may either replace or augment the standard pushbutton used to activate the pedestrian call feature.
Infrared Detector
The passive infrared detector makes it possible to automatically detect the presence of pedestrians in either the targeted curbside area or within the crosswalk. When used to detect pedestrians in the crosswalk, its function is to detect the presence of individuals requiring additional time to cross and accordingly extend the clearance interval to provide more time to cross. These detectors function by sensing changes in thermal radiation caused by movement within the field of view, much like the motion detector that is used for home security. A pedestrian entering the target area causes such a temperature change to occur, which in turn, is detected by the sensor.

## Slide 13: Illuminated Pushbuttons
Source: PBIC, www.pedbikeimages.org
Notes: Key Message: The illuminated pushbutton is a simple technology designed to provide immediate feedback to the pedestrian that the button is working and that the signal will change.
Est. Presentation Time: 1–3 minutes
Suggested Comments:
Use of the illuminated button may reduce the number of pedestrians who cross against the signal because they have no indication that a standard pushbutton is working. The illuminated button may also result in fewer pedestrians pushing the button multiple times since there is now an immediate response from the light.

## Slide 14: Lesson Summary
Signing and marking are important for controlling and segregating motorized and nonmotorized traffic.
Appropriate pedestrian signing and marking improve the pedestrian way-finding system.
ITS devices may improve the safety and efficiency of pedestrian crossing treatments.
Notes: Key Message: Summarize the lesson and discuss any questions or issues with students.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Summarize the lesson and discuss any questions or issues with students.