## Slide 1: Pedestrian Design at Intersections
Lesson 11
Publication No. FHWA-HRT-05-106
Notes: Lesson #: 11
Lesson Title: Pedestrian Design at Intersections
Learning Objectives:
Upon completion of this lesson, students will be able to:
Describe the major issues related to safely accommodating pedestrians at intersections.
Explain when, why, and how to use crosswalks, curb ramps, crossing and detection technology, pedestrian half-signals, curb extensions, signal timing, pushbuttons, refuge islands and roundabouts.
Student Participation:
Use the activity provided in the Federal Highway Administration University Course on Bicycle and Pedestrian Transportation Student Workbook (Student Workbook).
Followup:
Assign reading for lesson 12.
Session Time: 45–60 minutes

## Slide 2: Lesson Outline
Intersection design principles.
Purpose and design of crosswalks, curb ramps, technology, half-signals, curb extensions, pushbuttons, refuge islands, and roundabouts.
Notes: Key Message: Provide the students with an overview of the lesson.
Est. Presentation Time: 1 minute
Suggested Comments:
This slide is optional.

## Slide 3: Intersection Design Principles
Encourage crossing at intersection corners.
Make pedestrians visible to traffic.
Make vehicular traffic visible to pedestrians.
Encourage predictable pedestrian actions.
Ease movement to street level.
Minimize crossing distance.
Slow vehicular traffic.
Notes: Key Message: These are the design principles that make for safe and effective pedestrian crossings.
Est. Presentation Time: 2 minutes
Suggested Comments:
Explain to students why each of these is important.

## Slide 4: Reduced Visibility
Notes: Key Message: Designers must place themselves in the pedestrians’ shoes to determine what creates the safest and most efficient environment for pedestrians and vehicle users.
Est. Presentation Time: 2 minutes
Suggested Comments:
Here is an example of reduced visibility for both the motor vehicles and pedestrians when the pedestrians are trying to cross the street. What treatments could be used be used in this situation—curb extension? removal of parking?

## Slide 5: Alternative Design
Notes: Key Message: Improve visibility of both the motorist and the pedestrian by using curb extensions.
Est. Presentation Time: 2 minutes
Suggested Comments:
This increases visibility for both pedestrian and motorist, and it reduces crossing time. However, this will reduced the throughput of right-turning vehicles.

## Slide 6: Use of Crosswalks
Purpose:
  Control pedestrian movements.
  Promote a connected pedestrian network.
  Improve visibility of a crossing place.
Design Issues:
  Location.
  Marking types.
  Lighting.
  Maintenance.
Notes: Key Message: Crosswalks encourage pedestrians to cross in certain locations and provide motorists with a reasonable expectation of where pedestrians will be found.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Important crosswalk concepts and issues include:
Creating reasonable expectations of where pedestrians may cross a roadway. A crosswalk creates a visible indication for both motorists and pedestrians of where pedestrians may be expected to cross a roadway.
Controlling pedestrian actions and movement. When combined with signalization (as well as curb extensions and refuge islands, where appropriate), crosswalks can help to control pedestrian movement and make them more routine and predictable.
Knowing when and where crosswalks are appropriate. As noted in the Oregon Bicycle and Pedestrian Plan, some studies have found that pedestrians may develop a false sense of security when crossing a road in marked crosswalks. Other studies have found that motorists are more likely to stop for pedestrians in marked crosswalks, especially where pedestrian right-of-way laws are enforced.
Deciding where crosswalks might be located. Generally, marked crosswalks are located at all open legs of signalized intersections. They may also be provided at other locations. By the use of curb extensions, signage, and illumination, the visibility of pedestrian crossings can be enhanced.

## Slide 7: Common Crosswalk Types
Notes: Key Message: Common types of crosswalk pavement markings
Est. Presentation Time: 2 minutes
Suggested Comments:
These different types of crosswalks have been used and can be more visible; but they may be harder to maintain due to the increased amount of paint exposed to traffic.

## Slide 8
Purpose:
  Provide access for wheelchair users, strollers, luggage, handcarts, etc.
Design issues:
  Location.
  Slopes.
  Flat landing area.
  Obstructions in or near the ramp.
  Width.
Use of Curb Ramps
Notes: Key Message: Ramps should be constructed according to Americans with Disabilities Act (ADA) guidelines.
Est. Presentation Time: 2 minutes
Suggested Comments:
Refer to lesson 8.6, “Design Requirements,” or lesson 9.3, “Basic Sidewalk Elements,” for more information about curb ramps.

## Slide 9: Curb Ramp Slopes
Notes: Key Message: Curb Ramp Slope and Dimension Requirements
Est. Presentation Time: 2 minutes
Suggested Comments:
Discuss the use of the:
Ramp width.
Ramp slope.
Flare slopes.
Landings.
Detectable warnings.

## Slide 10: Slope and Counter Slope
Notes: Key Message: Slope and counter slope dimensions for curb ramps are important elements of accessible sidewalk and street crossing design.
Est. Presentation Time: 2 minutes
Suggested Comments: No lip, gap, or joint should be present at the base of the ramp. Slope and counter slope must have an algebraic difference of less than 11%. If not, then a 2-foot level landing is required. Detectable warnings, ramp dimensions, etc., are covered in the previous slide.

## Slide 11
Purpose:
  Provide visibility to crossing.
  Encourage and assist pedestrian crossings.
Design issues:
  Which treatment to use (lighting, flags, green signs, flashing beacons, staggered pedestrian crossings, etc.) and where to use?
Use of Crossing and Detection Technology
Notes: Key Message: In some locations, simply installing a crosswalk is not enough to ensure pedestrian safety at a crossing. Therefore, several other treatments may be used in conjunction with crosswalks to improve safety and provide greater visibility of pedestrians to motorists.
Est. Presentation Time: 3 minutes
Suggested Comments:
Many possible solutions have already been discussed in previous chapters relating to walkways and crosswalks:
Pavement markings and signing (lessons 10.4 to 10.8).
In-pavement flashers (lesson 10.9, “Intelligent Transportation Systems Technology”).
Automated detection devices (lesson 10.9, “Intelligent Transportation Systems Technology”).
Street lighting (lesson 9.5, “Ambience, Shade, and Other Sidewalk Enhancements”).
Pavement surfaces and tactile ground surface indicators (lesson 9.3, “Basic Sidewalk Elements”).

## Slide 12: In-Roadway Warning Lights
Notes: Key Message: In-roadway warning lights can be used to improve the visibility of pedestrian crossings.
Est. Presentation Time: 2 minutes
Suggested Comments: Discuss the cost of installation and maintenance and the use of the warning lights at crossings with significant nighttime activity and/or poor visibility.

## Slide 13
Purpose:
  Assist pedestrian crossings on high-volume, unsignalized intersections along arterials.
Design issues:
  If delay > 30 seconds, pedestrians will cross on their own.
  Adjust timing for pedestrian walking speeds.
  Place pedestrian signal heads on channelized islands.
  Provide audible signals where necessary.
Use of Pedestrian Half-Signals
Notes: Key Message: Half-signals may assist pedestrians in crossing the street at high-volume, unsignalized intersections along arterials without causing excessive delay for vehicular traffic.
Est. Presentation Time: 2 minutes
Suggested Comments:
A half-signal is a pedestrian actuated traffic signal that stops arterial traffic only, leaving the lower-volume cross street unsignalized and controlled by STOP signs only. It allows pedestrians to cross safely upon demand without creating major delays on arterial street traffic that a fully signalized intersection might impose.

## Slide 14: Example of Half-Signal
Notes: Key Message: Pedestrian half-signals are beneficial in some cases
Est. Presentation Time: 2 minutes
Suggested Comments: Used on wide arterials with small cross streets and low traffic volumes.

## Slide 15: Use of Curb Extensions
Purpose:
  Shorten pedestrian crossing distance.
  Shorten pedestrian signal phase.
  Allow pedestrians to see the traffic better.
  Allow traffic to see the pedestrians.
Design issues:
  Corner radius length.
  How far to extend into the street?
Notes: Key Message: Curb extensions provide a variety of benefits for facilitating safer pedestrian crossings at intersections.
Est. Presentation Time: 2 minutes
Suggested Comments:
Curb extensions project into the street, usually for a distance equal to the depth of a typical parallel parking space, thereby making it easier for pedestrians to see approaching traffic and giving motorists a better view of pedestrians. When motorists are better able to see pedestrians, they have a greater opportunity to stop before a crash can occur.

## Slide 16: Use of Signal Timing and Pushbuttons
Purpose:
  Stop vehicular traffic and provide pedestrian crossing phase.
Design issues:
  Location (near ramps, in medians, etc.).
  Lights (like an elevator call button) to indicate actuation of the pushbutton.
  Quick response time to actuation.
  WALK/DON’T WALK signal phase timing.
Notes: Key Message: Pushbuttons and signal timings should be used in a way that is least confusing for the pedestrian and most accommodating for both drivers and pedestrians.
Est. Presentation Time: 2 minutes
Suggested Comments:
Develop policies governing pedestrian signal timing and pushbutton actuation to ensure fair treatment for pedestrians. Make signal timing as consistent as possible, and adopt a clear pedestrian pushbutton warrant. Develop a desired level of service for pedestrian waiting and pushbutton response times and evaluate signalized intersections to see if the pedestrian level of service at signalized intersection falls within an acceptable range.

## Slide 17: Pushbuttons
Source: PBIC, www.pedbikeimages.org
Notes: Key Message: Pushbuttons are used to actuate pedestrian crossing signals and should be accessible to all pedestrians.
Est. Presentation Time: 1–3 minutes
Suggested Comments:
Some individuals may have difficulty operating pedestrian pushbuttons. In some instances, there may be a need to install a larger pushbutton or to change the placement of the pushbutton. Pedestrian pushbuttons should always be easily accessible to individuals in wheelchairs, and should be no more than 1.2 m (48 inches) above the sidewalk (see figures in Student Workbook for reach restrictions) to be within the reach limits of wheelchair users. The force required to activate the pushbutton should be no greater than 2.3 kilograms (5 pounds).
Pedestrian pushbuttons should be located next to the sidewalk landing, at the top of the ramp, and adjacent to the appropriate crosswalk ramp. If there are two pushbuttons at a corner (one for each crosswalk), the pushbuttons should be located on separate poles and adjacent to their respective ramps.
The pictures on this slide show three different types of pushbuttons and their respective signs.

## Slide 18: Use of Pedestrian Refuge Islands
Purpose:
  Provide a safe resting/waiting area for pedestrians.
  Allow pedestrians to cross only one direction of traffic at a time.
Design issues:
  Accessible path through island.
  Offset crosswalks to orient crossing pedestrians to oncoming traffic.
  Minimum dimensions—1.8 meters (m) long by 3.7 m wide (12 feet (ft) long by 6 ft wide).
  Highly visible approach nose.
  Guide strips for the visually impaired.
Notes: Key Message: On certain types of roadways, pedestrian refuge islands can increase safety for pedestrians without causing additional delay for motorists.
Est. Presentation Time: 1 minute
Suggested Comments:
Pedestrian refuge islands are defined as the areas within an intersection or between lanes of traffic where pedestrians may safely wait until vehicular traffic clears, allowing them to cross a street. Refuge islands are commonly found along wide, multilane streets where adequate pedestrian crossing time could not be provided without adversely affecting the traffic flow. These islands provide a resting area for pedestrians, particularly those who are unable to completely cross an intersection within the provided signal time. These refuge islands also provide a safety area for pedestrians caught in the street when a signal changes.

## Slide 19: Use of Roundabouts
Purpose:
  Lower vehicular speeds.
  Reduce the number of conflict points.
  Shorten crossing distances and waiting times.
Design issues:
  Marked versus unmarked crosswalks.
  Accessibility for visually impaired pedestrians.
  Splitter islands.
  Discouraging pedestrians from crossing to the center island.
Notes: Key Message: Roundabouts are an alternative design for intersections that present several tradeoffs in pedestrian and bicyclist safety.
Est. Presentation Time: 2 minutes
Suggested Comments:
A modern roundabout is built with a large, often circular, raised island located at the intersection of an arterial street with one or more crossing roadways and may take the place of a traffic signal. Traffic maneuvers around the circle in a counterclockwise direction, and then turns onto the desired street. All traffic yields to motorists in the roundabout and left-turn movements are eliminated. Unlike a signalized intersection, vehicles generally flow and merge through the roundabout from each approaching street without having to stop.
Roundabouts need to accommodate pedestrians and bicyclists. It is important that automobile traffic yields to pedestrians crossing the roundabout. Splitter islands at the approaches slow vehicles and allow pedestrians to cross one traffic lane at a time. Single‑lane approaches can be designed to keep speeds down to safer levels and allow pedestrians to cross. Multilane approaches have higher speeds, create multiple threats for pedestrians, and are not recommended.
Visually impaired pedestrians may have some trouble making crossings on roundabouts approaches due to the fact that the audio cues of circulating traffic make it difficult for these pedestrians to determine a gap (on the exiting side of the roundabout).

## Slide 20: Conflict Points at Intersections
Notes: Key Message: The number of conflict points on a roundabout is less than on a traditional intersection.
Est. Presentation Time: 2 minutes
Suggested Comments: Splitter islands can be used as pedestrian refuge islands. Visually impaired pedestrians may have difficulty discerning the circulating traffic from the traffic exiting the roundabout. This makes it difficult to identify a gap.

## Slide 21: Lesson Summary
Pedestrians can be accommodated even at wide, high-volume intersections.
A wide variety of design elements exist to make good pedestrian design possible at intersections.
Notes: Key Message: Summarize the lesson and discuss any questions or issues with students.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Summarize the lesson and discuss any questions or issues with students.