## Slide 1: Midblock Crossings
Lesson 12
Publication No. FHWA-HRT-05-108
Notes: Lesson #: 12
Lesson Title: Midblock Crossings
Learning Objectives:
Upon completion of this lesson, students will be able to:
Describe problems associated with using midblock crossings.
Explain the advantages of using medians for midblock crossings.
Explain the design considerations for using medians for midblock crossings.
Describe where and under what circumstances midblock crossings should be allowed.
Preinstruction:
Ask the students if they can locate midblock crossings in your community. Ask the students if these crossing locations are appropriate. Have them think about other places, locally, where a midblock crossing might be useful.
Student Participation:
Use the activity provided in the Federal Highway Administration University Course on Bicycle and Pedestrian Transportation Student Workbook (Student Workbook).
Followup:
Assign reading for lesson 13.
Session Time: 45–60 minutes

## Slide 2: Lesson Outline
Pros and cons of midblock crossings.
Advantages of using medians with midblock crossings.
Design considerations for using medians with midblock crossings.
Where midblock crossings should be allowed.
Notes: Key Message: Provide the students with an overview of the lesson.
Est. Presentation Time: 1 minute
Suggested Comments:
This slide is optional.

## Slide 3: Where To Use Midblock Crossings
Long distances between intersections.
Churches.
Schools.
Hospitals.
High pedestrian activity locations.
Notes: Key Message: Midblock crossings should be used where needed most and should follow the MUTCD guidance (traffic control devices should command respect, fulfill a need, etc.)
Est. Presentation Time: 1 minute
Suggested Comments:
Review these types of locations and discuss why they might be good candidates for midblock crossings.

## Slide 4: Advantages of Using Medians
Allow more frequent gaps.
Reduce conflicts.
Concentrate pedestrians crossings in one central location.
Cost less to build and maintain.
Notes: Key Message: This list provides the advantages of using medians. By having to address only one direction of traffic at a time, the pedestrian can typically find more frequent gaps. Since the crossing is midblock, there are typically no left turns, so conflicts are reduced as well.
Est. Presentation Time: 3 minutes
Suggested Comments:
Many times midblock crossings are used because adjacent intersection crossings are inconvenient. They might also be used in conjunction with a special attraction or an area that has a high pedestrian demand such as parking garages across from buildings (sky walks might be another alternative).

## Slide 5: Potential Issues with Midblock Crossings
High-speed suburban roadways create challenging conflicts.
Motorist do not expect midblock crossings.
Motorist do not always yield at midblock crossings.
Notes: Key Message: There are some disadvantages in using midblock crossings as well.
Est. Presentation Time: 1 minute
Suggested Comments:
High-speed, wide suburban roadways are challenging because motorists (who are generally characterized by a desire for high levels of mobility) do not expect pedestrians or midblock crossings. Unless there is a very high pedestrian demand, motorists can sometimes be caught off-guard by midblock crossings.

## Slide 6: Uses of Midblock Crossings
Local roads.
Collector roads.
Arterials with four lanes.
Arterials with six or more lanes.
Notes: Key Message: Midblock crossings can be used on a variety of roadways, but each application may differ.
Est. Presentation Time: 3 minutes
Suggested Comments:
Local roads: Use only under special conditions (schools, shopping centers, etc.)
Collector roads: Channel pedestrians to central locations and use a series of refuge islands in these locations.
Arterials: Medians greatly improve the safety of the crossing; signalization is not recommended unless the following conditions are present (in these circumstances, signalization may be helpful or even essential):
      On higher-volume roadways.
      Where gaps are infrequent.
      In school zones.
      Where elderly or disabled pedestrians cross.
      Where speeds are high.
      When a number of other factors are present
Multilane Arterials (six + lanes): Signalization or signal coordination may be the only option to create a safe crossing location. Higher-profile markings such as zebra crossings and advanced pedestrian crossing markings can be used as well.

## Slide 7: Design Considerations for Using Medians
Connection of desired locations.
Lighting.
Use of same techniques as in lesson 10 (various crosswalk types, signs, signals and markings).
Staggered/offset crossings.
Detection.
Notes: Key Message: There are many considerations to making median crossings safe and accessible.
Est. Presentation Time: 1 minute
Suggested Comments:
Many of the techniques and technologies learned in lessons 10 and 11 are applicable to median crossings. Offset or staggered crossings force the pedestrian to face traffic, making them more aware of potential threats. Detection, in-pavement lights, and other devices can make midblock locations more visible to motorists, commanding their respect. The use of signs, signals, and markings are important design considerations for median and midblock crossings. Grade-separated crossings include skywalks from building to building and below- and above-grade crossings.

## Slide 8: Design Considerations for Using Medians
Curb extensions to reduce crossing distance.
Width:
  ­ 2.4 m (8 ft) desirable.
  ­ 0.6 m (2 ft) minimum.
Ramps may be needed.
Drainage.
Notes: Key Message: There are many considerations to making median crossings safe and accessible (continued from previous slide).
Est. Presentation Time: 3 minutes
Suggested Comments:
Many of the techniques and technologies learned in lessons 10 and 11 are applicable to median crossings. Curb extensions, ramps, and drainage design, as well as any potential issues should also be considered.

## Slide 9: Pedestrian Crossing Examples
Sources: Southeast Neighborhood Traffic Management Plan, Vancouver, WA, and
Bicycle Facilities Guide: Types of Bicycle Accommodations.
Notes: Key Message: Here are two examples of pedestrian crossings.
Est. Presentation Time: 1–2 minutes
Suggested Comments:
The first figure is a staggered or offset crossing and the second is a pedestrian underpass. There are also pedestrian overpasses, pedestrian bridges, and several other creative at-grade and grade-separated crossings.

## Slide 10: Lesson Summary
Midblock crossings can be an effective part of the overall pedestrian network.
Midblock crossings can be created by using simple designs and logical guidelines.
Notes: Key Message: Summarize the lesson and discuss any questions or issues with students.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Summarize the lesson and discuss any questions or issues with students.