## Slide 1: Bicycle Facility Maintenance
Lesson 16
Publication No. FHWA-HRT-05-116
Notes: Lesson #: 16
Lesson Title: Bicycle Facility Maintenance
Learning Objectives:
Upon completion of this lesson, students will be able to:
Understand the importance of bicycle facility maintenance.
Understand the objectives of bicycle facility maintenance.
Plan an implementation strategy to effect bicycle facility maintenance.
Identify typical maintenance problems and solutions.
Preinstruction:
Show a few examples (e.g., slides, videotape) of poorly maintained bicycle facilities.
Explain the types of problems bicycle riders might encounter because of the illustrated problems.
Student Participation:
Divide the students into small groups and have them compile a list of bicycle facility maintenance problems specific to your area/location.
Have the students propose solutions to the identified problems.
Followup:
Assign reading for lesson 17.
Ask the students to compile a list of types of local bicycle parking facilities.
Session Time: 15–20 minutes

## Slide 2: Lesson Outline
Maintenance objectives.
Typical process.
Common problems.
User feedback.
Notes: Key Message: Provide the students with an overview of the lesson.
Est. Presentation Time: 1 minute
Suggested Comments:
This slide is optional.

## Slide 3: Maintenance Objectives
Strive to keep facilities hazard-free.
Encourage reporting of hazards.
Design and build facilities with maintenance in mind.
Program for maintenance.
Notes: Key Message: Maintenance should be considered in planning and design and should attempt to keep facilities hazard-free.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Common maintenance includes:
• Sweeping pavement edges and paved shoulders with sufficient care.
• Patching surfaces as smoothly as possible and requiring other agencies or private companies to do likewise whenever they dig up a road or trail.
• Making sure pavement overlay projects feather the new surface into the existing one or otherwise do not create new linear joints.
• Replacing such hazards as dangerous grates or utility covers as the opportunity arises.
• Patching potholes in an expeditious manner.
• Routinely cutting back all encroaching vegetation, especially on trails or popular bike routes.
Bicyclists should be encouraged to report maintenance problems and hazards. This can be accomplished by developing a bicycle spot improvement form, distributing copies throughout the bicycling community, and then making sure returned forms are acted upon in a timely fashion.
Design and build new roadways and bikeways in such a way as to reduce the potential for accumulating debris.

## Slide 4: Implementation Planning
Identify implementers.
Review policies and practices.
Review results.
Recommend changes.
Create spot improvement program.
Evaluate the process.
Notes: Key Message: Bicycle facility maintenance can be implemented through several basic steps.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Describe these steps in more detail with the students (see section 16.5 in Federal Highway Administration University Course on Bicycle and Pedestrian Transportation Student Workbook (Student Workbook)).

## Slide 5: Typical Maintenance Problems
Surface problems:
  Debris, pavement quality, snow removal.
Vegetation:
  Encroaching vegetation (trees and grass).
Signing and marking:
  Uniform and usable condition.
Notes: Key Message: There are several typical maintenance problems experienced on bicycle facilities.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Describe these maintenance problems and then ask the students if they can think of any local examples where poor maintenance is an issue.

## Slide 6: Feedback from Users
Source: Vermont Bicycle & Pedestrian Coalition, http://www.vtbikeped.org
Notes: Key Message: Constructive feedback can be obtained from bicyclists.
Est. Presentation Time: 1 minute
Suggested Comments:
This slide shows an example of a postcard that can be distributed at bicycle shops and other public buildings where bicyclists are likely to be. Ask students to consider what the potential disadvantages of a postcard-reporting system might be (city may not be able to respond immediately or within expected timeframe).

## Slide 7: Lesson Summary
Maintenance is an important function.
Formulate program objectives.
Develop implementation plan.
Notes: Key Message: Summarize the lesson and discuss any questions or issues with students.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Summarize the lesson and discuss any questions or issues with students.