## Slide 1: Bicycle Parking and Storage
Lesson 17
Publication No. FHWA-HRT-05-118
Notes: Lesson #: 17
Lesson Title: Bicycle Parking and Storage
Learning Objectives:
Upon completion of this lesson, students will be able to:
Explain the objectives of bicycle parking.
Describe the strategies for implementing bicycle parking in a community.
Describe the desirable elements of bicycle parking racks and areas.
Preinstruction:
The students should describe examples of bicycle parking facilities with which they are familiar. The students should then consider whether these facilities are adequate in terms of: 1) design; 2) capacity; 3) security (are the facilities in open, well-lit areas?); 4) ease of use; 5) convenience.
Student Participation:
Have the students identify an area where bicycle parking is needed. Ask them to design bicycle parking for this location. Have them think about:
Number of spaces needed.
Type of parking.
Lighting.
Followup:
Assign reading for lesson 18.
Session Time: 35–55 minutes

## Slide 2: Lesson Outline
Bicycle parking objectives.
Types of bicycle parking.
Identifying priority locations.
Rack area and rack designs.
Bicycle parking ordinances.
Notes: Key Message: Provide the students with an overview of the lesson.
Est. Presentation Time: 1 minute
Suggested Comments:
This slide is optional.

## Slide 3: Bicycle Parking Objectives
Provide well-located, secure bicycle parking at popular bicycling destinations.
Require new commercial, public, and high-density residential developments to include bicycle parking.
Notes: Key Message: Describe the objectives of bicycle parking and emphasize that bicycle parking is an important supporting yet critical element in bicycle programs.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Bicycle parking and storage is often an afterthought or addressed on a case-by-case basis as requests come in from bicyclists. Bicycle parking should be considered an important element in a citywide bicycle program and should be addressed in bicycle plans. Bicycle parking should be a consideration at existing high-demand locations as well as new developments. Public agencies should provide bicycle parking in public spaces, but private developments should also be encouraged or required (through city ordinances) to provide bicycle parking facilities.

## Slide 4: Types of Bicycle Parking
Notes: Key Message: Describe the three types of bicycle parking and for which situations each device is best suited.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
These pictures show three basic types of bicycle parking or storage. Bicycle racks are generally less expensive but provide less security and protection from weather. Bicycle lockers are intermediate in price but provide good security and may be suitable for certain white-collar locations. Bicycle lock-ups are typically cage enclosures or retail stores (like the Bikestation®) that provide the most security and protection from weather elements.

## Slide 5: Implementation Strategy
Install parking on public property.
Encourage businesses to provide parking.
Change zoning regulations to ensure that parking is provided in new developments.
Notes: Key Message: Describe the basic implementation strategy, which focuses on the three listed activities.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
The implementation strategy includes provision of bicycle parking on both public and private property. Zoning regulations or city ordinances have been used in a variety of cities to require bicycle parking on private development. Where these requirements have not been enacted, private businesses should be encouraged to provide bicycle parking.

## Slide 6: Implementation Elements
Identify key implementers.
Structure the program.
Identify priority locations.
Choose appropriate parking devices.
Implement.
Evaluate.
Notes: Key Message: Describe the implementation approach for bicycle parking strategies.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
These are typical implementation elements for bicycle parking strategies.

## Slide 7: Identify Priority Locations
Visual observation.
User input.
Land-use criteria.
Visibility.
Security.
Lighting.
Ease of access and avoiding conflict.
Notes: Key Message: Priority locations for bicycle parking are most easily identified by visual observation (places where bikes are parked with or without racks), but other criteria can be considered.
Est. Presentation Time: 5–8 minutes
Suggested Comments:
The list on the slide can be used to help identify locations for bicycle parking. The first and most obvious way is to look at where people are currently parking their bicycles (although this may not be the most desirable location). Numerous other criteria can be used to identify locations. Discuss the criteria with students and ask them which criteria they think are most important and why.

## Slide 8: Rack Area Design
Source: APBP Bicycle Parking Guidelines, Spring 2002
Notes: Key Message: The design of the rack area should allow for ease of use and circulation of bicyclists.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Describe the rack area design dimensions and indicate that the aisle width should be wider in high-traffic areas.

## Slide 9: Recommended Rack Designs
Source: APBP Bicycle Parking Guidelines, Spring 2002
Notes: Key Message: Describe the features of recommended bicycle racks. Indicate that many racks now being used may not have the features listed here and should be replaced when opportunities arise.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Describe the features of recommended rack design: 1) supports frame in 2 places; 2) prevents wheel from tipping; 3) enables frame and wheel(s) to be secured; 4) supports nontraditional frame; 5) resists vandalism and theft. Indicate that these rack types are just samples of designs that ARE recommended, and that there are many other designs that have similar desirable features.

## Slide 10: Designs NOT Recommended
Source: APBP Bicycle Parking Guidelines, Spring 2002
“Wheel benders”
Notes: Key Message: Describe the undesirable features of these bicycle rack designs.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Indicate that these rack types are just samples of designs that ARE NOT recommended, and that there are many other designs that have similar undesirable features.

## Slide 11: Parking Ordinances
Number of spaces required.
Types of permitted rack designs.
Location of bicycle parking/racks.
Other elements:
  Lighting.
  Signing.
  Weather protection.
Notes: Key Message: Describe the typical elements of bicycle parking ordinances. Emphasize that this is the best way to ensure the long-term availability of bicycle parking. Give examples of bicycle parking ordinances as handouts.
Est. Presentation Time: 5–8 minutes
Suggested Comments:
Describe the typical elements of bicycle parking ordinances. Emphasize that this is the best way to ensure the long-term availability of bicycle parking. Give examples of bicycle parking ordinances as handouts (numerous are available on city websites).

## Slide 12: Lesson Summary
Bicycle parking is an important supporting element.
Bicycle parking should not just happen—it should be part of a larger implementation strategy.
Notes: Key Message: Summarize the lesson and discuss any questions or issues with students.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Summarize the lesson and discuss any questions or issues with students.