## Slide 1: Tort Liability and Risk Management
Lesson 22
Publication No. FHWA-HRT-05-128
Notes: Lesson #: 22
Lesson Title: Tort Liability and Risk Management
Learning Objectives:
Upon completion of this lesson, students will be able to:
Describe the significance of tort liability as it relates to bicycle and pedestrian facilities.
Define basic terms related to tort liability.
Describe the process of developing a risk management strategy.
Preinstruction:
Ask the class to present what they found in either newspapers or magazines relative to the assignment for this lesson. After an individual student describes a pedestrian or bicycle crash, have the class consider who or what contributed to the occurrence of the crash. Be sure to have them think about more than one of the parties involved (including the local transportation agency, if appropriate).
Student Participation:
Have the students design a risk management plan related to pedestrian and bicycling issues. Focus on some of the issues discussed in other lessons (e.g., planning, programming, and maintenance) to illustrate that risk management is integrated with these other activities.
Followup:
Assign reading for lesson 23.
Assign the exercise for lesson 22.
Session Time: 20–35 minutes

## Slide 2: Lesson Outline
Trends in tort liability.
Basic definitions.
Common problems/issues.
Risk management strategies.
Notes: Key Message: Provide the students with an overview of the lesson.
Est. Presentation Time: 1 minute
Suggested Comments:
This slide is optional.

## Slide 3: Trends in Tort Liability
State DOTs:
  80 lawsuits per year.
  7% settled against.
  $60,000 average settlement.
  Defense costs $68,000 per case.
City/County Agencies
  3 lawsuits per year.
  50% settled against.
  $230,000 average settlement.
  Defense costs $72,000 per case.
Notes: Key Message: According to this survey, the tort liability of State DOTs contrasts with that of typical city and county departments.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
These statistics are from a survey of 61 agencies published in the Urban Transportation Monitor. From this survey, it appears that State DOTs are minimizing their tort liability and paying much smaller settlements than most city or county agencies. This is despite the fact that they have more than 25 times as many lawsuits filed against them per year.

## Slide 4: Basic Definitions
Tort.
Negligence.
Ordinary care.
Immunity:
  Sovereign.
  Limited.
Notes: Key Message: Define the key terms related to tort liability.
Est. Presentation Time: 5–8 minutes
Suggested Comments:
A tort is defined as a wrongful act, not including breach of contract or trust, that results in injury to another person’s property or the like and for which the injured party is entitled to compensation. When an individual is harmed by another party without criminal intent, he or she may be able file a tort claim. The tort claim must be based on establishing that the party had a duty to perform relative to the injured individual and that this duty was not performed with ordinary care, in a reasonable and prudent manner.
To demonstrate design negligence, the plaintiff’s attorney must be able to answer these basic questions:
• Was there a potentially dangerous defect?
• Was a defect a proximate cause of the crash?
• Was there contributory negligence on the part of the bicyclist or pedestrian?
• Did the agency have knowledge that the condition existed? and
• Were the agency’s actions discretionary or ministerial?
Ordinary care is defined as the level of care that a reasonably experienced and prudent professional or other individual would have taken in the same or a similar event or action. Ordinary care is distinguished legally from extraordinary care, which parties are not expected to meet. Standards for separating ordinary from extraordinary are based on the expectation that 85 percent of travelers operate in a responsible manner (the 85th percentile rule).
Immunity is defined as legal protection from court settlements. Sovereign immunity indicates that an agency is not required to pay settlements. Partial immunity puts a cap on how much can be awarded or limits exposure to certain areas, such as maintenance and operations.

## Slide 5: Common Problems in Tort Claims
Drainage grates.
Path discontinuity.
Inadequate curve radii.
Surface problems.
Notes: Key Message: Public agencies should be especially aware of some common problems that show up in many tort liability claims.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Describe these common problems and why they might be considered a liability.

## Slide 6: Common Problems in Tort Claims
Lack of consideration for bicyclists and pedestrians.
Bridges and underpasses.
Poor sight distance.
Poor maintenance.
Notes: Key Message: Public agencies should be especially aware of some common problems that show up in many tort liability claims.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Describe these common problems and why they might be considered a liability.

## Slide 7: Risk Management
Use proactive strategy:
  Document existing conditions.
  Review conditions in context of ordinary care guidelines and standards.
  Develop recommendations.
  Set priorities for action.
Notes: Key Message: A proactive approach using risk-management techniques is the most effective way to deal with tort liability.
Est. Presentation Time: 5–8 minutes
Suggested Comments:
By developing a realistic assessment of the degree to which your agency may be exposed to potential liability problems, you will have taken an important first step toward developing a practical risk-reduction strategy. It is important that this assessment be systematic, that it be keyed to anticipate and counteract a wide range of legal actions, and that it involve all affected public and private parties. The basic steps are shown on the slide.

## Slide 8: Lesson Summary
Tort liability is an issue (as it is in all road design aspects).
The risk associated with providing pedestrian and bicycle facilities can be managed.
A plan of prudent design, operations, and maintenance will help to manage the risk.
Notes: Key Message: Summarize the lesson and discuss any questions or issues with students.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Summarize the lesson and discuss any questions or issues with students.