## Slide 1: Traditional Neighborhood Design
Publication No. FHWA-HRT-05-096
Lesson 6

## Slide 2: Lesson Outline
What is traditional neighborhood design?
How does traditional neighborhood design encourage bicycling and walking?
What are the different elements of traditional neighborhood design?
Notes: Lesson #: 6
Lesson Title: Traditional Neighborhood Design
Learning Objectives:
Upon completion of this lesson, students will be able to:
Describe how traditional neighborhood design differs from other styles of suburban neighborhood design.
List the basic elements of traditional neighborhood design.
Preinstruction:
To contrast with the motivational activity of the last lesson, take the class for a walk through an older neighborhood or other equally pedestrian-friendly location in your area that has elements of traditional neighborhood design. If there is a new urbanist development in your area, take a field trip with the class, and critique its successful and unsuccessful features, in terms of pedestrian and/or bicycle travel.
Student Participation:
Have the students sketch out a completely new development using traditional neighborhood design concepts.
Followup:
Assign reading for lesson 7.
Provide the students with a copy of the local planning or zoning ordinance. Have them look for the sections relevant to nonmotorized transportation.
Session Time: 45–55 minutes

## Slide 3: Elements of Traditional Neighborhood Design
Basic street layout.
Use of alleys.
Street design speed.
Street width.
Curb radii.
Intersection geometry.
Notes: Key Message: Traditional neighborhood street design differs from standard suburban street design.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Explain the basic elements of traditional neighborhood street design, and how it is different from standard suburban street design. The slides that follow illustrate these concepts.
Discuss the current debate about traditional neighborhood design with students (see pages 6-1 and 6-2 in the Federal Highway Administration University Course on Bicycle and Pedestrian Transportation Student Workbook (Student Workbook)). Discuss the advantages and disadvantages of traditional neighborhood design. Point to local examples (if possible), and discuss what has and has not been accomplished in these developments.

## Slide 4: Elements of Traditional Neighborhood Design
Street trees and landscaping.
Street lighting.
Sidewalk width and location.
Building setbacks.
Parking.
Notes: Key Message: Traditional neighborhood street design differs from standard suburban street design.
Est. Presentation Time: 2 minutes
Suggested Comments:
Explain the basic elements of traditional neighborhood street design and how it is different from standard suburban street design. The slides that follow illustrate these concepts.

## Slide 5: Suburban Design
Source: ENR, May 9, 1994.
Notes: Key Message: There are significant differences between the layout of new urbanist developments versus standard suburban residential design.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Standard suburban street design is characterized by a hierarchical, tree-like pattern that proceeds from cul-de-sacs and local streets to collectors to wide arterials. The organization of the network collects and channels trips to higher capacity facilities. Automobiles are the most convenient choice for short, as well as long, trips.
By contrast, traditional neighborhood design calls for an interconnected network of streets and sidewalks to disperse vehicular trips and to make human-powered modes of travel (such as walking and biking) practical, safe, and attractive for short trips.

## Slide 6: Kentlands, MD
Notes: Key Message: Good street design makes walking and bicycling more convenient and comfortable.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Discuss the elements of the street design in this photograph that make the pedestrian environment more comfortable.

## Slide 7: Seaside, FL
Source: Alex McLean
Notes: Key Message: This is an example of a traditional neighborhood layout.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
This is an aerial view of Seaside, FL, which was the first new urbanist development in the United States. Development began in 1981 on this 80-acre site.
Describe how the street layout in this aerial photograph supports walking and bicycling.

## Slide 8: Celebration, FL
Notes: Key Message: Celebration, FL, is another example of traditional neighborhood design.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Celebration began development in the mid-1990s and has become one of the most well known among the hundreds of traditional neighborhood developments that have been built in the United States. At right are two views of the same street, one from the perspective of the motorist, and one from the perspective of the pedestrian.

## Slide 9: Celebration, FL
Notes: Key Message: Views of Celebration’s commercial center
Est. Presentation Time: 3–5 minutes
Suggested Comments:
These are views of the commercial center of Celebration.

## Slide 10: Lesson Summary
When done correctly, traditional neighborhood design encourages bicycling and walking.
There are many design elements that constitute a traditional neighborhood.
There are several other benefits besides those for bicycling and walking.
Notes: Key Message: Summarize the lesson and discuss any questions or issues with students.
Est. Presentation Time: 3–5 minutes
Suggested Comments:
Summarize the lesson and discuss any questions or issues with students.