## Slide 1
Introduction to Transportation Engineering Modules
Class 1: Planning for Pedestrians and Bicycles
Notes: Slides were developed by Carl Sundstrom, Daniel Rodriguez, and Laura Sandt of the University of North Carolina, with input from Rod Turochy and Jeff LaMondia at Auburn University. Funding was provided by the Southeastern Transportation Research, Innovation, Development and Education Center (STRIDE) as well as by the Pedestrian and Bicycle Information Center (PBIC). These slides were updated in 2015 by Carl Sundstrom and Kristen Brookshire.
Instructor Note: A few slides are “hidden” from the presentation. This information may still be relevant for your course, but these slides may be cut out for time.
Image source:
Photo (left): Tiffany Robinson http://www.pedbikeimages.org/pubdetail.cfm?picid=1848
Photo (right): Laura Sandt http://www.pedbikeimages.org/pubdetail.cfm?picid=1674

## Slide 2
Learning Objectives
Understand the motivations to plan for pedestrians and bicyclists
Identify the land use policies that affect our transportation choices
Understand plans as policy tools
Recognize challenges to plan development and implementation
Become familiar with useful strategies to address challenges

## Slide 3
Motivations to plan for pedestrians and bicyclists
The relationship between land use and transportation
Interaction between pedestrian and bike planning and other planning processes
Today’s Class

## Slide 4
History
Pre-1908
  Primary mode
1950s-1990s
  “Forgotten” mode
1990s-Present
  Resurgence in planning & design for ped/bike users
Muller, 2004
Notes: Speaker notes:
Cities and roads were designed at a walking/bicycle/transit scale before the rise of the automobile. During the 1950s-1990s, land development became much more auto-oriented with a development pattern that required the use of the automobile for nearly all trips. Roads were designed to move motor vehicles as quickly and efficiently as possible, often without any sort of provision for other modes. This trend is seeing some reversal as we see an increased interested in walkable neighborhoods and having transportation options.
References:
Muller, P. O. (2004). Transportation and Urban Form: Stages in the Spatial Evolution of the American Metropolis. Geography of Urban Transportation. Guilford Press: New York.

## Slide 5
What motivates us now to
plan and design for
pedestrians and bicyclists?
Notes: This is a transition slide

## Slide 6
25% increase in reported ped/bike trips from 2001 to 2009
Increases in walking and bicycling mode share
Chart: Percent of Daily Trips
| 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009
Bicycle | 0.008 | 0.007 | 0.009 | 0.009 | 0.01
Walk | 0.085 | 0.072 | 0.054 | 0.086 | 0.109
1. User Demand
Notes: Speaker notes:
The first motivation for planning for pedestrians and bicyclists is that the number of trips taken by walking and biking has been increasing over the past decade. Biking and walking make up 11.9% of trips in the U.S., which is a 25% increase compared to the last survey conducted in 2001 (National Household Travel Survey, 2009). The increase in demand for walking and bicycling leads to greater demand for infrastructure that supports those modes. While we have access to more recent numbers for the walking and biking commute mode share through the American Community Survey, but the 2009 NHTS is the most recent national survey of travel patterns for all trip purposes.
Reference:
The League of American Bicyclists. (2010). National Household Travel Survey 2009 Highlights. Accessed April 2, 2013 from http://www.bikeleague.org/resources/reports/pdfs/nhts09.pdf

## Slide 7
1. User Demand (cont’d): Big Cities on the Rise
Cities with higher rates of growth in the metro area compared to suburban area:
Berg, N., 2012
Notes: Note to Instructors: this slide may be cut for time. The next slide (#8) uses newer data, but is presented differently.
Speaker notes:
Recent estimates from the U.S. Census show significant population increases in the largest U.S. cities in the U.S. These cities are growing more quickly than the United States as a whole. Growth in cities can lead to greater density and greater demand for amenities within walking or biking distance.
References:
Berg, N. (2012). Big Cities on the Rise. The Atlantic Cities. June 28, 2012. Accessed April 2, 2013 from http://www.theatlanticcities.com/neighborhoods/2012/06/big-cities-rise/2406/
Image source:
Berg, N. (2012). Urban vs. Suburban Growth in U.S. Metros. The Atlantic Cities. June 29, 2012. Accessed April 2, 2013 from http://www.theatlanticcities.com/neighborhoods/2012/06/urban-or-suburban-growth-us-metros/2419/

## Slide 8
1. User Demand (cont’d): Big City Growth
Population growth in primary cities continues to outpace suburban growth
Frey, A. H., 2014
Notes: Speaker notes:
Recent estimates (through July 2013) from the U.S. Census Bureau show significant population increases in the largest U.S. cities (i.e. cities over 250,000 population). And as you can see on this graph, growth in primary cities is outpacing the growth in surrounding suburbs. These data affirm a reversal that counters decades of suburban-dominated regional growth among metro areas with more than 1 million people. Growth in cities can lead to greater density and greater demand for amenities within walking or biking distance.
References:
Frey, W. H. (2014). Will this be the decade of big city growth? Brookings Institution. May 23, 2014. Accessed June 8, 2015 from http://www.brookings.edu/research/opinions/2014/05/23-decade-of-big-city-growth-frey
Image source:
Same as above

## Slide 9
1. User Demand (cont’d): Bike Commuter Rates
League of American Bicyclists, n.d.
Notes: Speaker notes:
Each year the advocacy group, League of American Bicyclists, designates communities as “Bicycle Friendly.” Since 2000, bicycle commuting rates in large Bicycle Friendly Communities have increased 80%, while the national average has increased 47%. This graphic shows data from the decennial Census and the American Community Survey (ACS).
References:
League of American Bicyclists (n.d.). Infographic: Bicycle Friendly Community bike commuter rates grow faster. Accessed June 5, 2015 from http://www.bikeleague.org/reports
Image source:
Same as above

## Slide 10
1. User Demand (cont’d)
Not everyone can drive:
People younger than 16
People with some disabilities
Older adults
  A growing population
Greater interest in active lifestyles as a means of lowering risk of chronic diseases
Notes: Speaker notes:
There are many groups of people who can’t drive: people younger than 16, people with certain disabilities, and older adults. In fact, as Baby Boomers age, the percentage of older adults will nearly double from 12% of the population in 2000 to 21% of the population in 2050, increasing the population of people who will desire mobility but might not be able to drive. In addition, many people are becoming interested in active lifestyles that can help them lower their risk of chronic diseases.
References:
Shrestha, L. B. “The Changing Demographic Profile of the United States.” Congressional Research Service Report for Congress, May 5, 2006, pg. CRS-14. Available at: http://www.fas.org/sgp/crs/misc/RL32701.pdf.
Image source:
Top: http://www.pedbikeimages.org/pubdetail.cfm?picid=1055
Bottom: http://www.just5.com/story.php?story=6102011212803898410323&page=blog

## Slide 11
2. Safety Concerns
Ped/bike crashes account for nearly 15% of motor-vehicle crashes
Injury prevention is a top priority at the national, state, and local levels
Pedestrian and Bicycle Information Center using NHTSA FARS data
Chart: Pedestrians and Bicyclists Killed by Year
| 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
Pedestrians | 5449 | 5321 | 5228 | 4939 | 4763 | 4901 | 4851 | 4774 | 4675 | 4892 | 4795 | 4699 | 4414 | 4109 | 4302 | 4457 | 4818 | 4735
Bicyclists | 765 | 814 | 760 | 754 | 693 | 732 | 665 | 629 | 727 | 786 | 772 | 701 | 718 | 628 | 623 | 682 | 734 | 743
Notes: Speaker notes:
Even though biking and walking accounted for 11.9% of trips in the United States (The League of American Bicyclists, 2010), pedestrian and bicyclist crashes represent nearly 15 percent of motor vehicle collisions. The U.S. Department of Transportation has identified safety as its #1 priority, which is shared by State and local agencies looking for ways to reduce the number of transportation-related injuries.
References:
National Highway Traffic Safety Administration (2015). Traffic Safety Facts 2013. Accessed June 8, 2015. Available: http://www-nrd.nhtsa.dot.gov/Pubs/812139.pdf
U.S. Department of Transportation. Safer People, Safer Streets: Pedestrian and Bicycle Safety Initiative. More info: http://www.transportation.gov/policy-initiatives/ped-bike-safety/safer-people-safer-streets-pedestrian-and-bicycle-safety
Image source:
Pedestrian and Bicycle Information Center.

## Slide 12
2. Safety Concerns (cont’d)
Absolute numbers of ped/bike fatalities have been decreasing, but their share of all traffic fatalities has increased.
Alliance for Biking and Walking
Notes: Speaker notes:
While the absolute number of ped/bike fatalities and the fatality rate (fatalities per million population) have been decreasing, they haven’t been decreasing at the same rate as overall traffic fatalities. Thus, ped/bike fatalities make up a disproportionate share of traffic fatalities. This problem is especially pronounced in large U.S. cities.
References:
Alliance for Biking & Walking. 2014 Benchmarking Report. Available: http://www.bikewalkalliance.org/resources/benchmarking
Image source:
Alliance for Biking & Walking. 2014 Benchmarking Report. Available: http://www.bikewalkalliance.org/resources/benchmarking

## Slide 13
2. Safety Concerns (cont’d): Toward Zero Deaths
Eliminating fatalities and serious injuries for all road users
Employs a combination of engineering, enforcement, education, and emergency services (the 4 Es)
Evaluation is also important
Institutionalized at state or jurisdiction level
Also called “Vision Zero”
Notes: Speaker notes:
This focus on safety has translated into a National Strategy on Highway Safety called Toward Zero Deaths, which is supported by U.S. DOT and the American Association of State Highway and Transportation Officials (AASHTO). Rather than accepting a certain number of crashes as unavoidable, a TZD approach commits us to work across sectors and use every tool available to systematically analyze and work toward eliminating traffic crashes among all who use the roadways. The TZD approach targets areas for improvement and employs proven countermeasures, integrating the application of education, enforcement, engineering, and emergency medical and trauma services (the "4Es"). Some transportation agencies also refer to this comprehensive approach as “Vision Zero” or “Target Zero”
State example: Washington
City examples: San Francisco, Seattle, New York City, Washington DC
Image source:
From program websites
More Information:
http://safety.fhwa.dot.gov/tzd/
http://www.towardzerodeaths.org/home.php
https://www.transportation.gov/fastlane/tzd

## Slide 14
3. Liability
1990: Americans with Disabilities Act (ADA)
Self evaluation and Transition Plan
Some jurisdictions have been sued by disability advocates to bring them into compliance with the law
Notes: Speaker notes:
According to the Americans with Disabilities Act (or ADA) of 1990, recipients of federal funding are required to make transportation infrastructure, such as sidewalks, curb ramps, and signals, accessible and usable for all Americans. An ADA Transition Plan is required for agencies with more than 50 employees. Self-evaluation identifies barriers in the public rights-of-way (sidewalks, curbs, etc.). The Transition Plan takes that inventory, prioritizes improvements, and creates a schedule for implementation. Responsible party and cost information area also important elements of a Transition Plan.
Example of a lawsuit in Los Angeles (2015): http://www.latimes.com/local/lanow/la-me-ln-lawsuit-broken-sidewalks-20150331-story.html#page=1
References:
Federal Highway Administration. (2000). FHWA/FTA Memorandum: Announcement of USDOT Accessibility Regulations. Accessed April 2, 2013 from http://www.fhwa.dot.gov/environment/bicycle_pedestrian/guidance/accessibility_guidance/atl.cfm
Image source:
http://www.smartgrowthamerica.org/2009/10/21/topeka-misses-the-point/ Photo: Thad Allton, Topeka Capital-Journal.

## Slide 15
4. Health Concerns
Research:
Links sedentary lifestyles to negative health outcomes
Shows health benefits of providing ped/bike facilities
Centers for Disease Control and Prevention, 2004
Notes: Speaker notes:
In recent years, the health community has become more engaged in transportation issues, due to mounting evidence regarding the relationship between health and active transportation. More research is linking active transportation (such as walking and bicycling and transit use) with improved health, and also showing the flip side of the coin: car-oriented environments with highly sedentary populations are associated with a range of negative health outcomes such as diabetes, heart disease, and depression.
References:
Mokdad, A. H., Marks, J. S., Stroup, D. F., & J.L. Gerberding. (2004). Actual causes of death in the United States, 2000. JAMA: The Journal of the American Medical Association, 291(10), 1238-1245.
Image source:
Centers for Disease Control and Prevention. (2004). Fact Sheet: Physical Inactivity and Poor Nutrition Catching Up to Tobacco as Actual Cause of Death. http://www.cdc.gov/media/pressrel/fs040309.htm
Further reading:
Saelens, B.E., Moudon, A.V., Kang B., Hurvitz, P.M., & Zhou, C. (2014) Relation between higher physical activity and public transit use. American Journal of Public Health, Vol. 104, No. 5, pp. 854-859. doi: 10.2105/AJPH.2013.301696
Freeland, A.L., Banerjee, S.N., Dannenberg, A.L., & A.M. Wendel. (2013). Walking associated with public transit: moving toward increased physical activity in the United States. Am. J. Public Health. ePub. http://goo.gl/kT6d7 or http://ajph.aphapublications.org/doi/abs/10.2105/AJPH.2012.300912
Sandt, L., Pullen-Seufert, N., LaJeunesse, S., & D. Gelinne. (2012, May-June). Leveraging the health benefits of active transportation: Creating an actionable agenda for transportation professionals. TR News Magazine. Available: http://onlinepubs.trb.org/onlinepubs/trnews/trnews280.pdf
Frank, L.D., Sallis, J.F., Conway, T.L., Chapman, J.E., Saelens, B.E., & W. Bachman. (2006). Many pathways from land use to health: Associations between neighborhood walkability and active transportation, body mass index, and air quality. Journal of the American Planning Association. Vol 72 (1). DOI: 10.1080/01944360608976725
Federal Highway Administration maintains a Health in Transportation webpage that includes annual reports, available: http://www.fhwa.dot.gov/planning/health_in_transportation/
Walk It Out: Urban Design Plays Key Role in Creating Healthy Cities: http://www.sciencedaily.com/releases/2013/03/130307124427.htm

## Slide 16
4. Health (cont’d): Obesity Trends* Among U.S. Adults
(*BMI 30, or about 30 lbs. overweight for 5’4” person)
2000
2010
1990
No Data <10% 10%–14% 15%–19% 20%–24% 25%–29% ≥30%
Centers for Disease Control and Prevention, 2011
Notes: Speaker notes: These maps from the CDC show the percentage of people in each state with a body mass index of 30 or higher, which indicates obesity. As you can see, from 1990-2010, the percentage of obese Americans has increased dramatically throughout the country. While the factors that affect obesity rates are complex and include both nutrition and physical activity, it’s clear that work to support physical activity through providing opportunities for active transportation is a much-needed part of the solution.
References:
Obesity Trends Among U.S. Adults in Behavioral Risk Factor Surveillance System Survey Data from 1990, 2000, and 2010 from the Centers for Disease Control and Prevention. (2011). Arch Pediatr Adolesc Med, Vol. 165, No. 11.
Image source:
Obesity Trends Among U.S. Adults in Behavioral Risk Factor Surveillance System Survey Data from 1990, 2000, and 2010 from the Centers for Disease Control and Prevention. (2011). Arch Pediatr Adolesc Med, Vol. 165, No. 11.
Further reading:
Buehler, R., Pucher, J., Merom, D., & Bauman, A. (2011). Active travel in German and the USA: Contributions of daily walking and cycling to physical activity. American Journal or Preventive Medicine, Vol. 40 (9) pp. 241-250.

## Slide 17
5. Equity
Enhancing the ability of traditionally underserved populations to travel by non-motorized modes can:
  potentially lead to improved outcomes in public health, safety, and economic development;
  promote resource efficiency;
  strengthen inclusive neighborhood relations; and
  bolster public transit services
Notes: Speaker notes:
Lots of planning/engineering practices can be viewed through an equity framework, including project prioritization and investment, goal-setting, public input processes, and roadway design. Internal hiring and communication processes should also be evaluated to ensure cultural sensitivity. Data can be used to help identify equity-related needs/assets and communicate effectively.
Traditionally underserved populations include persons or communities that are low income, minority, elderly, may have limited English proficiency, and/or have a disability.
References:
Sandt, L., Combs, T., & Cohn, J. (2015). The 6th “E”: Pursuing equity in pedestrian and bicycle planning. Pedestrian and Bicycle Information Center. Available: http://www.pedbikeinfo.org/data/whitepapers.cfm
Image source:
Top: pedbikeimages.com / Dan Burden
Bottom: pedbikeimages.org / Dan Burden
Further reading:
LAB. The new majority: pedaling towards equity [Internet]. League of American Bicyclists; 2013. Available from: http://www.bikeleague.org/sites/lab.huang.radicaldesigns.org/files/equity_report.pdf

## Slide 18
6. Environmental Concerns
Air quality: Transportation is responsible for nearly 80% of CO and 55% of NO emissions in U.S.
Water quality: Storm water runoff is a major contributor to non-point-source water pollution
Notes: Speaker notes:
Transportation accounts for nearly 80% of the carbon monoxide and 55% of nitrous oxide that is produced in the United States. These pollutants lead to contamination of air and water supplies, which endangers human health. Replacing vehicle trips with zero-emissions bike and walking trips has the benefit of reducing greenhouse gases and water pollution.
Image source:
http://www.singlespeedgoldcoast.com/2012/06/car-travel-unhealthy.html
Further reading:
Mindell, J.S., Cohen, J.M., Watkins, S., & Tyler, N. (2011). Synergies between low carbon and healthy transport policies. Proceedings of the Institution of Civil Engineers – Transport. 164:127-39.
Article in the LA Times: http://goo.gl/QZwvo. Researchers in Europe have found that poor air quality associated with busy roads is correlated with higher rates of asthma in children. The study, which examined children’s health in 10 cities, concluded that 14% of chronic childhood asthma cases could be attributed to near-road traffic pollution.

## Slide 19
7. System Efficiency
Renewed focus on moving people, not vehicles
Ped/bike modes support transit systems
  E.g., bike share systems gaining traction in the U.S.
Notes: Speaker notes:
With DOTs and public works departments facing large budget shortfalls, we have to be smarter and more efficient with our transportation investments. This picture speaks volumes about the efficiency of moving people in ways other than single vehicle use.
Bike sharing is gaining popularity across the U.S. and system efficiency is among one of the many reasons a city might identify for starting a bike share system. Bike sharing may help with mode shift, but it also broadens the catchment area for transit service when bike share stations are located near transit stops and stations.
References:
City of Muenster Planning Office, 2001.
Image source:
City of Muenster Planning Office, 2001.

## Slide 20
7. System Efficiency (cont’d): Complete Streets
Pedestrians, bicyclists, motorists, and transit riders of all ages and abilities are able to safely move along and across a Complete Street.
Institutionalized through a resolution, ordinance, plan, and/or design guide.
Notes: Note to Instructors: you can cover this quickly if you will also be teaching Class 2, which introduces the concept of Complete Streets from the design perspective.
Speaker notes:
A more efficient system also means that people have choices about what mode of transportation they’d like to use. Complete Streets is a concept that has been gaining momentum in the U.S. over the past decade.
Complete Streets ensure that the entire right-of-way is planned, designed, constructed, operated, and maintained to provide safe access for all users.
A Complete Street will be different for every city and can differ within the same city, so there is not one cross section that should be applied uniformly.
Many agencies or jurisdictions start by adopting a resolution or policy that demonstrates support the concept, then implement this by creating and ordinance and updating their design guides.
More information:
Smart Growth America, National Complete Streets Coalition: http://www.smartgrowthamerica.org/complete-streets

## Slide 21
8. System Redundancy
National Geographic
Notes: Speaker notes:
Disaster preparedness and emergency management are not often talked about routinely in the field of transportation, but when large-scale disaster events do occur, traffic quickly becomes gridlocked and walking or bicycling is often the only option available. Similarly, some cities may use paths and trails for emergency access when roads are blocked due to weather or other extreme events.
Image source: http://news.nationalgeographic.com/news/2011/09/pictures/110908-about-911-september-9-11-twin-world-trade-center-towers-indelible/#/september-9-11-attacks-anniversary-ground-zero-world-trade-center-pentagon-flight-93-running-bridge_39996_600x450.jpg

## Slide 22
9. Return on Investment
Commerce and tourism
Property values, particularly near trails
Economic competitiveness
  Some benefits are difficult to measure
Flusche, 2012
Notes: Speaker notes:
  Various studies provide evidence of the high return on investment that ped/bike facilities offer. Many of these studies are done at the State-level or at the project-level in a city.
  As for measurement, impact on retail sales, property value and stability might be easier to measure and assign to ped/bike traffic or projects. Other impacts we might be interested in can be harder to measure (e.g., jobs, congestion, tourism).
Image source:
Flusche, D. (2012). Bicycling Means Business: The Economic Benefits of Bicycle Infrastructure. League of American Bicyclists http://www.advocacyadvance.org/site_images/content/Final_Econ_Update%28small%29.pdf
Further reading:
  Simmons, E., Kay, M., Ingles, A., Khurana, M., Sulmon, M., & Lyons, W. (2015). Evaluating the economic benefits of nonmotorized transportation: Case studies and methods for the Nonmotorized Transportation Pilot Program communities. John A. Volpe National Transportation Research Center for U.S. DOT FHWA. Available: http://www.pedbikeinfo.org/cms/downloads/NTPP_Economic_Benefits_White_Paper.pdf
  New York City Department of Transportation. The economic benefits of sustainable streets. Available: http://www.nyc.gov/html/dot/downloads/pdf/dot-economic-benefits-of-sustainable-streets.pdf
  Alliance for Biking & Walking. (2014). 2014 Benchmarking Report. See Chapter 4. Available: http://www.bikewalkalliance.org/resources/benchmarking
  PedalMN Video shows how bicycling is being promoted to support the tourism industry: http://www.youtube.com/watch?feature=player_embedded&v=ffACiRWM33U
  http://www.advocacyadvance.org/site_images/content/Final_Econ_Update%28small%29.pdf

## Slide 23
What is the interaction between
land use and transportation?
Notes: This is a transition slide

## Slide 24
Why Do We Have Cities?
To minimize travel & maximize exchange (to be closer together)
Notes: This slide is animated.
Speaker notes:
The next two slides are intended to point out an irony: humans congregated in cities to minimize their need for travel.
References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.
Image source: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 25
How Have We Built Our Urban Roadway System?
To facilitate travel over longer distances
Notes: This slide is animated.
Speaker notes:
Since World War 2, we have made it possible to travel more quickly over longer distances. This has led to larger, but less livable, cities. Despite our ability to travel more quickly than before, we spend more time in transport nowadays than our grandparents did.
References: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.
Image source: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 26
Land Uses and Walking
The accessibility and intensity of certain non-residential land uses, along with land-use diversity, are positively associated with walking for transportation.
A careful mix of land uses in a neighborhood can encourage physical activity.
McConville, et al. 2011
Notes: Speaker notes:
Dense development is associated with higher levels of walking and transit use and reduced automobile dependency (Ewing, nd). Compact , mixed-use development is fundamental to making communities walkable because it increases the number of origins and destinations that are within walking distance of one another (Leinberger, 2007; Saelens & Handy, 2008). Proximity to schools and retail, commercial, and municipal uses can encourage walking. Additionally, large numbers of pedestrians tend to attract more walkers because they indicate the vitality of an area and can create a secure walking environment with more eyes on the street. High densities, walking, and transit use reinforce one another: higher residential and employment densities mean that more riders will live or work within a quarter mile of a transit stop; high ridership levels can improve transit service; and transit riders typically start their trip on foot, so high ridership levels likely indicate high pedestrian levels.
References:
McConville, M. E., Rodríguez, D. A., Clifton, K., Cho, G., & Fleischhacker, S. (2011). Disaggregate land uses and walking. American Journal of Preventive Medicine, 40(1), 25-32.

## Slide 27
Land Use and Walking
Walking is most strongly related to:
  land use diversity
  intersection density
  # of destinations within walking distance
Bus and train use are related to
  proximity to transit
  street network design variables
  land use diversity (secondary factor)
  Ewing and Cervero, 2010
Notes: Speaker notes:
Travel variables are generally inelastic with respect to change in measures of the built environment. The combined effect on travel of several environmental variables on travel could be quite large. Population and job densities to be only weakly associated with travel behavior.
References:
Ewing, R., & Cervero, R. (2010). Travel and the built environment: A meta-analysis. Journal of the American Planning Association, 76(3), 265-294.

## Slide 28
The Evolution of Neighborhood Street Patterns
Frank, L., Kavage, S., & Litman, T., 2006
Notes: Speaker notes:
This slide shows the historical trends in neighborhood street pattern. Over time the development pattern connectivity decreased. This also shows how the suburban development patterns have reduced the linear feet of streets necessary to develop an area, which results in less impervious surface and lowers the cost of construction.
References:
Frank, L., Kavage, S., & Litman, T. (2006). Promoting public health through smart growth. Vancouver, BC: SmartGrowthBC. Available at http://www.smartgrowth.bc.ca
Image source:
Frank, L., Kavage, S., & Litman, T. (2006). Promoting public health through smart growth. Vancouver, BC: SmartGrowthBC. Available at http://www.smartgrowth.bc.ca

## Slide 29
Increasing Connectivity
Can you increase connectivity with paths & greenways?
  Reduces walking distances: YES
  Offers more route choices: YES
  Disperses traffic: NO
Notes: This slide is animated.
Speaker notes:
The question often arises: what about connecting cul-de-sacs with paths, won’t that have the same result? The answer is yes and no: it will make it possible to walk to destinations, but it won’t reduce traffic on the busy streets, creating dangerous and unpleasant walking environments.
References: FHWA/PBIC, Planning and Designing for Pedestrian Safety Course, 2009
Image source: FHWA/PBIC, Planning and Designing for Pedestrian Safety Course, 2009

## Slide 30
Lack of connectivity => few but large intersections
Notes: Speaker notes:
Large intersections are required to handle the traffic volumes created on arterials from a lack of connectivity.
References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.
Image source:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 31
Access Management
Every driveway is a potential conflict
Notes: Speaker notes:
Pedestrians face potential conflicts at driveways. Pedestrians and drivers alike hesitate at these conflict points and must make choices: Walk in front or in back? Pull forward or back up?
References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.
Image source:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 32
Access Management Reduces Conflicts at Driveways
(1)
(2)
Notes: This slide is animated.
Speaker notes:
Reducing the number of driveways means fewer conflicts. Two techniques are: (1) median (reduces left turns) (2) consolidate driveways. Both of these techniques improve the walking environment.
Student question: If you could choose only one of these two techniques (median or consolidate driveways), which would have more of a crash reduction factor?
Answer: the raised median, as left turns dominate in all crash types: car/car, car/bicyclist, and car/pedestrian.
References: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.
Image source: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 33
Reinventing the roadway:
Transform a 5-lane commercial strip to …
Notes: Speaker notes:
This slide illustrates a typical 5-lane commercially developed strip street, with very few incentives to walk.
References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.
Image source:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 34
…a safer road for everyone
What changed?
What didn’t change?
Notes: This slide is animated.
Speaker notes:
Student question: What is different?
Answer: separated sidewalks, bike lanes, consolidated IMPROVED access, underground utilities, raised median, narrower travel lanes. All beneficial to driver safety. What has not changed is the same number of lanes (4 through lanes) and no change in ROW and adjacent land use. This is an important point, most of this class will focus on what changes can be made within the right-of-way.
References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.
Image source:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 35
ROW design standards (Complete Streets approach?) and maintenance policies
Site design requirements and review process
Municipal code
  Mixed-use zones
  Form-based code
  Density bonuses
  Connectivity standards
  Streetscape amenities
  Parking requirements (design, location, amount)
Policies and Ordinances
Notes: Speaker notes:
All of the policies listed on the slide can positively or negatively affect the safety and comfort of pedestrian and bicyclists.
Note to Instructor:
Depending on time and student knowledge, you could ask how each of these policies may affect the built environment.
Example topics:
Design standards – sidewalk width, travel lane width, sidewalk buffer, bicycle facility consideration. How are broken sidewalks and curb ramps repaired? Is there a policy for snow removal?
Site design – pedestrian circulation, parking lot location, driveway access
Mixed-use zones – these can encourage density. Is an active use (i.e., commercial, retail) required for the ground floor?
Form-based code – can be applied to a corridor, neighborhood, or entire city. These regulate the form, scale, and massing of buildings rather than the use. Can encourage a more inviting, pleasant environment for pedestrians.
Density bonuses – Developers are allowed to build more density in exchange for providing something the city needs (affordable housing units, pedestrian amenities, green stormwater treatment, etc.)
Connectivity standards – how do cul-de-sacs and block lengths affect pedestrians and bicyclists (and drivers too)?
Streetscape amenities – when and where does the city require public restrooms, benches, trash receptacles, trees, etc.?
Parking requirements – do parking minimums create an oversupply of parking spaces? Are surface parking lots required to be at the rear of a building? What about pedestrian circulation and landscaping within a surface lot? Is shared parking allowed for mixed-use and other land uses that have different peak parking demand?
Further Reading:
Hou, N., Popkin, B. M., Jacobs, D. R., Jr., Song, Y., Guilkey, D., Lewis, C. E., et al. (2010). Longitudinal associations between neighborhood-level street network with walking, bicycling, and jogging: the CARDIA study. Health & Place, 16(6), 1206-1215.
Saelens, B.E. & Handy, S.L. (2008). Built environment correlates of walking: A review. Medicine & Science in Sports & Exercise, 40(7S), S550-S556. Available: http://www.ncbi.nlm.nih.gov/pubmed/18562973
Manville, M. & Shoup, D. (Fall 2004). People, parking, and cities. Access Magazine. No. 25. University of California, Los Angeles. Available: http://shoup.bol.ucla.edu/People,Parking,Cities.pdf
Weinberger, R., Kaehny, J., & Rufo, M. (2014). U.S. parking policies: An overview of management strategies. Institute for Transportation and Development Policy. Available: https://www.itdp.org/wp-content/uploads/2014/07/ITDP_US_Parking_Report.pdf

## Slide 36
What are the steps in the bicycle and pedestrian planning process?
Notes: This is a transition slide

## Slide 37
1. Develop Vision, Goals, and Objectives
Vision:
  “Washington DC will be a city where any trip can be taken on foot safely and comfortably, and where roadways equally serve pedestrians, bicyclists, transit users, and motorists”
Goals:
  “Reduce number of pedestrians killed”
Objectives:
  “Provide accessible, safe, and well maintained pedestrian facilities along and across all streets”
Solicit community input
Notes: This slide is animated.
Speaker notes:
What is the difference between a vision, goals, and objectives? What are some example of visions? Goals? Objectives?
Why is it important to have these in the plan?
Establishes values
Establishes priorities
Can establish benchmarks, against which we can show progress within the political process.
By having short-, medium-, and long-term goals, the plan can navigate the political cycle.
Further Reading:
Roughton, C., van Hengel, D., Duncan, A., Weigand, L., & Birk, M. (2012). Creating Walkable & Bikeable Communities: A user guide to developing pedestrian and bicycle master plans. Initiative for Bicycle and Pedestrian Innovation. Center for Transportation Studies, Portland State University.
Available: http://ppms.otrec.us/media/project_files/IBPI%20Master%20Plan%20Handbook%20FINAL.pdf

## Slide 38
2. Build an Information Base
Public and professional participation provides information about:
  Existing conditions
    Mode share
    Crash data
    Facility inventory
    Relevant laws
    Programs
Relevant plans
Maps and analyses
Priority corridors
Notes: Speaker notes:
Question for students: What are some possible elements of the information base that are not listed?
Demographics
Activity centers (attractors/generators)
Planned bicycle/pedestrian facilities
The facility inventory could include roadway characteristics and transit stops, not just sidewalks and bike facilities.
The plan’s goals and objectives might require additional data collection.
Remember that a plan is a policy tool – help educate decision-makers about key issues
Image Source:
www.pedbikeimages.org – Dan Burden

## Slide 39
3. Plan Actions/Recommendations
Policies
Infrastructure
Programs/projects
  Education
  Enforcement
  Encouragement
Show connection to goals/objectives
Tie to existing conditions
Notes: Speaker notes:
May want to include all these elements but set priorities: short, medium, and long term actions.
Short term: focus on easy, low-hanging fruit – quick things supported by the community, such as bike parking, sharrows, safety around school zones
Medium term: programs that take longer to develop – district-wide child safety curriculum, engineering improvements
Long term: more costly or controversial projects
Actions/recommendations should be specific, and time-bound. Ideally, you develop evaluation criteria to assess potential actions.
Priorities should reflect the goals/objectives and take into account existing conditions – we’ll talk more about prioritization in the data analysis lecture.

## Slide 40
4. Implementation
Accountability
Funding
Evaluation
Updating
Notes: Speaker notes:
The plan needs to have an implementation section. This section should describe:
  Who is accountable for implementation
  What funding sources support the plan
  How will the plan be evaluated
  When will the plan be updated
Once the plan is completed, there needs to be a strategy for implementing and evaluating the plan on an on-going basis. This includes accountability, political will, and stakeholder involvement. Getting the plan officially adopted will lend some legitimacy to the document. Accountability strategies need to be implemented right away, and planners and stakeholders should provide updates whenever any action is taken.
Preparing for implementation will involve many steps. One important aspect, however, is creating an environment of routine accommodation of pedestrian and bicycle planning. This idea is covered in depth in another lecture, “23 Ways to Fund Bicycle and Pedestrian Programs: Implementation through Institutionalization.“
Routine accommodation – know your repaving schedule – usually set 1-4 years in advance
The last point on this slide is a critical one, though it is frequently overlooked in the plan-making process. There must be a system in place to determine accountability and responsibility for different aspects of the plan. Creating a system for evaluation and plan updates can help communities determine if they are making any progress towards the goals of the plan and what needs to be amended or updated in order to do so.

## Slide 41
How do bicycle & pedestrian plans interact with other plans & policies?
Notes: This is a transition slide

## Slide 42
Topical Overlap Between Ped-Bike Plans and Other Plans/Policies/Tools
Transportation Plan
Zoning
Parks & Rec Plan
Land use plan
Non-plan
transportation
policies
Greenways Plan
Health Impact Assessment
NEPA
Development
Impact Assessment
Ped-Bike Plans
Notes: Speaker notes:
The middle of this slide shows elements of a plan – the motivation, development, and implementation of the plan. The elements depicted in circles surrounding the plan indicate some areas that should be checked for horizontal coordination with the plan. The overlap between these circles shows that there is some commonality amongst the various elements. We will use this diagram as a guide for discussing some of the connection between these tools, policies, and plans
References:
Adapted from: Aytur, S., Evenson, K., Rodriguez, D., & Salvesen, D. (2008). A framework for understanding pedestrian plan quality and its impacts. Unpublished presentation. Chapel Hill, NC.
Image source:
Adapted from: Aytur, S., Evenson, K., Rodriguez, D., & Salvesen, D. (2008). A framework for understanding pedestrian plan quality and its impacts. Unpublished presentation. Chapel Hill, NC.

## Slide 43
Impact Assessment
National Environmental Policy Act (NEPA)
  Health & safety of community members
  For projects involving federal dollars
  Replicated with State acts, like CA (CEQA)
Development impact assessment
  Utility impacts
  Traffic impacts
  Fiscal impacts
Notes: Speaker notes:
NEPA and development impact assessments are two ways that communities and states can find opportunities to improve pedestrian and bicycle facilities. NEPA requires that projects that are federally funded must complete environmental impact statements (EIS) describing the potential environmental effects that project may have. Non-motorized travel options, which can support human and environmental health, should be considered in EIS. Development impact assessments can also require considerations of a project’s effects on the walking environment.
Jurisdictions commonly require a Traffic Impact Assessment (TIA) for new developments and major redevelopments. Historically, these impact assessments have focused on the generation of automobile traffic and their impact on intersection LOS. However, the TIA presents a good opportunity for a multi-modal review. Jurisdictions could require that the project area map include greenway, sidewalk, bicycle, crossing facilities, and transit access on the proposed site and surrounding area. Counts and summaries of impacts should also include pedestrians and bicyclists.
References:
Adapted from: Aytur, S., Evenson, K., Rodriguez, D., & Salvesen, D. (2008). A framework for understanding pedestrian plan quality and its impacts. Unpublished presentation. Chapel Hill, NC.
Image source:
Adapted from: Aytur, S., Evenson, K., Rodriguez, D., & Salvesen, D. (2008). A framework for understanding pedestrian plan quality and its impacts. Unpublished presentation. Chapel Hill, NC.

## Slide 44
Health Impact Assessment
Population-level health effects
Steps
  Screen
  Scope
  Baseline
  Methodology to identify impacts & direction
  Findings
http://www.sfhealthequity.org/resources/hia-tools
Notes: Speaker notes:
Health impact assessments have been developed to try to address health issues that are not being adequately considered through development impact assessments or NEPA requirements. HIAs are excellent tools for bicycle and pedestrian planners because they can help show ways that bicycle and pedestrian planning can positively impact health. The San Francisco Department of Public Heath has developed a useful tool for conducting health impact assessments. (Right click on this link to access information about that tool.)
The methods used to make predictive judgments on health outcomes have varied. In some cases quantitative measures of health status and environmental conditions were used to describe existing conditions, providing general evidence of priorities and needs. Most HIA reports included an assessor’s judgment of the direction of the health impact (i.e., positive or negative), but not necessarily the magnitude.
The Healthy Development Measurement Tool includes a structured approach that evaluates land-use development plans and projects on over 100 community-level indicators of health, using objective development criteria as surrogates for improvements in health.
In one recent evaluation of HIAs, researchers categorized the results of HIAs as: (1) directly affecting the decision being made, (2) not affecting the decision but raising awareness of health issues, (3) having little impact because the decision was already favorable to health, and (4) being ignored or dismissed by the decision-makers.
For current stats and examples, check out the UCLA HIA clearinghouse: http://www.hiaguide.org/
Further reading:
Pedestrian and Bicycle Information Center. (2013). Using Health Impact Assessments to Evaluate Bicycle and Pedestrian Plans. White Paper. Available: http://www.pedbikeinfo.org/cms/downloads/WhitePaper_HIA_PBIC.pdf
Dannenberg, A. L., Bhatia, R., Cole, B. L., Heaton, S. K., Feldman, J. D., & Rutt, C. D. (2008). Use of health impact assessment in the U.S.: 27 case studies, 1999-2007. American Journal of Preventive Medicine, 34(3), 241-256.
San Francisco Department of Public Health. (2009). Healthy development measurement tool. Available at http://www.sfphes.org/enchia/enchia_HDMT.htm
San Francisco Department of Public Health. (2007). Eastern Neighborhoods Community Health Impact Assessment: Final Report. Available at
http://www.sfdph.org/phes/enchia.htm
Wismar, M., Blau, J, Ernst K., Figueras, J. (2007). The effectiveness of health impact assessment: Scope and limitations of supporting decision-making in Europe. Brussels: European Observatory on Health Systems and Policies. Available at http://www.euro.who.int/InformationSources/Publications/Catalogue/20071015_1.

## Slide 45
Transportation Plan
Regional document outlining transportation priorities
  Short-term (improvement program) and long range transportation plan
  Some citizen participation
    Heavier participation is project specific, as part of NEPA
  Indirect participation via MPO boards
Notes: Speaker notes:
Transportation plans don’t typically conform to a preconceived notion of a plan. Rather, the transportation plan embodies the rational planning approach. There is some public participation involved in the development of the plan. Most of the participation happens indirectly through representation on MPO boards, which are composed of elected officials in municipalities and counties. The concern here is that the needs of the community, particularly small communities, may not always rise as a top priority in a regional transportation plan. Despite the fact that there is so little public participation, transportation plans are critical documents as they describe the transportation projects for the next 25 to 30 years.

## Slide 46
Broad Types of Travel Demand Management
Often, the aim is to reduce congestion
  Enhancing modal choice
  Providing specific incentives for behavioral changes (timing, mode choice, etc)
  Substituting trips
 At the project level: substitute capacity expansion with “management of demand”
Notes: Note to instructors: this slide may be cut for time.
Speaker notes:
The aim of TDM programs is usually to reduce congestion, though TDM programs can provide many other benefits, such as positive health and environmental impacts. TDM can be supplied by enhancing mode choices and providing incentives. The ultimate idea is to substitute one mode for another. Significantly, TDM personnel are frequently not transportation professionals. Rather, they are marketing professionals working in the field of transportation. Many TDM people do not understand how planning works, but are amenable to learning about planning for transportation.
References:
Ferguson, E. (2000). Travel demand management and public policy. Aldershot, UK: Ashgate Publishing.
Meyer, M. D. (1999). Demand management as an element of transportation policy: Using carrots and sticks to influence travel behavior. Transportation Research Record A, 33(7/8), 575-599.
Image source:
Further reading:

## Slide 47
Greenways/Trails Plans
Access to facilities such as walking trails has a positive correlation with physical activity
People with access to parks are almost twice as likely to be physically active.
Notes: Speaker notes:
People with access to trails and parks tend to be significantly more active than those who do not.
References:
Active Living by Design. Available at http://www.activelivingbydesign.org/
Brownson, R.C., Bake, E.A., Housemann, R.A., & Bacak, S.J. (2001). Environmental determinants of physical activity in the United States. American Journal of Public Health, 91(12).
Image source: http://www.pedbikeimages.org / Laura Sandt. Photo taken in Lehighton, Pennsylvania

## Slide 48
Class Summary
There are many reasons to focus on pedestrians and bicyclists in the transportation network
Land use policies can greatly affect our transportation choices
Plans may be used as policy tools and should are not done in a vacuum
  Linked to many other plans and policies