## Slide 1
Introduction to Transportation Engineering Modules
Class 2: Pedestrian and Bicycle Facility Design
Notes: Slides were developed by Carl Sundstrom, Daniel Rodriguez, and Laura Sandt of the University of North Carolina, with input from Rod Turochy and Jeff LaMondia at Auburn University. Funding was provided by the Southeastern Transportation Research, Innovation, Development and Education Center (STRIDE) as well as by the Pedestrian and Bicycle Information Center (PBIC). These slides were updated in 2015 by Carl Sundstrom and Kristen Brookshire.
Image source:
Photo (left): Tiffany Robinson http://www.pedbikeimages.org/pubdetail.cfm?picid=1848
Photo (right): Laura Sandt http://www.pedbikeimages.org/pubdetail.cfm?picid=1674

## Slide 2
Learning Objectives
By the end of this class, students will be able to:
Give reasons for designing for pedestrian and bicycle use
Understand how the streetscape influences design
Give examples of roadway design for pedestrians and bicyclists
Give examples of intersection design for pedestrians and bicyclists
Identify opportunities to retrofit existing streets for pedestrian and bicycle use

## Slide 3
Designing streets for all users
Street hierarchy
Roadway segments
  Intersections
  Midblock crossings
Retrofitting streets
Today’s Class

## Slide 4
Complete Streets
Complete Streets are designed and operated to enable safe access for all users:
Pedestrians
Bicyclists
Motorists
Transit riders
People of all ages and abilities must be able to safely move along and across a Complete Street.
Notes: Speaker notes:
Complete Streets are streets that are designed to enable safe access for all users, including pedestrians, bicyclists, motorists and transit riders of all ages and abilities. Complete Streets design makes it easy to cross the street, walk to shops, and bicycle to work. They allow buses to run on time and make it safe for people to walk to and from train stations. There is no singular design prescription for Complete Streets; each one is unique and responds to its community context. A complete street may include: sidewalks, bike lanes (or wide paved shoulders), special bus lanes, comfortable and accessible public transportation stops, frequent and safe crossing opportunities, median islands, accessible pedestrian signals, curb extensions, narrower travel lanes, roundabouts, and more. A Complete Street in a rural area will look quite different from a Complete Street in a highly urban area, but both are designed to balance safety and convenience for everyone using the road.
References:
National Complete Streets Coalition & Boston Complete Streets Guidelines http://www.smartgrowthamerica.org/complete-streets/complete-streets-fundamentals/complete-streets-faq
Image source:
Top: www.pedbikeimages.org / Andy Hamilton
Bottom: National Complete Streets Coalition & Boston Complete Streets Guidelines

## Slide 5
Street Hierarchy
  Interstate
  Other Freeway/Expressway
  Other Principal Arterial
  Minor Arterial
  Major Collector
  Minor Collector
  Local
Traditional functional classification as used by most State DOTs:
(more ped/bike oriented)
(more auto/truck oriented)
Notes: Note to instructors: This slide could be skipped to save time as the hierarchy isn’t referenced again within the presentation.
Speaker notes:
This is the typical AASHTO Green Book hierarchy used by most State DOTs. Unlike the street types on the following slide, this street classification rarely takes land use and context into account.
Image source and references:
http://www.fhwa.dot.gov/environment/flex/ch03.htm

## Slide 6
Street Hierarchy
Walkable thoroughfare types
Serve a mix of modes
  Boulevard
  Avenue
  Street
Institute of Transportation Engineers “Designing Walkable Urban Thoroughfares: A Context Sensitive Approach”
Notes: Note to instructors: You can refer to these classifications/types when introducing design elements later in this presentation (i.e. describe which type each belongs to).
Speaker notes:
These street types represent a spectrum from pedestrian- to auto-oriented, but each street type can (and should) include design elements to improve safety and operation for bicyclists, pedestrians, and transit users. Street design decisions and land use decisions should complement one. Rural roads cover different street types as they are often the only connections between towns and should serve a variety of users.
Image Source and References:
Institute of Transportation Engineers “Designing Walkable Urban Thoroughfares: A Context Sensitive Approach”

## Slide 7
Design Principles
Due to the nature of Complete Streets, there are often competing interests between the different users. To design for pedestrian and bicyclist safety and comfort, the following design principles should be considered:
Safety
Conflicts
Predictability
Visibility
Separation
Delay
Accessibility
Notes: Speaker notes:
Safety – Slower speeds and geometric design (medians, shorter crossing distances) should be used to improve safety for all modes
Conflicts - Minimize conflicts at intersections through signal timing and phasing (protected lefts, leading pedestrian intervals), markings and signs, and geometric design.
Predictability - Consistent and careful design to ensure predictable movements, particularly for bicyclists at intersections and driveways and pedestrians at midblock locations.
Visibility – Curb extensions, lighting, pavement markings may all be used
Separation - Greater separation of modes as speeds and/or volumes increase (buffered bike lanes, separated bike lanes, etc.)
Delay – Reduced delay at crossings will yield improved and safer behaviors. Shorter block lengths and improved bicycle and pedestrian networks will reduce travel time.
Accessibility – Design all roads and crossings to meet ADA standards. This good design benefits all users.
Image source:
www.pedbikeimages.org / Dan Burden

## Slide 8
Roadway Design for Pedestrians & Bicyclists
Roadway segments
Intersections
Midblock crossings
Notes: Speaker notes:
This is a reiteration of the Complete Street design approach to designing the right-of-way. Not all streets will have each of these separate elements, but the street design should safely accommodate all travel modes. The upcoming slides will go into further detail on each of these zones.
Image source:
Carl Sundstrom

## Slide 9
Roadway Segments: Sidewalk Corridors
The sidewalk corridor is divided into 4 zones:
Curb zone
Furniture/green zone
  6-8 ft.
Pedestrian zone
  10-20 ft. urban/suburban main streets
  6-10 ft. suburban boulevards
Frontage zone
FHWA, 2001
Notes: Speaker notes:
This slide introduced the zone system, which describes one way to think about and design sidewalks.
To prevent the problems created by narrow curbside sidewalks, designers should consider the sidewalk the entire area that extends from the property line to the curb line. Furthermore, the pedestrian corridor should be separated into four distinct zones to prevent the various functions of the sidewalk from being in conflict. The four zones are:
    Curb zone
    Planter/furniture zone – used to provide a buffer to moving traffic, a place for landscaping, newspaper boxes, and other amenities like street furniture and bike racks
    Pedestrian/walking zone – this is sidewalk area that is kept clear of obstructions (café tables, signs, etc.) and the width is determined by pedestrian traffic
    Frontage zone – this zone provides shy distance from the wall and allows for space for door openings and places to stand without obstructing the sidewalk
References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.
Image source:
http://www.pedbikeimages.org/Dan Burden

## Slide 10
Roadway Segments: Sidewalks and Driveways
Intersection-style driveway…
…redesigned to slow down traffic
Notes: Speaker notes:
Anywhere where a driveway crosses a sidewalk, the pedestrian has the right of way. However, the design of the crossing area influences motorist behavior. If the driveway is designed like an intersection, this can discourage yielding and encourage high turning out speeds. Making it clear that the driver is crossing over a sidewalk increases driver awareness of pedestrian and slows down motorist speeds, which can lead to fewer and less severe crashes. Notice that in the second picture, the separated sidewalk keeps the pedestrian zone of the sidewalk level at the driveway. This can be helped by having a green/buffer zone so that there sidewalk is not at the back of curb where the driveway slope is.
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 11
Roadway Segments: Parking
Parallel
  Width: 8-10 ft.
Angled
  Reverse angled preferred
Notes: Speaker notes:
Prohibiting parking close to intersections and driveways improves sight distance and safety. Curb extensions (also known as bulb outs) can be provided to keep the intersections clear. Reverse-angle parking is preferred over the traditional pull-in angle parking for several reasons. It improves the site distance for cars pulling back into the travel lane and it directs people to the sidewalk rather than the roadway based on how car doors open.
Image source:
http://www.flickr.com/photos/chasqui/2996943823/sizes/o/in/photostream/

## Slide 12
Street Design - Segments
Bicycle facilities
Shared roadway
Bike lanes
Notes: Note to instructors: This slide may be cut to save time. It simply introduces concepts that will be described more fully in the coming slides.
Image: Carl Sundstrom

## Slide 13
Roadway Segment Bicycle Facilities:
Shared Roadway
Shoulders (Rural)
Rumble strips must be carefully installed so not to pose a safety problem to bicyclists
Allow for a min 4’ wide shoulder beyond the rumble strip
Provide periodic gaps in the rumble strips
Notes: Speaker notes:
There are two types of bicycle facilities (1) shared roadways (frequently on lower speed and volume roads or rural roads) and (2) bike lanes or paths. In rural areas, rumble strips are often provided for the safety benefits to motorists. However, they can pose a safety problem to bicyclists due to their width taking up the space off the roadway where bicyclist could travel and their depth that can lead to crashes and flat tires. Thus, careful design, especially on routes where bicycle travel is expected (such as scenic routes, routes connecting towns, and designated bike routes), is important.
AASHTO’s Guide for Bicycle Facilities, 4th Ed., recommends that there is at least four feet of clear space on the shoulder beyond the rumble strips. Additionally, periodic gaps should be provided to allow bicycles to move across the rumble strips as needed. Narrowing the rumble strip widths and reducing the depth may also be beneficial.
Image Source and References:
www.pedbikeimages.org - Bob Boyce

## Slide 14
Shared lane markings
Assist with lane positioning
Alert motorists to presence of bicyclists
Reduce wrong-way riding
Share the Road signs
Increase awareness of bicyclists
Roadway Segment Bicycle Facilities:
Shared Roadway
Notes: Speaker notes:
Shared Lane Markings (“Sharrows”) are bicycle marking symbols that use chevrons to indicate where in the roadway and the direction bicyclists are supposed to travel. These markings have many benefits including the following:
Indicating to bicyclists where to ride on streets with on-street parking to be sufficiently clear of the door zone
Connecting gaps in the bicycle network at locations where there is insufficient space on the road to provide bike lanes
Reducing the incidence of wrong-way riding on roads with only enough width to provide one bike lane - typically, this bike lane will be provided in the uphill, “climbing” lane with shared lane markings placed in the downhill direction
Providing a reminder to motorists to expect bicyclists and that they are allowed use of the roadway
Image Source and References:
Images from http://www.pedbikeimages.org/Carl Sundstrom.

## Slide 15
Roadway Segment Bicycle Facilities: Bike Lanes
Recommended width: 5’
Width should be increased when adjacent to on-street parking and on higher-speed roadways
AASHTO Guide for the Development of Bicycle Facilities, 4th Ed.
Notes: Speaker notes:
On-street bicycle lanes are recommended to be 5-6’ wide from the face of a curb to the bike lane stripe. Bicycle lanes wider than 6’ are not recommended without special markings as motorists may view them as travel lanes. When on-street parking is present adjacent to bicycle lanes, the minimum lane width is 5’ (6’ recommended) to encourage bicycles to ride outside the ‘door zone’. Painting a 2’ “buffer” between parked cars and the bike lane is another way to improve the safety of bike lanes adjacent to parking. The buffers could also be provided between the bike lane and travel lane on higher volume and speed roadways to improve the comfort and safety of the bike lanes.
On one-way streets, bicycle lanes should be installed on the right-hand side, unless conflicts can be greatly reduced by installing the lane on the left-hand side. Left-side bicycle lanes on one-way streets may also be considered where there are frequent bus or trolley stops, unusually high numbers of right-turning motor vehicles, or if there is a significant number of left-turning bicyclists.
Image Source and References:
Federal Highway Administration. (2006). University course on bicycle and pedestrian transportation: Bicycle lanes. (Publication No. FHWA-HRT-05-113). McLean, VA: Federal Highway Administration. Available at http://www.pedbikeinfo.org/collateral/lessons/Lesson15.pdf

## Slide 16
Roadway Segment Bicycle Facilities: Bike Lanes
Other on-road designs
Contraflow lanes
Buffered bike lanes
Separated Bike Lane
Notes: Speaker notes:
Contraflow:
A number of communities have created short segments of contraflow bike lanes in order to provide bicyclists unique access to residential streets. For example, the cities of Madison and Portland have both used this technique to open up a network of routes on residential streets that are not accessible in both directions both motor vehicle--essentially creating a very short stretch of roadway that is two-way for bikes but only one-way for cars.
Buffered:
Provide more bicyclist comfort
Provides more maneuvering space to avoid obstacles
Can be placed on roads with high…
  speeds or volumes
  parking turning over
  volume of heavy vehicles
Separated:
Separated bike lanes are also sometimes called “cycle tracks” or “protected bike lanes.” Separated bike lanes can operate as one-way or two-way facilities; their designs can integrate with turning automobile traffic at intersections or can be more fully separated; they can be designed at roadway grade, at sidewalk grade or at an intermediate grade; and they can be separated from the adjacent roadway or sidewalk with a variety of treatments including but not limited to on-street parking, raised curbs or medians, bollards, landscaping, or planters.
Other cases:
In some cases of high volume, high speed, and considerable truck traffic conditions, on-street bicycle facilities don’t provide an adequate level of accommodation. Additionally, in gateway approaches to special trip attractors such as elementary schools, on-street facilities are not adequate. In some of these cases, alternatives such as sidepaths should be considered--but very carefully. Sidepath bicycle facilities must be very carefully designed at the roadway and driveway intersections to ensure the safety of its users.
Further Reading
FHWA Separated Bike Lane Planning and Design Guide (2015)
http://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/separated_bikelane_pdg/

## Slide 17
Roadway Segment Design: Americans with Disabilities Act (ADA) Considerations
A good sidewalk is essential to meet ADA requirements:
Sidewalk surface must be smooth
Sidewalk have a clear minimum width of 36 inches
Sidewalk must be clear of obstructions
Driveways cannot slope more than 2 percent
Not every possible design can be anticipated in standards
Notes: Speaker notes:
While people in wheelchairs are visible, ADA covers disabilities that have no outward manifestations. By designing for people with disabilities, we are designing for everyone, especially as we get older. Updated and revised in 2004, the Americans with Disabilities Act (ADA) and the Architectural Barriers Act (ABA) Accessibility Guidelines for Buildings and Facilities state that walking surfaces should have a clear width minimum of 36 inches. This clear width minimum is the minimum width for passage and not a sidewalk width recommendation. The clear width is the width of section of the walkway that is completely free of obstacles, vertical obstructions and protruding objects. The 36 inch width is the minimum width required to provide sufficient space for a person who uses mobility aids to travel within the restricted space. However, restricting the pedestrian zone to 36 inches prevents passing and does not allow for 2-way travel. The ADA and ABA guidelines state that where sidewalks are less than five feet in width, passing spaces sufficiently wide enough for wheelchair users to pass one another or to turn around shall be provided at intervals of 200 feet. Sidewalks must allow a flat driveway crossing that is at least three feet wide with a side slope of less than 2 percent.
Image Source and References:
Ronkin, M. & Zegeer, C. (2005). Planning and designing streets for pedestrians. Powerpoint presentation prepared for North Carolina Department of Transportation.
National Center for Safe Routes to School. Safe Routes to School Guide. http://guide.saferoutesinfo.org/engineering/sidewalks.cfm#width:

## Slide 18
Tight
Simple
Square
Slow speed
Easy to understand
  If complex, broken into smaller steps
Avoid free-flow movements
Features of pedestrian-friendly intersections:
Intersections: Pedestrian Safety
Notes: Speaker notes:
This slide lists several important factors for pedestrian friendly intersection design. Some design solutions are offered in the following slides.
Image Source and References:
Images from http://www.pedbikeimages.org - Laura Sandt

## Slide 19
Large corner radii:
  Increase crossing distance
  Make crosswalk & ramp placement more difficult
  Allow high-speed turns by cars
Small radii are safer for pedestrians
Intersections: Curb Radius
Notes: Speaker notes:
Over time, intersections with large curb radii have been developed to allow for higher speed turns, improved vehicular flow, and truck travel. Design guides point out the obvious consequence of large corner radii: long crosswalks. But there are other negative consequences: they “pull the intersection apart” and make it hard to place ramps and crosswalks where pedestrians want to cross. Intersection design should consider the turning movements of the most common large vehicle for that street and the option of using multiple lanes and slow speeds to perform that turn.
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 20
Intersections: Curb Extensions
Most focus has been on reducing crossing distance
Other advantages:
  Better visibility (both ways)
  Traffic calming
  Room for street furniture
  Additional on-street parking
Notes: This slide is animated.
Speaker notes:
All of these points are self-explanatory except for the last one: once the curb extension is in place, parking can be moved closer to the crosswalk than it was before. Additionally, it adds comfort and safety for pedestrians who naturally want to wait where they can see and be seen rather than hidden by parked cars.
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 21
Intersections: Bike Lanes
Intersections provide a challenge due to conflicts between right-turning vehicles and through-moving bicyclists
Notes: Speaker notes:
Intersections provide many conflict points for bicyclists. Placement of bike lanes on the right side of the road can create potential conflicts for bicyclists moving straight forward and vehicles turning right. Therefore, careful intersection design for bicycles is critical.

## Slide 22
Intersections: Bike Lanes
NACTO Urban Bikeway Design Guide
Notes: Speaker notes:
There are several ways to stripe bicycle lanes at intersections depending on the presence of on-street parking and turn lanes. These two images are examples of intersection designs that accommodate bicyclists while minimizing the conflict with right-turning vehicles.
Image Source and References:
NACTO Urban Bikeway Design Guide

## Slide 23
Intersections: Bike Boxes
Reduces “right-hook” threat
Assists left-turning bicyclists
Alerts motorists to presence of bicyclists
Eliminates RTOR
NACTO Urban Bikeway Design Guide
Notes: Note to instructor: In this slide you want to emphasize ‘expected behavior” and speak about how we need to make movements of bikes/vehicles clear and predictable.
Speaker notes:
This is a design strategy to help prevent bicycle crashes caused by right turning automobiles. A bike box is a right-angle extension to a bike lane at the head of the intersection. The box allows bicyclists traveling to the intersection in a bike lane to get to the head of the traffic queue on a red light and then proceed ahead of motor vehicle traffic when the traffic signal changes to green. Bike boxes include an advance stop bar for motorists and right-turn on red restrictions.
This increases bicyclists visibility and offers the following benefits:
Right hook avoidance due to increased visibility
Left turn assistance (as a way to make a left-turn from a right-side bike lane without merging through traffic and as a way to make a “box left turn”)
Avoiding turning movement conflicts at intersections where bicyclists may continue straight but motorists must turn (often diverters on bike boulevards)
These designs are gaining acceptance in many cities but not universally endorsed. This is an urban treatment that might be useful in spot locations on bike corridor where there is a lot of turning traffic conflicts.
Image Source and References:
National Association of City Transportation Officials
Further Reading
Dill, J., Monsere, C. M., & McNeil, N. (2012). Evaluation of bike boxes at signalized intersections. Accident Analysis & Prevention, 44 (1) pages 126-134.

## Slide 24
Intersections: Signal Treatments
Use a short signal cycle length
  Long wait causes stacking: pedestrians wait in street, or don’t wait and cross against the signal
At high-use crosswalks, pedestrians should get a signal at every cycle
Notes: Speaker notes:
If pedestrians wait too long, there may not be enough room for them to stack safely on the sidewalk; many will start crossing against the light when there are gaps in traffic. In typical downtown environments and other areas of high pedestrian activity, pedestrian push buttons are not needed; pedestrians expect and should get a pedestrian cycle at every signal phase.
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 25
WALK comes on 3 seconds prior to the vehicular green to give pedestrians a head start
Looks like a regular signal to drivers
Can also be paired with a bike signal
Intersections: Leading Pedestrian Interval
Notes: Speaker notes:
LPI lets pedestrians start crossing before motor vehicles do. This means pedestrians are already 10-15 feet into the crosswalk when vehicles start their turns. This enables drivers to see the pedestrians; when pedestrians are present, drivers wait their turn.
This simple signal timing tweak enables pedestrians to get a head start and avoid the conflicts that occur when pedestrians and turning vehicles start their movements simultaneously. In this example, there is a heavy left turn movement from a one-way street to another.
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 26
The effectiveness of crosswalks can be increased with:
Proper location
High visibility markings
Illumination
Signing
Advance stop bars
Median islands
Curb extensions
Signals
Intersections: Crosswalks
Michael Ronkin
Notes: Speaker notes:
Physical treatments such as these listed do the most to improve pedestrian safety at crosswalks.
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.
Zegeer, C.V., Stewart, J.R., Huang, H.H., Lagerwey, P.A., Feaganes, J. & Campbell, B.J. (2005). Safety effects of marked versus unmarked crosswalks at uncontrolled locations: Final report and recommended guidelines. (FHWA-HRT-04-100). McLean, VA: Federal Highway Administration, Office of Safety Research and Development. Available at http://www.tfhrc.gov/safety/pubs/04100/04100.pdf

## Slide 27
Pedestrian view
Intersections: Crosswalk Visibility
Driver view
Same crosswalk from two vantage points:
Notes: Speaker notes:
The crosswalk markings are in very poor condition, but are still visible to a pedestrian waiting to cross. The same crosswalk is virtually invisible to the driver; yet it’s the driver who is expected to react to this traffic control device.
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 28
Intersections: In-Street Pedestrian Crossing Signs
Notes: Speaker notes:
In-street pedestrian crossing signs are an effective way to bring attention to crosswalks. This sign is the version accepted in the MUTCD.
Image Source and References
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 29
Rectangular Rapid Flashing Beacon (RRFB)
Pedestrian Hybrid Beacon (“HAWK”)
Midblock Crossings: Beacons
Notes: Speaker notes:
This slide shows two beacon countermeasures that are used to increase pedestrian safety at unsignalized crosswalks. The first is the Pedestrian Hybrid Beacon (as called in the MUTCD, also commonly known as a HAWK signal), a traffic beacon used to aid bicycle and pedestrian crossings that uses traditional traffic and pedestrian signal heads, but in a different configuration. This signal is blanked out when not activated. Once activated (by push button or other detection) the overhead signal begins flashing yellow and then solid yellow, advising drivers to prepare to stop. The signal then displays a solid red and shows the pedestrian a “Walk” indication. A bicycle signal may also be paired with a pedestrian head at these locations. Finally, an alternating flashing red signal [“wig-wag”] indicates that motorists may proceed when safe, after coming to a full stop. The pedestrian is shown a flashing “Don’t Walk” with a countdown indicating the time left to cross. Several studies, have evaluated the safety effects of the HAWK beacon: http://www.fhwa.dot.gov/publications/research/safety/10042/.
The RRFB is a simpler, less costly treatment, involving a pedestrian crossing sign with two bright alternating flashing lights beneath it, placed directly at or slightly in advance of a marked crosswalk. Three experiments examined pedestrians crossing two 4-lane roads and one 3-lane road with median islands. When pedestrians stepped into the crosswalk before installation of the rapid flash LED beacons, the average yield rate of motorists was 19%. When two rapid flash LED beacons were added (one on each side of the street) the yield rate increased to an average of 81%. When another set of rapid flash LED beacons were added to the medians the average yield rate jumped to 88%. Further research is showing yielding rates averaging 90% with some as high as 97%. Interim approval for RRFBs was received from FHWA in 2008.
Image Source and References:
Left: Image from http://www.pedbikeimages.org/Michael Cynecki
Right: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 30
Midblock Crossings: Multiple Threat
Crash Problem
1st car stops to let pedestrian cross, blocking sight lines
2nd car doesn’t stop and hits pedestrian at high speed
Notes: Speaker notes:
This image illustrates the problem.
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 31
Midblock Crossings: Advance stop/yield line
1st car stops further back, opening up sight lines
2nd car can be seen by the pedestrian
Notes: Speaker notes:
The advance stop bar has proven very effective at preventing multiple-threat crashes. In most cases the crash is avoided because the pedestrian stepped back and took evasive action (rarely can a car traveling at 40 MPH +/- stop in time if the driver has to react at the last second).
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 32
Midblock Crossings: Raised Median
Breaks complex crossing into two simpler crossings
Notes: Speaker notes:
The basic principle behind a median island is the pedestrian crosses half the roadway at a time, simplifying the task of assessing an adequate gap, making the crossing much safer. The pedestrian looks left, crosses to the island, looks right, crosses 2nd half. This is much easier than finding a gap long enough to cross all at once.
Note the angled or staggered cut-through that places pedestrians so they are facing oncoming traffic. In order to improve wayfinding for pedestrians with visual impairments, align the ends of the cuts with the crosswalk.
Image Source and References:
City of Charlotte, NC

## Slide 33
Street Retrofits: Bike Lanes
Considerations for retrofitting bike lanes on existing streets:
Reduction of travel lane width
Reduction in the number of travel lanes
Removal, narrowing, or reconfiguration of parking
Other design options
Notes: This slide is animated.
Speaker notes:
With limited space on most existing urban streets due to motor vehicle lanes and sidewalks, it can be a challenge to find the space to add bike lanes. Possible options to consider when retrofitting bicycle lanes into limited space on existing streets include:
Road diets
Removal of parking
Raising existing drainage grates, manholes and utility covers so that they are even with the pavement before striping a bike lane
Removal or relocation of obstructions such as guardrails, utility poles, or sign posts away from the edge of the roadway may gain some usable width.
Image Source and References:
Federal Highway Administration. (2006). University course on bicycle and pedestrian transportation: Bicycle lanes. (Publication No. FHWA-HRT-05-113). McLean, VA: Federal Highway Administration. Available at http://www.pedbikeinfo.org/collateral/lessons/Lesson15.pdf
Image from Oregon Department of Transportation. (1995). Oregon Bicycle and Pedestrian Plan.

## Slide 34
Street Retrofits: Road Diet
Benefits:
Reduces crossing distance
Reduces “multiple threat” crash types
Provides room for crossing island to break crossing into 2 simpler crossings
Reduces top end travel speeds
Buffers sidewalk from travel lanes (parking or bike lane)
Reclaims street space for “higher and better use” than moving peak hour traffic
Notes: Speaker notes:
Appropriate road diets provide many benefits to pedestrians, bicyclists, and other road users.
Reduces crossing distance through reducing the number of motor vehicle lanes
Reduces “multiple threat” crash types: 4-lane to 3-lane road diets move from 2-lanes in each direction to only one, thus drastically reducing the likelihood of a multiple threat crash
Provides room for crossing island to break crossing into 2 simpler crossings
Reduces top end travel speeds: The prudent driver now sets the speed rather than the fastest driver which can occur when there are multiple travel lanes
Buffers sidewalk from travel lanes (parking or bike lane)
Reclaims street space for “higher and better use” than moving peak hour traffic: Designing to for automobile capacity at peak hour leads to often unnecessarily wide roads. Road diets should pay close attention to intersection capacity to ensure that the delay and queues will not be unacceptable. This is often mitigated by turn lanes or signal retiming at the intersections.
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 35
Edgewater Drive (Orlando, FL)
Repaving project scheduled in 5-year work plan
Florida DOT required:
  Changes must be accepted by neighborhood and business association
  City must conduct before/after studies
Street Retrofits: Road Diet Example
Notes: Speaker notes:
The rightsizing of 1.5 miles of Edgewater Drive in 2002 was driven by the College Park Neighborhood Horizon Plan, which called for making this urban street friendlier to pedestrians and bicyclists. Locals wanted to see the street design support its main street status, instead of just serving as a drive-through street for commuters.

## Slide 36
36
Before
Notes: Speaker notes:
Before condition, 4 lanes with on-street parking. Through residential/commercial area

## Slide 37
After
Notes: Speaker notes:
Travel lanes reduced from 4 to 3, bike lanes were added
Additional costs to the resurfacing project were minimal – mostly paint and staff time

## Slide 38
Chart: Percent of Vehicles Traveling over 36 MPH
 | 0.15743
 | 0.074943
 | 0.097853
 | 0.088767
 | 0.29488
 | 0.1956
Street Retrofits: Road Diet Outcome
38
Notes: Speaker notes:
Effect of road diet on vehicle speeds.

## Slide 39
34% reduction in crashes per mile travelled
Traffic volumes remained similar (~20,000 ADT)
On-street parking utilization improved from 29% to 41%
Pedestrian volumes increased 23%
Bicyclist volumes increased 30%
Street Retrofits: Road Diet Outcome
Notes: Speaker notes:
In addition to the safety benefits, the increase in parking, pedestrians, and bicyclists likely resulting in benefits to the local business along the corridor

## Slide 40
“Complete Streets” are designed for all road users and based on the surrounding context
Effective engineering strategies to increase bicycle and pedestrian safety are available
Many streets can be retrofitted to provide a higher Quality of Service for all street users
Class Summary