## Slide 1
Introduction to Transportation Engineering Modules
Class 3: Pedestrian and Bicycle Data and Performance
Notes: Slides were developed by Carl Sundstrom, Daniel Rodriguez, and Laura Sandt of the University of North Carolina, with input from Rod Turochy and Jeff LaMondia at Auburn University. Funding was provided by the Southeastern Transportation Research, Innovation, Development and Education Center (STRIDE) as well as by the Pedestrian and Bicycle Information Center (PBIC). These slides were updated in 2015 by Carl Sundstrom and Kristen Brookshire.
Image source:
Photo (left): Tiffany Robinson http://www.pedbikeimages.org/pubdetail.cfm?picid=1848
Photo (right): Laura Sandt http://www.pedbikeimages.org/pubdetail.cfm?picid=1674

## Slide 2
Learning Objectives
By the end of this class, students will be able to:
Describe data needs for bicycle and pedestrian monitoring, analysis, and planning
Identify existing sources of data
Understand facility analysis tools (e.g., level of service, level of traffic stress) based on data

## Slide 3
Data collection goals and needs
Data sources
  Environment
  Behavior
    Mode share
    Volume counts
    Crashes
Facility analysis tools
Today’s Class

## Slide 4
Why Collect Data?
Planning and Funding
  Determine when/where people walk and bicycle (or not)
  Identify presence and quality of facilities
Benchmarking
  Show whether goals are being met (or need to be reevaluated)
  Compare to other areas
Accountability
Notes: Speaker notes:
Collecting accurate bicycle and pedestrian data has many benefits that range from justifying funding, to understanding why and where people travel by bike for on foot, to creating a safer environment for all road users. There are obvious overlaps among these goals – and, as you will see, overlaps in the data needs and sources.
Types of questions:
How many users? would-be users? How often? How much? Is there unmet (latent) demand?
What types of uses are present / needed? Recreational, commuting …
Where are users going/needing to go? Origins / destinations / access
What facilities are present & quality?
Will improvements make a difference? – evaluation importance
What is the quality of the facilities provided? Safety and Level of Service?
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.
Adapted from Bob Schneider. (2008). Data Collection and Performance Measures. Powerpoint presentation. UC Berkeley.
Image from Bob Schneider, UC-Berkeley.

## Slide 5
Data Needs
Environment
Facility inventory & traits
Land use
Population socio-demographics
Perceptions
Behavior
Volume and use
  Pedestrians
  Bicyclists
  Motor vehicle ADT & mix
  Transit
Crashes
Gap studies
Notes: Speaker notes:
There are two broad types of data, behavior data (including crashes) and environment data. Although our focus here will be on behavior data, the next few slides summarize some important environment data often encountered or needed in practice.

## Slide 6
National road data: TIGER Line files (US Census Bureau)
  Data from 2010 on is much higher quality then before
Regional road data: MPOs, County, State DOT
Often will have functional classification code (FCC), some geometric descriptions
Environment: Existing Data Sources, Roads
Notes: Speaker notes:
In terms of the environment, TIGER line files are a good national source of road data. They do not contain information on sidewalks or bicycle lanes. They contain a feature class codes (FCC), previously called functional classification codes, and it also contains minimum geometric descriptions. Given this limited data, researchers and practitioners often collect primary data about the environment (next slide).
Sample FCCs include:
Primary Highway With Limited Access Interstate highways and some toll highways are in this category (A1) and are distinguished by the presence of interchanges.
Secondary and Connecting Road This category (A3) includes mostly state highways, but may include some county highways that connect smaller towns, subdivisions, and neighborhoods. The roads in this category generally are smaller than roads in Category A2, must be hard- surface (concrete or asphalt), and are usually undivided with single-lane characteristics. These roads usually have a local name along with a route number and intersect with many other roads and driveways.
For all FCCs go to:
http://proximityone.com/tgrcfcc.htm

## Slide 7
Environment: Customized Data Collection
  Inventories (roads, sidewalks & paths)
    Data managed in GIS,
    CAD, & spreadsheets
  Focus on key destinations
    Libraries
    Schools
    Shopping centers
Notes: Speaker notes:
Primary data include inventories or audits. These involve walking or driving along streets, filling out pre-specified forms that include boxes to identify the presence and quality of sidewalks, lighting, transit stop landings, etc. Both pedestrian or bicyclist supports AND hazards or barriers are collected. These data are then inventoried in spreadsheets and managed using programs such as GIS or CAD. Since this data collection activity is resource intensive, it makes sense to prioritize certain locations that attract pedestrian or bicycle activity such as libraries, schools, and shopping centers.
Image Source and References: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 8
Environment: Customized Data Collection
  Qualitative infrastructure assessments
    Slopes
    Sight distances & visibility
    Crossing times
  Quantitative assessments
    Gaps studies: enough time to cross between cars?
Notes: This slide is animated.
Speaker notes:
Other data that are often collected includes sidewalk slope, cross-slope, and surface variation. These data can help answer questions such as: Is width or number of lanes of the crossing a concern? Is there the possibility of multiple threat collisions? Is speed of traffic a concern?
In the next slide we turn to behavior data.
Image Source and References:
-Zegeer, C.V., Henderson, D., Blomberg, R., Marchetti, L., Masten, S., Fan, Y., Sandt, L., Brown, A., Stutts, J. & Thomas, L. (2008). Evaluation of the Miami-Dade Pedestrian Safety Demonstration Project. (HS 810 964) Washington, D.C.: National Highway Traffic Safety Administration.
-FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 9
Census Bureau
  Work trips only
  Decennial Population Census
  American Community Survey
    Replaced Population Census “long form”
    Continuous data collection on a sample; may only be able to aggregate over several years
National Household Travel Survey (NHTS)
  Since 1969, every 5-7 yrs.
    Most useful for benchmarking, general trends
Behavior Data: National Sources
Notes: Speaker notes:
The US Census is the best source for information on the journey to work commute. All main travel modes are counted.
The American Community Survey (ACS) replaced the Decennial Census’ “long form”. It relies on continuous data collection on a sample. For small units of analysis you may only be able to aggregate data over several years.
The NHTS is another source of more detailed information about multiple trip types (not only the journey to work commute). It is based on a national sample, so small area analyses are frequently not possible EXCEPT when the municipality, county, or metro area in which the subunit is located has purchased a supplement of the NHTS.
Since small-area data are to come by, most localities end up collecting their OWN data. The next slides walk you through this process.
American Community Survey
http://www.census.gov/acs/www/about_the_survey/american_community_survey/

## Slide 10
Behavior: Customized Data Collection
What are you counting?
Where are you counting?
For how long?
Permanent? Temporary? Medium-term?
Notes: Speaker notes:
This is the general process of data collection.
First, it is important to define what you are counting: pedestrians only, pedestrians and bicyclists (separately or combined), or bicyclists only. What about cars?
Second, you define the locations where you will be counting, for example, sidewalks, intersections, shared-use paths, or on-street bicycling facilities.
Third, you define how often or for how long you will be conducting counts, for example: permanently, temporarily, or periodically.

## Slide 11
Counted by passing a point (screenline), entering an intersection, or using a particular facility (crosswalk)
  Manually
  With technology (infrared, tubes, video)
May be continuous or for a sampling period
Capture spatial coordinates for overlay / use with other data (e.g. crash rates/intersection; sidewalk inventory)
Pedestrian and Bicyclist Volume Counts
Notes: Speaker notes:
Data can be collected manually or by using technology such as infrared sensors or pneumatic tubes. Manual counts are generally time-consuming and costly, but the easiest to implement and can capture the most detail about trip characteristics. Intercept surveys are helpful when even more detail is required. Counts are often performed during good weather (often fall) and when school is in session to obtain a higher use count. Recording where the counts take place is important to then combine the data with other built environment information using GIS.

## Slide 12
Counts: An Example of Extrapolating
Estimating average annual daily traffic based on short counts
  Impute durations based on adjustment factors from comparable facility
  Midtown Greenway (MN) constantly monitored (24-7) with a counter
  Other trail monitored with 2-day counts during February 2012: 175 on Fri and 250 on Sat
Notes: Speaker notes:
When data collection is intermittent rather than continuous, it is sometimes necessary to use data from short-duration counts to extrapolate average use levels over time. Here, data from continuous counts on a similar facility (for example, a trail) can be used to create an adjustment factor to estimate how trail usage varies by time of year on a different facility (such as a different trail).
Image source:
http://www.pedbikeimages.org/
Left: Taken in 2011 by Lyubov Zuyeva
Right: Taken in 2010 by Laura Sandt

## Slide 13
  Adjust 2-day counts to reflect monthly average daily traffic (MADT)
    In February for fully observed trail, how representative are Fridays + Saturdays of an average day?
    Adjust 48-hr counts up or down
  Adjust February average to reflect annual average daily traffic (AADT)
    How representative is February of all months of year? Adjust using this figure
    Winter month counts likely to require inflation (they will be low counts for an average day in the year). Summer month counts would need to be deflated
    If 50%  multiply by 2. If 200%, multiply 0.5
Counts: An Example of Extrapolating
Notes: Speaker notes:
This is done in three steps:
1) Adjust the 2-day counts so that they reflect monthly average daily traffic
2) Adjust the monthly count averages (in this case February) to any monthly average daily traffic
3) Multiply by 365

## Slide 14
  Result is AADT
  Multiply result by 365 to get cumulative annual traffic
Data needs
  48-hr counts for non-monitored facility
  For fully monitored-facility
    AADT, MADT, ratio of mean day of week traffic to MADT for each month, ratio of MADT to AADT for each month
    All from existing automatic count data
Counts: An Example of Extrapolating (cont.’d)
Notes: Speaker notes:

## Slide 15
Counts: An Example of Extrapolating
  Midtown Greenway (MN) constantly monitored (2011)
Notes: Speaker notes:
From the table (see red oval), the average Friday traffic in February 2011 was 1.04 times February average daily traffic, and the average Saturday traffic was 1.27 times February average daily traffic. Therefore, for the Friday-Saturday monitoring period, the average daily traffic was 1.16 times the February average daily traffic.
Using this ratio, the 2012 February average daily traffic can be calculated from the 2012 48-hour
traffic count. The observed counts in the other trail were 175+250=425. Using the 1.16 ratio, we can calculate the 2012 February average daily traffic from the 2012 48-hour traffic count: 425/1.16 =366. This is the Average daily traffic for the 2012 site.
From the above table (see blue circle), the February MADT/AADT ratio is 0.18 (i.e., February average daily traffic is 18% of annual average daily traffic). This factor then is used to calculate AADT and annual traffic for 2012 for the site: AADT= 366/0.18= 2,033. If we multiply by 365 we get the cumulative annual traffic: 2,033*365= 742,045
Reference:
Example from Lindsey, G., Chen, J., Hankey, S., and Wang, X. 2012. Adjustment Factors for Estimating Miles Traveled by Non-motorized Traffic. Unpublished manuscript prepared for submission to the Transportation Research Board 2013 Annual Meeting. Humphrey School of Public Affairs, University of Minnesota, Minneapolis, MN, 2012.

## Slide 16
National sources focus on fatalities
Local interest in
  Crash Frequency
    Broken down by number of pedestrian/bicycle crashes
  Crash Types
  Crash Rates
    More useful for general trends / large area
    Number of pedestrian or bicycle crashes (numerator)
    Number of pedestrians or bicyclists, motorist ADT (denominator)
  Crash Locations
    Spatially-presented crash occurrence or rates
Crash Data
Notes: Speaker notes:
National sources of pedestrian and bicycle collision data tend to focus almost exclusively on fatal collisions. At the local level, more detail is often needed to guide ped/bike safety efforts and facility development. For example, it is important to understand which types of crashes are occurring, such as right-hook or left cross. While the frequency of crashes is useful, it is even more useful when paired with data about exposure, for example the average number of bicyclists or pedestrians in a city or at a location as well as the number of vehicles. Finally, it is important to collect location data in order to map crash frequency, type (if applicable), and/or collision rate.

## Slide 17
Crash Data: Police Reports
Notes: Speaker notes:
This slide shows a crash diagram and narrative from a police crash report. Detailed crash reports such as this one form the basis of databases. One example of a publicly available crash database is TIMS: The Transportation Injury Mapping System website, which provides data about collisions in the state of California based on the Statewide Integrated Traffic Records System (SWITRS).
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 18
  Identify types and characteristics of crash problems
  Identify high crash locations, corridors, areas
  Identify locations, corridors, areas with high crash potential
  Prioritize high crash locations, corridors, areas
  Identify appropriate treatments
  Evaluate safety effects of treatments
Safety Data Collection Goals
Locations of pedestrian crashes
Durham, NC, 2004-2009
Notes: Speaker notes:
By collecting and analyzing collision data, practitioners can pinpoint intersections or roadway segments with an above-average occurrence of ped/bike collisions and prioritize those areas for safety treatments.
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.
Durham County Pedestrian Crashes 2004-2009. bikewalkdurham.org

## Slide 19
Data collection goals and needs
Data sources
  Environment
  Behavior
    Mode share
    Volume counts
    Crashes
Facility analysis tools
Outline
Notes: Note to Instructor: This is a transition slide that can be cut for time

## Slide 20
Facility Analysis: Level of Service (LOS)
Describes/evaluates traffic flow and delay conditions
  Uses letters A-F
Defined in the Highway Capacity Manual (HCM)
Originally for vehicle traffic, but pedestrian and bicycle LOS measures have been developed
Notes: This slide is animated.
Speaker notes:

## Slide 21
Walking Level of Quality/Level of Service (LOQ/LOS)
Poor walking environment – low pedestrian LOS
Notes: Speaker notes:
Poor walking conditions, design, or inadequate maintenance can provide clues to the rationale behind pedestrian behavior.
Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 22
Walking Level of Quality/Level of Service (LOQ/LOS)
Rich walking environment – high pedestrian LOS
Notes: Speaker notes:
A counter-example to the previous slide
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 23
Provides a consistent, systematic evaluation of existing conditions
Puts results in terms that transportation professionals and the public can understand
Provides an objective way to identify needs and prioritize improvements
Provides a way to experiment with different improvement types and cross sections
Why Measure Level of Service?
Notes: This slide is animated.
Speaker notes:
Level of Service is a consistent and relatively easy way to identify needs for bicyclists and pedestrians while comparing different segments.
Image Source and References:
Bob Schneider. (2008). Analysis Methods (Facility Quality). Powerpoint presentation. UC Berkeley.

## Slide 24
Expanded pedestrian on pedestrian ands bicycle facilities
Revised transit chapter
Incorporated pedestrian, bicycle, and transit analyses in urban streets facilities, segments, and intersections
Multimodal Analysis in the Highway
Capacity Manual: HCM2010
Notes: Speaker notes:

## Slide 25
Presence of sidewalks, buffer (& widths)
Road (path, sidewalk) and traffic characteristics
  ADT & no. trucks/heavy vehicles
  Width & no. of lanes
  Speed limits
  Bike lane/shoulder presence
  Conflict point count (driveways/intersections)
Pedestrian and Bicycle LOS needs
Notes: Speaker notes:
Data needs:
Bike/ped facility inventories
Roadway inventories
are critical to developing and maintaining a safe and quality network.
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 26
Proximity of bicyclist to motor vehicles
Speed of traffic
Volume of motor vehicle traffic
Percent heavy vehicles
Pavement condition
Common Variables that Affect Bicyclists
Notes: Speaker notes:
Proximity to motor vehicles is determined by the average width of the outside lane.
Image Source and References: Bob Schneider. (2008). Analysis Methods (Facility Quality). Powerpoint presentation. UC Berkeley.
Photo (top): Cyclist in Cambridge, Massachusetts. Hunter, W. W., L. Thomas, R. Srinivasan, and C. Martell. Evaluation of Shared Lane Markings. Publication FHWA-HRT-10-041. FHWA, U.S. Department of Transportation, 2010.
Photo (bottom): Cyclist in Vancouver. Photo by clauretano http://www.flickr.com/photos/83569292@N00/5969248472
Slide content developed by Sprinkle Consulting, Inc.

## Slide 27
Bicycle LOS
ABSeg = Length weighted average segment bicycle score
e = The exponential function, where e is the base of natural logarithms
ABInt = Average intersection bicycle score
Cflt = Number of unsignalized conflicts per mile, i.e., the sum of the number of unsignalized intersections/mile & number of driveways/mile
Notes: Speaker notes:
Final Report: NCHRP Report 616 -- http://onlinepubs.trb.org/onlinepubs/nchrp/nchrp_rpt_616.pdf
User’s Guide: NCHRP Web document 128 -- http://onlinepubs.trb.org/onlinepubs/nchrp/nchrp_w128.pdf

## Slide 28
Bicycle Segment LOS (Abseg)
Vol = Volume of directional traffic (vph)
L = Total number of through lanes
PHF = Peak hour factor
Fs = Effective speed factor =; where S is the posted speed limit
HV = % of traffic that is heavy vehicles
PC5 = FHWA’s five point surface condition rating
We = Average effective width of outside through lane (if no on-street parking and shoulder/bike lane < 4 ft; if shoulder lane <=4, then add width to width of outside through lane)
Notes: Speaker notes:
This is the equation used to determine BLOS based on the variables just described.
Image Source and References:
Slide content developed by Sprinkle Consulting, Inc.

## Slide 29
Bicycle Intersection LOS (ABInt)
Wt = Total width of outside through lane and bike lane (if present)
CD = Crossing distance, the width of the side street (including auxiliary lanes and median)
Vol15 = Volume of directional traffic during a 15-minute period
L = Total number of through lanes on the approach to the intersection

## Slide 30
Segment Bicycle LOS C
MD 108—Howard County
No shoulder
12.5 foot lane
50 MPH speed limit
2 lanes, undivided
1500 veh/hr
Peak Hour factor=2
11% trucks
4 conflicts/mi
Surface condition=3
(default value for
good condition)
Notes: Speaker notes:
Image Source and References: Image from Dan Dodd. For a spreadsheet (first example tab) showing these calculations
Abseg= 0.507 ln(Vol/4*PHF*L) + 0.199Fs(1+10.38HV)2 + 7.066(1/PC5)2 - 0.005(We)2 + 0.760
Fs=1.12*(LN(50-20))+0.81 = 4.619
Abseg= 0.507 ln(1500/4*2*1) + 0.199 * 4.619*(1+10.38*0.11)2 + 7.066(1/3)2 - 0.005(12.5)2 + 0.760
Abseg= 0.507*5.234 + 0.199 0.9192*4.587 + 0.78511 - 0.78125+ 0.760
Abseg=7.6342
LOS = 0.20*(ABSeg) + 0.03*(exp(ABInt)) + 0.05*(Cflt) + 1.40
LOS = 0.20*(7.6342) + 0.05*(4) + 1.40
LOS = 3.127  C

## Slide 31
Segment Bicycle LOS B
MD 108—Howard County
9.5 ft shoulder
12 foot lane
45MPH speed limit
2 lanes, undivided
200 veh/hr
Peak Hour factor=2
4% trucks
3 conflicts/mi
Surface condition=3
(default value for
good condition)
Notes: Speaker notes:
Considering these conditions, the level of service should be B. Students can practice these calculations at home.
Image Source
Image from Dan Dodd.

## Slide 32
Important Bicycle LOS Model Caveats
Model not used to predict bicycle crashes; it is a suitability model
Model based on the perceptions of safety of a typical bicyclist
Model represents the typical conditions along a roadway segment (averages, not anomalies)
Slope and signage are not included in the model
“New” facility types cannot be evaluated (e.g., shared lane markings, cycle tracks, etc.)
Notes: This slide is animated.
Speaker notes:
There are many considerations to be aware of when using BLOS. These should be kept in mind when using and interpreting BLOS analyses.
Image Source and References:
Bob Schneider, UC Berkeley, Analysis Methods (Facility Quality) slides, 2008

## Slide 33
Facility Analysis: Pedestrian LOS
Pedestrian LOS ?
Pedestrian LOS ?
Notes: Speaker notes:
While the left image is of a facility with Pedestrian LOS A, the right image is clearly more pedestrian friendly.
Image Source and References:
Left: Image from http://www.pedbikeimages.org/Laura Sandt. Photo taken in Chapel Hill, North Carolina.
Right: Image from http://www.pedbikeimages.org/Dan Burden. Photo taken in East Lansing, Michigan.

## Slide 34
Multimodal LOS Measure Issues
Past HCM method focuses on speed, delay, and space
NCHRP 3-70 and other research suggest there are other factors
Auto volumes important to bike & ped service quality
LOS A
LOS C
LOS E
Notes: Speaker notes:

## Slide 35
Auto traffic and speeds
Percent trucks
Lateral separation between vehicles and pedestrians
  Buffers (plantings, barricades), parked cars
Crossing difficulty
  At intersections and mid-block locations
Pedestrian density
Pedestrian LOS Inputs
Notes: References:
Final Report: NCHRP Report 616 -- http://onlinepubs.trb.org/onlinepubs/nchrp/nchrp_rpt_616.pdf
User’s Guide: NCHRP Web document 128 -- http://onlinepubs.trb.org/onlinepubs/nchrp/nchrp_w128.pdf
Image sources:
(Top): Pedestrian walking in Tampa. Photo by Theo Petritsch. From FHWA. (2012). Proven Countermeasures for Pedestrian Safety. http://www.fhwa.dot.gov/publications/publicroads/12marapr/04.cfm
(Bottom): Photo by Dan Burden. From FHWA. (2012). Proven Countermeasures for Pedestrian Safety. http://www.fhwa.dot.gov/publications/publicroads/12marapr/04.cfm

## Slide 36
If there is pedestrian/bike shared use path parallel to street, use shared use method (HCM Chap. 18)
If sidewalk is NOT shared with bikes, then PLOS is worse of:
  Pedestrian density LOS (HCM, Chap. 18)
  Non-density LOS
Pedestrian LOS Model
Notes: Speaker notes:
Image source: FHWA. (2012). Bicycle Road Safety Audit Guidelines and Prompt Lists.

## Slide 37
Used to evaluate bicycle networks on a municipal level
Classifies road segments into four levels of traffic stress
  Highest ratings for separated facilities or those with low exposure and conflicts with other traffic (LTS 1 is suitable for children, LTS 2 for most adults)
Facility Analysis: Level of Traffic Stress (bicycles)
Source: City of Cambridge, MA
Notes: Source: May 2012 Mineta Transportation Institute report, "Low-Stress Bicycling and Network Connectivity" - available at: http://transweb.sjsu.edu/PDFs/research/1005-low-stress-bicycling-network-connectivity.pdf
Abstract:
For a bicycling network to attract the widest possible segment of the population, its most fundamental attribute should be low-
stress connectivity, that is, providing routes between people’s origins and destinations that do not require cyclists to use links that
exceed their tolerance for traffic stress, and that do not involve an undue level of detour. The objective of this study is to develop
measures of low-stress connectivity that can be used to evaluate and guide bicycle network planning. We propose a set of criteria
by which road segments can be classified into four levels of traffic stress (LTS). LTS 1 is suitable for children; LTS 2, based on
Dutch bikeway design criteria, represents the traffic stress that most adults will tolerate; LTS 3 and 4 represent greater levels of
stress.
As a case study, every street in San Jose, California, was classified by LTS. Maps in which only bicycle-friendly links are displayed
reveal a city divided into islands within which low-stress bicycling is possible, but separated from one another by barriers that
can be crossed only by using high-stress links. Two points in the network are said to be connected at a given level of traffic
stress if the subnetwork of links that do not exceed the specified level of stress connects them with a path whose length does
not exceed a detour criterion (25% longer than the most direct path). For the network as a whole, we demonstrate two measures
of connectivity that can be applied for a given level of traffic stress. One is “percent trips connected,” defined as the fraction of
trips in the regional trip table that can be made without exceeding a specified level of stress and without excessive detour. This
study used the home-to-work trip table, though in principle any trip table, including all trips, could be used. The second is “percent
nodes connected,” a cruder measure that does not require a regional trip table, but measures the fraction of nodes in the street
network (mostly street intersections) that are connected to each other. Because traffic analysis zones (TAZs) are too coarse a
geographic unit for evaluating connectivity by bicycle, we also demonstrate a method of disaggregating the trip table from the
TAZ level to census blocks. For any given TAZ, origins in the home-to-work trip table are allocated in proportion to population,
while destinations are allocated based on land-use data. In the base case, the fraction of work trips up to six miles long that are
connected at LTS 2 is 4.7%, providing a plausible explanation for the city’s low bicycling share. We show that this figure would
almost triple if a proposed slate of improvements, totaling 32 miles in length but with strategically placed segments that provide
low-stress connectivity across barriers, were implemented.

## Slide 38
LTS Identifies barriers and gaps between “islands” of low-stress bicycle routes
Level of Traffic Stress (bicycles)
Source: Mineta Transportation Institute (2012)
Notes: Source: May 2012 Mineta Transportation Institute report, Low-Stress Bicycling and Network Connectivity -- available at: http://transweb.sjsu.edu/PDFs/research/1005-low-stress-bicycling-network-connectivity.pdf

## Slide 39
Synthesizing Information
How to take all the information collected and prioritize?
  Behavioral and environment information
  Geographic information systems can help
    Overlay areas of common need
    Environmental justice concerns
Notes: Speaker notes:

## Slide 40
Facility Analysis: Overlapping Priorities Method
Sample Implementation Strategy:
Retrofitting existing roadways with sidewalks – how to develop a program to fill in missing sections of sidewalks over 20 years
Notes: Speaker notes:
The following example shows how Seattle prioritized their sidewalk improvements using a method that mapped the locations of highest priority for sidewalk improvements and began where these areas overlapped.
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 41
Plot Crashes on a Map: Area-Wide Problem
Notes: Reference:
Zegeer, C., Henderson, D., Blomberg, R., Marchetti, L., Masten, S., Fan, Y., Sandt, L., Brown, A., Stutts, J., & Thomas, L. (2008). Evaluation of the Miami-Dade pedestrian safety demonstration project. National Highway Traffic Safety Administration. Available: http://www.pedbikeinfo.org/cms/downloads/810964.pdf

## Slide 42
Urban village
Notes: This slide is animated.
Speaker notes:
Seattle first mapped out priority areas, such as “urban villages” (distinct neighborhoods)
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 43
Schools
Notes: This slide is animated.
Speaker notes:
A buffer around schools was then included.
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 44
Service providers
BINGO!
Notes: This slide is animated.
Speaker notes:
It shows service providers, etc. Where three or more overlap, then sidewalks can be retrofitted in these areas first. By spreading the costs over ten years, a little bit of money each year goes a long way towards retrofitting the most urgent needs. By looking primarily at arterials, transit is also served.
Image Source and References:
FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 45
Clarity about goals and uses is important when determining data needs
Variety of data needs and sources for pedestrian and bicycle modes
  Frequently less than for automobiles  customized data collection is important
Data can support prioritizing investments and help in decision-making
Different facility analysis tools may lead to varying assessments of a network.
Summary