## Slide 1: Facility and Network Analysis
Instructor course information
Notes: Report No. FHWA-SA-19-034

## Slide 2: Module Outline
Network analysis and the planning process
Level of service
Methods and measures for network analysis
  Including Level of Traffic Stress
Examples
Notes: Connection to other Module: This module builds on the content covered in the module, Bicycle and Pedestrian Data for Planning.

## Slide 3: Components of a Network Connectivity
Network completeness
  How much of the transportation network is available to people bicycling and walking?
Network density
  How dense are the available links and nodes of the bicycle and pedestrian network?
Route directness
  How far out of their way do users have to travel to find a facility they can or want to use?
Access to destinations
  What destinations can be reached using the transportation network?
Network quality
  How does the network support users of varying levels of experience, abilities, and comfort with bicycling or walking?
Notes: Key Message: Each of the components listed on the slide is also an analysis method that involves assessments of one or more types of performance measures, some of which will be introduced throughout this module.
Connection to other Module: Performance measures are covered in the module, Policies that Support Pedestrian and Bicycle Planning.
Source: FHWA. (2018). Guidebook for Measuring Multimodal Network Connectivity. [FHWA-HEP-18-032]. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_connectivity/
Background image is from FHWA. Bike Network Mapping Idea Book. (2016). [FHWA-HEP-16-054]. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/bikemap_book/

## Slide 4: Why Conduct Facility Analyses?
Identify missing or low-quality connections
  Necessary for long-term planning and near-term actions related to maintenance and ADA compliance
  Prioritize projects that fill gaps and address barriers
  Ideally, cost-effective solutions that optimize co-benefits
Compare existing network with proposed scenarios
Measure the long-term impact of investments
Notes: Key Message: In addition to the goals listed on the slide, the outputs of facility and network analyses can enhance accountability as decision makers weigh the potential outcomes of infrastructure and program investments.
Connection to other Module: A similar slide is presented in Bicycle and Pedestrian Data for Planning.
Source:
FHWA. (2016). Guidebook for Developing Pedestrian and Bicycle Performance Measures. [FHWA-HEP-16-037] Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/performance_measures_guidebook/
FHWA. (2018). Guidebook for Measuring Multimodal Network Connectivity. [FHWA-HEP-18-032]. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_connectivity/

## Slide 5: Data Types
Environment
Facility inventory & traits
Land uses
Population socio-demographics
Perceptions
Behavior
Volume and use
Pedestrians
Bicyclists
Motor vehicle ADT & mix
Transit
Crashes
Trip and mode share
Notes: Key Message: To analyze the network, you need data. This slide introduces the types of data you may need to find or collect for different analyses.
Notes: These data types are shown on a Venn diagram to remind us that there is some overlap in the collection and uses for these data. Each type of data only conveys part of the picture. For example, you will almost always need to relate behavior data back to the environment (e.g., facilities, population, conditions of use, etc.)
Connection to other Module: This slide appears in the module, Bicycle and Pedestrian Data for Planning. Crashes are covered in the module, Safety Analysis.
Source: This slide was adopted from a presentation by Carl Sundstrom and Libby Thomas for the Pedestrian and Bicycle Information Center (2011 & 2015).

## Slide 6: Factors for Prioritization
Attractors/destinations (land use)
Route network/connectivity
Existing conditions
Safety
Opportunity (upcoming projects)
Constraints (cost and legal)
Demand
Public input
Equity
Compliance
Notes: Key Message: There is no single way to identify and prioritize projects. The factors listed on this slide are some of the most common considerations. Agencies may choose to assign weights to the factors they include or choose a factor to start with and then add other factors as layers (e.g., start with an assessment of network quality – existing or planned – then layer it with safety data or socioeconomic data to assess equity). The factors are listed in no order, but this lesson will focus on analyses that address the first three bullets, which all relate to understanding network connectivity.
Notes: This list includes factors that were noted during the literature review for NCHRP Report 803: ActiveTrans Priority Tool Guidebook (2015) and included in the final tool developed as part of that project.
Connection to other Module:
Safety is covered in the module Safety Analysis
Demand is covered in the module Bicycle and Pedestrian Data for Planning
Public Input is covered in the module on Inclusive Public Engagement
Compliance is addressed in the module Accessibility and ADA
There is also a module on Equity, but the focus is not on measuring equity.
Source: Adapted from slides by Robert Schneider.
Lagerwey, P.A., M.J. Hintze, J.B. Elliott, J.L. Toole, and R.J. Schneider. (2015). Pedestrian and Bicycle Transportation Along Existing Roads: ActiveTrans Priority Tool Guidebook, National Cooperative Highway Research Program Report 803.

## Slide 7
U.S. DOT Transportation Planning, Decisionmaking, and Implementation (2016)
Notes: Key Message: Facility analyses can inform the iterative, comprehensive process of planning and implementing complete multimodal networks. The types of analyses that will be presented on subsequent slides can inform each step of the transportation planning process.
Notes: Planning tasks that may be involved in these steps include needs assessments, scenario analysis, project prioritization, and monitoring.
Connection to other Module: Planning for Walking and Bicycling
Source: FHWA. (2018). Guidebook for Measuring Multimodal Network Connectivity. [FHWA-HEP-18-032]. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_connectivity/

## Slide 8: Level of Service

## Slide 9: Level of Service in the HCM
Describes/evaluates traffic flow and delay conditions
  Uses letters A-F
  Defined in the Highway Capacity Manual (HCM)
  Originally for vehicle traffic, but pedestrian and bicycle LOS measures have been developed
“Providing mobility for people and goods is transportation’s most essential function” – HCM 6th edition
Notes: Key Message: “Traditional” LOS measures for the performance of the transportation system for vehicle. The letters A-F are used to classify flow that ranges from “free flow” all the way down to “forced or breakdown flow,” with free flow considered the ideal. LOS for vehicles can be measured along the roadway (flow) and at intersections (delay). While earlier versions of the HCM have focused on vehicle delay, the latest edition is focusing more on the people traveling, rather than the vehicle.
Notes: The Level of Service Model was introduced in the Highway Capacity Manual in 1965. In 2010, the HCM integrated a multimodal approach and with the 6th Edition the subtitle is now “A Guide for Multimodal Mobility Analysis.” This lesson is beginning with LOS because it is a measure that is common across many agencies and it is consistent and objective. This doesn’t mean that it is the best method, but it is important to be familiar with its applications and limitations. Agencies are asking themselves whether LOS is really a good measure of transportation system performance and considering placing emphasis on other measure such as vehicle miles traveled (VMT). There is an example of this from California toward the end of the presentation.
Student Question: What does “free flow” vehicular traffic mean for people walking and bicycling? How do you think the use of LOS should vary when you are considering different types of streets?
Connection to other Module: The module Designing for Walking and Bicycling briefly explains how LOS and the HCM fit in to the traditional engineering approach.

## Slide 10: Pedestrian and Bicycle LOS Data Needs
Street network data
  Number of lanes
  Paved shoulder width
  Outside lane width
  Pavement condition
  Presence of curb
  On-street parking (incl. % occupied)
  Bike lanes (incl. width)
  Sidewalks (incl. widths and buffers)
Motorized traffic data
  Speed
  Volume
  % heavy vehicles
Defined set of destinations or origin/destination zones
Notes: Key Message: Both models are based on stated preference research that covered a broad range of facility attributes. While the models are data-intensive, most of the data listed on the slide are straightforward to gather or collect.
Student Question: No measure is perfect, but what inputs are not included here that you think are crucial for understanding whether an environment is comfortable for walking and bicycling? [students might mention type of bicycle facility, surrounding land use, lighting, intersection treatments or delay, etc.]
Source: FHWA. (2018). Guidebook for Measuring Multimodal Network Connectivity. (2018). [FHWA-HEP-18-032]. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_connectivity/

## Slide 11: Bicycle Level of Service (BLOS)
Indicates overall quality of the network in terms of bicyclist comfort levels
  Used to assess the potential impacts of changes like building or removing a major facility on an area-wide network
Caveats
  Represents typical conditions along a roadway segment (averages, not anomalies)
  Slope and signage are not included
  Doesn’t evaluate buffered or separated bike lanes or bicycle-specific intersection treatments
    New research provides procedure for adding this (Foster et al., 2015)
Notes: Notes: The caveats should be kept in mind when using and interpreting BLOS analyses.
Source: Adapted from slides by Robert Schneider.
FHWA. (2018). Guidebook for Measuring Multimodal Network Connectivity. [FHWA-HEP-18-032]. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_connectivity/
Foster, N., Monsere, C. M., Dill, J., & Clifton, K. (2015). Level-of-Service Model for Protected Bike Lanes. Transportation Research Record, 2520(1), 90–99. https://doi.org/10.3141/2520-11

## Slide 12: HCM BLOS
ABSeg = Length weighted average segment bicycle score
e = The exponential function, where e is the base of natural logarithms
ABInt = Average intersection bicycle score
Cflt = Number of unsignalized conflicts per mile, i.e., the sum of the number of unsignalized intersections/mile & number of driveways/mile
Notes: Key Message: This slide shows how the HCM BLOS linear regression model uses the data inputs that were listed on a previous slide. The average segment bicycle score and average intersection bicycle score will be broken down on subsequent slides.
Notes: Instructors may skip this slide and the following two slides if students are not already familiar with the HCM. The assignment for this module references this equation, but understanding the equation is not essential for completing the assignment.
Source: Adapted from slides in the PBIC (2015) Pedestrian and Bicycle Transportation Short Series, which include content developed by Sprinkle Consulting, Inc.

## Slide 13: Bicycle Segment LOS (ABSeg)
Vol = Volume of directional traffic (vph)
L = Total number of through lanes
PHF = Peak hour factor
Fs = Effective speed factor =; where S is the posted speed limit
HV = % of traffic that is heavy vehicles
PC5 = FHWA’s five point surface condition rating (3 = default value for good condition)
We = Average effective width of outside through lane (if no on-street parking and shoulder/ bike lane < 4 ft; if shoulder lane <=4, then add width to width of outside through lane)
Notes: Key Message: The model considers four roadway and traffic conditions: 1) Peak traffic flow in the outside lane, 2) speed of traffic and percent of heavy traffic, 3) pavement surface condition, and 4) pavement width available for bicycling. The first three variables are impact scores and reflect perceived challenges to bicycling. The fourth variable is a benefit score and reflects perceived opportunities to bicycling.
Notes: “The first part of the [ABSeg] measures the impacts of peak hour vehicular traffic flow on bicyclists. Roads with high traffic volume on the outside lane would receive high BLOS score, indicating low suitability for bicycle travel. The second part of the BLOS equation measures the impacts of speed of travel and percent of heavy traffic (buses and trucks) on bicycle travel environment. Roads with high posted speed limit and high number of trucks and buses would receive high BLOS score, indicating low suitability for bicycle travel. Similarly, the third part of the BLOS equation measures the impact of pavement surface condition on bicycle ride quality and assigns high BLOS score for roadways with deteriorated pavements. These first three parts of the BLOS score and a constant term are added together to compute the raw BLOS score. The final BLOS score is computed by subtracting the benefits score (fourth term in the BLOS equation) based on pavement width available for bicycling from the raw score. Roadways with striped bike lanes, wide outside lanes, paved shoulders, or low on-street parking volumes would receive discounts from the raw BLOS score, resulting in low BLOS values or good level of service.”
Source: Adapted from slides in the PBIC (2015) Pedestrian and Bicycle Transportation Short Series, which include content developed by Sprinkle Consulting, Inc.
Speaker’s notes from City of Spartanburg Bicycle and Pedestrian Master Plan (2009), Appendix C. Available: http://www.cityofspartanburg.org/planning-zoning/bicycle-ped-plan/ (Accessed July 2019).

## Slide 14: Bicycle Intersection LOS (ABInt)
Wt = Total width of outside through lane and bike lane (if present)
CD = Crossing distance, the width of the side street (including auxiliary lanes and median)
Vol15 = Volume of directional traffic during a 15-minute period
L = Total number of through lanes on the approach to the intersection
Notes: Key Message: This slide breaks down the components of the average intersection bicycle score (ABInt)
Source: Adapted from slides in the PBIC (2015) Pedestrian and Bicycle Transportation Short Series, which include content developed by Sprinkle Consulting, Inc.

## Slide 15
City of Spartanburg, SC, via FHWA
Notes: Key Message: This slide shows what a BLOS measure can look like when applied to an entire road network.
Notes: The original state preference research was conducted on arterial and collector streets and that is how Spartanburg applied the model.
Source: FHWA. (2018). Guidebook for Measuring Multimodal Network Connectivity. [FHWA-HEP-18-032]. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_connectivity/
Adapted image from City of Spartanburg Bicycle and Pedestrian Master Plan (2009), Appendix C. Available: http://www.cityofspartanburg.org/planning-zoning/bicycle-ped-plan/ (Accessed July 2019).

## Slide 16: Pedestrian Level of Service (PLOS)
Indicates the level to which the infrastructure supports pedestrian travel, and how well pedestrian travel interacts with other modes.
Caveats
  Not applicable to local streets, paths, or trails
  Low sensitivity to changes in sidewalk width and buffer presence
Notes: Key Message: Very similar to BLOS. PLOS is also an attempt to adapt a commonly applied measure of motorized network performance to pedestrian facilities.; however, these origins are interesting considering capacity is rarely an issue for people walking. PLOS is most commonly used to document existing conditions, identify connectivity gaps, and evaluate network-wide quality.
Source: FHWA. (2018). Guidebook for Measuring Multimodal Network Connectivity. [FHWA-HEP-18-032]. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_connectivity/

## Slide 17: PLOS?
Pedbikeimages.org – Laura Sandt
Pedbikeimages.org – Dan Burden
Notes: Student Question: The image on the left shows a facility that would likely receive a higher PLOS measure. But which image shows a place you would be more comfortable walking?
Source: Adapted from slides in the PBIC (2015). Pedestrian and Bicycle Transportation Short Series.

## Slide 18: Methods and Measures for Network Analysis

## Slide 19: Five Step Analysis Process
Notes: Key Message: Regardless of the data available to you and the method(s) you choose for analysis, this decision should be grounded by the purpose of the analysis (Step 1) and the results should be packaged in a way that relates back to the planning process (Step 5). Part of packaging the results could include overlaying facility analysis results with other geographic data related to safety, equity, system usage, or other land use data.
Source: FHWA. (2018). Guidebook for Measuring Multimodal Network Connectivity. [FHWA-HEP-18-032]. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_connectivity/

## Slide 20: Network Analysis Methods
Network completeness
Network density
Route directness
Access to destinations
Network quality
Relatively easy to calculate
Requires network path analysis and place data
Requires more detailed data; could be applied as filter for above analyses
Notes: Key Message: The “components” of network connectivity that were introduced at the beginning of this lesson also serve as analysis method. The first couple listed on the slide are relatively easy to calculate using a variety of different measures. Network quality requires more detailed data and it is also a method that can be combined with the other methods, as illustrated on the next two slides.
Source: FHWA. (2018). Guidebook for Measuring Multimodal Network Connectivity. [FHWA-HEP-18-032]. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_connectivity/

## Slide 21: Network completeness
Presence or absence of sidewalks
FHWA
Notes: Key Message: This slide shows an example of the first method, network completeness, from Baltimore, Maryland. This map simply shows the presence or absence of sidewalks, regardless of their quality.
Source: FHWA. (2018). Guidebook for Measuring Multimodal Network Connectivity. [FHWA-HEP-18-032]. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_connectivity/

## Slide 22: Network completeness
Completeness measured in terms of high-quality (or low-stress) facilities
FHWA
Notes: Key Message: This map now shows network completeness in terms of high-quality (or low-stress) facilities. In more built-out areas, simple presence or absence may not be very informative and planners may need to turn to measures of quality when trying to analyze network completeness. This type of analysis can also be useful for assessing compliance with accessibility laws.
Notes: PLTS stands for Pedestrian Level of Traffic Stress. The method that Baltimore used was adapted from the Oregon Department of Transportation’s Analysis Procedures Manual, Volume 2. The PLTS methodology emphasizes compliance with accessibility laws. Poor pavement quality and noncompliant ramps result in poor scores and were scrutinized for this case study. With sidewalks present on most roadways, the results of the PLTS analysis provide insight into improvements needed to create a fully accessible network.
Source: FHWA. (2018). Guidebook for Measuring Multimodal Network Connectivity. [FHWA-HEP-18-032]. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_connectivity/

## Slide 23
Network Analysis Methods | Measures
Completeness | % or miles of planned walk/bike facilities that are complete % of street miles with walk/bike facilities
Density | Intersection density Connected node ratio Block length
Route directness | Out of direction travel as % of shortest path route Crossing opportunities
Access to destinations | Travelshed # or % of jobs accessible by walk/bike Access to community destinations
Network Quality | Level of Service (LOS) Level of Traffic Stress (LTS) Preference-based route utility or quality
Notes: This slide is animated
Key Message: There are a variety of measures (or questions to be answered), for each analysis method. We’ve already talked about LOS, so we will spend the next few slides covering LTS, which is increasingly being used by agencies to analyze network quality. The LTS measurement for bicycle travel was introduced in 2012 and is more commonly used than the measurement for walking.
Source: FHWA. (2018). Guidebook for Measuring Multimodal Network Connectivity. [FHWA-HEP-18-032]. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_connectivity/

## Slide 24: Bicycle Level of Traffic Stress (LTS)
Based on Dutch analysis approach
Rating of 1 through 4 for segments and intersections
  Final LTS rating is based on worst LTS component
Simple interpretation makes is suitable for a variety of contexts
Caveats:
  All-or-nothing classification sensitive only to “weakest link” improvements
  Data-intensive and assumptions can impact the usefulness of the results
Notes: Key Message: Bicycle Level of Traffic Stress accounts for different types of people who might be biking, and considers the experience of bicycling, such as comfort level and perception of safety, with the aim of highlighting low stress options for bicyclists. It is a more “user-oriented” measure of quality or connectivity. Criteria are proposed for classifying road segments by level of traffic stress depending on traffic characteristics (e.g., road width, traffic speed, the presence of a parking lane) and whether bikes are in mixed traffic, in bike lanes, or on segregated paths. A low level of stress can be achieved in mixed traffic on local streets with low traffic speeds. As the number of lanes, traffic speed, and traffic volume increase, providing a low level of stress requires progressively more protective measures – dedicated bike lanes and, ultimately, physically separated bikeways.
Notes:
-Level of traffic stress 1 (LTS 1) is meant to be a level that most children can tolerate;
-LTS 2, the level that will be tolerated by the mainstream adult population;
-LTS 3, the level tolerated by American cyclists who are somewhat confident, but still prefer having their own dedicated space for riding; and
-LTS 4, a level tolerated only by those characterized as “strong and fearless.”
The bullet list item “Final LTS rating is based on worst LTS component” is illustrated on the following slide.
Source: Source: Mekuria, M.C., P.G. Furth, and H. Nixon. (May 2012) Low-Stress Bicycling and Network Connectivity, Mineta Transportation Institute, Report 11-19.
https://transweb.sjsu.edu/sites/default/files/1005-low-stress-bicycling-network-connectivity.pdf

## Slide 25: Bicycle LTS
Mekuria, Furth, Nixon (2012)
Application on Hypothetical Street:
Notes: Instructor: choose a street in your community that has a bike lane alongside a parking lane and classify it for your students (or ask them to do it) or choose a different table from Mekuria et al. to score.
This slide is animated
Key Message: This example shows how the LTS rating is based on the lowest scoring factors (i.e., even though two factors are LTS 1, the other two override them so the segment is considered LTS 3).
Source: Adapted from slides by Robert Schneider.
Mekuria, M.C., P.G. Furth, and H. Nixon. May 2012. Low-Stress Bicycling and Network Connectivity, Mineta Transportation Institute, Report 11-19.

## Slide 26: Bicycle Level of Traffic Stress
Graphic by Toole Design Group
LTS 4
LTS 3
LTS 1 LTS 2
Notes: Key Message: The four ratings are loosely based on the “Types of Cyclists” research that originated in Portland, Oregon, and also on Dutch age-group based bicycle facility planning standards. LTS 1 would be suitable for children and LTS 2 is thought to be acceptable to many interested adult bicyclists (or potential bicyclists). Planners should adjust the user type definitions in an LTS model to reflect the demographics of riders relevant to a specific planning context.
Connection to other Module: This graphic is shown in User and Mode Characteristics.
Source: FHWA. (2018). Guidebook for Measuring Multimodal Network Connectivity. [FHWA-HEP-18-032]. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_connectivity/
Image from FHWA Bikeway Separation Guide (2019).

## Slide 27: Bicycle Level of Traffic Stress
So what does this like in terms of facilities?
Delaware Valley Regional Planning Commission, Bicycle LTS and Connectivity Analysis
Notes: Source: Image - https://www.dvrpc.org/webmaps/BikeStress/ (Accessed July 2019)

## Slide 28
Example:
Dual-purpose LTS data in Arlington County, VA
Practitioners use it for analysis
Public uses it for route choice
Bike Arlington, Arlington County Commuter Services
Notes: Key Message: We’ve covered how LTS data can be used by practitioners in a variety of planning contexts (e.g., project prioritization, scenario analysis, etc.), but it can also be presented in a way that is useful for the general public. Here, current or potential bicyclists can use this map to determine the route they are most comfortable with. They can weigh factors such as facility type and slope with route directness.
Source: Images – Bike Arlington, Arlington County Commuter Services. Available: http://www.bikearlington.com/maps-and-routes/ (Accessed July 2019).

## Slide 29: Example: Moving Away from Vehicle LOS in California
Legislation required shift in the way the State measures the environmental impact of transportation projects
  Research showed that increasing roadway capacity to mitigate congestion was detrimental to State goal of reducing greenhouse gas (GHG) emissions
  Updated California Environmental Quality Act guidelines on how to measure transportation impacts as part of environmental review
    Measures now include relationship to development, GHG emissions, public health, and vehicle miles traveled
Notes: Key Message: California has recently made significant changes to how the State measures the impacts of traffic project impacts. The new guidelines for the California Environmental Quality Act (CEQA), adopted in January 2019, align with the State’s goals of reducing GHG emissions, encouraging infill development (reducing sprawl), and improving public health through reduced use of single-occupancy vehicles and encouraging more active transportation. The bill shifted the emphasis away from how the transportation system affects drivers to how driving affects health, the environment, and surrounding community.
Notes: Currently, environmental review of transportation impacts focuses on the delay that vehicles experience at intersections and on roadway segments. That delay is often measured using a metric known as “level of service,” or LOS. Mitigation for increased delay often involves increasing capacity (i.e., the width of a roadway or size of an intersection), which may increase auto use and emissions and discourage alternative forms of transportation. Under SB 743, the focus of transportation analysis will shift from driver delay to reduction of greenhouse gas emissions, creation of multimodal networks, and promotion of a mix of land uses.
Source: California Governor’s Office of Planning and Research, “Transportation Impacts (SM 743).” Available: http://opr.ca.gov/ceqa/updates/sb-743/. [Accessed June 2019].

## Slide 30: Example: DDOT Bicycle Facility Evaluation
2010: Innovative bicycle facilities were installed at three locations in Northwest DC (two segments and one intersection) to provide increased safety, comfort, and convenience for bicyclists
Before/after multi-modal evaluation for the purpose of:
  Identifying recommended modifications to the constructed installations
  Providing guidance for the design and operation of future bicycle facilities
Notes: Key Message: For most of this lesson we’ve focused on methods and measures that can be used to assess a network for a variety of planning purposes. But what about after you’ve already selected a project? How can you collect data to conduct one or more types of analysis to understand what worked well, what isn’t working, and communicate findings to decision makers, the public, and maybe even the media?
Notes: Facilities included a two-way separated bicycle lane, a center median bicycle lane, and intersection treatments including bicycle boxes, bicycle signals, and the continuation of a contra-flow bicycle lane.
Source: District Department of Transportation Bicycle Facility Evaluation (2013). Available: https://ddot.dc.gov/page/bicycle-facility-evaluation

## Slide 31
  Two-way separated bike lane in Washington, DC
Pedbikeimages.org – Megan Kanagy

## Slide 32: DDOT Bicycle Facility Evaluation
Bicycle Facilities
District Department of Transportation (2013)
Notes: Key Message: The table on this slide and the two on the next slide show the types of analyses that were conducted for each location and the data need for each type of analysis.
Source: District Department of Transportation Bicycle Facility Evaluation. (2013). Available: https://ddot.dc.gov/page/bicycle-facility-evaluation

## Slide 33: DDOT Bicycle Facility Evaluation
Motor Vehicle Facilities
Pedestrian Facilities
District Department of Transportation (2013)
Notes: Student Question: Why do you think the department chose to conduct multiple types of analysis?
Source: District Department of Transportation Bicycle Facility Evaluation. (2013). Available: https://ddot.dc.gov/page/bicycle-facility-evaluation

## Slide 34: Summary
It is important to select an analysis that is appropriate for the intended application (i.e., the planning context)
Data needs and scale of analysis are both important factors in selecting methods and measures
Different facility analysis tools may lead to varying assessments of a network
Many measures have not been validated against behavior or use data