## Slide 1: Trails
Instructor course information
Notes: Report No. FHWA-SA-19-034

## Slide 2: Module Outline
Types of trails
Benefits of trails
Trail design and ADA
Evaluation and funding

## Slide 3: Types of trails

## Slide 4: Types of Trails
Sidepaths
Shared use paths
Rail trails
Flickr Creative Commons – Juan Monroy
Pedbikeimages.org – Reuben E Moore
Recreationaltrailsinfo.org – Stuart MacDonald
Notes: Key Message: There are various kinds of trails.
Notes: The term “trail” has various meanings across the country. Some people consider trails to be a path through rugged wilderness, some trails are historic routes, and some trails might be major highways (e.g., Tamiami Trail in south Florida). Trails can serve a range of purposes from neighborhood pedestrian connections to metropolitan bicycle and pedestrian networks, to long-distance tour routes. This presentation mostly focuses on nonmotorized transportation trails, but we will cover some aspects of recreational trails.
Source:
Image (bottom left): https://www.flickr.com/photos/juanomatic/8480536928/in/photolist-dVoYaW-qjLj5r-ptpmk-ptpvN-8vmj2v-eRuDqJ-rmxauE-7NefYF-7au4VC-dgBx6b-nooLM-fhz19D-dqqQ1v-cLj433-6Ag9at-ptoqX-5FAG4-9V2aqn-8uceAR-21cM8nh-7Nehu8-nQcVAr-6VTTVL-2EaTTf-ebU8Fe-JZfmn-ptpLg-8uceAX-5jNzMk-5jSPkE-ptpPC-8bbyyb-boiHFZ-5jNBNZ-9928cF-ptnWY-6VTTTb-bmm5AY-boiyxM-21nkn2N-ptpjF-aYNgjF-5JVKCJ-aFhEGt-4MHNsA-ptq2t-8hH6Hx-ptoaF-8hH8c8-boixx4

## Slide 5: Sidepaths
Physically separated paths for walking and bicycling
Immediately adjacent to roadways, usually in the ROW
Concerns
  Two-way traffic can lead to conflicts with other path users and drivers at intersections
  Intersection considerations similar for two-way separated bike lanes
FHWA
Notes: Key Message: Sidepaths offer a greater sense of safety for users than on-street travel, encouraging pedestrian and bicycle use in otherwise unappealing (high traffic, high speed) areas. This makes them a good option for filling gaps in network connectivity.
Notes: Sidepaths and two-way separated bike lanes are markedly similar: both are situated alongside roadways, but with a physical separation, and both allow for two-way travel. Two-way travel can cause conflicts when integrating with other road users (contra-flow travel is often not considered by motorists, especially at intersections) as well as between path users travelling in opposite directions.
Sources:
FHWA. (2019). Bikeway Selection Guide.
FHWA. (2016). Small Town and Rural Multimodal Networks. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/small_towns/fhwahep17024_lg.pdf

## Slide 6: Shared Use Paths
10’-15’ wide, physically separated from the road
Popular, low stress
Diverse user mix
Alternative connectivity to roadways
FHWA
Notes: Key Message: They serve as a complement to and extension of on-street facilities (not as alternatives to them) and offer the protection from motor vehicle traffic that many Americans seek when looking to leave their car behind in favor of biking, walking, or skating.
Notes: A shared use path provides a travel area separate from motorized traffic for bicyclists, pedestrians, skaters, wheelchair users, joggers, and other users. Shared use paths can provide a low-stress experience for a variety of users using the network for transportation or recreation. They can be great places for novice and child bicyclists to try out their bicycling skills prior to taking trips on urban streets. Shared use paths are frequently in high demand among bicyclists, joggers, in-line skaters, people walking dogs, people with disabilities, and a variety of other users. Systems of shared use paths in urban and suburban communities serve as the arterials of the bicycle and pedestrian transportation system.
Shared use paths are popular for their low stress environment (separate right-of-way from roads, typically no motorized uses).
Typically follow corridors such as utility cuts, water features, greenbelts, etc.
Source: FHWA. (2016). Small Town and Rural Multimodal Networks. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/small_towns/fhwahep17024_lg.pdf

## Slide 7: Rail Trails
Multi-purpose public paths
  Sited on old rail corridors
Accessible
  Flat, wide, typically straight
  Popular for recreation
Transportation potential
Recreationaltrailsinfo.org – Friends of the Northern Rail Trail
Notes: Key Message: Rail trails are multipurpose public paths created from former railroad corridors. These paths are flat or gently sloping, making them easily accessible and a great way to enjoy the outdoors. Rail trails are ideal for many types of activities—depending on the rules established by the local community—including walking, bicycling, wheelchair use, inline skating, cross-country skiing and horseback riding.
Notes:
Sub-type of shared use trails along specific corridors. Often located in rural areas but may serve arterial function in built-up areas.
Since siting is dependent upon existing rail corridors, there is less room to plan for specific connectivity goals. However, many rail corridors run from rural to urban areas, so there is potential to integrate rail trails into the bike/pedestrian transportation network.
Source:
Rails to Trails Conservancy. “Trail Building Toolbox.” Available: http://www.railstotrails.org/build-trails/trail-building-toolbox/ [Accessed July 2019]
FHWA. (2016). Small Town and Rural Multimodal Networks. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/small_towns/fhwahep17024_lg.pdf

## Slide 8: Recreational Trails
Intended for recreational use rather than transportation use
Do not use highway design guides for recreational trails
Appropriate design guides include:
    Mountain bike
    Equestrian
    Off-highway vehicle
Recreationaltrailsinfo.org – Tim Johnson for Burke County
Notes: Key Message: FHWA manages the Recreational Trails Program, which funds recreational trails for a wide variety of users, nonmotorized and motorized (e.g., mountain biking, equestrian, off-highway vehicles)
Notes: Recreational trails include trails for many uses, inlcuding:
Walking and wheelchair use
Skating or skateboarding
Equestrian
Nonmotorized snow trail activities including skiing
Bicycling
Other human powered vehicles
Aquatic or water activities
Motorized vehicular activities such as off-road motorcycle, all terrain vehicles, snowmobiling, etc.
In general, the intent is for outdoor recreation and to experience the trail, rather than getting from point A to point B.
Source:
Recreational Trails Program Annual Report. Available: https://www.fhwa.dot.gov/environment/recreational_trails/overview/report/2019/report2019.pdf [Accessed July 2019]
FHWA. “Recreation Trails.” Available: https://www.fhwa.dot.gov/environment/recreational_trails/ [Accessed July 2019]
Image shows part of the Mountains to Sea Trail in North Carolina.

## Slide 9: Benefits of trails

## Slide 10: Not Just Recreation…
Trails
Growth Management
Stewardship
Active Transportation
Economic Development
Water Quality Protection
Floodplain Management
Notes: Key Message: Trails have a foundation in many applications and serve a variety of purposes for a community.
Source: Figure adapted from Chuck Flink.

## Slide 11: Benefits of Trails
Economic
  Generate revenue, increase property values, access to jobs, job creation
Environmental
  Reduced VMT, flood/stormwater management, lower heat island effect
Social
  Improved public health, social interaction and community cohesion
Transportation
  Increased connectivity, low-stress travel, accessibility
Notes: Key Message: Trails and greenways provide numerous benefits to the community. Beyond the creation of recreational spaces, trails serve as accessible and comfortable transportation routes, economic growth generators, community gathering places, and (potentially) greenspace corridors/resource management systems.
Notes:
Trails improve access to employment, as well as generate revenue through tourism, increased foot traffic, and greater accessibility to commercial areas for those without automobiles. The creation of destination trails (e.g Great Alleghany Passage Trail) can promote tourism, which generates revenue for supporting businesses like hotels, restaurants, etc. This is especially important in rural areas.
Trails promote increased rates of physical activity, as well as promoting greater exposure to green space, both of which are linked to greater public health.
Impervious surfaces and green infrastructure have the potential to make trails an important component of environmental management. With careful planning these corridors can be simultaneously used as storm water management systems, wildlife corridors, etc.
Sources:
Source Merriam, D.; Bality, A.; Stein, J.; Boehmer, T. (2017). Improving Public Health through Public Parks and Trails: Eight Common Measures. Summary report. US Department of Health and Human Services, Centers for Disease Control and Prevention and US Department of the Interior, National Park Service.
O’Brien, Sarah, Matt Hayes, Sarah Searcy, Steve Bzomowski, Steven Bert, and Mary Duffy. (2018). Evaluating the Economic Impact of Shared Use Paths in North Carolina. North Carolina Department of Transportation.
American Trails. “Economic Benefits of Trail Tourism.” Available: https://www.americantrails.org/economic-benefits

## Slide 12: Economic Benefits of Trails
North Carolina Department of Transportation
Notes: Key Message: Economic benefits extend beyond the obvious benefits of connection to employment centers and tourism revenue.
Source: O’Brien, S., Hayes, M., Searcy, S., Bzomowski, S., Bert, S., and M. Duffy. (2018). Evaluating the Economic Impact of Shared Use Paths in North Carolina. North Carolina Department of Transportation.

## Slide 13: Trail Design and Accessibility

## Slide 14
Accessible pathway through Living Desert Zoo and Gardens State Park in Carlsbad, New Mexico
Recreationaltrailsinfo.org - New Mexico Energy, Minerals and Natural Resources Department

## Slide 15: Accessibility on Trails
Accessibility ensures that trails are available to all people
Trail should provide:
  Barrier-free access
  Equivalent access
  Comparable experience
Transportation trails should ensure transportation use
Recreational trails should keep a recreational feel
Trailside and trailhead facilities must be accessible
Notes: Key Message: Accessibility is an important part of trail development, because it is key to ensuring that trails are available to all groups, including the young, elderly, and people with disabilities. Because trails can provide both transportation and recreation, designers need to consider which accessibility guidelines apply.
Notes:
Buildings and sites: Standards issued under the Americans with Disabilities Act (ADA) address access in new construction and alterations to State and local government facilities, places of public accommodation, and commercial facilities. Similar standards apply under the Architectural Barriers Act (ABA) to facilities funded by the Federal government. This applies to trailside and trailhead facilities.
Transportation trails: The Access Board is developing new guidelines to cover access to public rights-of-way, including sidewalks, intersections, street crossings, and on-street parking. The Board is also addressing access to shared use paths providing off-road means of transportation and recreation.
Recreation trails: The Architectural Barriers Act (ABA) Accessibility Standards apply to national parks and other outdoor areas directly developed by the Federal government, but not to outdoor areas developed with Federal grants or loans. However, the ABA Outdoor Areas standards are best practices for outdoor recreational facilities, including recreational trails.
As of spring 2019, the U.S. Access Board is developing accessibility guidelines for shared use paths. In 2014, the US Access Board published guidelines for recreational trails (linked below). Shared-use paths are used by pedestrians so they fall under the accessibility requirements of the Americans with Disabilities Act of 1990. Trails for transportation purposes should comply with public rights-of-way guidelines, but trails intended primarily for recreational use may use recreation guidelines.
For accessible recreational trails, the most comprehensive resource is https://www.americantrails.org/resources/design-building/accessible-trails.
Connection to other Module: Module on Accessibility and ADA
Sources:
US Access Board. Available: https://www.access-board.gov/guidelines-and-standards
Rails to Trail Conservancy, webpage on accessibility. Available: https://www.railstotrails.org/build-trails/trail-building-toolbox/design/accessibility/ [Accessed May 2019]
ADA Access on Paved Bikeways, presentation, Michael Jones, Alta Planning & Design (2007) Available: http://www.parks.ca.gov/pages/1324/files/accessible_trails_fri2007.pdf
FHWA. (2006). Designing Sidewalks and Trails for Access. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/sidewalk2/
Public Rights-of-Way and Shared Use Paths: https://www.access-board.gov/guidelines-and-standards/streets-sidewalks
US Access Board (2014). A Summary of Accessibility Standards for Federal Outdoor Developed Areas. Available: https://www.access-board.gov/guidelines-and-standards/recreation-facilities/outdoor-developed-areas/a-summary-of-accessibility-standards-for-federal-outdoor-developed-areas

## Slide 16
Accessible crushed rock trail at the Mark Twain Birthplace State Historic Site in Missouri
Recreationaltrailsinfo.org - Monroe County Commission
Notes: Key Message: The surfaces of trails, passing spaces, and resting intervals must be firm and stable. A firm trail surface resists deformation by indentations. A stable trail surface is not permanently affected by expected weather conditions and can sustain normal wear and tear from the expected uses between planned maintenances.
Notes: Paving with concrete or asphalt may be appropriate for highly developed areas. For less developed areas, crushed stone, fine crusher rejects, packed soil, soil stabilizers, and other natural materials may provide a firm and stable surface. Natural materials also can be combined with synthetic bonding materials to provide greater stability and firmness. These materials may not be suitable for every trail.
Source: United States Access Board (2014). A Summary of Accessibility Standards for Federal Outdoor Developed Areas. Available: https://www.access-board.gov/guidelines-and-standards/recreation-facilities/outdoor-developed-areas/a-summary-of-accessibility-standards-for-federal-outdoor-developed-areas (Section 1017.2)

## Slide 17
Recreationaltrailsinfo.org – NM Energy, Minerals and Natural Resources Department
Recreationaltrailsinfo.org – Montgomery County
Notes: Notes: Remember that accessibility is not just about surface and slope. Consider elements such as handrails, interpretive signage, openings, etc.
Source:
Left image: Rotary Park in Tennessee
Right image: Living Desert Zoo and Gardens State Park in Carlsbad, New Mexico

## Slide 18: Accessibility on Trails
Exceptions for recreational trails:
  Significant impacts
  Alter setting or purpose of the facility
  Prohibited by law
  Impractical due to terrain or construction practices
Make accessible to the extent feasible
Notes: Key Message: Accessibility is important, but in some recreational areas, full accessibility may not be possible. There are some situations where exceptions may be necessary. Entities should consider all design options before using the exceptions. On outdoor recreation access routes, trails, and beach access routes, the exceptions apply only on the portion of the route where the condition applies.
Notes:
These exceptions are for recreational trails, not for shared use paths.
There is no accessibility requirement for trails not intended for pedestrian use, such as mountain bike, equestrian, snowmobile, or off highway vehicle trails. However, trailside and trailhead facilities should be accessible.
Connection to other Module: Module on Accessibility and ADA
Source:
Rails to Trail Conservancy, webpage on accessibility. Accessed May 2019. Available: https://www.railstotrails.org/build-trails/trail-building-toolbox/design/accessibility/
ADA Access on Paved Bikeways, presentation, Michael Jones, Alta Planning & Design (2007) Available: http://www.parks.ca.gov/pages/1324/files/accessible_trails_fri2007.pdf
Designing Sidewalks and Trails for Access. FHWA (2006). Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/sidewalk2/
United States Access Board (2014). A Summary of Accessibility Standards for Federal Outdoor Developed Areas. Available: https://www.access-board.gov/guidelines-and-standards/recreation-facilities/outdoor-developed-areas/a-summary-of-accessibility-standards-for-federal-outdoor-developed-areas
  Conditions for Exceptions: https://www.access-board.gov/guidelines-and-standards/buildings-and-sites/about-the-aba-standards/aba-standards/chapter-10-recreation-facilities#1019%20Outdoor%20Constructed%20Features

## Slide 19: Path Lighting
Pedbikeimages.org – Dan Burden
Notes: Notes: Talking points on the next slide

## Slide 20: Guidelines for Lighting
Lighting can improve safety at night or in dark conditions
Night use: prohibit or permit?
Consider placement of lighting to ensure visibility of:
  Underpasses, tunnels, etc.
  Intersections (public right-of-way)
  Access to popular destinations
Pedestrian-scale lighting
Notes: Key Message: Lighting improves the safety and security of users who travel the path at night. It also ensures their security as they approach destination centers such as hospitals, stores, etc.
Notes:
Lighting is especially important in areas that have reduced visibility, such as tunnels, underpasses, and intersections. Consider placement along access paths to key destinations such as hospitals and schools.
In some cases, night use may be prohibited or restricted. Lighting can be turned on only for select hours (e.g., until 10 pm and after 5 am).
  Where night use is prohibited, it is still necessary to ensure enough lighting at path-roadway intersections, as those intersections occur in the public right-of-way.
Pedestrian-scale lighting uses shorter light poles, with lower lights and closer spacing.
Use best practices at roadway crossings: ensure the lighting makes the trail users visible to the motorists, and not in shadow.
Avoid light pollution: favor lighting that meets Dark Sky policies.
Source: AASHTO. (2012). Guide for the Development of Bicycle Facilities, 4th Ed.

## Slide 21: Green Infrastructure
Stormwater management
  “Catch it where it falls”
  Pervious surfaces allow for natural flow of stormwater
  Reduces volume of water entering sewer system
Habitat & natural spaces
  Pocket parks, green corridors
Green infrastructure and trails
Recreationaltrailsinfo.org - Stuart Macdonald
Notes: Key Message: Green infrastructure is a cost-effective, resilient approach to managing wet weather impacts that provides many community benefits. Trails are an opportunity to create green infrastructure. Integrating green space, tree canopies, and impervious surfaces into trail design can contribute to storm water management efforts as well as increase transportation connectivity. The Federal Highway Administration published several examples in Case Studies in Realizing Co-Benefits of Multimodal Roadway Design and Gray and Green Infrastructure (2018).
Notes: Green infrastructure is designed to collect stormwater where it falls, allowing it to naturally filter into the ground. This reduces the volume of water entering grey infrastructure, reducing potential for flooding, etc. Green corridors and park infrastructure can provide wildlife corridors and ensure habitat protection.
Source:
US Environmental Protection Agency. “What Is Green Infrastructure.” Available: https://www.epa.gov/green-infrastructure/what-green-infrastructure
FHWA. (2018). Case Studies in Realizing Co-Benefits of Multimodal Roadway Design and Gray and Green Infrastructure. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_green_infrastructure/

## Slide 22: Trail crossings
Notes: Key Message: Nearly every trail will intersect with the road network. The designer needs to ensure safe crossings for trail users and motorists. There are right ways and wrong ways to construct trail crossings.
Notes:
Student Question:
Connection to other Module:
Source:
Proven Safety Countermeasures: https://safety.fhwa.dot.gov/provencountermeasures/

## Slide 23: Guiding Principles
Best practices for pedestrian crossings apply
Minimize trail users’ exposure to traffic
  Medians, perpendicular intersections, etc.
  Reduce speeds of approaches to crossings
Right-of-way considerations
  Pedestrian and bicyclists may have separate right-of-way laws
  Consider local laws in design
Minimize use of bollards and gates
Notes: Key Message: Most best practices guidelines for intersections apply to path crossings.
Notes:
Minimizing path users’ exposure to traffic. This can be achieved through intersection medians and other crossing treatments. Wherever possible, design path routes to create perpendicular intersections
Reduce speeds for path users and road users. This can minimize conflicts and give all parties additional time to recognize and yield right-of-way as appropriate.
In some states, bicyclists share pedestrian right-of-way, and in some they do not. When planning intersections between trails and roads, consider local laws. In uncontrolled intersections, pedestrians may have right-of-way while bicyclists do not. Plan crossing treatments to ensure safe and reasonable flow for trail users of multiple modes.
Bollards are crash hazards. They are generally ineffective, because a determined person will go around. Do not use bollards to control trail access unless there are no other options. If installed, bollard, gates, fences, or other barriers:
  Must not restrict access for people with disabilities.
  Must be easily visible, especially in low light conditions. Section 9C.03 of the MUTCD.
  Should have enough sight distance to allow users to adjust speed.
  Should permit passage, without dismounting, for adult tricycles, bicycles towing trailers, and tandem bicycles.
Connection to other Module: Intersections
Sources:
Federal Highway Administration. (2016) Small Town and Rural Multimodal Networks
AASHTO. (2012) Guide for the Development of Bicycle Facilities 4th Ed.
Federal Highway Administration. “Bollards, Gates, and Other Barriers.” Available: https://www.fhwa.dot.gov/environment/recreational_trails/guidance/bollards_access.cfm [Accessed June 2019].

## Slide 24: Crossing Types
Controlled vs. uncontrolled
  Where uncontrolled, consider warning signs, speed reductions, crossing treatments
Grade-separated
  Safer in high-traffic, high-speed areas
  Less connectivity between trail and roadway
  Expensive
Recreationaltrailsinfo.org – Stuart MacDonald
Pedbikeimages.org – Dan Burden
Notes: Notes:
Controlled crossings include yield- and stop-controlled crossings for both path users (bicyclists, pedestrians) and road traffic. In cases where there is greater path traffic than vehicle traffic, it may be more practical to use stop controls on road traffic. In cases where there is greater volume or faster flow of vehicle traffic in crossings, it may be better to place intersection controls on path users or provide additional measures for drivers like an RRFB or PHB (shown on following slides).
At uncontrolled crossings, visible marked crossings should be placed unless pedestrian counts are especially low. Where traffic speeds exceed 40 mph, and traffic volumes are high, it is recommended to incorporate speed reductions, traffic calming devices, warning signs, etc. into roadways.
Sources:
Federal Highway Administration. (2016) Small Town and Rural Multimodal Networks
AASHTO. (2012) Guide for the Development of Bicycle Facilities 4th Ed.

## Slide 25: Trail Crossing – Good? Bad?
Pedbikeimages.org – Dan Burden
Notes: Student Question: Ask students what’s wrong with this photo. What is right? Are there things that aren’t wrong, but could be better?
[Examples of “wrong” include the presence of bollards and the lack of detectable warnings on the ramp and refuge island. “Right” could be the presence of the median, which provides a refuge for users who need to cross one side of the road at a time. “Better” could include a raised crossing, advance stop/yield lines (these may not be visible in the photograph)]

## Slide 26: Crossing Treatments - RRFBs
Rectangular Rapid-Flashing Beacons
Used at marked midblock crossings
FHWA, Safe Transportation for Every Pedestrian
Notes: Key Message: The RRFB is a device used in combination with warning signs to provide a high-visibility strobe-like warning to drivers when trail users are in a crosswalk. Research shows that driver yielding rates can be as high as 98% but yielding rates as low at 19% have also been noted in the research.
Notes:
Device includes to rectangular-shaped yellow indications, each with an LED-array based light source, that flash with high frequency when activated by a pedestrian.
Particularly effective at multilane crossings with speed limits less than 40 mph. For roadways with higher speeds, the Pedestrian Hybrid Beacon may be appropriate (shown on next slide).
Often used in combination with pedestrian refuge islands, crosswalk visibility enhancements, and advance stop or yield markings and signs (as shown in the figure on the slide).
Connection to other Module: Designing for Walking and Bicycling
Sources:
Federal Highway Administration. (2016). Small Town and Rural Multimodal Networks
AASHTO. (2012) Guide for the Development of Bicycle Facilities 4th Ed.

## Slide 27: Crossing Treatments - PHBs
Pedestrian Hybrid Beacons
Used on high speed, multilane roads at unsignalized locations
FHWA, Safe Transportation for Every Pedestrian
Notes: Key Message: A PHB is a special type of beacon used to warn and control traffic at an unsignalized location to assist people crossing a street or highway at a marked crosswalk.
Notes:
Pedestrian Hybrid Beacon (PHB) is used on higher speed roads with multiple lanes of traffic.
Device consists of two red lenses above a single yellow lens. It rests in dark until activated. When activated, the beacon displays a sequence of flashing and solid lights that indicate the pedestrian walk interval and when it is safe for drivers to proceed.
Often used on roads where traffic speeds are high but where warrants to install a full signal are not met.
Often used in combination with raised islands, high visibility crosswalk markings, and advance stop or yield markings and signs.
Connection to other Module: Designing for Walking and Bicycling
Sources:
Federal Highway Administration. (2016). Small Town and Rural Multimodal Networks
AASHTO. (2012) Guide for the Development of Bicycle Facilities 4th Ed.

## Slide 28: Sidepath Considerations
Conflicts with perpendicular and parallel roads
  Consider turning vehicles
  Driver conditioning
    Path users travelling in unexpected directions creates ‘virtual blind spots’
Separation distance in intersection
  Increase separation in high-speed intersections
Notes: Key Message: Because they are sited adjacent to roadways, sidepaths pose additional challenges at intersections. When designing an intersection between a sidepath and a perpendicular road, the interactions with users of the parallel road must also be considered.
Notes:
Vehicles turning onto the parallel roadway are not conditioned to look for traffic approaching from behind them, as is the case with two-way sidepaths,. This creates ‘virtual blind spots’, or areas where drivers do not anticipate traffic to approach from and so do not look for intently.
  Additional signage warning drivers to check for pathway traffic approaching from behind may help reduce conflicts. Additionally, reducing the speed of vehicles on both perpendicular and parallel roads can reduce likelihood of crashes at crossings.
At high speed crossings, increasing the sidepath distance from parallel roads can increase path user comfort and reduce collisions. In low-speed crossings, the path should be routed closer to the parallel road to aid drivers in recognizing people crossing.
Sources:
Federal Highway Administration. (2016). Small Town and Rural Multimodal Networks
AASHTO. (2012) Guide for the Development of Bicycle Facilities 4th Ed.

## Slide 29: Rail Crossings
Special considerations when multi-use paths cross railroad tracks
  Minimize at-grade crossings if possible—above or below grade crossings are ideal
  Things to consider
    Location of the crossing
    Sight distance
    Angle and grade of the crossing
    Crossing surface
    Lighting
    Warning devices and signage
Rails to Trails Conservancy – Anthony Le
Notes: Key Message: Crossing a railroad tracks requires special considerations, regardless of whether the rail line is currently active.
Notes:
Location of the crossing – a good location will help minimize illegal crossings. It should not be near where trains usually stop, or near a curve or other feature which will reduce sight distance. Many of the same considerations that are considered when designing a road crossing will not operate in the same manner for bicyclists and pedestrians as it is easier for them to continue across.
Sight distance – a rail crossing must have adequate sight distance so that users can see a train coming. Users must also have enough time to be alerted to the crossing itself, come to a stop, and be aware of a train approaching.
Angle and grade of the crossing – bicyclists needs to cross railroad tracks at as close to a 90-degree angle as possible. If the approach angle is less, a wider concrete area can help a cyclist steer across at closer to perpendicular. The AASHTO bike guide and ADA specify grade requirements for a shared use path.
Crossing surface – the crossing surface should be the same or very similar to the shared use path. It should be slip resistant and smooth. ADA requires tactile warning strips for pedestrians prior to rail crossings.
Lighting – crossings should follow best practices with regards to lighting. Lights must be shielded from the locomotive driver.
Warning devices and signage – warning devices and signage guidance can be found in the MUTCD. Additional trail specific signage which encourages safe behavior can be installed. Two types of warning devices exist, active advance warnings, which actively alert users to the presence of the crossing or an oncoming train, and passive advance warnings which do not detect users or rail traffic.
Connection to other Module: The module Safety Analysis includes a video showing how rail tracks can create a dangerous obstacle for bicyclists.
Sources:
AASHTO. (2012) Guide for the Development of Bicycle Facilities 4th Ed.
FHWA. (2002). Rails With Trails: Lessons Learned. [NOTE: An updated version of this guide is underway as of 2019].

## Slide 30: Trail SIGNAGE

## Slide 31: Signage and Surface Marking
Wayfinding
Interpretive signage
Mile markers
Regulatory
Recreationaltrailsinfo.org- NYS Office of Parks, Recreation & Historic Preservation
Notes: Key Message: Signage can enhance the trail user’s experience by enhancing safety and also by pointing out landmarks, features, and stories associated with the trail.
Notes:
Branding
  Important to create a unified visual identity for the trail – helps promote the trail as an amenity.
Wayfinding
  Useful on most trails, especially complex trail systems.
  Can include mileage and other relevant messaging.
  Can point to locations off the trail as well as on the trail.
Interpretive
  Helps connect users to the trail by providing background, history, and information about the surrounding natural area.
  Can also include trail rules and regulations, and reminders of etiquette of trail use (shown on next slide).
Mile markers
  Can be placed at regular intervals on the trail.
  Helpful for those who use the trail for exercise, also for emergency response needs.
Regulatory
  Look to the MUTCD guide – Part 9 contains guidance relating to bicyclists, Part 2 contains information on warning signage, but this must be scaled to trail use.
  Important to consider size, placement and frequency of safety and other regulatory signs.
Sources:
AASHTO. (2012) Guide for the Development of Bicycle Facilities 4th Ed.
Rails to Trails ‘Signage and Surface Markings’ Available: https://www.railstotrails.org/build-trails/trail-building-toolbox/design/signage-and-surface-markings/ [Accessed May 2019]
Trail Signage Guidelines City of San Jose. Available: https://www.sanjoseca.gov/DocumentCenter/View/76027 [Accessed May 2019]

## Slide 32
Rails to Trails Conservancy – Anthony Le
Recreationaltrailsinfo.org – Stuart Macdonald
Notes: Left image: Monon rail trail in Indiana
Right image: Lackwanna River Heritage Trail in Carbondale

## Slide 33: Evaluation and funding

## Slide 34: Monitoring and Evaluation
  Economic impact analysis
  Trail use monitoring and user surveys
  Maintenance and inventory
Pedbikeimages.org – Dan Burden
Notes: Key Message: It’s important to monitor and evaluate trail usage and conditions. Understanding who is using the trail, when, and why can help support the case for future investment, guide maintenance plans, and dictate programming and other needs.
Notes:
Economic Impact – communities that invest in trails often want to know what impact the infrastructure is having economically.
User counts and traffic monitoring:
  Understanding trail usage is key to the ongoing maintenance of a trail.
  Establishing a count program on the trail will result in concrete data which can inform many decisions.
  User surveys can tell more of the story – for example – trip purpose, more detailed user demographics.
  Understanding the response to programming along the trail can help shape future programming decisions.
Maintenance – being able to monitor the trail use and conditions is important to be able to:
  Inform maintenance planning.
  Identify trouble spots or maintenance issues.
  Maintain awareness of user and/or traffic conflicts that need addressing.
Understanding trail use can also help with mitigating adverse impacts on the natural environment around the trail.
Note: the Highway Capacity Manual now contains a Level of Service calculation for Shared Use Paths.
Trail mapping is helpful for many reasons. Many organizations keep detailed GIS inventories of their trail systems.
Rails to Trails is working on piloting an assessment tool called T-Map, which will measure trail connectivity, assist with forecasting and demand modeling and help assess economic and health impacts of trails: https://www.railstotrails.org/our-work/research-and-information/trail-modeling-and-assessment-platform/
Connection to other Module: Modules on Facility Evaluation and Data and Applications of Data Collection
Sources: Rails to Trails ‘Trail Use: Evaluation, Programming and Management’ Available: https://www.railstotrails.org/build-trails/trail-building-services/trail-use-evaluation-programming-and-management/ [Accessed May 2019].
Image: http://pedbikeimages.com/mediumimages/pittsford.sunday.3(168).jpg

## Slide 35: Funding Sources
Federal Highway Programs
  Congestion Mitigation and Air Quality Improvement Program (CMAQ)
  Surface Transportation Block Grant Program (STBG)
  Transportation Alternatives (TA) Set-Aside
  Recreational Trails Program (RTP)
  Federal Lands Transportation Program
  Federal Lands Access Program
Department of the Interior Programs
  Land and Water Conservation Fund (LWCF)
State Programs
Foundation Grants
Notes: Key Message: There are several Federal sources for funding all kinds of trails. Some States have their own programs, and some foundations will support trails.
Notes: The Federal Surface Transportation Program has many possible funding sources for trails and for active transportation. We list the most likely programs here:
Congestion Mitigation and Air Quality Improvement Program (CMAQ): Must demonstrate a reduction of vehicle emissions. The most likely trail projects are trails that provide access to public transportation or that can demonstrate a likely mode shift from driving to bicycling and walking.
Surface Transportation Block Grant Program (STBG): In theory, any recreational trail is eligible under STBG, but State DOTs will only use these funds for projects that benefit transportation.
Transportation Alternatives (TA) Set-Aside: This is the single largest source of funds for trails for transportation purposes, including rail trails.
Recreational Trails Program (RTP): This is the single largest source of funds for Recreational Trails.
Federal Lands Transportation Program: Provides funds to Federal Land Management agencies for projects that provide access to or within Federal lands. This may include trails.
Federal Lands Access Program: Provides funds to State and local governments for projects that provide access to or within Federal lands. This may include trails.
Department of the Interior Program
Land and Water Conservation Fund (LWCF): Provides funds to support conservation and recreation projects, which may include trails.
State Programs: A few States have State grant programs for trails.
Foundation Grants: Several foundations will provide grants for trail projects.
Source: FHWA. “Funding Information,” Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/funding/ [Accessed June 2019]

## Slide 36: Congestion Mitigation and Air Quality Improvement Program (CMAQ)
Can be utilized in transportation projects to meet requirements of Clean Air Act
  Reduction of congestion
  Improvement of air quality
Nonattainment & maintenance areas
Major source for ped & bike projects
Notes: Notes:
CMAQ provides a flexible funding source to State and local governments for transportation projects and programs to help meet the requirements of the Clean Air Act. Funding is available to reduce congestion and improve air quality for areas that do not meet the National Ambient Air Quality Standards for ozone, carbon monoxide, or particulate matter (nonattainment areas) and for former nonattainment areas that are now in compliance (maintenance areas).
CMAQ is a significant funding source for pedestrian and bicycle projects in nonattainment areas, especially to provide access to transit.
Source:
FHWA. (n.d.) Congestion Mitigation and Air Quality Improvement Program Fact Sheet. https://www.fhwa.dot.gov/fastact/factsheets/cmaqfs.cfm
FHWA. (n.d.) Bicycle and Pedestrian Program Funding Information. https://www.fhwa.dot.gov/environment/bicycle_pedestrian/funding/

## Slide 37: Transportation Alternatives
Largest funding source for ped & bike projects
Used by States and large Metro planning areas
Project types:
  On and off-road ped & bike facilities
  Non-driver accessed to public transportation
  Community improvement activities
  Environmental impact mitigation
  Recreational trails
  Safe Routes to School
Notes: Key Message: The Transportation Alternatives (TA) Set-Aside provides funds for pedestrian and bicycle projects, historic preservation, and environmental projects. Each State solicits and selects projects for funding. Metropolitan planning areas representing urbanized areas with populations greater than 200,000 also solicit and select projects for funding.
Notes:
The TA Set-Aside authorizes funding for programs and projects defined as transportation alternatives, including on- and off-road pedestrian and bicycle facilities, infrastructure projects for improving non-driver access to public transportation and enhanced mobility, community improvement activities such as historic preservation and vegetation management, and environmental impact mitigation related to stormwater and habitat connectivity; recreational trail projects; and Safe Routes to School projects.
The TA Set-Aside is the single largest funding source for pedestrian and bicycle projects.
Source:
FHWA. (n.d.) Transportation Alternatives. https://www.fhwa.dot.gov/environment/transportation_alternatives/
FHWA. (n.d.) Bicycle and Pedestrian Program Funding Information. https://www.fhwa.dot.gov/environment/bicycle_pedestrian/funding/

## Slide 38: Recreational Trails Program
Federal transportation funds can be used for recreational trails
  RTP funds set-aside of Transportation Alternatives
  Funding to build and maintain trails for both motorized and nonmotorized uses
Recreationaltrailsinfo.org – Tim Johnson for Burke County
Notes: Key Message: The Recreational Trails Program provides funds for a wide variety of recreational trail uses, nonmotorized and motorized. Each State solicits and selects projects for funding.
Notes:
The Recreational Trails Program funds trails for many uses: pedestrian (including wheelchair); skating or skateboarding; equestrian; nonmotorized snow trail activities including skiing; bicycling; or other human powered vehicles, aquatic or water activities, and motorized vehicular activities such as off-road motorcycle, all terrain vehicles, snowmobiling, etc.
The RTP supports community facilities that contribute to economic development, habitat improvement, effective partnership development, public land stewardship, safe recreation, and inclusion on trails.
In some cases recreational trails can be components of transportation systems.
In general, RTP funded trails are primarily for recreation, not transportation. Do not insist on highway designs.
Source:
Recreational Trails Program Annual Report. Available: https://www.fhwa.dot.gov/environment/recreational_trails/overview/report/2019/report2019.pdf [Accessed July 2019]
FHWA. “Recreation Trails.” Available: https://www.fhwa.dot.gov/environment/recreational_trails/ [Accessed July 2019]
Image shows part of the Mountains to Sea Trail in North Carolina

## Slide 39: Summary
Trails serve as a complement to and extension of on-street facilities (not as alternatives to them)
Economic benefits extend beyond the obvious benefits of connection to employment centers and tourism revenue
There is specific guidance for trails related to accessibility, lighting, signage, and green infrastructure
Best practices for pedestrian crossings apply to trail crossings