## Slide 1: Accessibility and the Americans with Disabilities Act (ADA)
Instructor course information
Notes: Report No. FHWA-SA-19-034
Key Message: For pedestrians with disabilities, details matter, and poor design can be a barrier to travel. Design and infrastructure should serve mobility needs of all pedestrians.
Notes: As of the 2010 Census, over 56 million (18 percent) Americans 15 years and older and 52 percent of Americans age 65 and over have a disability.

## Slide 2: Module Outline
Legal history
Sidewalks
Crossings
Intersections
Shared streets

## Slide 3: Some Disabilities are Obvious
pedbikeimages.org – Dan Burden
Notes: Key Message: It is easy to recognize that people in wheelchairs or using walkers or canes have specific design needs.
Source: Adapted from M. Ronkin and C. Zegeer slides developed for North Carolina Department of Transportation (2005).
Image (right): http://www.pedbikeimages.org/mediumimages/montreal.2.(4).jpg

## Slide 4: Some Disabilities are Less Obvious
North Carolina DOT
Notes: Key Message: ADA also covers disabilities that have no outward manifestations, such as people with low vision or older adults who may have limited mobility. By designing for people with disabilities, we are designing for everyone, especially as we get older.
Source: Adapted from M. Ronkin and C. Zegeer slides developed for North Carolina Department of Transportation (2005).

## Slide 5: Legal History

## Slide 6: Legal History on Accessibility
1973
Rehabilitation Act (Section 504)
1990
Americans with Disabilities Act
2011
Proposed Guidelines for Pedestrian Facilities in the Public Right-of-Way (PROWAG)

## Slide 7: Legal History on Accessibility
Section 504 of the Rehabilitation Act (29 U.S.C. §794) and Title II of the Americans with Disabilities Act (ADA) (42 U.S.C. §§ 12131-12164) work together to require that recipients of federal financial assistance from USDOT and public agencies make public rights-of-way accessible for all pedestrians with disabilities
Notes: Notes: FHWA requirements under the ADA and Section 504 of the Rehabilitation Act of 1973 include oversight of State and local entities and recipients of Federal funds that are responsible for roadways and pedestrian facilities to ensure that they do not discriminate on the basis of disability in any highway transportation program, activity, service, or benefit they provide to the public.
Source:
FHWA Civil Rights Office. (n.d) “Americans with Disabilities Act (ADA).” https://www.fhwa.dot.gov/civilrights/programs/ada/ [Accessed May 2019]
FHWA Civil Rights Office. (n.d) “Questions and Answers about ADA/Section 504.” https://www.fhwa.dot.gov/civilrights/programs/ada/ada_sect504qa.cfm#q1
[accessed May 2019]

## Slide 8: Standards vs. Guidelines
The current enforceable accessibility standards for buildings and sites:
  DOJ ADA Standards adopted in 2010
  The 2010 ADA Standards also apply to curb ramps at intersections in the public right-of-way
Accessibility Guidelines:
  Developed by the U.S. Access Board
  Must be adopted by another responsible agency (DOJ or USDOT) to be enforceable
Notes: Key Message: The ADA standards focus mainly on facilities and sites and address some common features of sidewalks (like curb ramps), but further guidance is needed to address other conditions and constraints specific to public rights-of-way.
Notes: The responsible agencies would be the U.S. Department of Justice and the U.S. Department of Transportation.
Source: Public Right-of Way Accessibility Guidelines, (PROWAG), Juliet Shoultz, P.E, Transportation Systems Engineer, US Access Board.

## Slide 9: PROWAG
The Draft Guidelines are not enforceable standards
Public entities may refer to them for assistance in addressing the accessibility of facilities in the public right-of-way that are not addressed by the present DOJ ADA 2010 Standards (i.e., for facilities other than curb ramps at intersections).
Notes: Key Message: PROWAG refers to guidelines for public rights of way, including streets, sidewalks, and shared use paths.
Source:
FHWA. “Pedestrians and Accessible Design.” Available: https://www.fhwa.dot.gov/programadmin/pedestrians.cfm
FHWA. (January 23, 2006). Public Rights-of-Way Access Advisory.

## Slide 10: PROWAG covers:
Pedestrian access routes (including sidewalks, street crossings, curb ramps/blended transitions)
Detectable warning surfaces
Pedestrian signals
Roundabouts
On-street parking and passenger loading zones
Transit stops and shelters
Street furniture and other elements
Shared use paths (2013 revision)
Notes: Source:
United States Access Board. (2011) Proposed Accessibility Guidelines for Pedestrian Facilities in the Public Right-of-Way (PROWAG). Washington, D.C.
United States Access Board. “About the Rulemaking on Shared Use Paths.” Washington, D.C.: Available: https://www.access-board.gov/guidelines-and-standards/streets-sidewalks/shared-use-paths [Accessed May 2019]

## Slide 11: Transition Plans
The ADA requires public agencies with more than 50 employees to prepare a plan detailing how they will fix the facilities in their public right-of-way that are not currently accessible to individuals with disabilities
Should be coordinated with pedestrian master plans
Transition planning components:
  Identify physical obstacles to accessibility in PROW facilities
  Describe in detail the methods that will be used to make the facilities accessible
  Specify the schedule for taking the necessary steps to achieve compliance during each year of the transition period
  Indicate the official responsible for implementing the plan
Notes: Key Message: Inventories are often need for ADA Transition Plans, so this effort should be coordinated with any Pedestrian Master Planning efforts.
Source:
ITE, & Meyer, M. D. (2016). Transportation planning handbook, Chapter 13.
FHWA Civil Rights Office, Q&A, https://www.fhwa.dot.gov/civilrights/programs/ada/ada_sect504qa.cfm#q10 [accessed May 2019].

## Slide 12: Example: ADA Transition Plan
Eugene, Oregon, has a plan that was updated in 2015
Annual progress reports and an update every eight years since first plan in 1993
“[The City]….considers the Plan to not be just a fulfillment of a federal requirement, but rather an instrument by which the City can provide a richer mobility experience, to the extent possible, to persons with disability within the community.”
Notes: Notes: The plan’s title is Americans with Disabilities Act Transition Plan for Accessibility in Public Rights-of Way
Source: City of Eugene. Americans with Disabilities Act Transition Plan for Accessibility in Public Rights-of Way. Available:
https://www.eugene-or.gov/DocumentCenter/View/20712/2015_ADA_Transition_Plan_w_Annual_Updates?bidId=

## Slide 13: How Disabilities may affect travel

## Slide 14: Range of Disabilities
“To adequately provide for persons with disabilities, the designer should be aware of the range of disabilities to expect so that the design can appropriately accommodate them” –AASHTO Green Book (2018)
Including:
  Mobility disabilities
  Vision disabilities
  Cognitive disabilities
  Hearing disabilities
Notes: Notes: Emphasize that the ADA does not name disabilities; those listed on the slide are examples called out in the AASHTO Green Book.
Source: AASHTO. (2018). A Policy on the Geometric Design of Highways and Streets. Page 2-53.

## Slide 15: Mobility Disabilities
Stairs, curbs, narrow sidewalks, obstructed sidewalks, and irregular pavement surfaces are major obstacles
Some persons are able to walk without assistive devices, but often slowly and with difficulty
Aids include braces, canes, crutches, wheelchairs, scooters, or other devices

## Slide 16: Types of Vision Loss
FHWA
Notes: Source: FHWA. (2017). Accessible Shared Streets: Notable Practices and Considerations for Accommodating Pedestrians with Vision Disabilities. Report No. FHWA-HEP-17-096. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/accessible_shared_streets/index.cfm
Image (left): https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/accessible_shared_streets/images/figure07.png
Image (right): https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/accessible_shared_streets/images/figure07.png

## Slide 17: Vision Disabilities
Pedestrians with low vision:
  May have difficulty with depth perception
  May have reduced contrast sensitivity
  May have more difficulty in low light situations
  Are likely to have difficulty with glare
  Have difficulty reading signs and signals
Notes: Notes: Problems with depth perception mean that someone may have difficulty judging the approach speed of cars, trucks, and bicycles and judging the location of obstacles in their path. Reduced contrast sensitivity means that someone may not be able to see colors or color contrast accurately or distinguish a hole from a shadow.
Source: Slide by Janet Barlow (April 2019)

## Slide 18: Navigating with a Vision Disability
Non-visual cues used to navigate the street:
  Audible information
  Detectable edges
  Information received through touch
  Movement of other roadway users
  Visual contrast, via tone or color
  Direction of the sun or wind, which sometimes aid in maintaining orientation
Notes: Notes: Streets include a variety of cues that indicate where to walk and where and when to cross (i.e., sidewalk edges, curb ramps, crosswalk markings, pedestrian signals, and the sight and sound of vehicle and pedestrian movement). Often these are the same elements pedestrians with vision disabilities use for navigation (listed on the slide).
Source: FHWA. (2017). Accessible Shared Streets: Notable Practices and Considerations for Accommodating Pedestrians with Vision Disabilities. Report No. FHWA-HEP-17-096. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/accessible_shared_streets/index.cfm

## Slide 19: Navigating with a Vision Disability
Navigational aids include:
  Human guides
  Long white canes
  Dog guides
  Telescopes or other low vision aids
  Emerging technologies
  No aids!
Notes: Notes: Streets include a variety of cues that indicate where to walk and where and when to cross (i.e., sidewalk edges, curb ramps, crosswalk markings, pedestrian signals, and the sight and sound of vehicle and pedestrian movement). Often these are the same elements pedestrians with vision disabilities use for navigation (listed on the slide)
Human guides are used in specific situations (as opposed to everyday travel).
White canes may be used by individuals to probe the environment.
Only a small percentage of blind or visually impaired people use dog guides as a travel aid. Dog guides respond to commands from their human handlers and do not make decisions about routes or street crossings.
Telescopes are used primarily for reading signs.
Emerging technologies, such as digital navigation/wayfinding applications and hand-held devices that use ultrasonic echo-location to help pedestrians with vision disabilities detect objects. It is important to keep in mind that persons with vision disabilities could also have cognitive disabilities that might make reliance on technology difficult.
Source:
Slide adapted from Janet Barlow (April 2019)
FHWA. (2017). Accessible Shared Streets: Notable Practices and Considerations for Accommodating Pedestrians with Vision Disabilities. Report No. FHWA-HEP-17-096. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/accessible_shared_streets/index.cfm

## Slide 20: Cognitive Disabilities
Pedestrian signals and other pedestrian-related facilities should be:
  Simple
  Straightforward
  Consistent in their meaning
Notes: Notes: Cognitive disability is a term used when a person has certain limitations in mental functioning and in skills such as communicating, taking care of him or herself, and social skills.
Source: AASHTO. (2018). A Policy on the Geometric Design of Highways and Streets. Page 2-53.

## Slide 21: Hearing Disabilities
Important design considerations:
  Clear sightlines relatively free of visual obstructions
  Signage should be clear and placed in conspicuous locations
  Pedestrian signals should communicate the pedestrian signal phase in multiple formats, including vibrotactile
Notes: Source: AASHTO. (2018). A Policy on the Geometric Design of Highways and Streets. Page 2-53.

## Slide 22: Designing for Accessibility

## Slide 23: Sidewalks - General Principles
Sidewalk surface should be smooth
Sidewalk should be wide enough
Sidewalk should be clear of obstructions
Driveways should not slope excessively
When site conditions create constraints, providing accessibility to the extent practicable or feasible may be acceptable
Notes: Connection to Other Module: User and Mode Characteristics and Designing for Walking and Bicycling
Source: Ronkin, M. & Zegeer, C. (2005). Planning and designing streets for pedestrians. Powerpoint presentation prepared for North Carolina Department of Transportation.

## Slide 24: Sidewalks
Sidewalks should be clear of obstructions
  Draft PROWAG recommends 5’ minimum clear width
North Carolina DOT
Notes: Notes: All pedestrian facilities must meet ADA requirements. A clear travel way should be maintained by keeping a sidewalk clear of obstructions. The minimum “Pedestrian Access Route” is a continuous and unobstructed clear width that should be measured from the back of the curb (when furniture zone is not present). The zone system is helpful for illustrating this point (shown on the next two slides). Randomly arranged street furniture clutters the sidewalk and creates an “obstacle course.”
Connection to other Module: Designing for Walking and Bicycling
Source: Ronkin, M. & Zegeer, C. (2005). Planning and designing streets for pedestrians. Powerpoint presentation prepared for North Carolina Department of Transportation.

## Slide 25: The Zone System - Residential
FHWA/PBIC
Notes: Notes: The pedestrian environment may include the entire width of the environment, but a pedestrian zone should remain clear.
Connection to other Module: Designing for Walking and Bicycling
Source: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 26: The Zone System - Commercial
FHWA/PBIC
Notes: Notes: Same as previous slide, but in a dense urban environment. Designers may need to acknowledge the frontage and furniture zones that may encroach on available and usable pedestrian space, and all zones are important to include for a successful and vibrant pedestrian environment.
Connection to other Module: Designing for Walking and Bicycling
Source: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 27: Sidewalks
Cross-slope
  Draft PROWAG recommends 2% maximum with limited exceptions
  To allow for construction tolerance, designing sidewalks for 1.5% cross slope is a good practice
  Including at driveways
Notes: Notes: Cross-slope is set at 2% max to prevent tilting, but some slope is needed for drainage. Ideally, cross slope should be no more than 2% everywhere.
Exceptions at some crossings from PROWAG Ch R3: “Except as provided in R302.6.1 and R302.6.2, the cross slope of pedestrian access routes shall be 2 percent maximum.”
R302.6.1: Cross slope can be 5 percent maximum at pedestrian street crossings without yield or stop control.
R302.6.2: Permits pedestrian access route cross slope to match the grade of the street for midblock crossings.
Source: ADA for Roadway Design [PowerPoint Presentation] (2016). TRB Tools of the Trade. Dean Perkins, Florida DOT.

## Slide 28: Curb Ramps at Intersections
2 ramps at each corner are preferred
Level landings compliant with DOJ ADA 2010 Standards must be provided (unless impracticable or infeasible)
Max 1:12 ramp slope (with limited exceptions)
FHWA
Notes: Notes: Curb ramp design is especially important for wheelchair users. Corners should typically have two curb ramps, one for each street that is to be crossed. Curb ramps should also be designed to include level landings, without which the sidewalk can be quite difficult to navigate in a wheelchair (as shown in image on the right).
Source: Federal Highway Administration. (2001). Designing sidewalks and trails for access, Part II of II: Best practices design guide. Available at http://www.fhwa.dot.gov/environment/sidewalk2/

## Slide 29: Detectable Warnings
Does: replace missing edge cue (i.e., curb)
Does not: designate the best place to cross or provide alignment information
Minimum of 24 inches in direction of pedestrian travel
FHWA
Notes: Notes: Detectable warnings, a distinctive surface pattern of domes detectable by cane or underfoot, are used to alert people with vision impairments of their approach to streets and hazardous drop-offs. The ADA Accessibility Guidelines (ADAAG) require these warnings on the surface of curb ramps, which do not have the tactile cue otherwise provided by curb faces, and at other areas where pedestrian ways blend with vehicular ways. Detectable warnings must be installed in a color that contrasts with the adjoining surface, either light on dark or dark on light.
Source: ADA for Roadway Design [PowerPoint Presentation] (2016). TRB Tools of the Trade. Dean Perkins, Florida DOT.

## Slide 30: Pedestrian Street Crossings
Design elements that reduce the amount of time a person is in the street:
  Curb extensions
  Pedestrian refuge islands
Pedestrian signals should include visual, audible, and vibrotactile information (APS)
Pedestrian signals should provide adequate crossing time (≤3.5 feet/second)
Pedbikeimages.org – Carl Sundstrom
Notes: Notes: This image shows curb extensions that reduce the crossing distance.
Source:
Image: http://www.pedbikesafe.org/PEDSAFE/cm_images/CurbExt1.jpg

## Slide 31: Pedestrian Street Crossings
FHWA
Notes: Notes: This rendering shows how detectable warnings should be used on geometric design features that reduce crossing distance – curb extensions and a pedestrian refuge island.
Source: Federal Highway Administration, Safe Transportation for Every Pedestrian. Available: https://safety.fhwa.dot.gov/ped_bike/step/ [Accessed July 2019]

## Slide 32: Accessible Pedestrian Signals (APS)
Communicates information about pedestrian timing in nonvisual format such as audible tones, verbal messages, and/or vibrating surfaces (MUTCD, Section 4A.02)
MUTCD 4E.08 provides guidance on locating pushbuttons and APS devices
Required features of APS (MUTCD 4E.09-4E.13)
  Pushbutton locator tone
  Audible and vibrotactile indications of the WALK
  Tactile arrow aligned with the direction of travel on the crosswalk
  Automatic volume adjustment
Notes: Notes: Proposed PROWAG requires APS where pedestrian signals are installed.
Source: National Academies of Sciences, Engineering, and Medicine (2011). Accessible Pedestrian Signals: A Guide to Best Practices (Workshop Edition 2010). Washington, DC: The National Academies Press. https://doi.org/10.17226/22902.

## Slide 33: Roundabouts
Principles for designing roundabouts for those using non-visual cues:
  Use features to guide pedestrians away from where they should not cross
  Orient curb ramps in the direction of the crosswalk
  Ramps, channelization and splitter islands should all align
NCHRP
Notes: Notes: The image shows landscaping that discourages crossing to the central island and provides an edge that blind pedestrians can follow (i.e., trail) with the long cane to locate a curb ramp. Three principles for designing crosswalks for people who rely on nonvisual information are:
Landscaping, fences, or other features should restrict the ability of pedestrians to cross at locations other than crosswalks, or at least make it very clear where crossing is not intended and provide guidance to the crosswalk location.
Curb ramps should be oriented so that the running slope is in the same direction as the crosswalk and/or the edges of landscaping or ramps should be aligned in the direction of travel on the crosswalk.
The far side of the crosswalk and any channelization and splitter islands should be aligned with the nearside ramp and should be designed to compensate for the expected error in the crossing angle.
Source:
National Academies of Sciences, Engineering, and Medicine (2017). Crossing Solutions at Roundabouts and Channelized Turn Lanes for Pedestrians with Vision Disabilities: A Guidebook. Washington, DC: The National Academies Press. https://doi.org/10.17226/24678.
U.S. Access Board, “Modern Roundabouts,” Available: https://www.access-board.gov/enforcement/221-research/research-on-public-rights-of-way/modern-roundabouts. [Accessed June 2019].

## Slide 34: Separated Bike Lanes
Plan and design for accessible pedestrian routes across SBLs to:
  Transit stops and platforms
  Parking lots
  Midblock accessible parking spaces
  Loading zones
Pedbikeimages.org – Toole Design Group
Notes: Key Message: If not planned and installed carefully, separated bike lane installations can potentially impede access to the curb for alighting motor vehicle passengers or transit users.
Notes: It is possible to address this curb access issue by installing midblock curb ramps and buffers wide enough to accommodate wheelchair lifts. Detectable warning surfaces shall be used to indicate the boundary between a pedestrian route and the bicycle route where the connection is flush, rather than curbed. This is significant for sidewalk-level separated bike lanes.
Connection to other Module: More information on separated bike lanes in Designing for Walking and Bicycling.
Source: FHWA. (2015). Separated Bike Lane Planning and Design Guide. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/separated_bikelane_pdg/page00.cfm (includes a chapter about accessible parking)
Image: http://www.pedbikeimages.org/details.php?picid=2172

## Slide 35: Separated Bike Lanes
FHWA
Notes: Notes: The FHWA guide below includes more examples of designs that provide accessible routes to parking or transit facilities.
Source: FHWA. (2015). Separated Bike Lane Planning and Design Guide. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/separated_bikelane_pdg/page00.cfm

## Slide 36: Work Zones
Elements of an accessible temporary facility
  Communication devices
  Overhead protrusion protection
  Channelizing devices
    Handrails and guardrails
  Surfaces
  Temporary curb ramps/transitions
  Lighting
Notes: Key Message: As with vehicles, when pedestrians traverse the work zone, the route must be clearly marked, be provided with a suitable surface, and they must be protected from other traffic and work operations, including drop-offs. When they exit the work area, pedestrians need to be guided back to their original route. This slide highlights the devices and features that may be needed to provide an accessible route in a temporary traffic control zone.
Notes: The MUTCD requires that “When existing pedestrian facilities are disrupted, closed, or relocated in a TTC zone, the temporary facilities shall be detectable and shall include accessibility features consistent with the features present in the existing pedestrian facility.” This is reinforced by the PROWAG guidelines: “temporary routes are alterations to an existing developed pedestrian environment and are required to achieve the maximum accessibility feasible under existing conditions.”
Connection to other Module: Work zones are covered in the module on Temporary Facilities and Maintenance.
Source: The American Traffic Safety Services Association. (2012). Applying the Americans with Disabilities Act in Work Zones: A Practitioner Guide. Available: https://www.workzonesafety.org/files/documents/training/fhwa_wz_grant/ada_guide.pdf

## Slide 37: Shared Streets and public space

## Slide 38: What is a shared street?
Street with a shared zone that mixes pedestrians, bicyclists and vehicles in the same space
  Encourages low motor vehicle speeds
  Encourages low motor vehicle volumes
  Design elements indicate pedestrian priority
  Benefits
  More vibrant public space, flexible, more room for amenities, economic development
Notes: Notes: “Curbless streets” often function like shared streets but without pedestrian priority – rather they are designed to accommodate street festivals at certain times but then return to operating as a traditional street.
Source: FHWA. (2017). Accessible Shared Streets: Notable Practices and Considerations for Accommodating Pedestrians with Vision Disabilities. Report No. FHWA-HEP-17-096. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/accessible_shared_streets/index.cfm
Image: pedbikeimages.org – Dan Burden. http://www.pedbikeimages.org/details.php?picid=394

## Slide 39: Accessibility Requirements
Title II of ADA of 1990 – no person with a disability shall, because a public entity’s facilities are inaccessible or unusable, be excluded from participation or denied benefits…
Challenges of shared streets:
  Safe space
  Rules of the road
  Patterns of use
  Lack of orientation and wayfinding cues
  Street surface
  Defined crossings
Notes: Notes: There is no segregation of users and the “rules of the road” for shared streets rely more heavily on social interaction and visual cues, compared to typical streets. The patterns of use on shared streets vary, and patterns on the same street could even vary day-to-day. Decorative pavers are often employed as a design treatment, but this can be very disorienting.
Source: FHWA. (2017). Accessible Shared Streets: Notable Practices and Considerations for Accommodating Pedestrians with Vision Disabilities. Report No. FHWA-HEP-17-096. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/accessible_shared_streets/index.cfm

## Slide 40: Accessibility Surface Treatments
Detectable warning surfaces
Directional indicators
Detectable edges and changes in surface texture
Notes: Source: FHWA. (2017). Accessible Shared Streets: Notable Practices and Considerations for Accommodating Pedestrians with Vision Disabilities. Report No. FHWA-HEP-17-096. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/accessible_shared_streets/index.cfm

## Slide 41: Summary
Disabilities related to vision, mobility, hearing, and cognition call each effect how efficiently and safely users can understand and navigate public rights-of-ways
Public agencies and recipients of Federal funds are required to ensure that roadways do not discriminate based on disability
Roundabouts, separated bike lanes, and shared streets can all be designed or modified for accessibility