## Slide 1: Connections to Transit and Shared Mobility
Instructor course information
Notes: Report No. FHWA-SA-19-034

## Slide 2: Outline
Planning for transit
  First mile/last mile
Designing with transit
Shared mobility
Curbside management

## Slide 3: Why Walk, Bike, and Transit?
85% of transit trips are accessed by walking
1 in 6 walking trips is made to access transit
Bicycling and walking can extend the reach of a transit trip
Pedbikeimages.org - Philip Demosthenes
Notes: Key Message: These modes are all important parts of the transportation system, and often it is a combination of these modes that allows people to choose a mode other than a single-occupancy vehicle. The last bullet is especially important if an agency has a goal or target related to mode shift. They need to think about how these modes interact, and hopefully overlap, to provide options for users of all ages and abilities.
Source: Nathan McNeil, Jennifer Dill, Drew DeVitis, Russell Doubleday, Allison Duncan, and Lynn Weigand. (2017). FTA Report No. 0111: Manual on Pedestrian and Bicycle Connections to Transit. Federal Transit Administration, Washington, DC. Available: https://www.transit.dot.gov/about/research-innovation

## Slide 4: Benefits of Improving Bicycle and Pedestrian Access to Transit
Transit depends on safe pedestrian access
Help improve equity
Make the transit system work better for riders
Support more multimodal trips and more options
Improve health and wellbeing
Notes: Notes:
In most cases, transit users are pedestrians, either on foot or via wheelchair or other assistive device, on at least one end of their journey (Cervero, 2001). Having safe and convenient ways to walk to and from transit should be a primary objective.
People with lower incomes are less likely to have access to a car. Improving the ways that people can safely and conveniently access transit without a car can save money.
More options for accessing transit and perhaps people will even choose to walk or bike for part of their trip that might have been made by transit. For some systems, this could help alleviate overcrowding. An example of the opposite situation would be pedestrian and bicyclists who are able to easily switch to transit in case of poor weather or equipment malfunction, injury, etc.
Walking and bicycling to transit make the entire transportation system healthier, providing physical activity for riders and resulting in less pollution than if they had taken a motor vehicle to access transit.
Source: Nathan McNeil, Jennifer Dill, Drew DeVitis, Russell Doubleday, Allison Duncan, and Lynn Weigand. (2017). FTA Report No. 0111: Manual on Pedestrian and Bicycle Connections to Transit. Federal Transit Administration, Washington, DC. Available: https://www.transit.dot.gov/about/research-innovation

## Slide 5: Access for All Users
The access needs of all users must be considered
  Vulnerable groups
    Older adults, people with disabilities, youth
Access in all stages of trip
  En route to transit
  At transit stops
  On transit vehicles
Notes: Notes: Older adults, people with disabilities, and children have particularly high rates of pedestrian and transit transportation use (due to limited mobility, no access to cars, etc.). These groups have needs that will require additional infrastructure considerations. Every group participating in active transportation and transit has different needs and use characteristics. Insofar as possible these needs should all be addressed by the design of the transit system and transit access routes.
Connection to other Module: User and Mode Characteristics
Source: Nabors, D., Schneider, R., Level, D., Lieberman, K., Michell, C. (2008). Pedestrian Safety Guide for Transit Agencies. FHWA. [FHWA-SA-07-017]. Available: https://safety.fhwa.dot.gov/ped_bike/ped_transit/ped_transguide/

## Slide 6: Equity and Transit
Accessibility
  Spatial distribution
  Travel time
Personal security around transit
  At stops, stations, and on vehicles
Notes: Key Message: Accessibility refers to people’s overall ability to reach desired services and activities. It is important to examine if/how equitably a transit system is distributed among different populations. This requires considering the travel time between different destinations. Personal security around transit also represents an equity concern. For example, women are more likely to feel vulnerable to victimization and harassment near or at transit stations (Loukaitou-Sideris, 2014).
Source:
Foth, N., Manaugh, K., & El-Geneidy, A. M. (2013). Towards equitable transit: examining transit accessibility and social need in Toronto, Canada, 1996–2006. Journal of transport geography, 29, 1-10.
Nathan McNeil, Jennifer Dill, Drew DeVitis, Russell Doubleday, Allison Duncan, and Lynn Weigand. (2017). FTA Report No. 0111: Manual on Pedestrian and Bicycle Connections to Transit. Federal Transit Administration, Washington, DC. Available: https://www.transit.dot.gov/about/research-innovation
Loukaitou-Sideris, A. (2014). Fear and safety in transit environments from the women’s perspective. Security Journal, Vol. 27, No. 2, pp. 242-256.

## Slide 7: Who Plans for Transit?
Effectively and efficiently planning for transit will typically require interjurisdictional and interagency coordination:
  Transit agencies
  Local jurisdictions
  Regional Planning Agencies
  State Department of Transportation
  Inclusive public engagement
Notes: Key Message: Transit agencies typically take the lead, but their jurisdiction typically ends outside the transit vehicle, station, or stop. It is not unusual for several different agencies to maintain independent control over the various facilities that are used by someone walking or bicycling to and from a single transit stop.
Notes: All stakeholders should be involved in assessing, planning, and enhancing bicycle and pedestrian access to transit. It not, then local or regional goals about improving safety or shifting modes are unlikely to be met.
Source:
FHWA. (2006). University Course on Bicycle and Pedestrian Transportation. Lesson 18.
Nathan McNeil, Jennifer Dill, Drew DeVitis, Russell Doubleday, Allison Duncan, and Lynn Weigand. (2017). FTA Report No. 0111: Manual on Pedestrian and Bicycle Connections to Transit. Federal Transit Administration, Washington, DC. Available: https://www.transit.dot.gov/about/research-innovation

## Slide 8: First Mile/Last Mile
Los Angeles County Metropolitan Transportation Agency
Notes: Key Message: An individual’s trip is the entirety of their journey from origin point to destination. No one rolls out of bed at a transit stop.
“Public transportation agencies typically provide bus and rail services that may frame the core of such trips, but users must complete the first and last portion on their own; they must first walk, drive, or roll themselves to the nearest station.” (METRO, 2014)
Notes: The portion of the journey on either end of the transit trip is considered the First/Last Mile (regardless of actual distance). This should be a major component of transit planning.
Source: Los Angeles County Metropolitan Transportation Authority (METRO). (March 2014). First Last Mile Strategic Plan & Planning Guidelines.

## Slide 9: First Mile/Last Mile
Transit is not door-to-door
  Hence the importance of planning for the beginning and end of a person’s trip
How people access transit
  Walk/Bicycle
  Park-and-Ride
  Kiss-and-Ride
  Ride-hailing/TNCs
pedbikeimages.org - Dan Burden
Notes: Notes: As mentioned at the beginning of this module, the vast majority of transit users access transit by walking. However, access is multi-modal, and elements like ride-share, park-and-ride facilities, and drop-off facilities should not be neglected when planning for first/last mile improvements.
Sources:
Los Angeles County Metropolitan Transportation Authority (METRO). (March 2014) First Last Mile Strategic Plan & Planning Guidelines.
Federal Transit Administration. (August 2017). Manual on Pedestrian and Bicycle Connections to Transit

## Slide 10: Planning for the First/Last Mile
Access sheds
  Varies by mode
Networks
Funding
  “all pedestrian improvements located within one half mile of a public transportation stop or station shall have a de facto physical and functional relationship to public transportation”
  - FTA Policy Statement (2011)
Notes: Notes:
Access shed – The distance a person can travel in a fixed amount of time. Access sheds differ based upon mode; for example, a bicycle shed is larger than a walking shed, due to greater average speeds. Access sheds can be artificially shrunken by indirect street layouts, poor pedestrian connectivity, absence of secure parking, etc. Access sheds can be increased through improvements in transit infrastructure and right-of-way improvements that reduce the difficulty of travel in the area.
Networks - To have robust access sheds to transit, bicycle and pedestrian networks need to be interconnected, complementary, and purposefully redundant. Pedestrians and bicyclists are best served by safe and comfortable routes that tie as directly as possible into transit stop and station locations.
Funding – The Federal Transit Administration recognizes the importance of pedestrian and bicycle access to transit; therefore the agency has clarified its position on improvements that qualify for FTA funding.
Connection to other Module: The concept of connected networks is covered in Facility and Network Analysis. There are also numerous resources on this topic from the FHWA Office of the Environment.
Source:
Los Angeles County Metropolitan Transportation Authority (METRO). (March 2014) First Last Mile Strategic Plan & Planning Guidelines.
Nathan McNeil, Jennifer Dill, Drew DeVitis, Russell Doubleday, Allison Duncan, and Lynn Weigand. (2017). FTA Report No. 0111: Manual on Pedestrian and Bicycle Connections to Transit. Federal Transit Administration, Washington, DC. Available: https://www.transit.dot.gov/about/research-innovation

## Slide 11: Transit Access Shed
Atlanta Regional Commission via Federal Transit Administration
Notes: Key Message: Graphic representation of how access sheds vary by mode.
Notes: This is a simplistic approach that involves drawing buffers around the transit point of interest.
Question for Students: What factors related to accessibility are not considered with this approach?
Source: Figure 2-1 in Nathan McNeil, Jennifer Dill, Drew DeVitis, Russell Doubleday, Allison Duncan, and Lynn Weigand. (2017). FTA Report No. 0111: Manual on Pedestrian and Bicycle Connections to Transit. Federal Transit Administration, Washington, DC. Available: https://www.transit.dot.gov/about/research-innovation

## Slide 12: Access Shed - Walking
Federal Transit Administration (2017)
Notes: Key Message: A network analysis provides a more realistic view of walkability to transit than a simple walk shed of a set radius. In these images, the yellow lines represent walking routes within a half-mile of a rapid transit station. In the image on the left, red lines represent routes beyond a half-mile. The image on the right shows how the existing network limits walking options within a short distance of a station. Network analyses can also include factors like road type, topography, and built environment that affect the desire to walk on certain routes.
Connection to Other Module: Facility and Network Analysis
Source: Nathan McNeil, Jennifer Dill, Drew DeVitis, Russell Doubleday, Allison Duncan, and Lynn Weigand. (2017). FTA Report No. 0111: Manual on Pedestrian and Bicycle Connections to Transit. Federal Transit Administration, Washington, DC. Available: https://www.transit.dot.gov/about/research-innovation
Image (left): https://www.nctcog.org/nctcg/media/Transportation/DocsMaps/Plan/Landuse/TOD/BaylorMedical.pdf
Image (right): https://www.nctcog.org/nctcg/media/Transportation/DocsMaps/Plan/Landuse/TOD/North_Carrollton.pdf
Link to NCTCOG Active Transportation Routes to Rail study, 2014: https://www.nctcog.org/trans/plan/bikeped/active-transportation-routes-to-rail

## Slide 13: Example: LA Pathway Plan
Decreasing point-to-point distances through increased (and safer) road crossing opportunities and pedestrian shortcuts
Supporting multimodal transfers (bike-share to transit, transit to car-share, etc.)
Improving pedestrian facilities within existing areas through street lighting, sidewalk repairs, curb ramps, etc.
Notes: Notes: Los Angeles METRO developed a strategic plan targeting its first/last mile issue. The proposal was a regional transit access network made up of multimodal routes to and between transit. Proposed improvements focused on developing active transportation along specific access routes as determined through extensive GIS analysis. After identifying the desired access routes based on existing conditions, safety, etc. infrastructure improvements were identified to incentivize travel along those routes. The types of improvements are listed on the slide.
Source: Los Angeles County Metropolitan Transportation Authority (METRO). (March 2014) First Last Mile Strategic Plan & Planning Guidelines.

## Slide 14: Designing with Transit
Notes: Connection to other Module: The principles of design and design strategies introduced in the following modules all apply to the design of transit stations and the network leading up to transit stops and stations:
User and Mode Characteristics
Designing for Walking and Bicycling
Strategies for Safer Speeds
Intersections

## Slide 15: Key Concepts
Personal safety and security
Managing modal interactions
Comfort and sense of place
Universal design
Legibility and wayfinding
Pedbikeimages.org – Adam Coppola Photography
Notes: Notes:
Personal safety and security - Safety and security includes the personal safety of passengers getting to, waiting at, or leaving a station as well as the security of their belongings against theft. Concerns over personal safety are significant and can serve as a barrier for passengers accessing the transit system.
Managing modal interactions – Of course there are many design solutions to modal conflicts, but sometimes it’s a question of agency priorities to determine which modes are prioritized in different situations. [The next two slides cover this topic]
Comfort and sense of place - Seating, shelters, and other streetscape features like landscaping, trash receptacles, public art, etc. Shelter and seating are key elements of comfort and may be more important to riders who have walked or bicycled to the station, particularly riders with mobility limitations, and people with disabilities.
Universal design – The goal of universal design is to design for a wide a range of users so that as many people as possible, regardless of age or ability, can access spaces and products. It is a step beyond designing for accessibility for users with disabilities.
Legibility and wayfinding - If transit users cannot understand how to use a system, let alone get to or from a transit stop from their origin or destination, they will not use transit. Direct routes to stops, highly visible stops, signs, and consistent branding all help achieve this goal.
Connection to Other Module: Factors Influencing Mode Choice briefly covers wayfinding.
Source: Nathan McNeil, Jennifer Dill, Drew DeVitis, Russell Doubleday, Allison Duncan, and Lynn Weigand. (2017). FTA Report No. 0111: Manual on Pedestrian and Bicycle Connections to Transit. Federal Transit Administration, Washington, DC. Available: https://www.transit.dot.gov/about/research-innovation

## Slide 16: Transit Station Access Hierarchy
FHWA
Notes: Key Message: It is recommended to establish a modal hierarchy and design transit stations for vulnerable road users first. This hierarchy should be applied to minimize conflicts between vulnerable road users and other station users such as buses and other transit vehicles, private vehicles accessing pick-up and drop-off areas, and private vehicles parking at the station. It may be difficult to establish this hierarchy for existing stations, but it should always be kept in mind when designing new stations.
Source: Porter, C., Danila, M., Fink, C., Toole, J., Mongelli, E., Schultheiss, W. (2016). Achieving Multimodal Networks: Applying Design Flexibility and Reducing Conflicts. FHWA. [FHWA-HEP-16-055]

## Slide 17: Common Transit Conflicts
FHWA
Notes: Key Message: There are design solutions for each of these conflicts, but sometimes it’s more important to consider agency goals and priorities and the network. Not every street can serve every mode equally – decisions will need to be made about tradeoffs.
Notes: The left side depicts the problem of “leap frogging,” which occurs when a bus and bike are traveling on a roadway in the same direction and pass each other at multiple places. The bicyclist is traveling at a constant speed with the bus passing, pulling into a stop, departing the stop, passing the bicyclist, and traveling to the next stop. If agencies decide that a street with this conflict type is a priority route for both modes, then one potential solution is to float the bus top on an island between the bike lane and motor vehicle travel lanes (example shown on next slide). Or an agency may decide that there is a parallel route for one of the modes that can maintain network connectivity while separating the modes.
Road hazard - Between the resurgence of light rail and streetcars and increases in bicycling, conflicts between bicyclists and tracks may become more common. Tracks typically contain a gap, called the flangeway, which can be a hazard for bicycle tires. In wet conditions, tracks may be slippery, causing bicyclists to lose control. Track surface materials, pavement markings, and geometric features like medians may help mitigate this conflict.
Crossings – will be covered on subsequent slides. The conflicts at pedestrian crossings are often related to the placement of transit stops.
Source: Porter, C., Danila, M., Fink, C., Toole, J., Mongelli, E., Schultheiss, W. (2016). Achieving Multimodal Networks: Applying Design Flexibility and Reducing Conflicts. FHWA. [FHWA-HEP-16-055]

## Slide 18
Pedbikeimages.org – Seattle DOT
Notes: Notes: This example from Seattle, Washington, shows how a floating bus island allows the bus to stop in-lane, which decreases delay for the bus while allowing it to re-enter traffic without waiting for a gap in passing drivers. The bike lane separation also prevents conflicts between bicyclists and stopped buses.

## Slide 19: Pedestrian Crossings
Pedestrians may make riskier crossing decisions to access transit, especially as a transit vehicle is approaching
Transit corridors often have high pedestrian crash rates
Safety measures include:
  High-visibility marked crossings near transit stops
  Median refuge islands
  Flashing beacons
  Crosswalk lighting
  Leading pedestrian intervals at intersections
Notes: Key Message: Pedestrian crossings are necessary to reach a transit stop, and they are the most likely places where safety conflicts will arise. The design of pedestrian crossings has been covered in other modules, but the topic bears repeating here because the design and placement of crossings often needs to be considered in conjunction with decisions about the design and placement of transit stops. The internal layout of transit stations needs to consider the flow and interaction of all modes, just like any site plan, and safe pedestrian crossings are key.
Notes: A study looked at transit-bound and non-transit bound pedestrians crossing Huntington Avenue in Boston and found that when a transit vehicle was waiting or approaching, pedestrians crossed at greater speeds and were willing to accept smaller gaps to cross (Meng and Dulaski, 2014). Other research has shown that transit corridors, with higher levels of pedestrian activity, often are high-risk locations and that transit riders represent a high percentage of crashes involving pedestrians. (Pulugurtha and Penkey, 2010)
Source: Nathan McNeil, Jennifer Dill, Drew DeVitis, Russell Doubleday, Allison Duncan, and Lynn Weigand. (2017). FTA Report No. 0111: Manual on Pedestrian and Bicycle Connections to Transit. Federal Transit Administration, Washington, DC. Available: https://www.transit.dot.gov/about/research-innovation

## Slide 20: Bus Stop Location
Should be:
  Connected to the sidewalk network
  Highly visible
  Not impede sidewalk movement
  Additional considerations:
  Sight lines between passengers and drivers
  Stopping at areas commonly used by people on foot
  Proximity to key destinations
  Safety of crossings
  Ease of transfers
pedbikeimages.org - Dan Burden
Notes: Key Message: Bus stops are the entry points (gateways) into the transit system. Safe, well-maintained bus stops improve user opinions of transit and can lead to greater transit ridership. Good bus stop placement can work toward each of the concepts listed at the beginning of this section. Placement can improve safety and security, minimize modal conflicts, contribute to a sense of place, and achieve universal design.
Notes: Siting should consider the ease and safety of transfers, and where possible, be integrated with ride-share, bike-share, and other transportation modes.
Source: Nabors, D., Schneider, R., Level, D., Lieberman, K., Michell, C. (2008). Pedestrian Safety Guide for Transit Agencies. FHWA. [FHWA-SA-07-017]. Available: https://safety.fhwa.dot.gov/ped_bike/ped_transit/ped_transguide/ar zones… in Multimodal networks guide

## Slide 21: Bus Stop Location
Far-side of intersection
  Preferred when feasible because can cross in a crosswalk behind the bus where they are more visible to oncoming traffic.
Near-side of intersection
In-lane vs. pullout
Midblock
Clear zones?
  Bus stops should be placed as close to the travel way as
  reasonable, once clear zones are considered.
Notes: Key Message: Bus stop placement is a key component of reducing conflicts between bus passengers, pedestrians, bicyclists, and motorists. Bus stops should be located at appropriate distances based on the context of the area. For example, bus stop spacing in central business districts is less than 400 feet. Stops at intersections are preferable to minimize traffic disruptions and to facilitate transfers, but there are instances where a midblock stop is necessary because of proximity to key destinations or to maintain appropriate stop spacing. This is especially likely in suburban settings.
Notes: There are tradeoffs with each of these decisions. Whether a transit vehicle stops at the beginning of a block or at the end of the block, whether it stops in the travel lane or uses a pullout, there are implications for transit delay, turning vehicle traffic, pedestrian safety, bicycle conflicts etc. The resources at the end of this section go into detail about these decisions.
Midblock - At midblock bus stop locations, depending on the proximity of other crosswalks, a midblock crossing may be necessary and may require enhanced crossing treatments.
Clear zone - Bus stops are often located in areas with high pedestrian volumes, but they also serve suburban and rural areas where buses may be the only form of transit. As a method to improve safety, designers sometimes develop “forgiving” roadway designs that include relatively large clear zones. However, this approach may preclude the inclusion of desirable bus stop elements such as bus shelters. AASHTO resources such as the Roadside Design Guide afford flexibility when determining the clear zone.
Source:
Porter, C., Danila, M., Fink, C., Toole, J., Mongelli, E., Schultheiss, W. (2016). Achieving Multimodal Networks: Applying Design Flexibility and Reducing Conflicts. FHWA. [FHWA-HEP-16-055]
Nathan McNeil, Jennifer Dill, Drew DeVitis, Russell Doubleday, Allison Duncan, and Lynn Weigand. (2017). FTA Report No. 0111: Manual on Pedestrian and Bicycle Connections to Transit. Federal Transit Administration, Washington, DC. Available: https://www.transit.dot.gov/about/research-innovation

## Slide 22: Bicycles and Transit
Bicycle parking
Bicycles on transit vehicles
Bike share access to transit
pedbikeimages.org – Linda Shepard Salzer
pedbikeimages.org – Dan Burden
Notes: Notes: Many who bike to transit also wish to bike from transit to their destination. Balancing the desire to take bikes on transit with issues of overcrowding is challenging but can be managed through careful planning. On-transit facilities like bike hooks, front-of-bus bike racks, etc. can make taking personal bikes on transit more feasible. Additionally, incorporating bike share facilities into transit stops can reduce the demand for taking bikes onto transit vehicles. Bike parking is a critical piece of infrastructure, and parking options range from simple inverted U racks to personal bike lockers.
Connection to Other Module: Bicycle parking is briefly covered in Factors Influencing mode choice.
Source: Transit Cooperative Research Program. (2012). Guidelines for Providing Access to Public Transportation Stations.

## Slide 23: Example: ARC Walk. Bike. Thrive!
Atlanta Regional Commission active transportation plan
  Focus on expanding pedestrian and bike infrastructure, safety/accessibility improvements
  Explicitly ties pedestrian improvements to transit use
    Improve roadways around transit
    Improve pedestrian access to stops
    Reduce conflict between bikeway and transit
    Improve bike parking availability
Notes: Key Message: The Walk.Bike.Thrive! plan and the supplemental report, Bike to Ride, focus on expanding pedestrian and bicycle infrastructure in the Atlanta region and making improvements for safety and accessibility.
Notes:
Bike parking is a priority for all bike users, and a relatively inexpensive initiative. Multiple options of increasing security are identified in the plan.
Atlanta addresses the challenge of access at large stops for pedestrians and bicyclists by identifying signage and right-of-way patterns that make navigating park-and-ride stations safe and convenient for pedestrians.
Atlanta’s plan identifies a need for more direct routes between homes in less dense areas and transit centers through the implementation of access trails (this is like the pedestrian short cuts/cut-throughs identified in LA METRO’s plan)
Source: Atlanta Regional Commission. (May 2016). Walk. Bike. Thrive! Available: https://atlantaregional.org/plans-reports/bike-pedestrian-plan-walk-bike-thrive/

## Slide 24: Design and Guidance Resources
Available from:
  Federal Highway Administration
  Federal Transit Administration
  National Association of City Transportation Officials
  Institute of Transportation Engineers
  American Public Transit Association
  Transit Cooperative Research Program
    Reports 95 and 153; Synthesis 62

## Slide 25: Legal Argument for Improved Transit Access
pedbikeimages.org - Toole Design Group
National trends
  Transit agencies are increasingly held liable for safety of passengers while:
    Waiting for transit
    Getting on/off transit
    Transferring between transit
Notes: Notes: Civil cases in multiple states have held transit agencies liable for injuries sustained by transit users who are traveling to, waiting for, and transferring between transit. Transit agencies are actively planning stop siting, route patterns, and infrastructure improvements (with interagency cooperation) that prioritize user safety through all stages of their trip.
Connection to other Module: Accessibility and ADA
Source: Nabors, D., Schneider, R., Level, D., Lieberman, K., Michell, C. (2008). Pedestrian Safety Guide for Transit Agencies. FHWA. [FHWA-SA-07-017]. Available: https://safety.fhwa.dot.gov/ped_bike/ped_transit/ped_transguide/

## Slide 26: Shared mobility
Notes: Notes: The slide titled “Shared Mobility Service Models” explains what will be covered in the rest of the lesson.

## Slide 27: Shared Mobility
Carsharing
  Zipcar, car2go
Ridesourcing or ridehailing
  Transportation Network Companies (TNC) like Uber, Lyft
Shared micromobility
  Bike share
    Including electric assist bikes
  Electric kick scooters
  Other small vehicles
pedbikeimages.org – Ryan Snyder
Notes: Key Message: Recent transportation and technology trends are potentially shifting how people move around an area and how they make decisions about transportation. TNCs, shared mobility, micromobility, and automated vehicles could all make big impacts on mode share and the maintenance and future designs of our transportation infrastructure. We’ll mostly be talking about shared micromobility, but also the impact of TNCs. There is also some overlap with the categories shown on the slide as some of the ridesourcing companies are investing in micromobility.
Notes: It’s important to think about how these emerging modes could have negative impacts or benefits for some people. It’s important to consider the users of these new modes, and who has access to these technologies. How do the modes interact with each other? Who is funding the expansion of and profiting from these new technologies? Individuals who are low-income or have disabilities might be excluded without careful planning and the appropriate policies, but in certain scenarios they might benefit.
Student Question: What issues or benefits might occur from the introduction of these emerging technologies?
Connection to other Module: A version of this slide appears in the Introduction module

## Slide 28: Shared Mobility Service Models
FHWA
Notes: Key Message: This figure defines the five service models and the modes offered within each. Some of the modes are considered “incumbent” – these are the ones that have been around for decades like taxis, public transit, traditional car rental, etc. The rest are considered innovative, like ridesourcing and bike sharing. For this section of the lesson we will focus mostly on the membership-based self-service models like bike sharing and scooter sharing. These are often categorized as “micromobility” or “shared active transportation.” We will also spend a little bit of time talking about the relationship between ridesourcing and transit and some of the implications for curbside management.
Notes: Shared mobility has become a ubiquitous part of the urban transportation network, encompassing a variety of modes ranging from public transportation, taxis, and shuttles to carsharing, bikesharing, and on-demand ride and delivery services. Fundamentally, these services can be categorized into five groupings: 1) membership-based self-service models, 2) P2P self-service models, 3) non-membership self-service models, 4) for-hire service models, and 5) mass transit systems. Some distinguish among the shared services between sequential (use by one user and then another, e.g., bikesharing and carsharing) and concurrent models (shared by many at one time, e.g., microtransit, carpooling, ridesplitting) (Transportation Research Board, 2015).
Source: Shaheen, S., Cohen, A., Zohdy, I. (2016). Shared Mobility: Current Practices and Guiding Principles. Federal Highway Administration [FHWA-HOP-16-022].

## Slide 29: Planning for and Managing Shared Micromobility
Safety
Accessibility
Equity
Fees and pricing
Data sharing
Parking/right of way
Integration with other modes
Community engagement
Kristen Langford – pedbikeimages.org
Notes: Notes:
Safety
Ensuring a high standard of safety is a top priority for shared micromobility companies.
Accessibility
In order to ensure that Shared Active Transportation Companies provide a reliable, convenient transportation option for citizens, cities should consider how many small vehicles should be made available and ensure that small vehicles are appropriately distributed across the service area.
Equity
In order to meet the mobility needs of their residents, cities with Shared Active Transportation systems must also focus policies and programs that ensure that these transportation systems are understood and can be used by all.
This includes developing permit or license requirements and programming to address: Outreach and engagement; Financial access; Employment; Access and reliability.
Fees and pricing
Cities should ensure that the full cost of regulating and managing Shared Active Transportation companies is considered when setting fees.
Data sharing
Companies operating in the public right of way must provide cities and local governments with accurate, complete, and timely data about how Shared Active Transportation services are used and, in an appropriately anonymized fashion, who is riding.
Parking/right of way
Despite being “dockless,” allowing Shared Active Transportation companies and customers to leave small vehicles on public property requires cities and local governments to designate places where those small vehicles may be parked.
Parking can be provided in the street or on the sidewalk by means of painted boxes, street corrals, signed sidewalk racks, or geo-fencing.
Integration with other modes
Companies should prioritize ways to incorporate shared micromobility with other modes such as public transportation.
Community engagement
As new mobility options emerge, cities may want to require companies to provide community engagement and education programming to offset the burden to the city of explaining what is going on.
Examples of community engagement: Company participation or attendance at public events and meetings; Company participation or provision of bike education classes, distributed equitably throughout all neighborhoods; Companies partner with job-training programs, youth programs.
Source: National Association of City Transportation Officials (NACTO). (Version July 2018). Guidelines for the Regulation and Management of Shared Active Transportation.

## Slide 30: Bike Share
2007: launch of IT-based public bike sharing in the U.S.
  Exponential growth since 2011
Good for point-to-point or roundtrip
Station-based (docked) vs. free-floating (dockless)
Bicycles can be pedal-powered or electric-assist
Membership: annual, monthly, daily, or per-trip
Implementation: government, non-profit, and/or private company
Notes: Key Message: Traditionally, bike sharing systems have been self-serve station-based, but as of 2019, a growing proportion of systems now have bikes with built-in technology to provide flexible, “dockless” locations for more convenience and wider range of access.
“To create these systems, cities, local governments, and trusted civic partners (e.g. downtown alliances, community-based development organizations) have typically followed a careful, coordinated process; developing structured public-private partnerships, vetting companies through competitive bidding, and managing and regulating systems through binding contracts, to ensure the best outcomes for the public.” (NACTO, 2018). This approach will stand in contrast to dockless bikes and e-scooters that began appearing in the public right-of-way in 2017 and 2018.
Notes: Bike share is recognized as an option for first and/or last mile transit connections, and many are advocating for bike share to be considered as a mass transit option. In addition to improving connections between transit and bike share, several systems across the United States are working to lower the barriers to access. Strategies for encouraging equitable bike share include improving access in underserved areas, offering cash payment options, hiring community “champions” to improve outreach, and subsidizing rates. Most United States bike share systems are funded through a combination of Federal grants, private donations, and sponsorships.
Source:
Pedestrian and Bicycle Information Center, “Bike Share.” Available: http://www.pedbikeinfo.org/topics/bikeshare.cfm [Accessed July 2019].
National Association of City Transportation Officials (NACTO). (Version July 2018). Guidelines for the Regulation and Management of Shared Active Transportation.

## Slide 31: Micromobility Use Trends
NACTO
Notes: Key Message: Dockless pedal bikes quickly proliferated in 2017. While some cities experimented with dockless systems, these bikes were almost entirely owned and operated by private, for-profit companies. By 2018 electric-assist bikes, or e-bikes, emerged as a popular option, replacing most dockless pedal bikes in these fleets. The orange bar shows the emergence of e-scooters in 2018, which will be covered in a couple of slides.
Notes: 84 million trips were taken on micromobility vehicles in the US in 2018, more than double the 2017 number of trips. E-scooters made up more than half of these trips.
Source: National Association of City Transportation Officials (NACTO). (2019). Shared Micromobility in the U.S.: 2018 Available: https://nacto.org/shared-micromobility-2018/ [Accessed July 2019]

## Slide 32: E-bikes and Bike Share
Exist as part of docked and dockless systems
Potential to provide mobility to more areas and groups
  Topography/hills
  Older adults
High daily use rates per vehicle compared to other shared micromobility options
  In US cities with mixed-fleet bikeshares, e-bikes are used twice as frequently as traditional pedal bikes
Notes: Notes: E-bikes can expand access to those with limited physical abilities, those living in hilly regions, commuters who want a more comfortable ride, etc. They are being used and tested in numerous cities within the U.S. and internationally.
Source: National Association of City Transportation Officials (NACTO). (2019). Shared Micromobility in the U.S.: 2018 Available: https://nacto.org/shared-micromobility-2018/ [Accessed July 2019]

## Slide 33: E-scooters
Dockless electric kick scooter rental systems emerged in the U.S. in 2018
Accounted for >50% of shared micromobility rides in 2018
Legal status can be difficult
Industry volatility
Data challenges
  Injury reporting
  Data standards and sharing
Notes: Key Message: E-scooters are a legal grey area in many states – not defined in motor vehicle codes, not classified as bicycles. Where can they operate? By the beginning of 2019, 26 states had introduced more than 44 e-scooter bills. (NACTO, 2019)
Data challenges – Operator data undercounts crash/injury events (discrepancies between operator data and hospital data). Other challenges include the lack of suitable codes on crash reports, (leading scooter injuries to be classified in many different ways), and data-sharing formats and agreements between operators and jurisdictions.
Source:
National Association of City Transportation Officials (NACTO). (2019). Shared Micromobility in the U.S.: 2018 Available: https://nacto.org/shared-micromobility-2018/ [Accessed July 2019]
Pedestrian and Bicycle Information Center [webinar] “Dockless Electric Kick Scooter Systems: What We Know and Don’t Know.” (2018).

## Slide 34: Example: San Francisco’s proactive approach to crash data collection
Updated police crash report and trauma registry questions to support “tagging” of incidents involving emerging modes
Notes: Notes: The recent proliferation of new mobility technologies presents a challenge to the local and state governments who regulate them, and the hospitals and trauma centers charged with treating injuries associated with these emerging vehicle types. This methodology in San Francisco is a response to the need for timely and high-quality data to empirically track and better understand injuries arising from use of these formerly uncommon vehicles. It provides an opportunity to study emerging innovations and to inform data-driven injury prevention efforts (Vision Zero SF, 2019).
Connection to Other Module: A version of this slide appears in the Introduction.
Source:
Slide developed by Michael Clamann for the Pedestrian and Bicycle Information Center (2019)
Vision Zero SF Injury Prevention Research Collaborative. (2019). A Methodology for Emerging Mobility Injury Monitoring in San Francisco, California Utilizing Hospital Trauma Records: Version 1.0. San Francisco, CA. Available: https://www.sfdph.org/dph/EH/PHES/PHES/TransportationandHealth.asp

## Slide 35: Micromobility and Transit
Transit ridership and bikeshare use
  Relationship may be density-dependent
Bikeshare can alleviate crowding on transit vehicles
  Fewer bikes on transit
  Substitution for short transit trips
Challenges
  Compliance with funding sources
  Coordination with private operators
Notes: Key Message: In dense urban centers, bike share often serves as a substitution mode for crowded rail and bus systems, reducing ridership but effectively increasing capacity. In less-dense areas, bike share has been shown to serve as a complementary mode, increasing access to transit and leading to increased ridership.
Notes:
The exact relationship between bike share use and modal shifts in transportation seem to depend greatly on the nature of the urban environment, its existing transit infrastructure, etc. Local planning knowledge is key to leveraging bike share effectively.
The ability to leave a bike when riding transit and pick one up when disembarking alleviates fears over bicycle parking and security while also reducing over-crowding on transit vehicles. This results in more positive user experience.
Some users elect to use only bike share when available, reducing demand on transit systems and opening up capacity (especially in peak times)
Few planning departments have actively taken advantage of these relationships when planning transit improvements and routing. Challenges include the unclear funding status of bike share (which is recognized as public transit by some funding organizations and not others), as well as the private operation of some systems. However, the opportunities that successful bike share and transit integration present indicates a need for more intensive planning.
Source:
Griffin, Greg Phillip and Sener, Ipek Nese. (Jan 2017). Planning for Bike Share Connectivity to Rail Transit. For Texas A&M Transportation Institute.
Shaheen, Susan; Martin, Elliot; and Cohen, Adam. (2013). Public Bikesharing and Modal Shift Behavior: A Comparative Study of Early Bikesharing Systems in North America. UC Berkeley Transportation Sustainability Research Center
Martin E.W. and Shaheen S.A. (2014). Evaluating Public Transit Modal Shift Dynamics in Response to Bikesharing: A Tale of Two U.S. Cities. Journal of Transport Geography.
Griffin, G. (April 2017). “Connecting the Dots.” Planning Magazine. American Planning Association.

## Slide 36: Future Directions
Integrating bike share and transit-fare systems
  Reduce barriers to use
Increased equity
  Extension of bike access to underserved areas of city
  Information and options for underrepresented demographics
Notes: Notes: Los Angeles is integrating its bike share and transit fare systems to allow direct transfer from transit to bike share without having to pay a second fare for the bike share.
Studies show that underrepresented demographics are interested in using bike share but lack information about how to use it and ways it can be more affordable. Programs like Better Bike Share Partnership are working on educational programs to increase understanding of bike share options for underserved communities.
Source: Nathan McNeil, Joseph Broach, and Jennifer Dill. (June 2017). Evaluating Efforts to Improve the Equity of Bike Share Systems. Transportation Research and Education Center at Portland State University.

## Slide 37: Ridesourcing (Ridehailing)
Use a mobile app to connect passengers with drivers
  Unlike taxi/limousine, drivers use their personal vehicles
UC-Davis study of seven major US cities
  49-61% of ridesourced trips would have otherwise been taken by transit, walking, biking, or not taken at all
  Relationship with transit (substitutive or complementary)? It may depend on the type of transit
Users most likely to be young, college-educated, affluent, and living in urban areas
Notes: Notes: “After using ride-hailing, the average net change in transit use is a 6% reduction among Americans in major cities. As compared with previous studies that have suggested shared mobility services complement transit services, we find that the substitutive versus complementary nature of ride-hailing varies greatly based on the type of transit service in question. Ride-hailing attracts Americans away from bus services (a 6% reduction) and light rail services (a 3% reduction). Ride-hailing serves as a complementary mode for commuter rail services (a 3% net increase in use).” (Clewow and Mishra, 2017)
Source: Clewlow, Regina R. and Gouri Shankar Mishra (2017). Disruptive Transportation: The Adoption, Utilization, and Impacts of Ride-Hailing in the United States. Institute of Transportation Studies, University of California, Davis, Research Report UCD-ITS-RR-17-07

## Slide 38: Ridesourcing and Transit
Partnerships between transit agencies and transportation network companies (TNCs)
  Commonly provides subsidized TNC trips
  May target first/last mile connections, paratransit users, people in low-density areas, late-night riders, and/or “guaranteed ride home” participants
Challenges
  Data-sharing agreements
  ADA compliance
  Ridesourced rides replacing transit trips
Notes: Source:
National Academies of Sciences, Engineering, and Medicine. (2019). Partnerships Between Transit Agencies and Transportation Network Companies. Washington, DC: The National Academies Press. https://doi.org/10.17226/25425.
Clewlow, Regina R. and Gouri Shankar Mishra (2017) Disruptive Transportation: The Adoption, Utilization, and Impacts of Ride-Hailing in the United States. Institute of Transportation Studies, University of California, Davis, Research Report UCD-ITS-RR-17-07

## Slide 39: Shared Mobility Resources
Available from:
  Shared Use Mobility Center
  National Association of City Transportation Officials
  Better Bike Share Partnership
  North American Bikeshare Association
  Federal Highway Administration
  Federal Transit Administration

## Slide 40: Curbside management

## Slide 41: What is curbside management?
Traditional
  Transit
  Parking (storage)
  Pedestrian/bicycle
New demands for curb space
  Ridesourcing/micromobility
  Freight
  Activation
Wikimedia Commons
Notes: Key Message: For several decades, curb space uses and regulations have been assembled piecemeal in response to property and business owners, and overwhelmingly allocated to private vehicle storage. The proliferation of shared mobility options like bike share, for-hire vehicles companies, micromobility modes, and e-commerce package deliveries has intensified demand for curb access.
Source: Institute of Transportation Engineers. (n.d.). Curbside Management Practitioners Guide. Available: https://www.ite.org/technical-resources/topics/complete-streets/curbside-management-resources/
Image: Some cities are allocating curbside space for shared active transportation, such as this example of a designated bike share parking area in Braddon, Australia

## Slide 42: Public Right of Way
Policy/ Priorities
  Specifically - Multimodal safety, ADA compliance, parking, congestion/trip generation, freight/delivery, emerging modes
  But also: sustainability, safety, resilience
  Seattle example – curbside management policy goals:
    Mobility
    Access for People
    Access for Commerce
    Activation
    Greening
    Storage
Notes: Key Message: Curbside management exists at the nexus of transportation, land use, and economic development. Its complexity arises from interlocking demands that are both political and logistical, weaving together a dense set of challenges including multimodal safety, ADA compliance, parking policy, congestion and trip generation, urban freight movement and delivery, and emerging mobility options. Managing curb space effectively requires matching regulations and operations to clear policy goals: universal access; sustainable ecosystems; resilient economies; and a safe, reliable, and equitable transportation system.
Notes: Six essential functions of the right-of-way (from the City of Seattle):
Mobility – The movement of people and goods, including sidewalks, bicycle lanes and protected bikeways, dedicated bus or light rail/streetcar lanes, and general-purpose vehicular travel lanes.
Access for People – People arriving at their destination or transferring between different modes of transportation. This includes transit stops, passenger loading/unloading zones, taxi zones, short-term parking, bicycle parking, and curb extensions.
Access for Commerce – Goods and services reaching their customers and markets primarily through commercial vehicle or truck loading zones.
Activation – Provision of vibrant social spaces that encourage people to interact and congregate. Uses that drive activation include food trucks, restaurant patios or sidewalk cafes, parklets, public art installations, seating, and street festivals (including farmers markets).
Greening – Enhancements to aesthetics as well as environmental health via such accoutrements as planted boulevard strips, streets trees, planter boxes, rain gardens, and bio-swales.
Storage – Provision of storage for vehicles and equipment, including bus layover spaces, reserved spaces for specific uses such as police or government vehicles, short-term vehicle and bicycle parking, longer-term on-street parking, and construction vehicles.
Source: Institute of Transportation Engineers. (n.d.). Curbside Management Practitioners Guide. Available: https://www.ite.org/technical-resources/topics/complete-streets/curbside-management-resources/

## Slide 43: Planning for Curbside Management
Key concepts
  Curbs are flexible space
  Layered approach to modal
Notes: Notes:
“Flex zones” accommodate different right-of-way functions along segments of the roadway. Different types of implementation include:
  Multiple functions simultaneously in the same space i.e. combined commercial and passenger loading zones.
  Different functions at different times for the same space i.e. peak-period travel lane used for off-peak parking or loading.
  Multiple functions simultaneously at different portions of the road i.e. designated loading zone, parklets, and curb extensions on same block face.
Layered network approach promotes the designation of different priorities along different segments near one another with goal of allowing the overall network to serve all users effectively even though any given individual roadway segment may not serve all users.
  i.e., designation of roadway corridor to prioritize transit and transit-supportive modes while identifying separate parallel corridors to prioritize vehicular throughput and access needs, respectively.
Source: Institute of Transportation Engineers. (n.d.). Curbside Management Practitioners Guide. Available: https://www.ite.org/technical-resources/topics/complete-streets/curbside-management-resources/

## Slide 44: Competing Needs
Passengers, freight, parking
Bicycle
  Protected Bike Lane
  Shared Mobility Parking
Pedestrians
  Wider sidewalks
  Curb extensions
  Parklets
Notes: Notes:
Bicycles
A protected bike lane is a dedicated bicycle facility that is located within or next to the roadway but is distinct from both the sidewalk and roadway while being separated from the latter by vertical barriers or elevation differences. They can be one-way or two-way. Typically located on curbside with adequate room for vehicle doors to open. Separation of travel lanes can occur through on-street parking, raised medians, bollards, planters, etc. Pavement treatments such as colored or textured markings are used to separate bike and pedestrian space at sidewalk level.
Bicycle parking may be provided in public right-of-way with sidewalk bicycle racks or on-street bicycle corrals. Bike share stations are often in either flex zone or directly behind curb on sidewalk. Regulations typically establish parking for dockless bikeshare and other mobility devices in landscape/furniture zone of sidewalk, but some cities (ex. Seattle and Austin) have painted parking areas on sidewalk to provide more clarity and reduce clutter.
Pedestrians
Wider sidewalks accommodate more pedestrians of all ages and abilities and are less exposed than narrow sidewalks at back of curb.
Curb extensions at crossings make pedestrians more visible, shorten crossing distances, and slow vehicle turn movements.
Parklets expand the pedestrian realm beyond existing curb line to activate additional public space. Can convert on-street parking to urban park features such as landscaping, benches, public art, or “streateries” with seating, patios, and other amenities. Done without disrupting the sidewalk for mobility.
Source: Institute of Transportation Engineers. (n.d.). Curbside Management Practitioners Guide. Available: https://www.ite.org/technical-resources/topics/complete-streets/curbside-management-resources/

## Slide 45: Summary
Access for all users must be considered the in design and placement of transit stops and stations
Most transit riders arrive on foot and well-planned bicycle and pedestrian access can increase the transit service area
Regardless of the changing micromobility technologies, there are common factors that agencies can manage and regulate