## Slide 1: School Travel
Instructor course information
Notes: Report No. FHWA-SA-19-034

## Slide 2: Module Outline
School travel patterns
Safe Routes to School
School zone design
School site selection

## Slide 3: School Travel Patterns

## Slide 4: Fewer Kids Walking or Biking
For K-8 students
1969
  48% walk/bike
  12% driven
2017
  10.4% walk/bike
  54.2% driven
Mike Cynecki
Notes: Notes: The National Household Travel Survey is conducted approximately every eight years. Long-term trends demonstrate a decline in walking and bicycling to school. But for the nation, the ways in which children travel to school have not changed much in the last couple of decades. The means of travel were within the margin of error at 10% confidence for the 2001, 2009, and 2017 surveys.
Student Question: Ask students how they traveled to and from school when they were younger. What were the factors for their family in making that decision?
Source:
Adapted from slides developed by the National Center for Safe Routes to School (2016)
The National Center for Safe Routes to School and the Safe Routes to School National Partnership (2010). U.S. Travel Data Show Decline In Walking And Bicycling To School Has Stabilized: Safe Routes to School Programs Encourage Active, Safe Trips to School. Chapel Hill, NC & Boulder, CO.
FHWA NHTS Brief: Children’s Travel to School (March 2019). Available: https://nhts.ornl.gov/assets/FHWA_NHTS_%20Brief_Traveltoschool_032519.pdf
Image: Chamberlin Elementary School, Burlington, VT provided by Mike Cynecki.

## Slide 5: Means of Travel To School (2017)
Source: FHWA using 2017 NHTS data
Notes: Key Message: Percentage of children being driven to school has grown in the last 50 years, while walking and biking have plummeted. Overall, in the last two decades the means of travel to school have remained about the same with over half of trips being made in private vehicles, one third being on school buses, and one tenth being made via walking or biking.
Source: FHWA NHTS Brief: Children’s Travel to School (March 2019). Available: https://nhts.ornl.gov/assets/FHWA_NHTS_%20Brief_Traveltoschool_032519.pdf

## Slide 6: Parents Driving
School travel by private vehicle accounts for 10-14% of morning rush hour traffic
Joel Cranford
Notes: Source: Slide from the National Center for Safe Routes to School (2016)
McDonald N., Brown A., Marchetti L., Pedroso M. (2011). U.S. School Travel 2009: An Assessment of Trends. American Journal of Preventive Medicine, 41(2), 146-151.

## Slide 7: Is Distance the Problem…
Students living within one mile or less who walk or bike to school
  1969: 89%
  2009: 35%
Students will walk farther than the assumed half-mile, often up to 1.5 miles
Still, #1 reason cited by parents for children not walking
Dan Burden
Notes: Key Message: Distance from school is an important factor but is not the only component. The percentage of students living within one mile of school who walk has also shrunk dramatically.
Notes: Studies suggest students frequently walk greater distances than are used as planning benchmarks. Despite evidence to suggest that students are willing and able to walk further than the benchmark distances, parent’s perception of distance to school is still the number one cited reason for children not walking.
Source: Adapted from slides developed by the National Center for Safe Routes to School (2016)
National Center for Safe Routes to School. (October 2011) How children get to school: School travel patterns from 1969 to 2009.
National Center for Safe Routes to School. (n.d.) The Decline of Walking and Biking, Available: http://guide.saferoutesinfo.org/introduction/the_decline_of_walking_and_bicycling.cfm

## Slide 8: How Did We Get Here?
School siting issues: increasingly sited in low-density urban fringes
  Further from residential areas
  Fewer connecting streets
Individual barriers: parents’ perceptions of traffic, adverse weather, crime…
Changing urban form
  Low intersection density in newer developments = less walkable
Community issues
Mark Fenton
Notes: Key Message: A generation ago, schools were small and located in the center of communities and the proximity to residential neighborhoods encouraged walking and bicycling. Today, schools are built on bigger sites, farther out. Among individual barriers, traffic danger is the second most common barrier cited by parents (CDC, 2005). Ironically, parents concerned about safety sometimes respond by putting their child in the car and driving them, which may not be a safer alternative, and more parents driving their children to school results in more cars on the road, often making it even less safe for others to walk and bike. Communities also have individual issues that make it hard to walk or bicycle: lack of sidewalks or sidewalks in disrepair, adverse weather, traffic flow problems, abandoned buildings, or illegal behaviors.
Notes: School siting issues are covered later in the module.
[a note on “weather” as a barrier] It’s possible that “weather” as a barrier is reflective of changed social norms in contemporary America, where people are accustomed to driving an automobile for almost every trip. That makes it very easy to forego walking and to jump in the car at the first sign of cold or rain or heat.
Source: Key Message text adapted from slides developed by the National Center for Safe Routes to School (2016).
Marc Schlossberg, Jessica Greene, Page Paulsen Phillips, Bethany Johnson & Bob Parker (2006). School Trips: Effects of Urban Form and Distance on Travel Mode, Journal of the American Planning Association, 72:3, 337-346
Noreen C. McDonald (2010). School Siting, Journal of the American Planning Association, 76:2, 184-198, DOI: 10.1080/01944361003595991
U.S. Centers for Disease Control and Prevention. (2005). “Barriers to Children Walking to or from School United States.” Morbidity and Mortality Weekly Report. Web.

## Slide 9: Safe Routes to School

## Slide 10: SRTS Programs
Make walking and bicycling safe ways to get to school
Encourage more children to walk and bike to school
Programs focus on the 5 Es
  Education
  Encouragement
  Engineering
  Enforcement
  Evaluation
Equity is now considered a 6th E
Notes: Key Message: Promoting walking and biking to school is an ideal strategy to increase physical activity and health among children, but we only want to do it if it is safe. And that’s where Safe Routes to School programs come in.
Source: Adapted from slides developed by the National Center for Safe Routes to School (2016)

## Slide 11: Benefits of SRTS Programs
Improve safety for pedestrians and bicyclists
Reduce traffic congestion around schools
Reduce emissions
Improve children’s health
Notes: Notes: While making it safer to walk or bike was the original goal in Denmark, there are many other potential benefits of SRTS programs.
Local SRTS programs may play a role in:
Reducing traffic congestion and vehicle emissions around schools (which may impact air quality).
Improving children’s health by giving children the opportunity to get the physical activity that they need.
Source: Adapted from slides developed by the National Center for Safe Routes to School (2016)

## Slide 12: Other Benefits of SRTS Programs
Cost savings for schools (reduce need for “hazard” busing)
Teach fundamental safety skills
Benefit local economy
Strengthen family bonds
Increase child’s sense of freedom and responsibility
Provide more transportation options for everyone
Notes: Notes: Local SRTS programs may also help by:
Saving money for schools by reducing the need for hazard busing (Hazard busing is when bus service is provided for children who live close to school because the routes are not safe for walking).*
Teaching students fundamental safety skills and remind drivers to watch out for children.
Funding construction projects that benefit local economies.
Giving parents and children the chance to walk and bicycle together – strengthening family bonds.
Or, for older children, increasing their sense of freedom and building a sense of responsibility.
And finally, SRTS programs can increase options for how all people get around their communities.
* As an example of the costs of hazard busing: In the State of Illinois, a study revealed that in 2006 the cost to bus students who lived within 1.5 miles of their schools but had to be bused due to hazards totaled almost $70 million, and the cost had been trending upward since 2000. [Center for Neighborhood Technology. (2007, January). School safety busing: Serious safety hazards in Cook County,1980-2006]
Source: Adapted from slides developed by the National Center for Safe Routes to School (2016)

## Slide 13: The Es: Education
Provide students and community with skills to walk/bike safely
Educate about the benefits of active transportation
Inform community members about changes in traffic patterns, engineering projects, etc.
Notes: Key Message: Planning successful Safe Routes to School (SRTS) education activities require considering how children and adults learn best. Children benefit from a combination of educational methods such as group activities, hands-on skill building, and discussion. Incorporate safety training into SRTS programs (this includes both classroom and in-the-field instruction). Young students may need instruction on safe street-crossing behaviors, traffic laws, etc. Older students may be taught bicycling techniques and safety. Educational efforts should extend to family and community members. Increasing awareness of school routes, traffic laws, and driver safety can lead to increased road safety.
Source:
National Center for Safe Routes to School, SRTS Guide: Education. Available: http://guide.saferoutesinfo.org/education/index.cfm [Accessed May 2019]
Safe Routes Partnership, “The 6 E’s of Safe Routes to School.” Available: https://www.saferoutespartnership.org/safe-routes-school/101/6-Es [Accessed May 2019]

## Slide 14: The Es: Encouragement
Generating enthusiasm and increased walking and bicycling for students through events, activities, and programs
International Walk to School Day (Oct.) and Bike To School Day (May)
National Center for Safe Routes to School
Notes: Key Message: Programming and community outreach generates support for SRTS programs and policies that support walking and bicycling. Special events are an effective way to introduce new students, families, and community members to walking and bicycling.
Notes: In addition to Walk and Bike to School Day, other examples include walking groups and bike trains. For schools that do not have supportive infrastructure, walking or biking at school activities is an option.
Source: Safe Routes Partnership, “The 6 E’s of Safe Routes to School.” Available: https://www.saferoutespartnership.org/safe-routes-school/101/6-Es [Accessed May 2019]

## Slide 15: The Es: Engineering
Design, implementation, operation and maintenance of traffic control devices or physical measures
Engineering strategies for:
  Around the school
  Along the school route
  Crossing the street
  Slowing down traffic
Include the community by using audit tools to identify problems
National Center for Safe Routes to School
Notes: Key Message: Engineering strategies are best used in conjunction with education, encouragement and enforcement activities. Strategies focus on the area around the school, along the school route, street crossings, and slowing down traffic.
Notes: The next section on school zone design covers some engineering strategies.
Connection to other Module: Designing for Walking and Bicycling, Strategies for Safer Speeds, Accessibility and ADA
Source: National Center for Safe Routes to School, SRTS Guide, Engineering. Available: http://guide.saferoutesinfo.org/engineering/index.cfm [Accessed May 2019]

## Slide 16: The Es: Enforcement
Deter unsafe traffic behaviors through enforcement of new and existing traffic regulations
  Drivers AND pedestrians
Ensure safety at crossings
Address environmental concerns
  Abandoned property, loose dogs, etc. create unsafe environments for students
Kristen Brookshire
Notes: Key Message: Enforcement of both driver and pedestrian traffic rules will ensure that safe practices are followed. Providing additional enforcement at road crossings is an important component of ensuring safety for students.
Source: Safe Routes Partnership, “The 6 E’s of Safe Routes to School.” Available: https://www.saferoutespartnership.org/safe-routes-school/101/6-Es [Accessed May 2019]

## Slide 17: The Es: Evaluation
Making sure that the underlying problem is identified so that proper strategies are selected
Setting reasonable expectations about what the program can do
Identifying changes that will improve the program
Determining if the program is having the desired results
  Ensuring that programs and initiatives are supporting equitable outcomes
Notes: Key Message: Evaluation is key to establishing which initiatives and improvements have resulted in more kids walking/biking to school.
Notes: Surveys of parents help provide insight into their rationale for choosing whether to drive their student or allow them to walk/bike and can give program directors a better understanding of what improvements might affect parent’s decision making.
Source:
Safe Routes Partnership, “The 6 E’s of Safe Routes to School.” Available: https://www.saferoutespartnership.org/safe-routes-school/101/6-Es [Accessed May 2019]
National Center for Safe Routes to School, SRTS Guide: Evaluation. Available: http://guide.saferoutesinfo.org/evaluation/index.cfm [Accessed May 2019]

## Slide 18: The Es: Equity
Ensure SRTS programs benefit all demographic groups
  Low-income students, students of color, students with disabilities, students of all genders
Prioritize schools with the highest need
  Can help reduce health and educational disparities in underserved communities.
Kristen Brookshire
Notes: Source: Safe Routes Partnership, “The 6 E’s of Safe Routes to School.” Available: https://www.saferoutespartnership.org/safe-routes-school/101/6-Es [Accessed May 2019]

## Slide 19: The Es: Equity
Notes: Notes: These data are also presented in the module on Equity.
Source: Safe Routes Partnership, Equity in Safe Routes to School, Available: https://www.saferoutespartnership.org/safe-routes-school/101/equity [Accessed May 2019]
Image: https://www.saferoutespartnership.org/sites/default/files/pictures/sr2s_infographic_sidewalks2-jpg.jpg

## Slide 20: SRTS Example – Fort Collins
City program partnered with school district, bike advocacy groups, etc.
Focus on educational programming, especially through partnerships with Bike Fort Collins
  School rotation schedule improves reach and equity
  Bike clubs, bike field trips, walkathons, family bike rodeos, etc.
Evaluation and annual reporting
Notes: Notes:
Fort Collins’ SRTS program has a strong educational and encouragement focus.
  Partner with bike advocacy groups to provide in-class bike-ped safety instruction to school children. Goal is to reach every elementary school once every three years with an in-depth SRTS bike-ped program.
  Through partnerships with local bike event organizers, including FoCo Fondo, promote active living through after-school bike clubs, bike field trips, etc.
  Encourage whole-family participation through sponsoring community events like bike rodeos.
  Educational and encouragement programming presents bike and pedestrian travel as a fun, social experience and leads to greater program involvement for students.
  Engineering improvements are often supported through Colorado DOT’s SRTS grant program.
Source: City of Fort Collins, Safe Routes to School. Available: https://www.fcgov.com/saferoutes/ [Accessed May 2019]

## Slide 21: International Education Examples
In Berlin, children take cycling training and skills test in 3rd or 4th grade
  Police supervise lessons on off-street training grounds
  Police then accompany for ride on city streets
Similar program at Dutch schools
  Free bicycles provided for students who don’t own one
Bicycling Ambassadors program used in Toronto and some American cities
Notes: Notes: Bicycling Ambassadors program is when well-trained cyclists are sent into neighborhoods around their city to promote cycling and offer bike training.
Source: Pucher, J. R., & Buehler, R. (Eds.). (2012). City cycling (Vol. 11). Cambridge, MA: MIT Press.

## Slide 22: Research Shows Programs Work
A study of 801 schools between in 2007-2013 found increases in walking and bicycling
  25% increase (5% per year) with education and encouragement programs
  18% increase with infrastructure improvements
Notes: Key Message: A study of 801 schools between 2007-2013 in the District of Columbia, Florida, Texas and Oregon found that:
Schools with SRTS education and encouragement programs saw a yearly 5% increase in walking and bicycling rates, and
Schools with infrastructure improvements resulted in an 18% increase in walking and bicycling (McDonald et al, 2014).
The impacts were independent, suggesting that a school that combines engineering improvements with education and encouragement could potentially see increases in walking or biking of up to 43% over 5 years.
Notes: The study looked at school travel data from 801 schools between 2007-2013 in DC, Florida, Oregon and Texas. Researchers examined 378 schools implementing Safe Routes to School, showing that Safe Routes to School education, encouragement, and infrastructure programming all led to increases in walking and bicycling to school. This research also examined the income levels, and ethnic and racial makeup of these schools and found no difference in results.
Source: Slide developed by the National Center for Safe Routes to School (2016)
McDonald, N.C. et al. (2014). Impact of the Safe Routes to School program on walking and bicycling. Active Living Research, Research Review, May 2015.
Background image from Kristen Brookshire, walk to school event in Fuquay-Varina, North Carolina.

## Slide 23: SRTS History
1970: concept began in Denmark
1997: first U.S. SRTS program in Bronx, NY
2005: Transportation Bill established Federal SRTS program
  State DOTs decided how to spend dedicated SRTS funds on infrastructure changes and non-infrastructure activities
  States required to have a full time SRTS coordinator
2012 – present: SRTS became an eligible activity that competed alongside other programs
Notes: Notes: SAFETEA-LU was adopted in 2005 and with it, each State DOT received annual Federal funding to implement a SRTS program. In 2012, the surface transportation bill known as MAP-21 made SRTS an eligible activity that competed alongside other activities in the category of “Transportation Alternatives.” Another major change was that they activities were no longer funded at 100% Federal funding; now local communities must cover 20% of the project cost as a match. The 2015 FAST Act preserved funding for SRTS without many changes to the Transportation Alternatives Program.
Source: Safe Routes Partnership, “History of Safe Routes to School.” Available: https://www.saferoutespartnership.org/safe-routes-school/101/history [Accessed May 2019].

## Slide 24: School zone design

## Slide 25: Design Principles Near Schools
Reduce speed of vehicles
Improve access and mobility
Separate modes
Improve visibility
Reduce pedestrian crossing distance
Kristen Brookshire
Notes: Key Message: Ideally, the school zone starts at the front door and encompasses the campus and as many blocks as possible that surround the school and have a high concentration of school-generated traffic. Often the school zone includes the streets along the school and usually the area one to two blocks around it. The school zone should be marked with special signing to alert drivers of the high concentration of children. School crossing signs, speed signs, school zone pavement markings and other traffic calming devices remind drivers to treat the area with special care and attention.
Source: National Center for Safe Routes to School, SRTS Guide, Engineering. Available: http://guide.saferoutesinfo.org/engineering/index.cfm [Accessed May 2019]

## Slide 26
FHWA
Notes: Key Message: As multiple travel modes intersect around the school zone conflicts often occur on the school site and at intersection or driveway crossings nearby. Children walking or biking to school are particularly vulnerable. Designers should consider vehicle speeds, intersection geometry, crossing treatments, and pedestrian and bicycle facilities along key routes to school. Education and enforcement should encourage proper driver, pedestrian, and bicyclist behavior.
Source: FHWA (2017). Achieving Multimodal Networks: Applying Design Flexibility and Reducing Conflicts. Section on School Access. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_networks/part02.cfm#s2

## Slide 27: Managing Speed
Design school zones and surrounding streets for safety of students
  Reduce speeds
  Maximize visibility at crossings
Traffic calming designs
  Vertical Elements
    Speed tables, speed humps, raised crossings
  Gateway/pinch points
  Crossing treatments
Notes: Key Message: Managing the traffic conditions within school zones, and along routes to schools, is an important part of ensuring safety of students biking and walking to school.
Notes: Traffic calming design elements should be incorporated into streetscape within and around school zones. Traffic calming measures consist of horizontal, vertical, lane narrowing, roadside, and other features that use self-enforcing physical or psycho-perception means to produce desired effects.
Connection to other Module: Strategies for Safer Speeds
Source: National Center for Safe Routes to School, Safe Routes to School Online Information Guide

## Slide 28: Examples of Traffic Calming Measures
Speed hump/bump/table
Medians/refuge islands
Roundabouts
Raised crosswalks
Raised intersection
Curb extensions
NACTO
Notes: Key Message: Many of these measures also improve the visibility of the pedestrian and reduce their crossing distance (i.e., the amount of time they are exposed in the roadway).
Notes: Callout for some common traffic calming methods that are effective at increasing safety of pedestrians and bicyclists. Road diets are another intervention that can improved safety for all road users near a school.
Connection to other Module: Strategies for Safer Speeds
Source: NACTO (2013). Urban Streets Design Guide. Available: https://nacto.org/publication/urban-street-design-guide

## Slide 29: Signage and Warnings
Inform drivers of special conditions in school zones
School speed limits
  Typically lower during school hours
  Signs, overhead flashers, speed feedback signs
School zone signage
  Warn drivers of increased pedestrian activity in school zones
  Prepare drivers to look for children
Pedbikeimages.org – Dan Burden
Notes: Key Message: School zones have greater numbers of pedestrians, and children are unpredictable. Informing drivers of school zones prepares them to look for children who may be hard to see, or who may act in unexpected ways around traffic. Signs warn drivers of these conditions and reduce conflicts.
Notes: School zones may be designated and identified with signs and pavement markings as outlined in the MUTCD. School zones may specify a reduced speed limit during school hours or when children are present. Periodic school zone enforcement is a common and effective method for reducing speeds in school zones. The lower bound for school zone speed limits may be set by State statute.
Source:
National Center for Safe Routes to School, Safe Routes to School Online Information Guide.
FHWA (2017). Achieving Multimodal Networks: Applying Design Flexibility and Reducing Conflicts. Section on School Access. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_networks/part02.cfm#s2

## Slide 30: Signage and Warnings
FHWA
Notes: Source: FHWA. (2009). Manual on Uniform Traffic Control Devices

## Slide 31: Design for Children
Special considerations for children
  Clear and legible paths of travel
  Encourage predictable behavior
  Consider children’s size in design elements
Signal timing should accommodate slower walking speeds and large groups
ADA compliance
  School zones shall be designed for accessibility
  Sidewalk ramps, accessible crossing signals, etc.
Notes: Key Message: Children are impulsive and unpredictable; design school zones with signage and infrastructure that encourages students to walk/bike in specific controlled corridors. This increases predictability for other road users.
Notes: Children are short and hard for drivers to see; consider sightlines at lower heights at intersections, high-traffic areas, etc. Signage warning drivers to be aware of children is crucial.
Connection to other Module: Accessibility and ADA; User and Mode Characteristics
Source: FHWA (2017). Achieving Multimodal Networks: Applying Design Flexibility and Reducing Conflicts. Section on School Access. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_networks/part02.cfm#s2

## Slide 32: School site selection

## Slide 33: School Siting Issues: A Generation Ago
Small (average: 127 students)
Located in community centers
48% of kids walked or biked to school
Mike Cynecki
Notes: Key Message: Schools have changed a lot in recent years. A generation or more ago, schools were small and located in the centers of communities. The proximity of schools to residential neighborhoods encouraged walking and biking.
Source: Slide from the National Center for Safe Routes to School (2016)
Environmental Protection Agency. (2003). “Travel and Environmental Implications of School Siting.” Washington DC, Report No. 231-R-03-004. Web.
Image: Barnes Elementary School, Burlington, VT provided by Mike Cynecki. (Note: this image was taken in 2008 near a centrally located school site.)

## Slide 34: School Siting Issues: Today
Current average enrollment: 520 students
Mega-schools up to 2,800 students
Schools located on 10 to 30+ acres fringe land
Lowest-cost construction
Google Imagery, Creekland MS in Lawrenceville, GA (2010)
Notes: Key Message: Today, schools are built to accommodate a far larger number of students. In the 2011-2012 school year, the average school attendance for public elementary and secondary schools was 520 students (NCES). The reasons for the change in school siting include current land use patterns, school siting standards, and lack of coordination between planners and school officials.
Notes: Some “mega-schools” may house up to 2,800 students, such as the school shown in this photo. Schools are increasingly being built on fringe land on the periphery of towns and cities, on parcels anywhere from 10 to 30 acres or more in size. By increasing the distance between home and school, these more distant schools often remove the option of physically active trips to school and encourage higher levels of auto use and pollution.
Source: Slide from the National Center for Safe Routes to School (2016)
National Center for Education Statistics (NCES). Average enrollment and percentage distribution of public elementary and secondary schools, by level, type and enrollment size: Selected years, 1982–83 through 2011-12.
Image: The photo is of Creekland Middle School in Lawrenceville, GA. The school, which was built in 1996, sits on a 46-acre plot and has an enrollment of approximately 2,850, making it one of the largest middle schools in the United States by enrollment.

## Slide 35: Trends in Site Selection
Communities have been shifting from small, neighborhood schools to larger schools located in low-density regions with less street connectivity
  Driven by 1.) lack of affordable land in developed communities and 2.) demand for larger outdoor facilities
Conflict between ‘community school’ advocates and ‘school sprawl’
  Diversity goals, facility needs, etc. pose barriers to local school siting
  Large, decentralized schools less walkable, less integrated, but more facilities
Notes: Notes: Trend away from small neighborhood schools to larger decentralized schools where there is adequate space for large athletic facilities, community amenities (e.g., adult sports leagues). Partially driven by demand for those facilities, partially by financial reality (large parcels in densely developed areas are prohibitively expensive). Leads to conflict between advocates of smaller, central ‘neighborhood schools’ and advocates of larger schools with expanded facilities.
Source: Noreen C. McDonald. (2010). School Siting. Journal of the American Planning Association, 76:2, 184-198, DOI: 10.1080/01944361003595991

## Slide 36: Siting Considerations
Available land
  Facilities such as ballfields, parking, drop-off areas, etc.
  Future growth
Age of students
  As student age (elementary, middle, high) increases, so do space requirements
  Often planners attempt to site elementary schools within neighborhoods; high schools rarely so.
    Concerns over traffic, NIMBY, etc.
Districting and equity
Notes: Notes:
While many of the mentioned facilities do not explicitly relate to the quality of education at a school (and in fact may not be related to education at all), many school facility planners emphasize that community members expect these facilities to be a part of a school and failing to incorporate them generates conflict with the community.
Planners must anticipate potential for growing enrollment, which historically has meant having undeveloped land on school parcels that can be built out.
Age of the students plays a role: most planners make effort to site elementary and junior high schools within neighborhoods (enrollment is smaller, need fewer facilities, safety of access, etc.), but typically site high schools outside of neighborhoods (high schools generate significant vehicle traffic, local community members dislike having teenagers around their homes, need for athletic facilities, etc.).
Siting also needs to consider districting and equity. Assigning students to small, neighborhood schools can result in de facto segregation in areas where there are distinct demographic patterns in neighborhoods. One major reason for creating large schools (from the 1960s on) was the opportunity to assign racially and economically diverse student population to schools, to ensure all children receive similar education quality. Creating small neighborhood schools should be considered within the context of ensuring an equitable educational system for a diverse student population.
Source: Noreen C. McDonald. (2010). School Siting. Journal of the American Planning Association, 76:2, 184-198, DOI: 10.1080/01944361003595991

## Slide 37: Siting and Active Transportation
Distance from school strongly influences likelihood to walk/bike
Factors such as population density, tree cover, intersection density positively affect walking/biking rates
  Schools sited in low-density fringe areas lead to lower rates of active transportation
Lack of pedestrian infrastructure in region reduces likelihood of walking
  Problematic in low-density, auto-centric suburban developments
Notes: Notes:
School siting and the surrounding conditions have a significant effect on students’ likelihood of walking or biking to school.
Low-density sites are unappealing for pedestrian access, and often pose connectivity challenges for bikers/walkers from surrounding communities.
When siting schools in low-density suburban developments that do not have substantial pedestrian infrastructure, active transportation will be difficult to encourage.

## Slide 38: Areas for Potential Change
Smaller parcel guidelines
  Small parcels = wider range of potential sites in urban/suburban areas
  Shared facilities
State support
  State funding for renovations
Consider pedestrian access in new sites
  Pedestrian access is not primary in site selection process
Notes: Notes:
Large parcel guidelines eliminate possible urban/suburban sites from being considered. Smaller, denser school sites with shared outdoor facilities provide an opportunity to site school facilities within dense neighborhoods in cost-effective ways.
State funding can influence decisions to create new schools or renovate existing ones. Incentivizing the renovation or expansion of existing sites within neighborhoods can avoid some of the problems posed by creating new ex-urban schools. This may work well in some communities where existing facilities are old but capable of supporting the enrollment of the community.
As currently practiced, site selection planners rarely consider the pedestrian access of a school site until the sites have been proposed and selected. This prioritizes size and facilities goals over access. Prioritizing sites with easy and safe community access will improve walking/biking rates and environmental goals.
Source:
1. Marc Schlossberg , Jessica Greene , Page Paulsen Phillips , Bethany Johnson & Bob Parker (2006). School Trips: Effects of Urban Form and Distance on Travel Mode, Journal of the American Planning Association, 72:3, 337-346
2. Noreen C. McDonald. (2010). School Siting. Journal of the American Planning Association, 76:2, 184-198, DOI: 10.1080/01944361003595991

## Slide 39: Summary
Children in low-income communities are more likely to walk to school; those communities are also less likely to have sidewalks
Designers should consider vehicle speeds, intersection geometry, crossing treatments, and pedestrian and bicycle facilities along key routes to school
Safe Routes to School programs have numerous community benefits and have been shown to increase walking and bicycling to school