## Slide 1: Temporary Facilities and Maintenance
Instructor course information
Notes: Report No. FHWA-SA-19-034

## Slide 2: Module Outline
Interim designs
Maintenance objectives
Common problems
Snow removal
Work zones

## Slide 3: Pop-Up projects and interim designs

## Slide 4
PeopleForBikes
Notes: Key Message: Pop-up projects and interim designs are considered “quick-build” projects.
Source: PeopleForBikes. (2016). Quick Builds For Better Streets: A New Project Delivery Model For U.S. Cities. Available: https://s3-us-west-2.amazonaws.com/static.peopleforbikes.org/images/glp/PeopleForBikes-Quick-Builds-for-Better-Streets-Report.pdf [Accessed July 2019]

## Slide 5: Pop-ups and Interim Designs
Pedbikeimages.org – Kristen Brookshire
“Quick-build projects”
  Led by a city government or other public agency
  Installed roughly within one year of the start of planning
  Planned with the expectation that it may undergo change after installation
    Built using materials that allow for such changes
Wikimedia Commons - DCRainbowCrosswalks
Notes: Source: PeopleForBikes. (2016). Quick Builds For Better Streets: A New Project Delivery Model For U.S. Cities. Available: https://s3-us-west-2.amazonaws.com/static.peopleforbikes.org/images/glp/PeopleForBikes-Quick-Builds-for-Better-Streets-Report.pdf [Accessed July 2019]

## Slide 6: Quick-Builds: Policies
Designated team of specialists
A system for seizing opportunities
Institutionalized urgency
Reliable funding strategy
Contracting plan
System of measurement
PeopleForBikes
Notes: Notes:
Team of specialists: Any agency pursuing quick-build projects should designate at least one specialist to be involved with every such project. In addition, these projects require buy-in from engaged politicians or top executives; nimble and creative designers; money handlers, both in budgeting and procurement; and communications and outreach professionals.
System for seizing opportunity: When opportunities knock, cities will fail to take advantage of them unless there is a process in place that can swing rapidly into action and put a project atop the priority list.
Institutionalized urgency: Installation deadlines are mandatory, whether dictated by the first big snowfall of winter, by a repaving schedule, or by a mayoral pledge.
Funding strategy: Most state and federal grants are designed around the capital-project model. Quick-build work requires different tricks.
Contracting plan: Quick-build jobs are rarely compatible with full bid cycles. Cities need either on-call contracts or in-house crews.
System of measurement: Objective metrics are an essential part of the process, both for making necessary adjustments and ultimately for demonstrating success.
Source: PeopleForBikes. (2016). Quick Builds For Better Streets: A New Project Delivery Model For U.S. Cities. Available: https://s3-us-west-2.amazonaws.com/static.peopleforbikes.org/images/glp/PeopleForBikes-Quick-Builds-for-Better-Streets-Report.pdf [Accessed July 2019]

## Slide 7: Quick-Builds: Design
Built using materials that allow for change after installation
Flexible implementation plan
Maintenance plan in place
A collaborative design process
Pedbikeimages.org – Kristen Brookshire
Notes: Notes:
Flexible materials: The materials used for quick-builds should be appropriate for rapid deployment, robust when in place, and appropriate for your particular city’s streets. These can be categorized into barrier elements, surface treatments, street furniture, landscaping elements, signs, and programming.
Flexible implementation plan: This is like “A system for seizing opportunity.” Quick builds rarely fit a typical process for permitting and installation, so you should expect to have to troubleshoot and be creative in order to make the project a reality.
Maintenance plan: Replacing torn posts, repainting colored pavement, and clearing paths of snow or debris won’t break your bank, but they do require time, money and equipment.
A collaborative design process: Mapping out design and programming elements for quick-builds typically involves a high degree of collaboration and communication. At any phase, projects may require collaborations between city staff and stakeholder agencies, neighborhood groups, business organizations, advocacy organizations, and local artists. Such partnerships are important for procurement of materials, creating a programming/activation plan, and creating a plan for ongoing stewardship once the project is built.
Source: Street Plans Collaborative. (2016). Tactical Urbanist’s Guide to Materials and Design. Available: http://tacticalurbanismguide.com/guides/tactical-urbanists-guide-to-materials-and-design/

## Slide 8
An outreach plan
Clear and specialized communications
Engaging activation strategies
Quick-Builds: Public Involvement
Notes: Notes:
Outreach plan: With these projects, installation comes in the middle of the public outreach process, not near the end.
Clear and specialized communications: Along with direct outreach, a quick-build project needs language and images that help the public understand that it’s a way to improve public involvement, not circumvent it.
Engaging activation strategies: Public programming and attractive elements to keep the public involved are critical for a quick-build’s success.
Source: PeopleForBikes. (2016). Quick Builds For Better Streets: A New Project Delivery Model For U.S. Cities. Available: https://s3-us-west-2.amazonaws.com/static.peopleforbikes.org/images/glp/PeopleForBikes-Quick-Builds-for-Better-Streets-Report.pdf [Accessed July 2019]

## Slide 9: Maintenance

## Slide 10: Maintenance Objectives
Strive to keep facilities hazard-free
Encourage reporting of hazards
Design and build facilities with maintenance in mind
Program for maintenance
pedbikeimages.org - Dan Burden
Notes: Notes: Maintenance should be considered in planning and design and should attempt to keep facilities hazard-free.
Common maintenance includes:
• Patching surfaces as smoothly as possible and requiring other agencies or private companies to do likewise whenever they dig up a street, trail, or sidewalk.
• Making sure pavement overlay projects feather the new surface into the existing one or otherwise do not create new linear joints.
• Replacing such hazards as dangerous grates or utility covers as the opportunity arises.
• Patching potholes in an expeditious manner.
• Routinely cutting back all encroaching vegetation, especially on trails, sidewalks, or popular bike routes.
Design and build new roadways, bikeways, and sidewalks in such a way as to reduce the potential for accumulating debris.

## Slide 11: Importance of Pedestrian Facility Maintenance
Key component of transportation network
Relationship between maintenance and accessibility
Critical for safety
Improved mobility
Asset management
pedbikeimages.org - Dan Burden
Notes: Notes:
Key component of transportation network: in many states, the definition of a street or highway is inclusive of everything within the public right-of-way including all the pedestrian facilities contained within.
Relationship between maintenance and accessibility: When pedestrian facilities are built, the essential accessibility requirement is to create an accessible pedestrian route within the public right-of-way to link access points and destinations. The accessible path needs to allow access between intersections and at transition points (curb ramps, medians, crosswalks, etc.). The need for relatively expensive paratransit increases when facilities become inaccessible because of poor maintenance.
Critical for safety: Improved safety through proper maintenance can result in a reduction in crashes with motorists and a reduction in trips, slips, and falls. The seriousness of falls seems to disproportionately impact older adults.
Improved mobility: A break in the network due to poor maintenance can potentially eliminate walking or transit option for people (or force the choice to drive, if a car is available to them), or prevent a trip all together if a person has not other options besides walking.
Asset management: Protect initial investment and preserve pedestrian level of service with monitoring and timely repair.
Source: Federal Highway Administration. (2013). Guide for Maintaining Pedestrian Facilities for Enhanced Safety. Available: https://safety.fhwa.dot.gov/ped_bike/tools_solve/fhwasa13037/

## Slide 12: Common Maintenance Problems for Pedestrians
Sidewalks
  Crumbling, cracked, or uplifted segments
  Uneven bricks/pavers
Crossings
  Damaged detectible warning plates
  Faded crosswalk markings
  Pedestrian signal malfunction
Seasonal or day-to-day
  Encroaching vegetation (trees, grass)
  Drainage, snow or ice
pedbikeimages.org – David Wistey
pedbikeimages.org - Dan Burden
Notes: Student Question: Ask students if they can think of any local examples where poor maintenance is an issue.
Source: Federal Highway Administration. (2013). Guide for Maintaining Pedestrian Facilities for Enhanced Safety. Available: https://safety.fhwa.dot.gov/ped_bike/tools_solve/fhwasa13037/
Image (top): http://www.pedbikeimages.org/mediumimages/mi.grandville.badsidewalk-large.jpg
Image (bottom): http://www.pedbikeimages.org/mediumimages/Crosswalk3.JPG

## Slide 13
Importance of Bicycle Facility Maintenance
Key component of transportation network
Critical for safety
Enables mobility and encourages use of non-motorized transportation
Asset management
pedbikeimages.org - Dan Burden
Notes: Key Message: Maintenance should be considered in planning and design and should attempt to keep facilities hazard-free.
Notes:
Common maintenance includes:
• Sweeping pavement edges and paved shoulders with sufficient care.
• Patching surfaces as smoothly as possible and requiring other agencies or private companies to do likewise whenever they dig up a road or trail.
• Making sure pavement overlay projects feather the new surface into the existing one or otherwise do not create new linear joints.
• Replacing such hazards as dangerous grates or utility covers as the opportunity arises.
• Patching potholes in an expeditious manner.
• Routinely cutting back all encroaching vegetation, especially on trails or popular bike routes.
Bicyclists should be encouraged to report maintenance problems and hazards. This can be accomplished by developing a bicycle spot improvement form, distributing copies throughout the bicycling community, and then making sure returned forms are acted upon in a timely fashion.
Design and build new roadways and bikeways in such a way as to reduce the potential for accumulating debris.
Source: FHWA. (2006). University Course on Bicycle and Pedestrian Transportation, Lesson 16, Bicycle Facility Maintenance.
Image: http://pedbikeimages.org/largeimages/mi.newcenter.unbikeable-large.jpg

## Slide 14: Common Maintenance Problems for Bicyclists
Surface problems
  Debris, pavement quality
Vegetation
  Encroaching vegetation (trees, grass)
Signing and marking
  Uniform and usable condition
pedbikeimages.org - Dan Burden
Notes: Student Question: Ask students if they can think of any local examples where poor maintenance is an issue.
Image (Top): http://www.pedbikeimages.org/mediumimages/mi.grandville.nograte2-large.jpg
Image (Bottom right): http://www.pedbikeimages.org/mediumimages/mi.westgrand.railcrossing-large.jpg

## Slide 15: Snow Removal

## Slide 16: Snow Removal
Common challenges to pedestrian travel after snowfall:
  Street plowing that pushes snow onto sidewalks or blocks crosswalks
  Clogged or obstructed drains that create puddles at curb ramps
  Patches of ice that create slip hazards
  Stretches of snow and ice covering sidewalks
pedbikeimages.org - Katy Lang
pedbikeimages.org - Dan Burden
Notes: Key Message: Jurisdictions should have policy and action plans that address these key issues.
Notes: Notice in image: partially shoveled sidewalk, but no access to the intersection.
Source: Federal Highway Administration. (2013). Guide for Maintaining Pedestrian Facilities for Enhanced Safety. Available: https://safety.fhwa.dot.gov/ped_bike/tools_solve/fhwasa13037/
Image (Top): http://www.pedbikeimages.org/mediumimages/47b90816e2690c014bcec50a2da59ea7.jpg
Image (Bottom): http://pedbikeimages.org/mediumimages/audit1.transit_shelter.mammoth2jpg.jpg

## Slide 17: Snow Removal
Practices
  Pre- and post-treatment of ice and snow
  Acknowledging costs and securing funding
  Servicing transit stops and ROW
Policies
  Agency agreements
  Performance measures
  Americans with Disabilities Act (ADA)
Programs
  Public education, communication, reporting
pedbikeimages.org - Dan Burden
Notes: Notes: In places prone to heavy snowfall, master/comprehensive plans and mobility plans should address winter maintenance as an important element of a complete and accessible network. The responsibility of clearing sidewalks or ROW may fall on different stakeholders (lessees, property owners, city) and these expectations should be clearly communicated.
Source: City of Minneapolis, Pedestrian and Bicycle Winter maintenance Study (April 2018), http://www.minneapolismn.gov/www/groups/public/@publicworks/documents/webcontent/wcmsp-210946.pdf

## Slide 18: Work Zones

## Slide 19: Work Zone Principles for Pedestrians and Bicyclists
Plan and design for accessibility
Advance warning and guidance
Separate pedestrians and bicyclists from vehicular traffic
Illumination and reflectorization
Accommodation for people experiencing disabilities
pedbikeimages.org – Tab Combs
Notes: Key Message: There are several planning and design elements helpful in accommodating pedestrians and bicyclists in work zones.
Notes: Preserving access to transit and businesses is another consideration.
Source: FHWA. (2006). University Course on Bicycle and Pedestrian Transportation, Lesson 21, Bicycle and Pedestrian Accommodation in Work Zones.

## Slide 20: Work Zone Toolbox
Protective barriers
Covered walkways
Temporary routes
Signage
Diversions and detours
pedbikeimages.org – Dan Burden
Notes: Notes:
The type of temporary traffic control treatment will depend upon the type of work being performed, the duration of the work, how pedestrians might be affected by the work activity, or potential hazards/impediments to travel.
Treatments left in place over several days that do not have workers present at all times will require more extensive efforts to accommodate pedestrians.
Sources: American Road and Transportation Builders Association. (2018). Pedestrian Accommodation in Work Zones: A Field Guide. Available: https://www.workzonesafety.org/files/documents/training/fhwa_wz_grant/artba_pedestrian_accommodation_wz.pdf

## Slide 21: Example of sidewalk closure and pedestrian detour
Notes: Source: MUTCD figure 6H-29 Crosswalk Closures and Pedestrian Detours (TA-29)

## Slide 22: Work Zones
Elements of an accessible temporary facility
  Communication devices
  Overhead protrusion protection
  Channelizing devices
    Handrails and guardrails
  Surfaces
  Temporary curb ramps/transitions
  Lighting
Notes: Key Message: As with vehicles, when pedestrians traverse the work zone, the route must be clearly marked, a suitable surface must be provided, and pedestrians must be protected from other traffic and work operations, including drop-offs. When they exit the work area, pedestrians need to be guided back to their original route. This slide highlights the devices and features that may be needed to provide an accessible route in a temporary traffic control zone.
Notes: The MUTCD requires that “When existing pedestrian facilities are disrupted, closed, or relocated in a TTC zone, the temporary facilities shall be detectable and shall include accessibility features consistent with the features present in the existing pedestrian facility.” This is reinforced by the proposed PROWAG guidelines: “temporary routes are alterations to an existing developed pedestrian environment and are required to achieve the maximum accessibility feasible under existing conditions.”
Connection to other Module: This slide is also shown in the module on Accessibility and ADA.
Source: The American Traffic Safety Services Association. (2012). Applying the Americans with Disabilities Act in Work Zones: A Practitioner Guide. Available: https://www.workzonesafety.org/files/documents/training/fhwa_wz_grant/ada_guide.pdf

## Slide 23: Work Zones
pedbikeimages.org - Katy Lang
It’s not just road projects that might encroach on pedestrians’ usable path
Storefront and business renovations
Other right-of-way changes
Notes: Image (left): http://www.pedbikeimages.org/largeimages/20180524_125532.jpg
Image (right): http://www.pedbikeimages.org/largeimages/cc10a4bccc60e4fe9954b625634ee69e.jpg

## Slide 24: Work Zones: Case Studies
Virginia DOT
  Work Zone Pedestrian and Bicycle Guidance
District DOT (DC)
  Pedestrian Safety and Work Zone Standards
Washington Area Bicyclist Association
Notes: Key message: The last few slides will show examples of places that have already implemented standards or published guides to accommodate pedestrians and bicyclists in the case of construction in the right-of-way.

## Slide 25: Virginia DOT: Work Zone Pedestrian and Bicycle Guidance (2016)
Presents basic guidelines for work zone traffic control
Intended to illustrate the principles of proper work zone traffic control
Includes accessibility “checklist” for projects
Notes: Notes:
Presents basic guidelines for work zone traffic control for pedestrians and bicyclists.
Intended to illustrate the principles of proper work zone traffic control, including:
  Compliance with ADA standards.
  Bicycle/shared use Paths.
  Guide to selecting appropriate treatments.
  Accessibility “checklist” for pedestrians and bicycles.
Source: VDOT Work Zone Pedestrian and Bicycle Guidance, May 2016

## Slide 26: Virginia DOT
Notes: Source: VDOT Work Zone Pedestrian and Bicycle Guidance, May 2016

## Slide 27: District DOT: Pedestrian Safety and Work Zone Standards (2007)
Guide for covered and open walkways from construction
Preferred methods for routing pedestrians safely through work zones
Notes: Notes:
Provides guidance and standards to District DOT employees for reviewing construction of protected walkways on sidewalks and roadways.
Provides guidance on preferred methods for routing pedestrians safely through work zones occupying public space in the District of Columbia, including:
  Construction standards.
  Sidewalk and roadway treatments.
  Protection of users in different phases of construction.
  ADA compliance and transit access.
Source: District DOT, Pedestrian Safety and Work Zone Standards (December 2007)

## Slide 28: District DOT
Notes: Source: District DOT, Pedestrian Safety and Work Zone Standards (December 2007)

## Slide 29
Work areas can be very unfriendly places for pedestrians and bicyclists, BUT there are ways to accommodate all types of traffic in a work area.
Flickr Creative Commons- BeyondDC

## Slide 30: Summary
Quick-build projects are an option for quick implementation with the option to adjust
Plan and budget for the maintenance of pedestrian and bicycle facilities
Temporary traffic control zones must include an accessible pedestrian route