## Slide 1: The Benefits of Designing Streets for Walking and Bicycling
Instructor course information
Notes: Report No. FHWA-SA-19-034

## Slide 2: Module Outline
Why do we need streets designed for walking and bicycling?
  Safety
  Equity
  Health
  Environmental stewardship
  Community vitality
  Transportation efficiency

## Slide 3: Safety
pedbikeimages.org – Dan Burden

## Slide 4: Safety Through Design
Anticipate and design for active travel
Design considerations:
  Safety (reduce conflicts)
  Accessibility
  Predictability
  Visibility
  Separation
  Minimize delay
  Context sensitivity
pedbikeimages.org – Ann McGrane
Notes: Key Message: Basic principles of Safe Systems establish that walking and bicycling are civil rights, which need to be not only accommodated, but prioritized in roadway design.
Notes: Design considerations for pedestrian & bicycle safety:
Safety (reduce conflicts) – Slower speeds and geometric design (medians, shorter crossing distances) should be used to improve safety for all modes to eliminate or minimize conflicts.
Accessibility – All roads and crossings should meet ADA standards. This good design benefits all users.
Predictability – Design should provide clear right-of-way assignments, visibility of all users, and a clear path of travel for all modes.
Visibility – Curb extensions, lighting, pavement markings may all be used to improve visibility.
Separation – Greater separation of modes should be used as speeds and/or volumes increase (buffered bike lanes, separated bike lanes, etc.).
Minimize delay – Reduced delay at crossings will yield improved and safer behaviors. Shorter block lengths and improved bicycle and pedestrian networks will reduce travel time.
Context sensitivity – Design should incorporate and support the natural environment and adjacent land use.
Key values of Systematic Safety (based on Vision Zero in Netherlands):
Safe mobility is a civil right.
The road system owner is responsible for ensuring road safety.
Traffic safety programs must be proactive, eliminating safety risks before they cause serious death or injury.
Principles of Systematic Safety (based on Vision Zero in Netherlands):
Speed control & separation
Functional harmony
Predictability and simplicity
Forgiveness and restrictiveness
State awareness
Connection to other Module: The design considerations are also listed on the slide “Design Principles” in the module, Designing for Walking and Bicycling.
Source:
Systematic Safety: The Principles Behind Europe’s Vision Zero by Peter Furth. Available: http://www.northeastern.edu/peter.furth/wp-content/uploads/2017/01/Systematic-Safety-Action-Plan-for-Boston.pdf
PBIC, Pedestrian and Bicycle Transportation Short Series (2015)
FHWA, Achieving Multimodal Networks: Applying Design Flexibility & Reducing Conflicts (2016). Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_networks/

## Slide 5: Safety in Numbers
Inviting and inclusive design leads to increased use
More people on the street leads to more awareness/ expectation and improved safety and security
R. Schneider, J. Vargo, A. Sanatizadeh (2017)
Notes: Key Message: Safety in numbers is the idea that increased visibility of people walking and bicycling can lead to increases in drivers’ expectations to see people walking and biking. According to a 2011 study that examined 24 California cities over an 11-year period (1997-2007) there is “growing evidence to suggest that cities with higher bicycling rates also have better road safety records.”
Source: Marshall, W. E., & Garrick, N. W. (2011). Research Article: Evidence on Why Bike-Friendly Cities Are Safer for All Road Users. Environmental Practice, 13(1), 16-27. doi:10.1017/s1466046610000566
Image Source: Schneider, R. J., Vargo, J., & Sanatizadeh, A. (2017). Comparison of US metropolitan region pedestrian and bicyclist fatality rates. Accident Analysis & Prevention,106, 82-98. doi:10.1016/j.aap.2017.04.018

## Slide 6: Safety for All
NCHRP 893: Systemic Pedestrian Safety Analyses
Designing for the most vulnerable road users translates to safety benefits for less vulnerable road users as well
Notes: Key Message: Designing for the most vulnerable road users translates to safety benefits for less vulnerable road users as well.
As this table shows, countermeasures designed to reduce crashes for pedestrians almost always lead to reduced crashes for motorists as well.
Notes: A crash modification factor (CMF) is a multiplicative factor used to compute the expected number of crashes after implementing a given countermeasure at a specific site. (A CMF below 1 indicates a crash reduction, while a CMF greater than 1 indicates an increase in crashes. A CMF of 1 would indicate no change in the number of crashes.)
Connection to Other Module: Safety Analysis and Countermeasure Selection explains CMFs in more detail.
Source: Thomas, L., Sandt, L., Zegeer, C., Kumfer, W., Lang, K., Lan, B., ... & Schneider, R. J. (2018). NCHRP 893: Systemic Pedestrian Safety Analysis (No. Project 17-73). National Cooperative Highway Research Program.
(Image is Table 17 in the report)

## Slide 7: Equity
Notes: Key Message: The high cost of car ownership means that low-income families will have to spend a greater portion of their income on owning and operating a car or choose not to have one. If automobile travel is the only feasible mode of transportation in a community, low-income families are placed at a large disadvantage with very limited mobility. By providing safe and convenient pedestrian and bicycle facilities, the community can ensure that all citizens have access to a viable mode of transportation.
Source: Pedestrian and Bicycle Information Center (2019). “Equity.” Available: http://www.pedbikeinfo.org/factsfigures/facts_equity.cfm. [Accessed June 2019]
Image taken by Lyuba Zuyeva on the Beltline Trail in southwest Atlanta, March 2019.

## Slide 8: Pathways to Equity
Walkable places = offset the high cost of housing and transportation
Improved access to employment and education opportunities
Promote physical activity for people with high risk of inactivity in rural areas
Can provide opportunities for community revitalization
pedbikeimages.org – Lyubov Zuyeva
Notes: Key Message: Walkable urban places can decrease combined household and transportation costs and mitigate the impact of rising housing costs in most growing metro areas. And in all areas, including rural communities, trails may be beneficial in promoting physical activity among segments of the population at highest risk for inactivity.
Notes:
A 2016 study found that for the 30 largest metro areas in the U.S., looking at moderate-income household (80 percent of area median income) spending on housing and transportation, and considering access to employment, the data show that the most walkable urban metros are also the most socially equitable (Leinberger and Rodriguez).
Low transportation costs and better access to employment offset the higher costs of housing. However, for equity to be a benefit of active transportation, facilities need to reach the people who need them the most. Bridging the Gap research found that 90 percent of streets have sidewalks in high income communities, compared to sidewalks on only 50 percent of streets in lower income communities. The same research also found that land use laws and development regulations in lower- and middle-income communities are less likely to include requirements that would promote walking and bicycling.
Sources:
Leinberger, Christopher and Michael Rodrigues. (2016) Foot Traffic Ahead. The George Washington University School of Business. Available: https://smartgrowthamerica.org/resources/foot-traffic-ahead-2016/
Thrun E, Chriqui JF, Slater SJ, Barker DC, and Chaloupka FJ. (2012). Using Local Land Use Laws to Facilitate Physical Activity - A BTG Research Brief. Chicago, IL: Bridging the Gap Program, Health Policy Center, Institute for Health Research and Policy, University of Illinois at Chicago. Available: http://www.bridgingthegapresearch.org/_asset/5q86hg/btg_land_use_pa_FINAL_03-09-12.pdf
Brownson, R. C., Housemann, R. A., Brown, D. R., Jackson-Thompson, J., King, A. C., Malone, B. R., & Sallis, J. F. (2000). Promoting physical activity in rural communities. American Journal of Preventive Medicine,18(3), 235-241. doi:10.1016/s0749-3797(99)00165-8
Possible exercise: Invite students to break out in groups and examine the combined housing and transportation affordability index for some of the region’s neighborhoods—utilizing online mapping interface provided by the Center for Neighborhood Technology, https://htaindex.cnt.org/

## Slide 9: Serving People of all Ages and Abilities
Accessibility vs. mobility
Vulnerable populations
Different road users have different needs and levels of comfort
pedbikeimages.org – Dan Burden
Notes: Key Message: Building streets so that they can accommodate people from age 8 to age 80 (approx.) means that the streets will work better for everyone.
Notes:
Accessibility vs. Mobility
As we learned in the Introduction module, the current U.S. road network is primarily designed for automobiles.
By improving facilities and awareness for bicycling and walking needs, we fill an unmet demand for those who are unable to or choose not to drive a car.
Active transportation increases accessibility. Previously, planners and engineers focused only on mobility, or the movement of people. Accessibility recognizes that transportation is the means to access employment, education, healthcare, housing, and other opportunities. By focusing on the needs of the people and not just their movement (mobility), we can more equitably improve transportation and active transportation.
Vulnerable Populations
Adding or enhancing active transportation facilities can more evenly distribute space for different users of the street, and especially those unable to drive, such as the elderly, children, low-income, or people with disabilities. This is especially crucial for quality of life and sense of freedom.
In an assessment of health-related community characteristics, Urban Land Institute found that Latinos, African Americans, and millennials are more likely to report that crime or traffic in their neighborhood makes it unsafe to walk (America in 2015: A ULI Survey of Views on Housing, Transportation, and Community).
Different street users have different needs and levels of comfort
Different individuals using a street will have different needs and demands of that street.
  Some individuals use sidewalks for a recreational purpose, while other users must use the sidewalk to commute to work or access transit.
We must ask ourselves, who is using streets, for what purposes, and do they have what they need in orderly to safely fulfill those purposes?
Active transportation infrastructure can mean different things to different people.
  For example, a confident and experienced bicycle rider might feel fine with a shared lane marking or bike lane, but a family might prefer a separated bike lane.
Source: 8-80 Cities has additional resources to think about designing for people of all ages and abilities. Available: https://www.880cities.org/about-8-80-cities/

## Slide 10: health
pedbikeimages.org – Laura Sandt

## Slide 11: Individual Health
Provide opportunities for physical activity
Support aging in place
pedbikeimages.org – Dan Burden
Notes: Notes: Walking and bicycling provide important opportunities to be physically active:
Walking at a rate of 3 MPH burns 250 calories per hour, and bicycling at 10-12 MPH burns 475 calories per hour, three to six times as much as a person would burn while sitting (Ainsworth et al., 2011)
“Public transit users take 30% more steps and spend roughly 8 more minutes walking each day than drivers.” (APHA, 2010).
Source:
Ainsworth, B. E., Haskell, W. L., Herrmann, S. D., Meckes, N., Bassett Jr, D. R., Tudor-Locke, C., ... & Leon, A. S. (2011). 2011 Compendium of Physical Activities: a second update of codes and MET values. Medicine & science in sports & exercise, 43(8), 1575-1581.
American Public Health Association (2010). Get the Facts: Active Transportation Benefitting Health, Safety, and Equity. Available: https://www.apha.org/-/media/files/pdf/topics/transport/apha_active_transportation_fact_sheet_2010.ashx?la=en&hash=E2DD3E9B1BFD861B57C490A5FA0FC18FC201FE15 [Accessed July 2019]

## Slide 12
Health Benefits Associated with Regular Physical Activity
Lower risk of all-cause mortality
Lower risk of cardiovascular disease mortality
Lower risk of cardiovascular disease
Lower risk of hypertension
Lower risk of type 2 diabetes
Lower risk of adverse blood lipid profile
Lower risk of cancers of the bladder, breast, colon, endometrium, esophagus, kidney, lung, and stomach
Increased cognition
Reduced risk of dementia
Improved quality of life
Reduced anxiety
Reduced risk of depression
Improved sleep
Slowed or reduced weight gain
Weight loss
Prevention of weight regain
Improved physical function
Lower risk of falls (older adults)
Lower risk of fall-related injuries
Improved bone health (age 3-17 years)
Improved cardiometabolic health (age 6-17 years)
Source: Table 2.1 from the Physical Activity Guidelines for Americans: 2nd Edition, 2018,
U.S. Department of Health and Human Services
Notes: Key Message: Physical activity is vital for healthy aging and can reduce the burden of chronic diseases and prevent early death. Active people generally live longer and are at less risk for serious health problems like heart disease, type 2 diabetes, obesity, and some cancers. For people with chronic diseases, physical activity can help manage these conditions and complications. One in ten premature deaths could be prevented through physical activity. Physical activity such as active transportation can also help cope with stress and anxiety (if the user has adequate facilities) and active transportation can help boost energy and mood.
Source: Centers for Disease Control and Prevention. “About Physical Activity.” Available: https://www.cdc.gov/physicalactivity/about-physical-activity/index.html [Accessed July 2019]

## Slide 13: Community Health
pedbikeimages.org – Brandon Whyte
Promotes and enables social interaction and engagement
Notes: Key Message: The social interaction possible when the number of people walking increases is a major factor for improving quality of life. Comfortable and accessible pedestrian environments offer alternatives to personal vehicles, which limit opportunities for social contact with others. By providing appropriate pedestrian facilities and amenities, communities enable the interaction between neighbors and other citizens that can strengthen relationships and contribute to a healthy sense of identity and place.
Notes:
Active transportation promotes and enables social interaction and engagement, which can lead to a happier and more connected community A study from Texas of people who moved to walkable community found that the people who moved had a higher number of social interactions, such saying hello or chatting with a neighbor, or asking to borrow items. They also felt that they could count on their neighbors if they needed to, and that their neighborhood was “close-knit.”
Many people choose to walk or bicycle while on vacation. “Outdoor activities such as bicycling and walking are the most popular activities for people on vacation from work. They are more popular than visiting museums or national parks, doing beach and water activities, and shopping.”
Student Question: How can we enable and empower people to enjoy life more by not just walking and biking while on vacation, but during everyday trips?
Source:
Shannon H. Rogers, John M. Halstead, Kevin H. Gardner and Cynthia H. Carlson. (2010). Examining Walkability and Social Capital as Indicators of Quality of Life at the Municipal and Neighborhood Scales. Applied Research in Quality of Life.
Zhu X, Yu CY, Lee C, Lu Z, Mann G. (2014). A retrospective study on changes in residents’ physical activities, social interactions, and neighborhood cohesion after moving to a walkable community Preventive Medicine.

## Slide 14: The Health Risks of Inaction
Globally, physical inactivity accounts for roughly 9% of premature mortality (Lee et al., 2012)
In the US, obesity costs account for ~9% of all health care spending (APHA)
Some of these negative outcomes are “attributable to auto-oriented transportation that inadvertently limits opportunities for physical activity” (APHA)
Notes: Source:
American Public Health Association (2010). Get the Facts: Active Transportation Benefitting Health, Safety, and Equity. Available: https://www.apha.org/-/media/files/pdf/topics/transport/apha_active_transportation_fact_sheet_2010.ashx?la=en&hash=E2DD3E9B1BFD861B57C490A5FA0FC18FC201FE15 [Accessed July 2019]
Lee, I. M., Shiroma, E. J., Lobelo, F., Puska, P., Blair, S. N., Katzmarzyk, P. T., & Lancet Physical Activity Series Working Group. (2012). Effect of physical inactivity on major non-communicable diseases worldwide: an analysis of burden of disease and life expectancy. The Lancet, 380(9838), 219-229.

## Slide 15: Health and Aging in Place
Mobility-related injuries are leading cause of injuries and death in older adults (65+)
Older adults 50% more likely than younger individuals to be struck and killed by car while walking
Older adult pedestrian fatality rates are increasing
Decreased mobility results in declining health and social isolation
Strategies to increase mobility for elderly:
  Transit Oriented Development
  Age-friendly street design
Notes: Key Message:
Notes:
Design age-friendly streets by…
Reduced crossing distance
Slower walking speed signal timing
Pedestrian recall (non-actuated)
Accessible Pedestrian Signals (APS)
Leading Pedestrian Intervals (LPI)
Speed Management
Source:
PBIC, Creating Age-Friendly Streets – Part 1 (2019)
PBIC, Creating Age-Friendly Streets – Part 2 (2019)

## Slide 16
Environmental Stewardship
Source: EPA.GOV
Notes: Key Message: The transportation sector is responsible for roughly a third of all greenhouse gas emissions (GHG). In the U.S., air pollution results in about 60,000 premature deaths per year and traffic-related air pollution results in about 250,000 cases of pediatric asthma cases.
Notes: Designing facilities to support sustainable, people-powered travel and reduce the reliance on GHG-emitting vehicles is vital for energy conservation and environmental stewardship.
According to the U.S. Environmental Protection Agency, the transportation sector accounted for the largest share of greenhouse gas emissions (29%) in the United States in 2017. Light-duty vehicles, which includes passenger vehicles and light-duty trucks, account for most transportation sector emissions at 59%.
Building infrastructure for vehicles, such as streets and parking lots, increases the impervious surface of an area which can exacerbate stormwater runoff, urban flooding, and the urban heat island effect. Promoting pedestrian and bike infrastructure provides an opportunity to integrate green infrastructure into street design and produce co-benefits for urban heat island, stormwater, and flood mitigation as well as pedestrian health and safety.
Source:
Environmental Protection Agency. (2019). “Fast Facts U.S. Transportation Sector Greenhouse Gas Emissions, 1990-2017” Available: https://www.epa.gov/greenvehicles/fast-facts-transportation-greenhouse-gas-emissions.
Achakulwisut, P., Brauer, M., Hystad, P., & Anenberg, S. C. (2019). Global, national, and urban burdens of paediatric asthma incidence attributable to ambient NO2 pollution: estimates from global datasets. The Lancet Planetary Health, 3(4), e166-e178.

## Slide 17: Inefficiencies and Impacts of Auto-Oriented Transportation
In 2017, 76% of Americans drove to work alone.
Wikimedia Commons
Notes: Key Message: Automobile exhaust is a significant source of nonpoint source pollution in our air and water in the United States.
Source: Social Explorer, American Community Survey 5-year Estimate (2017) Table: SET128.

## Slide 18: Greener Infrastructure
Trail and pedestrian/bicycle projects offer opportunities for:
  Stormwater management
  Improved air quality
  Reduced urban heat island effect
  Reduced noise pollution
  Creation of recreational open space
Pedbikeimages.org – Laura Sandt
Notes: Key Message: Green infrastructure benefits the environment. There are opportunities to incorporate green infrastructure into active transportation facilities.
Notes: Stormwater can be a particularly critical issue for many urban areas. Due to the changes in climate and ongoing urbanization of many regions, extreme rainfall events and resulting urban flooding events are becoming more common. Research from University of Maryland and Texas A&M, Galveston, affirmed that in much of the United States, urban flooding is occurring and is a growing source of significant economic loss, social disruption, and housing inequality. Many Complete Streets solutions use less pavement such as right-sized roads, rechannelizations/road conversations, and skinny streets, and many can be accomplished without building overly wide streets. Generally, starting a conversation about how the street is designed and how much space is dedicated for vehicles vs. other uses allows an additional opportunity to consider other treatments and approaches, such as green streets for improved stormwater treatment.
Sources:
The Value of Green Infrastructure: A Guide to Recognizing Its Economic, Environmental, and Social Benefits by Center for Neighborhood Technology and American Rivers. Available: https://www.cnt.org/sites/default/files/publications/CNT_Value-of-Green-Infrastructure.pdf
Galloway, G., Brody, S. et al. (2018). The Growing Threat of Urban Flooding. The Center for Disaster Resilience at the University of Maryland and Center for Texas Beaches and shores at Texas A&M University, Galveston Campus. Available https://cdr.umd.edu/urban-flooding-report
Smart Growth America. (2015). “The Many Benefits of Complete Streets.” Available: https://smartgrowthamerica.org/resources/the-many-benefits-of-complete-streets/

## Slide 19
Community Vitality
pedbikeimages.org – Heather Bowden
Notes: Key Message: Better conditions for walking have intangible benefits to the quality of life in cities and towns. In a growing number of communities, the level of walking is considered an indicator of a community's livability—a factor that has a profound impact on attracting businesses and workers as well as tourism. In cities and towns where people can regularly be seen out walking, there is a perception that these are safe and friendly places to live and visit.
Notes: Economic benefits can be difficult to measure, but politically, these might be the most important benefits to demonstrate. Potential data sources include sales tax filings, leases and rents, property value, real estate transactions, business establishment, employment figures, and building permits. Each of these have pros and cons for measurement and the “benefit” may vary within a community. For example, increasing property values can mean that some residents and business owners may be forced out.
Source: Pedestrian and Bicycle Information Center. (2019). “Equity.” Available: http://www.pedbikeinfo.org/factsfigures/facts_equity.cfm

## Slide 20: Community Vitality
Business benefits
  Increased real estate value
  Increased customer access
  Less demand for customer parking
  More frequent visits and more money spent (by those who arrive by bike)
Photo by Omer Rana on Unsplash
pedbikeimages.org – Ryan Snyder
Notes: Key Message: Walking and bicycling are affordable forms of transportation. Many studies have shown that support for and investment in pedestrian and bicycle infrastructure results in economic benefits for individuals, businesses, and communities.
Notes: Cities, politicians, developers, and voters all care about the return on investment and economic benefits of infrastructure and how money is spent.
By investing in bicycling and walking infrastructure, a community is building a strong economic multiplier.
Student Question: Read and discuss the quality of this evaluation of economic benefits from New York City DOT: http://www.nyc.gov/html/dot/downloads/pdf/dot-economic-benefits-of-sustainable-streets.pdf
Sources:
Urban Land Institute (2016). Active Transportation and Real Estate: The Next Frontier. Washington, DC. Available: http://uli.org/wp-content/uploads/ULI-Documents/Active-Transportation-and-Real-Estate-The-Next-Frontier.pdf
CDC Physical Activity https://www.cdc.gov/physicalactivity/about-physical-activity/pdfs/healthy-strong-america-201902_508.pdf
Leinberger, Christopher and Michael Rodrigues. (2016) Foot Traffic Ahead. The George Washington University School of Business. Available: https://smartgrowthamerica.org/resources/foot-traffic-ahead-2016/
Michael Anderson and Mary Lauren Hall. (n.d.) Protected Bike Lanes Mean Business. PeopleForBikes and Alliance for Biking and Walking. Available: https://www.peoplepoweredmovement.org/site/images/uploads/Protected_Bike_Lanes_Mean_Business.pdf

## Slide 21: Community Vitality
Employer benefits
  Physically active employees take fewer sick days
  Healthier employees are more productive
  Less demand for employee parking spots
Job creation benefits
  17 jobs per $1M walk/bike/trail project (more than for road-only)
Individual benefits
  Increased property value near a trail, greenway, or sidewalk
  Reduces healthcare costs
  Reduces employment commute and parking costs
  Individual cost benefit and savings for car ownership and parking
Notes: Key Message: Increased levels of bicycling and walking result in significant benefits to the economy. Politically, this is likely the most important benefit to remember.
Notes: More on job creation benefits:
A 2011 study found that bike projects created more jobs, 11.4 per $1 million, than road-only jobs, which created 7.6 per $1 million.
  Source: Bicycle Infrastructure: A National Study of Employment Facts. http://www.peri.umass.edu/fileadmin/pdf/published_study/PERI_ABikes_June2011.pdf
Rails-to-Trails shared data from the American Association of State Highway and Transportation Officials, with updated numbers indicating that 17 jobs are created for every $1 million spent on greenways, sidewalks, and bicycle facilities.
  Source: https://www.railstotrails.org/resourcehandler.ashx?name=trail-investment-a-good-deal-for-the-american-economy&id=14675&fileName=RTC_Trail_Benefits_Fact_Sheet_All_Use.pdf
Sources:
Urban Land Institute (2016). Active Transportation and Real Estate: The Next Frontier. Washington, DC. Available: http://uli.org/wp-content/uploads/ULI-Documents/Active-Transportation-and-Real-Estate-The-Next-Frontier.pdf
Centers for Disease Control and Prevention. Physical Activity Builds a Healthy Strong America. Division of Nutrition, Physical Activity, and Obesity. Available: https://www.cdc.gov/physicalactivity/about-physical-activity/pdfs/healthy-strong-america-201902_508.pdf

## Slide 22: Community Vitality
Societal benefits
  Recoup time and money lost to congestion
  Avert collision and injury costs
  Bicycle tourism can spur economic development and job creation
Notes: Notes:
The cost of congestion for the nation in 2014 was $160 billion, accounting for an additional 6.9 billion hours driven and 3.1 billion gallons of fuel purchased by urban Americans due to congestion. For the average auto commuter, the cost of congestion was $960 in 2014.
Complete Streets are designed to provide safe access to all users, including pedestrians and bicyclists. Smart Growth America found that their Complete Street case study projects averted $18.1 million in collision and injury costs in one year. In some cases, the avoided collision costs in the first year alone exceeded the entire project cost. The projects also cost less per mile than average arterial roads, and they achieved significant results despite these lower costs.
Sources:
Schrank, D., Eisel, B., Lomax, T., and Bak, J. (August 2015). 2015 Urban Mobility Scorecard. Texas A&M Transportation Institute and INRIX, Inc.. Available: https://static.tti.tamu.edu/tti.tamu.edu/documents/mobility-scorecard-2015.pdf
Smart Growth American (2015). Safer Streets, Stronger Economies. Available: https://smartgrowthamerica.org/resources/evaluating-complete-streets-projects-a-guide-for-practitioners/

## Slide 23
TRANSPORTATION Efficiency
Cycling Promotion Fund
Notes: Notes: Planning for active transportation provides opportunities to plan for more effective use of limited resources.

## Slide 24: Transportation Efficiency
In 2017, 45% of vehicle trips were 3 miles or less, and 21.4% were 1 mile or less (NHTS)
If you provide facilities for walking and bicycling, more people are likely to walk and bike
Thereby reducing the number of cars on the road, congestion, and increasing efficiency of road network utilization
Unsplash– Connor Williams
Notes: Key Message: Increased levels of bicycling and walking result in significant benefits for transportation efficiency and the network. If you build facilities for walking and bicycling, more people are likely to walk and bicycle.
Notes:
According the 2017 National Household Travel Survey, 45% of vehicle trips were 3 miles or less (a 15-minute bike ride) and 21.4% were 1 mile or less (a 10-minute walk).
With limited urban land supply and high driving demand, most major U.S. cities experience high levels of congestion. Increasing levels of active transportation would result in benefits for all mode users, as the transportation network would be more efficiently used. A more efficient use of the road system reduces vehicular congestion as well as parking demands.
Increasing biking and walking facilities assists those currently using active transportation. It also indirectly benefits all road users, by changing travel behaviors of some, and again more efficiently using the road network.
Residents are 65% more likely to walk in a neighborhood with sidewalks. And cities with more bike lanes per square mile have higher levels of bicycle commuting.
Rural areas also benefit from walking and biking facilities. Fully separated multi-use and greenway paths work better in rural communities as destinations can be further apart and roads can have higher speeds.
Sources:
Giles-Corti, B., & Donovan, R.J. (2002). “The relative influence of individual, social, and physical environment determinants of physical activity.” Social Science & Medicine, 54 1793-1812.
Dill, Jennifer and Theresa Carr. (2003). “Bicycle Commuting and Facilities in Major US Cities: If You Build Them, Commuters Will Use Them.” Transportation Research Record: Journal of the Transportation Research Board, No. 1828, TRB, 2003, pp 116-123.

## Slide 25: Efficiency & Cost of Projects
Standalone bicycle and pedestrian projects are often small in scale and cost
Individual projects of a similar type can be aggregated into one fundable package within the STIP/TIP
  Provides flexibility to fund small projects as they are ready
  No additional time to gain individual spot on STIP/TIP
Bundled projects can also support acceleration of other phases of implementation (i.e., procurement of batches of traffic control devices)
Notes: Source: FHWA (2018). Strategies for Accelerating Multimodal Project Delivery. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_delivery/fhwahep19006.pdf

## Slide 26
Taking a systems approach
pedbikeimages.org- Megan Kanagy
Notes: Key Message: Taking a systems approach means looking beyond just the transportation sector role in supporting bicycle and pedestrian infrastructure and recognizing the broader system or context in which this work takes place.
Image: Although these cyclists have a two-way cycle track in Washington, DC, traffic congestion is blocking the intersection and the ability for people on bicycles and pedestrians to safely cross. Simply building more and better bike facilities may not be enough, without also thinking about the factors that are affecting vehicle use.

## Slide 27: Recognizing Interconnectedness
Dr. Rod McClure
Notes: Key Message: The benefits we discussed today are all intertwined. Improving opportunities for active travel can lead to a convergence of benefits in multiple sectors, including the economy, environment, health, etc.
Subsequent modules will look at land use, ways to limit the growth of vehicle miles traveled and optimize roadway design for active travel will have synergistic effects on safety/injury prevention, the environment, health, and equity and access to education, jobs, etc.
Source: Rod McClure presentation at April 2019 Safe Systems Summit, Durham, NC. Available: https://www.roadsafety.unc.edu/wp-content/uploads/2019/05/Tues-keynote_McClure-1.pdf

## Slide 28: Summary
Designing for walking and bicycling can:
  Benefit all road users
  Promote physical activity
  Support more equitable communities
  Promote environmental stewardship
  Improve the efficiency of our transportation system