## Slide 1: Factors Influencing Mode Choice
Instructor course information
Notes: Report No. FHWA-SA-19-034

## Slide 2: Module Outline
Factors associated with walking and bicycling
Land use and site design policies
Motivations to walk and bike
Select examples of strategies that encourage active travel

## Slide 3: Why Do We Have Cities?
To minimize travel and maximize exchange
(to be closer together)
FHWA/PBIC
Notes: Key Message: The next two slides are intended to point out an irony: humans congregated in cities to minimize their need for travel.
Source: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 4: How Have We Built Our Urban Roadway System?
To facilitate travel over longer distances
FHWA/PBIC
Notes: [This slide is animated]
Key Message: Since World War 2, we’ve forgotten why we have cities and have facilitated travel over longer distances, making cities less livable.
Source: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 5: Who Are Streets For?
pedbikeimages.org – Ryan Snyder
pedbikeimages.org – Dan Burden
Notes: Key Message: Historically, streets were the basic structure of urban form – they represented the intersection of public and private space and operated as a gathering place. Streets evolved with the emergence and dominance of the automobile. Non-automobile modes became “alternative” modes. This was codified in the U.S. with the 1956 Federal Highways Act, which established road-building as an engineering domain and efficiency as the primary objective.
Notes: Image on the left is in Copenhagen, Denmark; right is in Charlottesville, Virginia
Connection to other Module: For more on the history of streets and transportation planning, see the Introduction module.
Source: Adapted from slides by Tab Combs.
Image (left): http://www.pedbikeimages.org/mediumimages/dscn3883.jpg
Image (right): http://www.pedbikeimages.org/mediumimages/va.charlottesville.wideroad-large.jpg

## Slide 6: Factors Associated with Walking and Bicycling
Land use
Community design
Transportation system
This is where we will be spending time for this lesson
Notes: Key Message: Land use and community design refer to characteristics such as population and employment density, mix of uses, building setbacks, etc. These are often referred to as the “D” variables – Density, Diversity, Design, Destination accessibility (or availability), and Distance to transit.
Notes: Characteristics of the transportation system will be covered throughout subsequent modules, but generally this includes sidewalks, bike lanes, trails, sidewalk and bicycle facility connectivity, slower auto speeds, and fewer arterial roadways.

## Slide 7: Factors Associated with Walking and Bicycling
Other:
Natural environment
  Topography, precipitation, temperature
Socioeconomic characteristics
  Auto ownership, age, physical ability, gender, student status, income
pedbikeimages.org – Lyubov Zuyeva
Notes: Key Message: These factors are no less significant than the factors listed on the previous slide. Many of the factors listed on this slide and the previous slide have important interactions with each other and their relationship to walking and/or bicycling can be either positive or negative. However, as transportation professionals, your students are not likely to influence policies and practices that influence these factors.
Image: http://www.pedbikeimages.org/mediumimages/DSC03735.JPG

## Slide 8: Socioeconomic Factors
Safe Routes to School National Partnership
Notes: Key Message: Even though transportation practitioners do not have a direct influence on socioeconomic status, socioeconomic status is an important factor that should be considered throughout the planning process, including project identification and prioritization.
Notes: Low income Americans have the highest rates of walking and bicycling to work, and bicycling is growing most rapidly among people of color. Most transit riders are low to moderate income, and more than 60 percent walk to or from transit. The safety and convenience of walking and bicycling is vitally important for low-income people and people of color.
Connection to other Module: Equity
Source: Zimmerman, Sara; Lieberman, Michelle; Kramer, Karen; and Sadler, Bill. (2015). At the Intersection of Active Transportation and Equity. Oakland, CA: Safe Routes to School National Partnership.

## Slide 9: LAND USE and Site Design Policies
Notes: Key Message: The next few slides will introduce land use policies that affect mode choice.

## Slide 10: Land Use – Zoning
Conventional
  Single-use districts
Form-based
  Form, scale, mass
Overlays
  Areas with alternative requirements or incentives
City of Cincinnati Form-Based Code
Notes: Notes:
Form-based code – can be applied to a corridor, neighborhood, or entire city. These regulate the form, scale, and massing of buildings before the use. They can encourage a more inviting, pleasant environment for pedestrians. By contrast, conventional zoning codes focus primarily on establishing single-use districts and regulations for each use.
Overlay districts/zones – are commonly used in conventional zoning codes to provide additional regulations to existing zones in specific geographic areas. They offer significant flexibility by avoiding blanket requirements and addressing specific policies in specific areas. Their flexibility and ability to pinpoint policy areas make them useful tools to promote or require developments and facilities that accommodate walking, bicycling, and/or transit in the most appropriate areas.

## Slide 11
Unsplash - Michael Tuszynski
Notes: Notes: Housing as far as the eye can see. This is likely the result of conventional zoning that calls for single-family residential districts.
Image: This is a photo of Herriman, UT, https://unsplash.com/photos/2osRMlJLdbU

## Slide 12: Land Use – Zoning
Density
  Reduces distance between daily activities
  Low density is only practical because of cars
  Lot coverage, not just building heights, can achieve density
Mix of use
  Reduces distances between daily activities
City of Charlottesville
Notes: Notes:
Zoning for greater density can make walking and biking more attractive options. Research overwhelmingly shows that density is significant for promoting walking and transit use. Examples of policies to support greater density include lower minimum lot sizes, allowing accessory dwelling units (ADUs) (various configurations are shown in the image on the slide), and inclusive zoning that allows multifamily units (as opposed to single-family zoning that excludes multifamily dwellings).
Mix of Use – Mixed-use zones generally allow for a higher density development and a variety of uses, making active transportation options more doable for more trips. Mixed-use zoning may be applied at all levels of planning, from comprehensive Unified Development Ordinances to individual zoning changes on a site-by-site basis. Segregated land uses are typically enshrined by conventional zoning, which designates large areas for single uses only.
Source:
FHWA. (2016). Noteworthy Local Policies that Support Safe and Complete Pedestrian and Bicycle Networks. Available: https://safety.fhwa.dot.gov/ped_bike/tools_solve/docs/fhwasa17006-Final.pdf
Ewing, R., & Bartholomew, K. (2013). Pedestrian- & transit-oriented design. Washington, D.C. Urban Land Institute and American Planning Association.
Image of accessory dwelling unit types from: City of Charlottesville. (2015). Accessory Dwelling Units: A Guide to Accessory Apartments in Charlottesville, VA.

## Slide 13
Unsplash - Ludovic Charlet
Notes: Notes: This photo of San Francisco shows one type of density in the foreground – small-scale structures that cover a high percentage of their respective lot. In the background you can see high-rise buildings, which is what often comes to mind when the word “density” is mentioned.
Image: https://unsplash.com/photos/WEoOcjCzl00

## Slide 14: Land Use – Connectivity
Frank, L., Kavage, S., & Litman, T. (2006)
Notes: Key Message: This slide shows the historical trends in neighborhood street pattern. Over time the development pattern connectivity decreased. This also shows how suburban development patterns have reduced the linear feet of streets necessary to develop an area, which results in less impervious surface and lowers the cost of construction. A grid-like network can be required or encouraged through development ordinances, including overlay zones.
Notes: The traditional grid has several advantages from the traffic engineering standpoint:
Traffic is dispersed rather than concentrated.
Alternative routes are available when one route become unusually clogged.
The need for traffic signals, and resulting interruptions in traffic flow, are kept at a minimum by the many left-turn opportunities available.
The direct routes in a grid can also result in a reduction in vehicle miles traveled compared to a more suburban street pattern (Proft and Condon 2001 cited in Ewing & Bartholomew 2013).
Source:
Frank, L., Kavage, S., & Litman, T. (2006). Promoting public health through smart growth. Vancouver, BC: SmartGrowthBC. Available: http://www.smartgrowth.bc.ca
Ewing, R., & Bartholomew, K. (2013). Pedestrian- & transit-oriented design. Washington, D.C. Urban Land Institute and American Planning Association.

## Slide 15
pedbikeimages.org – Dan Burden
Notes: Key Message: “Lollipop” style developments lack connectivity; long distances between destinations discourage walking.
Image: http://www.pedbikeimages.org/mediumimages/usa.aerial.sprawl2-large.jpg

## Slide 16: Land Use Tools – Urban Form
Connectivity standards
Density bonuses
Streetscape amenities
  Street tree spacing
Complete Streets policies
Infill development
Montgomery Planning
Notes: Key Message: This slide introduces some of the tools that an agency might employ to preserve or create an urban form that supports making trips by walking or bicycling.
Notes:
Connectivity standards may specify desired/maximum block lengths (maximum: typically 600ft), limit cul-de-sacs, require stub street connections to new development, etc.
Density bonuses allow developers to build at higher densities in exchange for providing something the city needs (e.g., affordable housing units, pedestrian amenities, stormwater treatment, etc.).
Streetscape policies describe when and where cities require benches, public restrooms, trashcans, street trees, lighting, bicycle parking, etc. Well-spaced street trees provide shade, privacy, better aesthetics, and a sense of safety for pedestrians by buffering them from vehicular traffic.
Complete Streets is a policy and design approach that requires all modes to be considered in the planning, design, operation, and maintenance of a street. In some communities this takes the form of a resolution, ordinance, executive order, and/or it is woven throughout a design manual or comprehensive plan.
Infill development: agencies may encourage or incentivize the development of vacant or underutilized lots (included surface parking lots) within an urban area to meet a variety of community goals, such as creating mixed uses, reducing travel time, and preserving open space.
Connection to Other Module: More on Complete Streets policies in the module, Policies that Support Bicycle and Pedestrian Planning.
Source:
Sanders, Carrie. (2018). “Parking Lots: Before and After.” The Third Place: A Montgomery Planning Department Blog, Available: http://montgomeryplanning.org/blog-design/2018/01/parking-lots-before-and-after/
Ewing, R., & Bartholomew, K. (2013). Pedestrian- & transit-oriented design. Washington, D.C. Urban Land Institute and American Planning Association.
Images: Montgomery Planning. The before and after images show the Pike and Rose redevelopment in Montgomery County, Maryland, which transformed a large area of surface parking near a metro station into a walkable, urban, mixed-use development.

## Slide 17: Land Use Tools – Site Design
Parking requirements (design, location, amount)
Pedestrian and bicycle circulation within site
Access management
Pedbikeimages.org – Dan Burden
Notes: Key Message: Design decisions at the parcel or site level can also affect mode choice. Sites that cater to automobile access are often hostile to pedestrians and bicyclists because they make access challenging for people on foot or bike.
Notes:
Parking requirements/policies should consider development type and size, surrounding land use, demographics, availability of transportation choices, and off-site parking.
Some parking policies that can improve walking and biking include lowering parking minimums or enacting parking maximums, parking in-lieu fees, standards for ped/bike circulation and access within sites (especially surface parking lots). Parking in-lieu fees refer to arrangements in which developers pay a fee to the city in return for not building the amount of on-site parking required by the zoning code. Fee revenue is typically used to build shared public parking, or sometimes invested into transit or bike/ped infrastructure or amenities.
Access management policies and regulations can prevent conflicts between motor vehicles exiting a driveway and passing bicyclists and pedestrians. Pay special attention to driveway location and spacing. The problem of driveway access is very pronounced on commercial corridors where every business has a driveway to its own parking lot.
The top image is problematic – there is little variation (texture or physical separation) between the street, pedestrian path, and driveway. The bottom image shows a parking lot that was designed for safe pedestrian circulation.
Connection to Other Module: Design strategies for access management are covered in the module, Designing for Walking and Bicycling.
Source:
Federal Highway Administration. (2006). University Course on Bicycle and Pedestrian Transportation. Washington, DC.
Shoup, Donald. (1999). “Instead of Free Parking.” Access, 15.

## Slide 18: Land Use Tools – Economic Development
Penalties for absentee property owners
Small-scale loans/grants to help local business owners purchase and improve their storefronts
Business improvement districts (BIDs)
pedbikeimages.org – Dan Burden
Notes: Key Message: While not strictly land use policies, policies that target economic health can improve the pedestrian environment.
Notes: Disincentivizing property owners from sitting on vacant land allows other business the opportunity to provide services and contribute to an area’s economy. Cities can also work with business owners by aiding local small business owners in purchasing the spaces they rent and making improvements and maintain the facades. Similarly, local associations like BIDs can work with cities to improve and maintain sidewalks, benches, landscaping, bike parking, lighting, and other streetscape amenities.
Source: Zaccaro, Heather. (2019). Blind Spots: How Unhealthy Corridors Harm Communities and How to Fix Them. Washington, DC: Urban Land Institute.

## Slide 19: Example: Land Use Policies in Small Towns
Many of these policies and tools can be applied in small town and rural settings
Davidson, NC (population 10,944, WFC Bronze)
  Cul-de-sacs only permitted in special cases
  Block length maximum: 600ft
Evanston, IL (population 74,500, WFC Gold)
  Downtown and business districts require commercial use on the ground floor
  Density bonuses granted for below-grade parking, plazas and public art, transit facility improvements, and mixed-use development
Notes: Notes: Both communities featured on this slide also have Complete Streets policies. Walk Friendly Communities (WFC) is a national recognition program developed to encourage towns and cities across the U.S. to establish or recommit to a high priority for supporting safer walking environments.
Source:
Walk Friendly Communities. “Communities.” http://walkfriendly.org/communities/
Town of Davidson. Town of Davidson Planning Ordinance, Section 11: Streets and Greenways.
City of Evanston. Evanston, IL Code of Ordinances, §6-15-13-11. - INCENTIVE SYSTEM.
Image: Walk Friendly Communities. http://walkfriendly.org/

## Slide 20: Vulnerable Populations and “Walkability”
Research has consistently demonstrated that supportive built environments for walking are linked to higher rates of walking and physical activity
  Is this relationship the same for socioeconomically disadvantaged populations?
    Review of 17 studies found average effect of built environment on walking was 2.3 times stronger for advantaged than disadvantaged groups
Notes: Notes: Indicators of walkability in the studies that were reviewed focus on residential density, street connectivity (or intersection density), and land use mix. Other less common indicators are transit availability, the density of businesses or services, pedestrian facility availability, retail floor area ratio, perceived environmental supports, and Walk Score.™ Many of the studies combined the indicators into a single index rather than studying them separately.
Connection to other Module: Equity
Source: Arlie Adkins, Carrie Makarewicz, Michele Scanze, Maia Ingram & Gretchen Luhr. (2017). Contextualizing Walkability: Do Relationships Between Built Environments and Walking Vary by Socioeconomic Context? Journal of the American Planning Association, 83:3, 296-314.

## Slide 21: Vulnerable Populations and “Walkability”
Potential planning responses:
  Recognize that the effects of the built environment may vary by socioeconomics
  Use holistic approaches to improve walkability
  Expand walkability definitions to address a range of social and physical barriers
  Partner across agencies, disciplines, and professions
  Evaluate interventions in different socioeconomic environments
Notes: Key Message: Planners must be sensitive to community concerns about gentrification and displacement in the face of planned built environment improvements that may benefit more advantaged populations.
Connection to other Module: Equity
Source: Arlie Adkins, Carrie Makarewicz, Michele Scanze, Maia Ingram & Gretchen Luhr. (2017). Contextualizing Walkability: Do Relationships Between Built Environments and Walking Vary by Socioeconomic Context? Journal of the American Planning Association, 83:3, 296-314.

## Slide 22: Motivations to Walk or Bike

## Slide 23: Motivations to Walk or Bike (or Not)
Sidewalks and bike lanes, but no one is walking or bicycling…
Pedbikeimages.org – Siam Pewsawang
Robert Schneider
Notes: Key Message: These two slides highlight that a variety of factors—not just design or presence of infrastructure—influence whether people walk and bike in an area.

## Slide 24: Motivations to Walk or Bike (or Not)
No facilities, but people are walking and bicycling…
Pedbikeimages.org – Ryan Snyder
Pedbikeimages.org – Dan Burden
Notes: Key Message: These two slides highlight that a variety of factors—not just design or presence of infrastructure—influence whether people walk and bike in an area.

## Slide 25: Theory of Routine Mode Choice Decisions
Source: Robert Schneider (2013)
5) Habit
2) Basic Safety & Security
3) Convenience & Cost
4) Enjoyment
Pedestrian, Bicycle, Transit, or Automobile?
1) Awareness & Availability
SITUATIONAL TRADEOFFS
Socioeconomic Factors
Notes: Key Message: The previous section presented land use and design factors that are associated with walking and bicycling trips, but what motivates people to choose walking and bicycling when there are options among other modes like driving and transit?
Notes:
Awareness & Availability. People must be aware of the mode and have it available as an option to travel to an activity.
Basic safety & Security. People seek a mode that they perceive to provide a basic level of safety from traffic collisions and security from crime.
Convenience & Cost. People seek a mode that will get them to an activity using an acceptable amount of time, effort, and money.
Enjoyment. People seek a mode that provides personal (physical, mental, emotional), social, or environmental benefits.
Habit. People who chose a mode regularly are more likely to consider it as an option in the future.
Student Question: For #3, ask students to consider how perceptions play a role. E.g., short distances to activities decrease the barriers to walking and bicycling, but are people good at judging things like walking distance or the amount of time they must wait for a bus or train? Cost could relate to the availability and price of automobile parking, the pricing scheme of a bikeshare system, or the cost of a transit pass.
Source: Schneider, R. J. (2013). Theory of routine mode choice decisions: An operational framework to increase sustainable transportation. Transport Policy, 25, 128–137.

## Slide 26: Strategies to Increase Walking and Bicycling
Awareness & Availability
  Individualized marketing programs, community-wide education campaigns, Bike to Work Day, Walk to School Week, other encouragement programs
Basic Safety & Security
  Sidewalks and bicycle paths, improve pedestrian crossings, design roadways for slower automobile speeds, enforce traffic laws, improve lighting, provide secure bicycle parking
Convenience and Cost
  Higher population and employment densities, finer mix of land uses, reduce building setbacks, reduce off-street parking, provide market rate on-street parking
Enjoyment
  Plant street trees/landscaping, zone for active uses on ground floors, design streets for slow-speed activities, promote environmental and social benefits of walking and bicycling
Habit
  Offer information to people who move & change job locations, explore roadway and parking pricing strategies
Notes: [This slide is animated, when you start clicking, the strategies will appear under each line, one at a time]
Student Question: Can you think of strategies for some or all these five steps?
Connection to other Module: Many of these strategies will be covered in other lessons. The lesson on Inclusive Engagement includes brief mention of education and encouragement programs.
Source: Schneider, R. J. (2013). Theory of routine mode choice decisions: An operational framework to increase sustainable transportation. Transport Policy, 25, 128–137.

## Slide 27: Awareness, Availability, and Convenience
Bicycle parking
  Balance convenience and security needs
  Locate in visually prominent places
Pedbikeimages.org – Laura Sandt
Pedbikeimages.org – Charlie Zegeer
Pedbikeimages.org – Dan Burden
Notes: Key Message: The next few slides will cover wayfinding and bicycle parking – two strategies that improve the awareness, availability, and convenience for walking and bicycling. Bicycle parking is a strategy that may involve policy change at the local level.
Notes: Planning for bicycle travel includes planning for bicycle parking. People will be reluctant to travel by bike if there is no good location to store their bicycle at the destination. Parking should balance convenience and security; user needs vary based on the nature of the trip. Short-term parking serves destinations where bikes will likely be locked for less than two hours while users visit businesses or other destinations. This type of parking typically takes the form of bike racks and should be in a prominent, visible location that is convenient to the destination. For areas where users need long-term parking (where bikes will be left for many hours) security and protection from weather are greater priorities. Long-term parking may be provided at transit stops or workplaces and includes bike lockers or sheltered secure enclosures. For events, bike valet service or corrals can be used to accommodate a large quantity of bikes temporarily.
Source: Broom, Nathan, et al. (2015). Essentials of Bike Parking Revision 1.0. Association of Pedestrian and Bicycle Professionals (APBP).

## Slide 28
Pedbikeimages.org – PeopleForBikes
Notes: Notes: This image shows bicycle parking what is in full view of sidewalks and pedestrian path. Even though this photo was taken during the day, this appears to be an area that would be well-lit at night.
Image: http://www.pedbikeimages.org/mediumimages/alyson%20west%20-%20protectedbikelanebikeparkingPFB.jpg

## Slide 29: Awareness, Availability, and Convenience
Wayfinding
  Establish presence of walk/bike routes
  Provide directions and travel times to destinations (people tend to overestimate travel times)
Pedbikeimages.org – Toole Design Group
Notes: Key Message: Bicycle-specific wayfinding indicates to both bicyclists and motorists that a route is part of the bicycle network. Signage can provide consistent branding and appearance for the area bike network, direct bicyclists to recommended routes, and provide information about distance and travel time to destinations—which may be especially useful for reducing barriers to entry for new or infrequent bicyclists. Signage that combines bicycle and pedestrian information can be used by both user types. Pedestrian wayfinding that includes key destinations and travel times is also important for inspiring people decide to make a trip by foot.
Notes: Wayfinding is a strategy that may involve policy change at the local-level and/or coordination at the regional-level.
Source: National Association of City Transportation Officials (NACTO). “Bike Route Wayfinding Signage and Markings System” in Urban Bikeway Design Guide.
Image (left): http://www.pedbikeimages.org/mediumimages/Toole%20Design%20Group%20Dropbox%20-%20Wayfinding_2014-08-07%20DC%20and%20Arlington_2014-08-07%
Image (right): http://www.pedbikeimages.org/mediumimages/Toole%20Design%20Group%20Dropbox%20-%20Wayfinding_Omaha_Benson%20D1-11.png

## Slide 30
Pedbikeimages.org – Laura Sandt
Pedbikeimages.org – Sarah Heaton Kennedy
Notes: Key Message: Transit information can also be incorporated into bicycle or pedestrian wayfinding, as shown in these examples from Portland, OR, (left) and Charlotte, NC (right).
Image (left): http://www.pedbikeimages.org/largeimages/dscn2893.jpg
Image (right): http://www.pedbikeimages.org/largeimages/travel_006.jpg

## Slide 31: Convenience and Cost
Barriers to walk/bike
Short distances to activities ↓ Long distances to activities ↑
Planning time
Travel time
Barriers to driving
Limited car parking ↑ Plentiful parking ↓
Planning time
Travel time (searching for spot & walking from parking)
Physical effort
Bad weather
Hills
Lack of lighting
Price (limited parking is often expensive)
Source: Robert Schneider (2013)
Notes: Key Message: People seek to travel to activities using a mode that requires less time, effort, and money. The last few slides included examples of strategies that increase the convenience of walking and bicycling, and in some ways reduce the effort. However, sometimes that’s not enough to encourage people to walk and bike. Most of the land use tools discussed earlier can be used to bring activities closer together, but when activities are already somewhat close together and walking/bicycling/transit are reasonable options, sometimes it’s adjustments to the availability and pricing of car parking that can hasten the decision to choose another mode.
Source: Schneider, R. J. (2013). Theory of routine mode choice decisions: An operational framework to increase sustainable transportation. Transport Policy, 25, 128–137.

## Slide 32: Convenience and Cost – Parking
Most parking in US cities is free or underpriced
Pricing parking spots can:
  Ensure availability
  Reduce the need for parking minimums
  Incentivize the use of other modes
Regressive?
  Still a “user pays” system (don’t pay if you don’t use)
  On-street parking prices are often lower than transit fares, but drivers are on average more affluent than transit riders
Notes: Key Message: Manville and other parking pricing advocates argue that most US cities underprice their parking, especially on-street parking. Downtown on-street parking is valuable real estate yet keeping the price low is divorcing price from value. Consider that the value of a parking spot is different based on geographic location (Bozeman vs Manhattan), time of day, day of the week, nearby amenities or activities, etc. Pricing parking dynamically so that there are always a few available spaces would reduce the need for parking minimums (a policy response to the artificially created parking shortages caused by keeping parking costs free or too low), reduce driver “cruising,” and incentivize other modes (especially if transit prices are reduced or made lower than parking costs).
Source:
Michael Manville. (2014). “Parking Pricing,” in Stephen Ison and Corinne Mulley (Eds.), Parking: Issues and Policies (Transport and Sustainability, Volume 5), Emerald Publishing: 137–155.
The Guardian. “Why we should be paying more for parking – Video explainer.” Available: https://www.theguardian.com/world/video/2018/oct/30/why-we-should-be-paying-more-for-parking-video-explainer

## Slide 33: Example: SFpark
Expected benefits:
  Easier parking, faster public transit, safer bicycles and pedestrians, and better businesses and neighborhoods
Results:
  Average occupancy fell, but minimum vacancy had no change
  Transit speeds: mixed results, some improvement
  Ped/bike safety: no strong evaluation metrics!
SFMTA
Notes: Key Message: SFpark was a Federally-funded demonstration project to test market pricing of parking in San Francisco. “SFpark’s explicit goals were to reduce cruising (its slogan was “live more, circle less”), increase the speed and reliability of transit, and make walking and cycling safer. For researchers, SFpark provided a real-world test of performance pricing.” (Manville and Chatman, 2016).
Notes:
Before:
  Highest on-street rate $3.50/hr, median off-street rate $10.00/hr
Intervention:
  Introduced rates that varied by block, time of day, and day of week
  Relaxed time limits at many meters
  “Smart” parking meters to make payment easier
Results:
  Average occupancy fell, but minimum vacancy had no change (average occupancy calculated over long period of time; minimum vacancy = the share of minutes that a block has at least one space open)
  Transit speeds: mixed results, some improvement (where double parking rates fell, transit speeds increased slightly)
  Ped/bike safety: traffic volumes decreased in pilot areas (where parking availability improved), but speeds increased. However, Sfpark did not make explicit conclusions about ped/bike safety.
Question for Students: How could SFpark more explicitly evaluate whether the program has any affect on ped/bike safety? What data would they need?
Sources:
Manville, M. and Chatman, D. (2016). “Market-priced parking in theory and practice.” Access. 49. Available: https://www.accessmagazine.org/fall-2016/market-priced-parking-in-theory-and-practice/
SFMTA. (2014). SFpark Pilot Project Evaluation. Available: http://direct.sfpark.org/wp-content/uploads/eval/SFpark_Pilot_Project_Evaluation.pdf

## Slide 34: International Lessons: Encouraging Walking and Bicycling
Discourage driving and make bicycling convenient
  Stricter limits on autos (e.g., registration, licensing, congestion pricing, parking removal)
Cultural supports for walking/bicycling
  Tradition
  Peer network
  Education
  Enforcement
  Grassroots advocacy
Pedbikeimages.org – Laura Sandt
Notes: Key Message: In addition to infrastructure improvements and facilities, having the cultural supports in place is necessary to foster a walking and bicycling environment.
Notes: Bicycling is a social activity in other countries and people are accustomed to being able to ride everywhere comfortably. In countries like the Netherlands, bicyclists’ skills are tested at a young age, so children grow up with an awareness for bicycling that they carry with them even if they eventually drive cars. However, in many other countries the fees associated with being licensed and registering/operating a vehicle are much more prohibitive than they are in the United States. As for enforcement, automated enforcement is much more common abroad than it is in the U.S.
Student Question: If you have traveled abroad, how was your experience different with walking and/or bicycling?
Connection to other Module: The module Designing for Walking and Bicycling includes some international examples of design strategies.
Source: Adapted from slides by Laura Sandt for the Pedestrian and Bicycle Information Center (2011).

## Slide 35: Summary
Factors associated with walking and bicycling interact with each other and may not have the same relationship for all socioeconomic groups
Land use policies can hinder or encourage walking and bicycling trips
People make situational tradeoffs when choosing a travel mode