## Slide 1: Designing for Walking and Bicycling
Instructor course information
Notes: Report No. FHWA-SA-19-034

## Slide 2: Module Outline
Traditional engineering approach
Design flexibility
Safe, comfortable networks
Bikeways
Walkways

## Slide 3: Traditional Engineering Approach

## Slide 4: Traditional Engineering Approach
Capacity
  Calculate the number of trips that will be generated by this facility
  Assess the current capacity of the roadway
  Determine changes to existing design to accommodate increased traffic
  Determine parking and access needs
  Assess traffic control
Notes: Source: slide adapted from Wes Kumfer
Image (left): https://itetripgen.org/Content/images/ITECover.png
Image (middle): http://www.trb.org/Resource.ashx?sn=HCM6cover
Image (right): https://store.transportation.org/APS_Repository/Images/ItemThumnails/4126.jpg

## Slide 5: Traditional Engineering Approach
Level of Service
  What is level of service?
    A qualitative measurement of volume to capacity and perceived driving condition.
  How do we know if a roadway is designed for the “right” amount of traffic?
    Capacity Analysis Density Level of Service
Notes: Source: slide adapted from Wes Kumfer

## Slide 6: Traditional Engineering Approach
Speed
  Designers use speed to establish geometric design features
    Curvature
    Super elevation
    Width of travel lanes
    Clear zones
    Shoulders
Speed at which drivers operate affects mobility and safety
Notes: Key Message: Speed is a complex subject that can be controversial.
Notes: The speed at which drivers operate their vehicles directly affects two performance measures of the highway system—mobility and safety. Designers of highways use a designated design speed to establish design features; operators set speed limits deemed safe for the road; but drivers select their speed based on their individual perception of safety. There is general agreement that the risk of injuries and fatalities increases with speed.
Connection to other Module: Strategies for Safer Speeds
Source: FHWA. (2009). Speed Concepts: Informational Guide. [FHWA-SA-10-001]. U.S. Department of Transportation. Available: https://safety.fhwa.dot.gov/speedmgt/ref_mats/fhwasa10001/

## Slide 7: Traditional Engineering Approach
FHWA, Speed Concepts: Informational Guide (2009)
Notes: Notes:
Designated design speed: a selected speed used to determine the various geometric design features of the roadway
Inferred design speed: the maximum speed for which all critical design-speed-related criteria are met at a location
Operating speed: the speeds at which vehicles are observed operating during free flow conditions. The 85th percentile of the distribution of observed speeds is the most frequently used measure of the operating speed. But there are flaws with this approach that will be covered in the next lesson.
Speed limit: The maximum lawful vehicle speed for a specific location. There are two types of speed limits, posted speed and statutory speed. Definitions of each are provided below.
  “Posted speed – one of two speed limit types (statutory speed is other type); the maximum lawful vehicle speed for a particular location as displayed on a regulatory sign. Posted speeds are displayed on regulatory signs in speed values that are multiples of 5 mph.” (FHWA 2009)
  “Statutory speed – one of two speed limit types (posted speed is other type). Numerical speed limits (e.g., 25 mph, 55 mph), established by state law that apply to various classes or categories of roads (e.g. rural expressways, residential streets, primary arterials, etc.) in the absence of posted speed limits.” (FHWA 2009)
Connection to other Module: Strategies for Safer Speeds
Source: FHWA. (2009). Speed Concepts: Informational Guide. [FHWA-SA-10-001]. U.S. Department of Transportation. Available: https://safety.fhwa.dot.gov/speedmgt/ref_mats/fhwasa10001/

## Slide 8: Traditional Engineering Approach
When proposed trips are added, the solution to increase capacity and maintain/improve LOS often involves:
  More or wider through lanes
  More turn lanes
  Complex signals
Higher design speed solutions also include:
  More or wider through lanes
  Broad, smooth curves
  Clear zone free of fixed objects
  Wide shoulders
  Feels comfortable to drive fast
Notes: Notes: Traffic Impact Assessments (TIA) that are often required by local agencies for developments of a certain size focus on the generation of car trips and their recommendations assume that new car trips must not increase congestion. Peak-hour car trips are often prioritized over all other times and modes.
Source:
slide adapted from Wes Kumfer
FHWA. (2009). Speed Concepts: Informational Guide. [FHWA-SA-10-001]. U.S. Department of Transportation. Available: https://safety.fhwa.dot.gov/speedmgt/ref_mats/fhwasa10001/

## Slide 9: Traditional Engineering Approach
What are the negative outcomes or “trade-offs”?
  Dangers from high speeds and high volumes of motorists
  Difficult or impossible for pedestrians to cross
  Uncomfortable for bicyclists
  Difficult for transit to stop
Notes: Source: slide adapted from Wes Kumfer

## Slide 10: Street Hierarchy
Traditional functional classification as used by most State DOTs:
(more ped/bike oriented)
(more auto/truck oriented)
Interstate
Other Freeway/Expressway
Other Principal Arterial
Minor Arterial
Major Collector
Minor Collector
Local
AASHTO “Flexibility in Highway Design”
Notes: Key Message: This is the typical hierarchy, inspired by the AASHTO Green Book, used by many State DOTs. Unlike the street types on the following slide, this street classification rarely takes land use and context into account.
Source: Adapted from the Pedestrian and Bicycle Information Center Transportation Short Series, Class 2 (2015).

## Slide 11: Street Hierarchy
Walkable thoroughfare types
Serve a mix of modes
ITE, Designing Walkable Urban Thoroughfares: A Context Sensitive Approach
  Boulevard
  Avenue
  Street
Notes: Notes: These street types represent a spectrum from pedestrian- to auto-oriented, but each street type can (and should) include design elements to improve safety and operation for bicyclists, pedestrians, and transit users. Street design decisions and land use decisions should complement one another. Rural roads cover different street types as they are often the only connections between towns and should serve a variety of users.
Source:
Adapted from the Pedestrian and Bicycle Information Center Pedestrian and Bicycle Transportation Short Series, Class 2 (2015).
Institute of Transportation Engineers. (2010). Designing Walkable Urban Thoroughfares: A Context Sensitive Approach.

## Slide 12: Street Hierarchy
Less of a focus on “hierarchy” and more of a focus on context in the 2018 AASHTO Green Book
  Rural
  Rural Town
  Suburban
  Urban
  Urban Core
Notes: Notes: AASHTO Green Book classifies these contexts to determine geometric design.

## Slide 13: Design flexibility

## Slide 14: Design Flexibility
Flexibility to approaching bicycle and pedestrian facility design, using:
  AASHTO guides
  NACTO guides
  FHWA guides
  ITE guides
  ADAAG guidelines
  State DOT guides
Notes: Key Message: There area a variety of resources to use as guidelines for design. FHWA encourages agencies to appropriately use these guides and other resources to help fulfill the aims of the 2010 USDOT Policy Statement on Bicycle and Pedestrian Accommodation Regulations and Recommendations - "...DOT encourages transportation agencies to go beyond the minimum requirements, and proactively provide convenient, safe, and context-sensitive facilities that foster increased use by bicyclists and pedestrians of all ages and abilities, and utilize universal design characteristics when appropriate."
Notes: FHWA supports a flexible approach to bicycle and pedestrian facility design, particularly in urban areas. The American Association of State Highway and Transportation Officials (AASHTO) bicycle and pedestrian design guides are the primary national resources for planning, designing, and operating bicycle and pedestrian facilities. The National Association of City Transportation Officials (NACTO) Urban Bikeway Design Guide and the Institute of Transportation Engineers (ITE) Designing Walkable Urban Thoroughfares guide builds upon the flexibilities provided in the AASHTO guides, which can help communities plan and design safe and convenient facilities for pedestrian and bicyclists. Additional guidance for rural areas can be found in the FHWA guide, Small Town and Rural Multimodal Networks (2016).
Source: FHWA. (August 20, 2013). Memorandum: Bicycle and Pedestrian Facility Design Flexibility. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/guidance/design_flexibility.cfm [Accessed May 2019]

## Slide 15: Design Flexibility
Designers sometimes express concern about liability when applying design flexibility
A flexible design approach has three key elements:
  Engineering judgment
  Documentation
  Experimentation
Understanding the flexibility within, and engineering principles behind, design guidance helps drive the advancement of the design practice
Notes: Key Message: Designers should understand the flexibility within, and engineering principles behind, design guidance.
Notes: Designers sometimes express concern about liability when applying design flexibility. Due to these concerns, some designers adhere strictly to their interpretation of established design criteria, sometimes at the expense of providing adequate bicycle and pedestrian facilities. However, strictly adhering to the most conservative design values without considering other relevant factors may not constitute reasonable care on behalf of the designer. Likewise, a designer who deviates from established design guidance is not necessarily negligent, particularly if the designer follows and documents a clear process, using engineering judgment, when dealing with design exceptions, and experimentation.
Engineering judgment
Understanding engineering principles and the assumptions and contingencies incorporated into standards and guidelines.
Documentation
Documenting memoranda, engineering studies, and other methods that capture engineering judgment behind design solution.
Experimentation
Liability concerns should not limit innovations, experimentation, and versatile applications of existing design treatments and proven safety countermeasures. The experimentation process helps drive the advancement of the design practice and the adoption of new traffic control devices in the MUTCD.
Connection to other Module: Intersections
Source: FHWA. (2016). Achieving Multimodal Networks: Applying Design Flexibility & Reducing Conflicts. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_networks/

## Slide 16: Design Principles
There are often competing interests between the different users. To design for pedestrian and bicyclist safety and comfort, consider:
  Safety (reduction of conflicts)
  Accessibility
  Predictability
  Visibility
  Separation
  Minimization of delay
  Context sensitivity
FHWA
Notes: Key message: Designing for different users requires specific principles to be considered in the planning/design process.
Notes:
Safety (reduction of conflicts) – Slower speeds and geometric design (medians, shorter crossing distances) should be used to improve safety for all modes to eliminate or minimize conflicts.
Accessibility – Design all roads and crossings to meet ADA standards. This good design benefits all users.
Predictability – Design should provide clear right of way assignments, visibility of all users, and a clear path of travel for all modes.
Visibility – Curb extensions, lighting, pavement markings may all be used.
Separation – Greater separation of modes as speeds and/or volumes increase (buffered bike lanes, separated bike lanes, etc.)
Minimization of delay – Reduce delay at crossings will yield improved and safer behaviors. Shorter block lengths and improved bicycle and pedestrian networks will reduce travel time.
Context sensitivity – Design incorporates and supports the natural environment and adjacent land use.
Source:
Pedestrian and Bicycle Information Center Transportation Short Series, (2015).
FHWA. (2016). Achieving Multimodal Networks: Applying Design Flexibility & Reducing Conflicts. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_networks/

## Slide 17: Elements of the Roadway–Curb Radii
Size of the corner relates directly to the length of the crosswalk
“Accommodate” large vehicles, don’t “design” for them
Smaller turning radii
  Position vulnerable users in more visible locations
  Provide space for properly aligned curb ramps
  Reduce vehicle turning speed
NACTO
Notes: Key Message: Curb radii should be designed to maximize pedestrian space and shorten pedestrian crossing distance to the greatest extent feasible. The designer should distinguish between “designing for” and “accommodating” the needs of large vehicles. Accommodating means allowing for a particular vehicle to complete a turn with latitude to use adjacent or opposing lanes on the origin or destination street.
Notes: Generally, for local urban streets, curb radii should be between 10–15 feet unless special circumstances require a larger radius. Where on-street parking or bike lanes are present, designers should use the “effective” curb radii, rather than the actual, to create a more compact intersection that encourages slower speeds.
Connection to other Module: Intersections
Source:
FHWA. (2016). Achieving Multimodal Networks: Applying Design Flexibility & Reducing Conflicts. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_networks/
NACTO (2013). Urban Streets Design Guide, Corner Radii, Available: https://nacto.org/publication/urban-street-design-guide/intersection-design-elements/corner-radii/ [Accessed July 2019]
San Francisco Better Streets Plan, “Curb Radius Changes.” Available: https://www.sfbetterstreets.org/find-project-types/pedestrian-safety-and-traffic-calming/traffic-calming-overview/curb-radius-changes/
Image: https://nacto.org/wp-content/themes/sink_nacto/views/design-guides/retrofit/urban-street-design-guide/images/corner-radii/effective-turning-radius.png

## Slide 18: Elements of the Roadway – Lane Width
Lane widths are sensitive and crucial to various needs
  Travel lanes
  Safety islands
  Bike lanes
  Sidewalks
Narrower streets help promote slower driving speeds
  Reduce crash severity Reduce crossing distances
  Shorter signal cycles
Notes: Key Message: Travel lanes are striped to define the intended path of travel for vehicles along a corridor and lane width is an important design criteria. Narrower lanes can improve comfort and safety for vulnerable users. By narrowing lanes, designers can create space for a separated bike lane, a widened sidewalk with buffer and reduced crossing distances, or a standard bike lane and widened buffer. Historically, wider travel lanes (11–13 feet) have been favored to create a more forgiving buffer to drivers, especially in high-speed environments where narrow lanes may feel uncomfortable or increase potential for side-swipe collisions. The AASHTO Green Book offers substantial flexibility regarding lane widths, allowing a range between 9 and 12 feet depending on desired speed, capacity, and context of a roadway.
Source:
NACTO. (2013). Urban Streets Design Guide, “Lane Width,” Available: https://nacto.org/publication/urban-street-design-guide/street-design-elements/lane-width/ [Accessed July 2019]
FHWA. (2016). Achieving Multimodal Networks: Applying Design Flexibility & Reducing Conflicts. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_networks/

## Slide 19: Elements of the Roadway – Lane Width
FHWA
Notes: Key Message: Designers have avoided using narrower lane widths in the past due to concerns about safety and congestion especially on arterial roadways. However, research on suburban and urban arterials has shown that in most cases, travel lane widths between 10 and 11 feet as a part of a thoughtful, integrated design of arterials and collectors do not negatively impact overall motor vehicle safety or operations and have no measurable effect on vehicular capacity.
Notes: This figure shows how once MV travel lanes are narrowed, space is freed up for other uses like a bicycle lane with two feet of physical separation.
Source: FHWA. (2016). Achieving Multimodal Networks: Applying Design Flexibility & Reducing Conflicts. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_networks/

## Slide 20: Elements of the Roadway-- Driveways
Narrowing driveways, tightening turning radii, and improving driveway definition can improve safety for people walking
Maintain grade of intersecting sidewalk or shared use path
Mark conflict areas in bike lanes
Minimize the number of driveways to reduce conflicts
Model Street Design Manual – Michele Weisbart
Notes: Key Message: Driveways are the source of most conflicts with motor vehicles on sidewalks. Proper driveway design and consideration is critical to the safety and comfort of pedestrians. Both the design of driveways and the number of driveways (often referred to as “access management”) affect the safety and comfort of people walking and bicycling.
Notes: Driveways should prioritize pedestrians and bicyclists by maintaining the grade of an intersecting sidewalk or shared use path and altering the grade of the motorist’s path of travel. This design makes it clear to the driver that they are crossing a sidewalk. Notice that the separated sidewalk keeps the pedestrian zone of the sidewalk level at driveways. Driveway flare radii should be minimized to ensure slow vehicle turning speeds and to reduce the exposure time for pedestrians.
Student Question:
Connection to other Module:
Source: FHWA. (2013). PEDSAFE: Pedestrian Safety Guide and Countermeasure Selection System. “Driveway Improvements.” Available: http://www.pedbikesafe.org/PEDSAFE/countermeasures_detail.cfm?CM_NUM=20 [Accessed June 2019].
Image from FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course. driveway_configurations_fig_66_modified

## Slide 21: Complete Streets
pedbikeimages.org – Andy Hamilton
Complete Streets are designed and operated to enable safe access for all users:
  Pedestrians
  Bicyclists
  Motorists
  Transit riders
People of all ages and abilities must be able to safely move along and across a Complete Street
Notes: Key Message: A Complete Street in a rural area will look quite different from a Complete Street in a highly urban area, but both are designed to balance safety and convenience for everyone using the road.
Notes: Complete Streets are streets that are designed to enable safe access for all users, including pedestrians, bicyclists, motorists, and transit riders of all ages and abilities. Complete Streets design makes it easy to cross the street, walk to shops, and bicycle to work. They allow buses to run on time and make it safe for people to walk to and from train stations. There is no singular design prescription for Complete Streets; each one is unique and responds to its community context. A Complete Street may include sidewalks, bike lanes (or wide paved shoulders), special bus lanes, comfortable and accessible public transportation stops, frequent and safe crossing opportunities, median islands, accessible pedestrian signals, curb extensions, narrower travel lanes, roundabouts, and more.
Connection to other Module: The module, Policies that Support Pedestrian and Bicycle Planning, discusses Complete Streets policies.
Source:
PBIC (2015). Pedestrian and Bicycle Transportation Short Series.
Chicago Department of Transportation. (2013). Complete Streets Chicago: Design Guidelines
Smart Growth America. “National Complete Streets Coalition.” https://smartgrowthamerica.org/program/national-complete-streets-coalition/
City of Boston. (2013). Boston Complete Streets Guidelines.

## Slide 22: Complete Streets
What makes streets ‘incomplete’ (from a non-car mobility perspective)?
  Lack appropriate accommodations for the various modes
  Mismatch between users’ needs and the accommodations available
  External forces (human or not) expose users to insecurity or hostility
pedbikeimages.org – Dan Burden
Notes: Notes: “Pivoting to a pedestrian-first modal hierarchy may frustrate people who drive. Nevertheless, the transportation profession is coming to understand that more roads, more lanes, and longer signal cycles only induces more traffic. Complete streets favors the prudent driver: people who drive slowly, safely, and respectfully. In urban settings, the pedestrian-first hierarchy adheres to the performance standard of optimizing the movement of people, and not simply the movement of vehicles, which has been the traditional priority in transportation.“ (Chicago DOT 2013)
Source: Chicago Department of Transportation. (2013). Complete Streets Chicago: Design Guidelines.

## Slide 23: Complete Streets Example: Chicago
Adopted a pedestrian-first modal hierarchy
Street design supports context and modal priorities not limited by rigid engineering standards
Chicago DOT, Complete Streets Chicago: Design Guidelines
Notes: Key Message: CDOT uses modal hierarchies to inform design and operation decisions.
Notes:
“Design trees are intended to help engage the community through the process of street selection and design.
  Transit > Pedestrian > Bicycle > Automobile - along a major transit corridor
  Bicycle > Pedestrian > Transit > Automobile - along a bicycle priority street with bikeways or a bicycle boulevard
  Automobile > Pedestrian > Bicycle > Transit - in an industrial corridor or along a parkway with no bus service
Traditional street design process begins with automobile volume and speed as main inputs. This process inverts that approach by looking first at the building and roadway typology. Following the design trees, automobile volume and speed become outputs.” (Chicago DOT 2013)
Source: Chicago Department of Transportation. (2013). Complete Streets Chicago: Design Guidelines

## Slide 24: Complete Streets Example: Chicago
Key Complete Streets themes influence:
  Cross-sections
  Intersection Design
  Signal timing
  Maintenance scheduling
  Other agency operations
Chicago DOT, Complete Streets Chicago: Design Guidelines
Notes: Key Message: CDOT uses modal hierarchies to inform design and operation decisions.
Notes:
Modal Hierarchy: All transportation projects and programs, from scoping to maintenance, will favor pedestrians first, then transit riders, bicyclists, and automobiles.
Typology: Typology classifies streets by roadway function and surrounding context, including right-of-way width, building type, and land use. It will serve as a methodology to ensure that the design and use of a street will complement the surrounding area, and vice versa.
Design values: Design values provide flexible guidance for accommodating and balancing road user needs when making decisions. Design trees provide guidance towards the range of street design options.
Procedures: CDOT’s project delivery process is defined in six steps—project selection, scoping, design, construction, measurement, and maintenance—with feedback loops, stakeholder involvement, and approval processes. The process can be scaled to fit the size of the individual project, from repaving to reconstruction. A Complete Streets notebook clarifies important tasks within each step.
Source: Chicago Department of Transportation. (2013). Complete Streets Chicago: Design Guidelines

## Slide 25: International Example of Design Flexibility: Dutch Sustainable Safety Design Paradigm
Considers that roads should be self-explanatory
If designed for access, road should not provide high mobility
If designed for mobility, road should not provide high access
Safety should always be maintained
Well-designed roads have a healthy flow
pedbikeimages.org – Dan Burden
Notes: Notes: In the early 1970s the Netherlands shifted from the auto-centric approach to a Safe Systems (defined as Sustainable Safety in 1997) approach in response to public protests of the high numbers people killed, particularly children (~400 in 1971). The public also opposed the degradation of the public realm, environment, and quality of life resulting that comes with widening roadways through cities. The Dutch Sustainable Safety program has proven to be among the most effective in the world. It is a proactive approach to prevent fatalities and serious injuries through roadway design practices. Because of the program’s success, many practitioners look to the Netherlands for inspiration and guidance. (FHWA Bikeway Selection Guide, 2019, page 8)
Source: slide from Wes Kumfer
Image from Delft, Netherlands
For additional information see FHWA’s report, Bicycle Network Planning and Facility Design Approaches in the Netherlands and the United States. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/network_planning_design
Image: http://www.pedbikeimages.org/mediumimages/delft1.pigmentedbikelanes(5).jpg

## Slide 26: Resources for Navigating Design Flexibility
FHWA Achieving Multimodal Networks
PBIC Design Resource Index
Notes: Source: PBIC. Design Resource Index. Available: http://www.pedbikeinfo.org/resources/resources_details.cfm?id=4975

## Slide 27: Safe, Comfortable Networks

## Slide 28: Principles
Exemplary pedestrian and bicycle networks satisfy each of these principles:
  Cohesion
  Directness
  Accessibility
  Alternatives
  Safety and security
  Comfort
Notes: Key Message: What are the principles of exemplary pedestrian and bicycle networks?
Notes:
Cohesion – Illustrates how different types of facilities can be integrated so that longer distance travel by foot or bike can be accommodated and even encouraged. In a cohesive network, opportunities for direct travel between destinations are made possible by focusing on links between existing infrastructure and destinations.
Directness – A network should minimize the distance a person must travel to reach a destination, prioritizing a convenient path between destinations
Accessibility – the principle of accessibility refers to the ability of a network to serve all its users regardless of age or ability. A network should recognize and accommodate a range of user needs and prioritize those users who are unable to drive.
Alternatives – The presence of alternate routes that provide choices to nonmotorized road users is a sign of a well-connected, comprehensive transportation network. Alternatives are a key consideration for providing route options to different types of users, who may be traveling for different purposes.
Safety and security – A connected network that is intended to support pedestrian and bicycle travel should provide a safe route to a variety of destinations. Personal security is another area of emphasis.
Comfort – Agencies should not lose sight of the importance of comfort in a person’s decision to walk or bike.
Source: FHWA. (2015). Case Studies in Delivering Safe, Comfortable and Connected Pedestrian and Bicycle Networks. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/network_report/

## Slide 29: Principles -- Low-Stress Bicycle Networks
“An all ages and abilities network”
Emphasis on quality of bikeway over mere presence
Serve a broad audience of existing and potential bicyclists
FHWA, Bikeway Selection Guide
Notes: Notes: The target design user influences the safety, comfort, connectivity, and cohesion of the bicycle network. Exposure to high motor vehicle traffic speeds and volumes is the primary contributor of stress. High-comfort/low-stress networks serve the most people while low-comfort/high-stress networks serve the least. A Low-Stress Bicycle Network (also referred to as an “all ages and abilities network” or a “high comfort network”) is one that is designed to be safe and comfortable for all users. By serving a broad audience of existing and potential bicyclists, low-stress networks maximize system use by serving high percentages of shorter distance transportation and utilitarian trips for all types of bicyclists.
Source: FHWA (2019). Bikeway Selection Guide. Available: https://safety.fhwa.dot.gov/ped_bike/tools_solve/docs/fhwasa18077.pdf

## Slide 30: Bikeways

## Slide 31: Bicycle Network
A seamless interconnected system of bikeways
Thoughtfully planned to provide necessary and desired connections and access
Informs bikeway type selection by showing where higher quality facilities are needed most
pedbikeimages.org – Chicago DOT
Notes: Notes: What type of bikeway should be chosen on this street or in this plan given real-world context, constraints, and opportunities?
Source: FHWA (2019). Bikeway Selection Guide. Available: https://safety.fhwa.dot.gov/ped_bike/tools_solve/docs/fhwasa18077.pdf
Image: http://www.pedbikeimages.org/mediumimages/alyson%20west%20-%20youngboybikelanePFB.jpg

## Slide 32: Principles -- Bike Lanes
Bikeway type selection should not be done in isolation. Selection should consider seven principles:
  Safety
  Comfort
  Connectivity
  Directness
  Cohesion
  Attractiveness
  Unbroken flow
FHWA, Bikeway Selection Guide
Notes: Notes:
Safety – The frequency and severity of crashes are minimized and conflicts with motor vehicles are limited.
Comfort – Conditions do not deter bicycling due to stress, anxiety, or concerns over safety.
Connectivity – All destinations can be accessed using the bicycle network and there are no gaps or missing links.
Directness – Bicycling distances and trip times are minimized.
Cohesion – Distances between parallel and intersecting hike routes are minimized.
Attractiveness – Routes direct bicycles through lively areas and personal safety is prioritized.
Unbroken flow – Stops, such as long waits at traffic lights are limited and street lighting consistent.
Source: FHWA, Bikeway Selection Guide (2019). Available: https://safety.fhwa.dot.gov/ped_bike/tools_solve/docs/fhwasa18077.pdf

## Slide 33: Bikeway Degree of Separation
FHWA
Notes: Key Message: Image shows bikeway facilities by increasing degrees of separation.
Connection to Other Module: Trails will cover the last category – off-street trails and sidepaths.
Source: FHWA (2015). Separated Bike Lane Planning and Design Guide. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/separated_bikelane_pdg/page00.cfm

## Slide 34: Separated Bike Lanes
Exclusive facility for bicyclists physically separated from motor vehicle traffic
Integral to the development of low-stress bicycle networks
  Enhance safety for all road users
  Encourage more bicycling
  Preferred by bicyclists and motorists alike
FHWA, Separated Bike Lane Guide
Notes: Notes: A separated bike lane—also referred to as a cycle track or protected bike lane—is an exclusive facility for bicyclists that is located within or directly adjacent to the roadway and is physically separated from motor vehicle traffic with a curb, median, or other vertical element. On-street parking may supplement physical separation. Separated bike lanes are integral to the development of low-stress bicycle networks because they enhance safety for all road users, encourage more bicycling, and are preferred by bicyclists and motorists alike.
Source:
FHWA. (2015). Separated Bike Lane Planning and Design Guide. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/separated_bikelane_pdg/page00.cfm
FHWA. (2016). Achieving Multimodal Networks: Applying Design Flexibility & Reducing Conflicts. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_networks/

## Slide 35: Separated Bike Lanes
Once an SBL has been identified, the design process can be summarized by these four steps:
  Establish directional and width criteria
  Select forms of separation
  Identify midblock design challenges and solutions
  Develop intersection design
NYC DOT
Notes: Notes: The categories listed on the slide form the basis of a four-step design process where the decisions within each step inform future design decisions, resulting in an iterative design process based on available street width, transportation priorities, and other project goals. The selection of separated bike lane width and directional characteristics depends on a combination of factors that are most often determined by the existing street and surrounding network characteristics. The most critical considerations are to reduce conflicts with turning vehicles, provide enough width for safe operations and ease of maintenance, and ensure predictable behavior by the street users.
Source: FHWA. (2015). Separated Bike Lane Planning and Design Guide. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/separated_bikelane_pdg/page00.cfm

## Slide 36: SBL Four-Step Design:
Direction and width
  Reduce conflicts with turning vehicles, provide sufficient width for safe operations and ease of maintenance, and ensure predictable behavior by the street users
Form of separation
  Delineator posts, bollards, concrete barrier, raised median, planters, raised lanes, parked cars, parking stops
Midblock considerations
  Driveways, transit stops, accessible parking, loading zones
Intersection design
  Turning movements, intersection design, signalization strategies, signal phasing, bicycle turning movements
Notes: Key Message: Providing one-way separated bike lanes on each side of a two-way street creates a predictable design for managing user expectations, but there are many other configurations to consider, including two-way separated bikes on one-way or two-way streets or a center-running alternative.
Notes: Images shown on next slide.
Source: FHWA. (2015). Separated Bike Lane Planning and Design Guide. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/separated_bikelane_pdg/page00.cfm

## Slide 37
Austin, TX
Decatur, GA
St. Louis, MO
Seattle, WA
Notes: Images from pedbikeimages.org
Top left: Kristen Brookshire http://www.pedbikeimages.org/mediumimages/Kristen%20Brookshire%20-%20StLouis_SBL.jpg
Top right: Cheryl Burnette http://www.pedbikeimages.org/mediumimages/48b67f8033ae54e292802844e47a6e28.jpg
Bottom left: Toole Design Group http://www.pedbikeimages.org/mediumimages/Toole%20Design%20Group%20Dropbox%20-%2020140925_115345.jpg
Bottom right: Greg Griffin http://www.pedbikeimages.org/mediumimages/7729823002_7fba814860_k.jpg

## Slide 38: On-Street Bike Lanes
Designated by pavement markings and signs
Recommended width: 5-6’
On-street marking width: 7’
Pedbikeimages.org – Dan Burden
Pedbikeimages.org – Lyubov Zuyeva
Notes: Notes: On-street bicycle lanes are recommended to be 5-6’ wide from the face of a curb to the bike lane stripe. Bicycle lanes wider than 6’ are not recommended without special markings as motorists may view them as travel lanes. When on-street parking is present adjacent to bicycle lanes, the minimum lane width is 5’ to encourage bicycles to ride outside the ‘door zone’.
Source: Federal Highway Administration. (2006). University course on bicycle and pedestrian transportation: Bicycle lanes. (Publication No. FHWA-HRT-05-113). McLean, VA: Federal Highway Administration.
Image (left): http://www.pedbikeimages.org/mediumimages/bike.crossings.boulder-(99).jpg
Image (right): http://www.pedbikeimages.org/mediumimages/Asheville_BufferedBikeLane_onthebridge.jpg

## Slide 39: On-Street Bike Lanes: Door Zone
Pedbikeimages.org – Dan Burden
Notes: Key Message: These images show how the entire width of a bike lane may not be safely used by bicyclists when the bike lane is immediately adjacent to on-street vehicle parking. Design solutions include marking a buffer space or floating the parking out next to the travel lane to create a separated bike lane adjacent the curb.

## Slide 40: Bike Boxes
Advance stop lines 3-5 m (~10-16 ft) ahead of cars at intersections
Enhance cyclist visibility and safety
In Copenhagen, 117 intersections equipped with advance stop lines, traffic signal priority, and special lane markings for cyclists
Pedbikeimages.org – Toole Design Group
Notes: Source: Pucher, J. R., & Buehler, R. (Eds.). (2012). City Cycling. Cambridge, MA: MIT Press.

## Slide 41: Resurfacing: Opportunity for Bicycle Network Development
Methods for retrofitting bike lanes on existing streets:
  Reduction of travel lane width
  Road diet
  Removal, narrowing, or reconfiguration of parking
  Other design options
Randy Dittberner, Virginia DOT
Notes: Key Message: Adding a bikeway during a resurfacing project requires reconfiguration of the existing roadway design to "create" the space for the new bicycle facilities.
Notes: Nearly every agency that maintains roadways has a resurfacing process or schedule. The process is typically built around the consideration of pavement conditions as a key determining factor in scheduling resurfacing projects-that is, the worse the pavement, the higher a roadway will rank on the resurfacing list. In addition to pavement condition, other factors are sometimes considered when evaluating streets for resurfacing, such as improving safety or the opportunity to provide bicycle facilities. However, due to the need for additional time for plan development, public outreach, and the design of new marking plans, this process is often not conducive to adding bicycle facilities during a resurfacing project. Several factors that will enhance the feasibility of including bikeways through the resurfacing process are:
Providing adequate time
Multimodal approach and including key staff
Review the bike plan
Flexibility in design (flexibility is necessary in two areas: process and design)
Connection to other Module: Module on Temporary Facilities and Maintenance
Source: FHWA. (2016). Incorporating On-Road Bicycle Networks into Resurfacing Projects. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/resurfacing/resurfacing_workbook.pdf

## Slide 42: Shared Roadways
A roadway open to both bicycle and motor vehicle travel where bicyclists and motorists negotiate the space
  Lack of separation
  Motorists have a large advantage
  Creates stressful environment for bicyclists
Comfort and safety varies based on traffic operating speeds and volumes
Pedbikeinfo.org – Carl Sundstrom
Notes: Key Message: In shared lanes, bicyclists ride in mixed traffic, therefore their comfort and safety varies widely based on traffic operating speeds and volumes. Shared lanes can be a positive and affordable solution when designed correctly and used in the correct context; however, most bike/car crashes in the U.S. occur in shared lanes that are applied to inappropriate contexts and environments.
Notes: The terms “shared lanes” or “shared roadways” may encompass streets with shoulders (often in a rural context), wide outside lanes, or lanes with shared lane markings that indicate where in the roadway and the direction bicyclists are supposed to travel. Shared lane markings may be used on streets with speed limits of 35 miles per hour or less.
Source: FHWA. (2019). Bikeway Selection Guide. Available: https://safety.fhwa.dot.gov/ped_bike/tools_solve/docs/fhwasa18077.pdf

## Slide 43: Shared Roadways – Bicycle Boulevards
A low-stress roadway that offers priority to bicyclists
Combination of pavement markings, traffic calming, and route signs
Pedbikeimages.org - Adam Fukushima
FHWA
Notes: Key Message: The bicycle boulevard builds on the shared roadway concept, using a combination of traffic calming devices on neighborhood streets that slow and divert motor vehicle traffic while allowing through-street access for bicycles. This design is most effective in traditional street grids with alternative routes for heavier motor vehicle traffic.
Notes:
Opportunity—Traditional street grids offer many miles of local streets that can be converted to bicycle boulevards.
Bicycle boulevards can improve conditions for pedestrians, with reduced traffic and improved crossings.
Bicycle boulevards may attract new or inexperienced cyclists who do not feel comfortable on arterials and prefer to ride on lower traffic volume streets.
Low cost—The major costs are for traffic control and traffic calming devices.
Traffic calming techniques are increasingly favored by residents who want slower traffic on neighborhood streets.
Bicycle travel on local streets is usually compatible with local land uses.
Source:
PBIC (2011). Graduate Course on Pedestrian and Bicycle Planning
FHWA. (2016). Small Town and Rural Multimodal Networks Guide. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/small_towns/
Image (bottom left): http://ruraldesignguide.com/files/mixed-traffic/bicycle-boulevard/2-5.jpg
Image (top right): https://www.pedbikeimages.org/details.php?picid=1557

## Slide 44: Shared Roadways - Europe
Many Dutch & German residential streets are traffic-calmed to 30 km/h (~18.6 mi/h) or less
Many home zones where speed limit is “walking speed” (<7 km/h or ~4.3 mi/h)
  Permits walking, bicycling, and playing on the street
  Implemented with few changes to street design
  177 home zones in Freiburg, Germany
Notes: Source: PBIC (2011). Graduate Course on Pedestrian and Bicycle Planning.

## Slide 45: Walkways

## Slide 46: Sidewalk Corridors
Pedestrian realm
  Frontage zone
  Pedestrian zone
  Furniture zone
General principles
Smooth surface
Meets minimum “Pedestrian Access Route” width
Clear of obstructions
Notes: Key Message: Sidewalks reduce the “walking along the road” crash type.
Notes: All pedestrian facilities must meet ADA requirements. A clear travel way should be maintained by keeping a sidewalk clear of obstructions. The minimum “Pedestrian Access Route” is a continuous and unobstructed clear width that should be measured from the back of the curb (when furniture zone is not present). The zone system is helpful for illustrating this point (shown on the next slides). Randomly arranged street furniture clutters the sidewalk and creates an “obstacle course.”
To prevent the problems created by narrow curbside sidewalks, designers should consider the sidewalk the entire area that extends from the property line to the curb line.
Furthermore, the pedestrian corridor should be separated into four distinct zones to prevent the various functions of the sidewalk from being in conflict. The four zones are:
Curb zone
Planter/furniture zone
Pedestrian/walking zone
Frontage zone
The term “sidewalk corridor” encompasses these four zones.
Connection to other Module: Accessibility and ADA
Source: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 47: Sidewalk Corridors
Notes: Notes: The pedestrian realm is commonly referred to as the sidewalk. It is divided it into four zones, much like the segmentation of a roadway. The figure illustrates various arrangements of the zones, which are highly contextual and location specific. There are numerous permutations for high-quality pedestrian realm design.
The frontage zone is the area between the walkway and building, fence or yard. Typically this is the edge of the right of way. It may be nothing more than the “shy” distances adjacent to a building (the place where people stand to window shop, where the utility meters are, and where the door mat is). Or it may contain a stoop, outdoor café, landscaping, benches, and bike parking. Where there is a front lawn with no fence, the frontage zone width is zero.
The walking zone is the area dedicated to walking. Just like any travel lane, it should provide a logical path of travel. It must be ADA-compliant and clear of all obstructions. It should be straight and continuous. Attempts to create meandering sidewalks usually fail because people want to walk in the most direct route possible. It should be sized to provide enough space for the expected pedestrian volumes, but not overly wide as to appear barren.
The sidewalk furniture zone is located between the curb and walking zones, and contains items such as street trees, planters, bus shelters, parking meters, utility poles and boxes, lamp posts, signs, bike racks, news racks, benches, waste receptacles, and drinking fountains. Placing these items in this zone keeps the walking zone free of obstructions. This zone is often landscaped in residential neighborhoods and provides some level of separation between children playing on the sidewalk and moving traffic.
The curb zone is the space immediately next to the roadway and may be used by people getting in and out of vehicles or for loading and unloading (whether such uses are permitted or not).
Source: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course

## Slide 48: Sidewalk Elements
Curb ramps
  2 ramps at each corner are best
  Level landings should be provided
Detectable warnings
  Replaces missing edge cue (i.e., curb)
  Does not designate the best place to cross or provide alignment information
NACTO
Notes: Key Message: Curb ramp design is especially important for wheelchair users. Corners should typically have 2 curb ramps, one for each street that is to be crossed. Curb ramps should also be designed to include level landings, without which the sidewalk can be quite difficult to navigate in a wheelchair. Detectable warnings, a distinctive surface pattern of domes detectable by cane or underfoot, are used to alert people with vision impairments of their approach to streets and hazardous drop-offs. The ADA Accessibility Guidelines (ADAAG) require these warnings on the surface of curb ramps, which do not have the tactile cue otherwise provided by curb faces, and at other areas where pedestrian walkways blend with vehicular travelways. Detectable warnings must be installed in a color that contrasts with the adjoining surface, either light on dark or dark on light.
Connection to other Module: Module on ADA and Accessibility
Source:
Federal Highway Administration. (2001). Designing sidewalks and trails for access, Part II of II: Best practices design guide. Available: http://www.fhwa.dot.gov/environment/sidewalk2/
ADA for Roadway Design [PowerPoint Presentation] (2016). TRB Tools of the Trade. Dean Perkins, Florida DOT.
Image (bottom right): https://nacto.org/wp-content/themes/sink_nacto/views/design-guides/retrofit/urban-street-design-guide/images/corner-radii/curb-radius.png

## Slide 49: Walkways and Bikeways -- Rural Design
Think creatively to establish connected facilities within communities
Many facilities can support walking and bicycling access to key destinations
FHWA
Notes: Key Message: In many small towns and rural communities, active transportation is even more common than it is in urban areas. However, infrastructure to support active transportation is often limited or absent. The image on the slide shows how adjacent roadways or shared use paths may complement the transportation function the primary roadway (in this case, a state road).
Notes: Many small and rural communities are located on State and county roadways that were built to design standards that favor high-speed motorized traffic, resulting in a system that makes walking and bicycling less safe and more uncomfortable. These roadways can be retrofitted and redesigned over time to provide a transportation network that better serves the safety, health, and economic interests of the community. A safe and direct network provides convenient access to key destinations, while minimizing exposure to motor vehicle traffic. In addition to physical safety, user comfort is an important aspect of a multimodal network. Typically, additional separation between motor vehicles and those walking or bicycling or slowing motor vehicles to walking and bicycling compatible speeds, is desired to create a more comfortable network.
Connection to other Module: The module on User and Mode Characteristics covers common design challenges in rural areas.
Source: FHWA. (2016). Small Town and Rural Multimodal Networks. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/small_towns/

## Slide 50: Walkways and Bikeways -- Rural Design
Notes: Notes:
Top left: Mixed facility – yield road
Top right: Visually separated facility – advisory path
Bottom left: physically separated facility – shared use path
Bottom middle: physically separated facility – bike path
Bottom right: physically separated facility – bike path
Source:
Upper left: FHWA. (2016). Small Town and Rural Multimodal Networks. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/small_towns/
Upper right: Western Transportation Institute (CC-BY-SA), Rural Design Guide Image Gallery
Bottom left: Alta Planning + Design (CC-BY-SA), Rural Design Guide Image Gallery
Bottom center: Alta Planning + Design (CC-BY-SA), Rural Design Guide Image Gallery
Bottom right: Alta Planning + Design (CC-BY-SA), Rural Design Guide Image Gallery

## Slide 51: Crosswalk Visibility
What a pedestrian sees
Notes: Key Message: Marked crosswalks must be visible to the DRIVER. These crosswalk markings are in very poor condition but are still visible to a pedestrian waiting to cross.
Source: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 52: Crosswalk Visibility
What a driver sees
Notes: Key Message: The same crosswalk is virtually invisible to the driver; yet it’s the driver who is expected to react to this traffic control device.
Source: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 53: Summary
The traditional approach to engineering roadways prioritizes the flow of motor vehicles
Agencies and professional organizations are adopted a more context sensitive approach that recognizes tradeoffs for all modes
Designers are encouraged to use their judgment, document their decisions, and consider experimentation
Lane width, driveways, and curb radii affect the safety and comfort of people walking and bicycling
A connected bicycle network will include facilities with varying degrees of separation