## Slide 1: Strategies for Safer Speeds
Instructor course information
Notes: Report No. FHWA-SA-19-034

## Slide 2: Module Outline
Introduction to the problem of speed and speeding
  Crashes and risk
  The role of policy
  85th percentile speed
  Vision Zero
Strategies for safer speeds
  Setting speed limits
  Automated speed enforcement
  Road design (including road diets and traffic calming)

## Slide 3: Introduction to speed and Speeding
Notes: Key Message: Vehicle speed seriously impacts pedestrian and bicyclist safety not only by increasing the chances of a crash, but also by increasing the risk of death when these vulnerable road users are involved in a crash.

## Slide 4: Speeding
Traveling too fast for conditions or in excess of the posted speed limits
  Nearly 30% of all fatal motor vehicle crashes in the nation are speeding-related
Poses a significant risk of death and injury to not only drivers and passengers of speeding vehicles, but also other road users
Complex issue involving engineering, driver behavior, education, and enforcement
Speeding as the cause of a crash is likely underreported
Notes: Notes: The definition of speeding offered in the first bullet is uniform, but the investigation and reporting of crashes is much less uniform across states and jurisdictions. For example, some state crash report forms only allow officers to select one or two contributing causes. Speeding involvement in pedestrian and bicyclist fatalities was reported only about 8% of the time (8.0% for pedestrians and 8.6% for bicyclists).
Source:
FHWA. “Safety Performance Management.” Available: https://safety.fhwa.dot.gov/hsip/spm/ [Accessed June 2019]
NHTSA. (May 2014). Speed Management Program Plan. Available: https://www.nhtsa.gov/sites/nhtsa.dot.gov/files/812028-speedmgtprogram.pdf
Tara Casanova Powell. (January 2019). Speeding Away From Zero: Rethinking a Forgotten Traffic Safety Challenge Governors Highway Safety Association. Available: https://www.ghsa.org/resources/Speeding19

## Slide 5: Speeding-involved Fatalities by Posted Speed Limit
Pedestrian
Bicyclist
NHTSA
Notes: Notes: Fatality data combined for 2010 through 2015.
Student Question: Our experience tells us that posted speed limit does not equal the actual speed of travel, but does looking at the posted speed limit help you conjure an image of the type of roadway design? What about the number of people walking and bicycling – which streets would you expect to see more people walking and bicycling?
Source: Coleman, H., & Mizenko, K. (2018, March). Pedestrian and bicyclist data analysis (Research Note. Report No. DOT HS 812 502). Washington, DC: National Highway Traffic Safety Administration. Available: https://www.nhtsa.gov/sites/nhtsa.dot.gov/files/documents/812502_pedestrian-and-bicyclist-data-analysis-tsf-research-note.pdf

## Slide 6: Fatalities by Posted Speed Limit and Land Use
Pedestrian
Bicyclist
NHTSA
Notes: Key Message: Fatal pedestrian and bicyclist crashes were more likely to occur on roads with lower posted speed limits in urban areas than in rural areas.
Notes: Fatality data combined for 2010 through 2015.
Source: Coleman, H., & Mizenko, K. (2018, March). Pedestrian and bicyclist data analysis (Research Note. Report No. DOT HS 812 502). Washington, DC: National Highway Traffic Safety Administration. Available: https://www.nhtsa.gov/sites/nhtsa.dot.gov/files/documents/812502_pedestrian-and-bicyclist-data-analysis-tsf-research-note.pdf

## Slide 7
Governors Highway Safety Association
Notes: Key Message: Recent studies have also suggested that even small decreases in travel speed can reduce pedestrian crash and injury severity. For example, research on the relationship of speed and crash severity at speeds under 30 mph shows an increase of 1 or 2 mph in vehicle impact speed results in significantly higher risk of severe injury and fatality for pedestrians (Kroyer, Jonsson, and Várhelyi 2013).
Source:
Kröyer, H. R.G., Jonsson, T., & Várhelyi, A. (2013). Relative fatality risk curve to describe the effect of change in the impact speed on fatality risk of pedestrians struck by a motor vehicle. Accident Analysis and Prevention, 62, 143-152
Powell, Tara Casanova. (January 2019). Speeding Away From Zero: Rethinking a Forgotten Traffic Safety Challenge Governors Highway Safety Association. Available: https://www.ghsa.org/resources/Speeding19
Image: https://www.ghsa.org/sites/default/files/publications/files/PedestrianFatalityRisk.jpg

## Slide 8
FHWA (data from 2011 AAA Foundation study)
Notes: Notes: Think beyond the point of impact and consider how speed affects the peripheral vision of drivers.
Source:
FHWA. (2016). Achieving Multimodal Networks: Applying Design Flexibility & Reducing Conflicts. Available: https://www.fhwa.dot.gov/environment/bicycle_pedestrian/publications/multimodal_networks/
Tefft, B.C. (2011). Impact Speed and a Pedestrian’s Risk of Severe Injury or Death. AAA Foundation for Traffic Safety.

## Slide 9: Federal Policy
No national maximum speed limit
Grant funds through NHTSA may be used to address speeding
“Current federal-aid programs do not ensure that states fund speed management activities at a level commensurate with the national impact of speeding on fatalities and injuries.”
- National Transportation Safety Board, 2017
Notes: Sources:
National Transportation Safety Board. (2017). Reducing Speeding-Related Crashes Involving Passenger Vehicles. Safety Study NTSB/SS-17/01. Washington, DC.
Powell, Tara Casanova. (January 2019). Speeding Away From Zero: Rethinking a Forgotten Traffic Safety Challenge Governors Highway Safety Association. Available: https://www.ghsa.org/resources/Speeding19

## Slide 10: State Policy
Setting speed limits
  Laws set maximum speed limit for each type of roadway and for special situations (e.g., school zones)
  Trend toward increasing speed limits at the higher end, with limited examples of states giving more local control at the lower end
Automated enforcement
  Enact legislation to permit, limit, or prohibit
Notes: Notes: Many state legislatures have contributed to a new national trend of authorizing even higher speed limits on freeways and interstates. At the same time, some states, often in conjunction with Vision Zero efforts, are authorizing localities to reduce their maximum speed limit with the intent of creating a safer travel environment for vulnerable road users. Examples can be found in Washington, New York, and Massachusetts. An automated enforcement system uses an electronic camera to enforce traffic laws by assisting with detection of infractions and providing photo documentation of the vehicle or driver violating the traffic law. Studies on automated speed enforcement (ASE) consistently show statistically significant reductions in crashes following the introduction of ASE, yet only 137 U.S. communities in 14 states (plus the District of Columbia), currently use ASE (IIHS, May 2019). Commonly cited concerns include legal questions and public opinion.
Source:
Powell, Tara Casanova. (January 2019). Speeding Away From Zero: Rethinking a Forgotten Traffic Safety Challenge Governors Highway Safety Association. Available: https://www.ghsa.org/resources/Speeding19
Insurance Institute for Highway Safety, “Speed.” Available: https://www.iihs.org/topics/speed#effects-of-speed-limits-on-safety. [Accessed May 2019].
Poole, B., Johnson, S., and Thomas, L. (December 2017). An Overview of Automated Enforcement Systems and Their Potential for Improving Pedestrian and Bicyclist Safety. Pedestrian and Bicycle Information Center. Chapel Hill, NC.
Image: S4-5 from Figure 7B-1 (School Area Signs) in the 2009 edition of FHWA’s MUTCD.

## Slide 11: What determines speed?
Design speed
  A selected speed used to determine the various geometric design features of the roadway
Posted speed
  An operational decision for which the owner and operator of the facility is responsible (subject to State statutes)
Operating speed
  Drivers’ speed based on their individual perception of safety and comfort
Notes: Notes: The definition of design speed comes from the AASHTO Green Book, which recommends that topography, anticipated operating speed, adjacent land use, and functional classification be considered in this decision. Anticipated operating and posted speeds should be considered in the selection of the design speed, but there is no regulation establishing a more direct relationship.
Source: FHWA. (October 7, 2015). Memo “Information: Relationship between Design Speed and Posted Speed.” Available: https://www.fhwa.dot.gov/design/standards/151007.cfm

## Slide 12: 85th Percentile Speed
The speed at or below which 85% of drivers are traveling at during free-flow traffic conditions
A “spiral of cause and effect”:
  Post-1918: preferences of growing mass of motor vehicle operators for wider roads and faster speeds
  Designers build roads for “anticipated use”
  The use of 85th percentile speed to set speed limits emerged as early at the 1940s; it remains common practice
Notes: Notes: “after 1918, highway design followed a spiral of cause and effect, resulting in faster and faster speeds and wider and wider pavements. The motivating force behind this spiral was the driving speed preferences of the great mass of vehicle operators. The public authorities were never able to impose or enforce speed limits for very long if the majority of drivers considered the limits unreasonably low. Now, many current engineering practices use the 85th percentile speed—or the speed at which the majority of drivers travel—as the method of setting speed limits.” (from Road Safety Fundamentals).
Student Question: Ask students to consider the “spiral of cause and effect.” What problems arise when using 85th percentile speeds to set speed limits? [students may mention that raising the speed limit to the 85th percentile effectively increases the 85th percentile speed or that deferring to driver behavior ignores an area’s crash history or the safety of people walking and bicycling].
Source:
National Transportation Safety Board. (2017). Reducing Speeding-Related Crashes Involving Passenger Vehicles. Safety Study NTSB/SS-17/01. Washington, DC.
FHWA. (2017). Road Safety Fundamentals; Concepts, Strategies, and Practices that Reduce Fatalities and Injuries on the Road. UNIT 1: Foundations of Road Safety. U.S. Department of Transportation. Available: https://rspcb.safety.fhwa.dot.gov/rsf/Unit1.aspx#ch2

## Slide 13: Vision Zero
A strategy to eliminate all traffic fatalities and severe injuries, while increasing safe, healthy, equitable mobility for all
Key priorities:
  Managing speed
  Centering equity
  Engaging communities
Vision Zero Network
Notes: Key Message: Vision Zero challenges the assumption that traffic deaths and severe injuries are inevitable side effects in our transportation system. Broadly, Vision Zero is an approach to traffic safety that can be put into action by agencies that adopt policies, action plans, and new practices designed to eliminate traffic fatalities and serious injuries. This strategy was first adopted in Sweden in the 1990s but is spreading across the United States.
Source: Vision Zero Network. “What is Vision Zero.” Available: https://visionzeronetwork.org/about/what-is-vision-zero/ [Accessed May 2019].

## Slide 14: Strategies for Safer Speeds

## Slide 15: High-Visibility Enforcement
Officers target certain high-crash or high-violation geographical areas using expanded patrols
  Intended to convince the public that speeding and aggressive driving actions are likely to be detected and that offenders will be arrested and punished
  Research findings on effectiveness are inconclusive
Pedbikeimages.org – Dan Burden
Notes: Key Message: This is a labor-intensive approach that has not been demonstrated to be effective, yet it is still standard practice for many law enforcement agencies across the county.
Source: Richard, C. M., Magee, K., Bacon-Abdelmoteleb, P., & Brown, J. L. (2018). Countermeasures that work: A highway safety countermeasure guide for state highway safety offices (Final Report No. DOT HS 812 478, 9th ed.) (p. 567). McLean, VA: National Highway Traffic Safety Administration.

## Slide 16: Automated Speed Enforcement (ASE)
Highly effective – 28 studies showed crash reductions between 8% and 49%
Limited use – only 14 states and D.C. allow their use (as of 2018)
Public support
  Studies show maintained or increased public support for ASE after implementation
Support from professional associations
  GHSA, AASHTO, NACTO
Notes: Notes: An automated enforcement system uses an electronic camera to enforce traffic laws by assisting with detection of infractions and providing photo documentation of the vehicle or driver violating the traffic law. Cameras can be fixed or mobile. Some jurisdictions refer to speed cameras as “safety cameras.” Most speed cameras measure the speed of a vehicle at a single spot, but more recent technology can measure average speeds over a certain distance (used in Australia and the United Kingdom). Speed cameras usually are programmed so they will not be activated unless a vehicle is traveling significantly faster than the posted limit — typically 10 or 11 mph faster, although in certain places such as school zones the tolerance may be lower. Recent evaluations are available from Portland, OR; New York City; and Montgomery County, MD. Some states use them in work zones.
AAA Foundation asks about ASE as part of its annual national survey. In 2017, 48% of drivers ages 16 and older said they supported the use of speed cameras on residential streets.
Sources:
Powell, Tara Casanova. (January 2019). Speeding Away From Zero: Rethinking a Forgotten Traffic Safety Challenge Governors Highway Safety Association. Available: https://www.ghsa.org/resources/Speeding19
Insurance Institute for Highway Safety, “Speed.” Available: https://www.iihs.org/topics/speed#effects-of-speed-limits-on-safety. [Accessed May 2019].
Poole, B., Johnson, S., and Thomas, L. (December 2017). An Overview of Automated Enforcement Systems and Their Potential for Improving Pedestrian and Bicyclist Safety. Pedestrian and Bicycle Information Center. Chapel Hill, NC.
National Transportation Safety Board. (2017). Reducing Speeding-Related Crashes Involving Passenger Vehicles. Safety Study NTSB/SS-17/01. Washington, DC.

## Slide 17: Decreasing Speed Limits
Pedestrian and Bicycle Information Center (Source: Table 3E-2 from Highway Safety Manual, 1st ed.)
Notes: Key Message: Pedestrians and bicyclists are particularly vulnerable to speeding and to incrementally higher speeds in general.
Notes: Most of the research about the effect of changing speed limits has been conducted on higher speed roads, but new research is emerging as agencies evaluated speed limit reductions as part of Vision Zero strategies. Speeds tend to change by smaller amounts than the change in limits.
Source: Poole, B., Johnson, S., and Thomas, L. (December 2017). An Overview of Automated Enforcement Systems and Their Potential for Improving Pedestrian and Bicyclist Safety. Pedestrian and Bicycle Information Center. Chapel Hill, NC.

## Slide 18: Example - Boston
www.iihs.org
Notes: Notes: Boston lowered the default speed limit on city streets from 30 mph to 25 mph beginning January 9, 2017. It publicized the change via advertisements, social media and traditional media outlets. The city's move came after the Massachusetts legislature in 2016 amended state law to allow cities and towns to lower speed limits from 30 mph to 25 mph on municipal roads in densely populated areas or business districts. Unless otherwise posted, the speed limit on all City of Boston roadways is 25 mph. Researchers used Providence, Rhode Island, as a control cite and studied arterials, collectors, and local roads in both cities. Future research will examine changes in crashes.
Source: Insurance Institute for Highway Safety. “City drivers slow down for lower speed limit in Boston.” (August 28, 2018). Available: https://www.iihs.org/news/detail/city-drivers-slow-down-for-lower-speed-limit-in-boston
Image (left): https://www.iihs.org/media/4e90439f-383c-4036-8616-d1223d19ce79/FXPzKw/News/082818-Boston.jpg

## Slide 19: Street Design
Dan Burden – pedbikeimages.org
Notes: Key Message: Roadway infrastructure is generally more costly to deploy than behavioral interventions like enforcement and education, but streets are the foundation of a safe environment for walking and bicycling.

## Slide 20
FHWA
Notes: Key Message: The intended speed of this road is 35 miles per hour, but the wide design of the road and the number of lanes leads drivers to drive much faster.
Source: FHWA. (2017). Road Safety Fundamentals; Concepts, Strategies, and Practices that Reduce Fatalities and Injuries on the Road. UNIT 1: Foundations of Road Safety. U.S. Department of Transportation. Available: https://rspcb.safety.fhwa.dot.gov/rsf/Unit1.aspx#ch2
Image: https://rspcb.safety.fhwa.dot.gov/rsf/images/unit1_speedLimit35.png

## Slide 21: Street Design
Drivers respond to visual cues
Street geometry
Landscape
Development
Intersections
Perceived conflict
Perceived safety
Brandon Whyte - Pedbikeimages.org

## Slide 22
These two roads might have same speed limit, but are designed to signal and encourage very different behaviors
Dan Burden – pedbikeimages.org

## Slide 23: Traffic Calming
“To support the livability and vitality of residential and commercial areas through improvements in non-motorist safety, mobility, and comfort.” FHWA & ITE
FHWA
Alta Planning + Design (CC-BY-SA)
Notes: Key Message: These objectives are typically achieved by reducing vehicle speeds or volumes on a single street or a street network. Traffic calming measures consist of horizontal, vertical, lane narrowing, roadside, and other features that use self-enforcing physical or psycho-perception means to produce desired effects.
Source: FHWA. (2017). Traffic Calming ePrimer. Available: https://safety.fhwa.dot.gov/speedmgt/traffic_calm.cfm. Accessed May 2019.
Left image – Altamont, New York http://ruraldesignguide.com/files/photos/pg4-24_Alta.jpg
Right image – Alexandria, Virginia

## Slide 24: Traffic Calming
Reduces traffic speed
Reduces motor vehicle collisions
  When collisions do occur, traffic calming can diminish their severity
Enhances drivers’ ability to see and react
Improves safety for pedestrians and cyclists
Can increase pedestrian and bicycling activity
pedbikeimages.org – Lyuba Zuyeva
Notes: Source: Powell, Tara Casanova. (January 2019). Speeding Away From Zero: Rethinking a Forgotten Traffic Safety Challenge Governors Highway Safety Association. Available: https://www.ghsa.org/resources/Speeding19
Image: http://www.pedbikeimages.org/mediumimages/Median_Chokers_onLakeAve_InmanPark.jpg

## Slide 25: Examples of Traffic Calming Measures
Speed hump/bump/table
Medians/refuge islands
Roundabouts
Raised crosswalks
Raised intersection
Curb extensions
NACTO
Notes: Source: NACTO. (2013). Urban Street Design Guide. Available: https://nacto.org/publication/urban-street-design-guide/

## Slide 26: Traffic Calming Visualized
City of Austin Vision Zero Action Plan 2016-2018
Notes: Key Message: This image shows how geometric design features work in conjunction with traffic signal timing and land use policies (block lengths, building setbacks, and streetscaping) to produce traffic calming effects.
Source: City of Austin. 2016-2018 Vision Zero Action Plan. Available: http://austintexas.gov/visionzero

## Slide 27: Traffic Calming – Curb Radii
Small corner radii = shorter crossing distances and lower vehicle speeds
More visibility for pedestrians and bicyclists
Notes: Source: Federal Highway Administration (2006). University Course on Bicycle and Pedestrian Transportation.

## Slide 28: Road Diets
Notes: Key Message: Purpose and benefits shown on the slide.
Connection to other Module: Road diets are also covered in Designing for Walking and Bicycling.
Source: Federal Highway Administration, Proven Safety Countermeasures. Available: https://safety.fhwa.dot.gov/provencountermeasures/road_diets/

## Slide 29: Before…
NACTO
Notes: Source: NACTO. (2013). Urban Street Design Guide. Available: https://nacto.org/publication/urban-street-design-guide/

## Slide 30: …After
NACTO
Notes: Notes: Notice: still has same amount of travel lanes, still has street parking, but safer and more hospitable for all users.
Source: NACTO (2013). Urban Street Design Guide. Available: https://nacto.org/publication/urban-street-design-guide/

## Slide 31: Benefits of Road Diets
Reduces pedestrian crossing distance
Reduces “multiple threat” crash types
May provide room for pedestrian refuge island to break crossing into two simpler crossings
Reduces top end travel speeds
Buffers sidewalk from travel lanes (parking or bike lane)
Reclaims street space for “higher and better use” than moving peak hour traffic
Notes: Key Message: Appropriate road diets provide many benefits to pedestrians, bicyclists, and other road users. A road diet can be a low-cost safety solution when planned in conjunction with a simple pavement overlay, and the reconfiguration can be accomplished at no additional cost.
Sources: FHWA/PBIC. (2009). Planning and Designing for Pedestrian Safety Course.

## Slide 32: Before…
FHWA
Notes: Source: Federal Highway Administration. (2018). Road Diet Countermeasure Tech Sheet. Every Day Counts 4 – Safe Transportation For Every Pedestrian. Available: https://safety.fhwa.dot.gov/ped_bike/step/docs/techSheet_RoadDiet2018.pdf

## Slide 33: After…
FHWA
Notes: Source: Federal Highway Administration. (2018). Road Diet Countermeasure Tech Sheet. Every Day Counts 4 – Safe Transportation For Every Pedestrian. Available: https://safety.fhwa.dot.gov/ped_bike/step/docs/techSheet_RoadDiet2018.pdf

## Slide 34: Summary
Higher vehicle speeds increase the likelihood and severity of a crash
People generally understand that speeding is risky, but it remains a publicly-accepted driving behavior
Infrastructure-based approaches can prevent or mitigate speeding
Managing speed is a key priority for Vision Zero